## Slide 1: See, AIBO; Run! AIBO Motion and Vision Algorithms
Team Advisor: Ethan J. Tira-Thompson
Teaching Assistant: P. Matt Jennings
Team Members: Haoqian Chen,
Elena Glassman, Chengjou Liao,
Yantian Martin, Lisa Shank, Jon Stahlman

## Slide 2: AIBO:
The Legend.
The Dog…

## Slide 3: History of AIBO
Sony’s Entertainment Robot
AIBO – Artificially Intelligent roBOt
Or aibo – Japanese for “companion”
Originally intended for purchase by home users
Found to be a relatively cheap, versatile platform that could be used by educators and researchers

## Slide 4: AIBO: Technical Specifications
64 bit Processor
20 Degrees of Freedom
Microphone
Accelerometer
Infrared Distance Sensor
Pressure Sensors
The Kitchen Sink

## Slide 5: Tekkotsu
Application framework for AIBO
Under development at CMU’s Robotics Lab
TekkotsuMon - server-side interface to code running on robot
To accomplish our goals, we built upon Tekkotsu platform
Our advisor, Ethan Tira-Thompson, is a chief researcher for the project

## Slide 6: Run, AIBO, Run!
Originally attempted to stabilize image from AIBO’s camera
  Software methods
  New walking motions
Modified walk parameters
Measured performance using accelerometers
Stability vs. Speed

## Slide 7: How Our Walk Was Developed
Tekkotsu’s default walk is taken from CMU’s RoboCup soccer team
Our new motion was created by modifying this walk’s parameters

## Slide 8: Get Your Move On!
Using the TekkotsuMon GUI

## Slide 9: Changing Things Up: The Parameters
Lift Velocity
Down velocity
Lift Time
Down time
Body Height/Angle
Period
Position Coordinates
Hop and Sway

## Slide 10: Accelerometers
Each consists of a mass/spring system
Measure force and displacement on joints as robot walks
We graphed the way force varies with time to evaluate stability of new walking algorithm

## Slide 11: Our Upright Walk vs. CMU RoboCup Walk
RoboCup
Upright
Quarter Speed

## Slide 12: Our Upright Walk vs. CMU RoboCup Walk
RoboCup
Upright
Half Speed

## Slide 13: Our Upright Walk vs. CMU RoboCup Walk
RoboCup
Upright
Three Quarter Speed

## Slide 14: Our Upright Walk vs. CMU RoboCup Walk
RoboCup
Upright
Full Speed

## Slide 15: See, AIBO, See!
Developed an algorithm that allows AIBO to follow a pink line
Gradually improved algorithm based on perceived weaknesses

## Slide 16: How does AIBO see?
CCD Camera
(YUV)
Raw Image Translated on Computer
(RGB)
AIBO

## Slide 17: Segmented Vision
AIBO camera captures YUV format
Bitmapped images are too large to send over network efficiently, so the images must be compressed

## Slide 18: RLE (Run-Length Encoding)
The data is then converted into a series of color run triplets
Triplets are sent to the computer, where they are placed into an array
Vision segmentation and run-length encoding is performed on board the AIBO

## Slide 19: Line Following Algorithms
Hough Transformation
VS.
Hack Algorithm

## Slide 20: Hough Transformation
Represent a line in an image in a different way: Parameter Space
Example – a line in image space can be represented as:
y = mx + y0
The Hough method “transforms” this equation to parameter space:
y0 = y - mx

## Slide 21: Hough Transformation (cont’d)
A discrete parameter space called an accumulator is created. All points in the original image are converted using Hough Transform into this parameter space.
Points with the same slope and y-intercept are accumulated into the same cell of the accumulator.
The highest cell is found, thus finding the most prominent line (marked in red).

## Slide 22: Hough Transformation (cont’d)
Advantages:
  Will almost always find the most prominent line
  Ignores static and foreign objects (unless they have defined edges)
Disadvantages:
  Implementation in a robot is too computationally expensive
  Processes too slow for a real-time image, like the AIBO’s

## Slide 23: A Hack Gains Greatness
A hack is defined as an inelegant and usually temporary solution to a problem
Ironically, the hack line following algorithm we developed (with the help of Alok Ladsariya) became our best solution.

## Slide 24: The Basic Line Following Algorithm
Take in decoded segmented vision
Create RegionMap
  First each pixel is set to pink or not-pink
  Give each pink region a unique number… remember PaintBucket?
Turn toward largest region on horizontal center line

## Slide 25: The Basic Line- Following Algorithm
Primary target – displayed as blue dot
  at intersection of largest region & center row
Direction adjustment
  Turns L if blue dot to L of center column
  Turns R if blue dot to R of center column
A few fundamental assumptions allow us to keep the algorithm simple
  The line will be the largest region
  The line will cross the center row once

## Slide 26: Improvements
Definition: Lost = no regions exist in center row
If lost  stop forward motion & rotate
   determine rotation direction by which side of image contained dot more commonly
    In last 15 frames
Adjust direction with speed proportional to blue dot’s distance from center column

## Slide 27: Algorithm Issues

## Slide 28: Algorithm Issues
A Dashed Line
  The breaks in the line trigger the ‘lost’ behavior briefly
  But even so, the break is not long enough to lose the dog completely.
Walking along happily…
AHH!! BREAK IN THE LINE!!
Found line, walking along happily…

## Slide 29: Algorithm Issues
Branching lines:
  branch recognized as one region
  the average taken of all x values of region’s pixels in center row
  once the shorter branch gets below center row, target jumps to longer branch (line)

## Slide 30: Algorithm Issues
Dog can lose line when
  Special case: line slopes toward center of image
Slope-Opposite-Direction Method
  Two more blue dots
    Above and below center
  used to find slope of the line
  If special case true:
    Compromise and go straight!

## Slide 31: Unsolved Algorithm Issues
Extremely sharp curves (< 90 deg.)
Similar to branching issue (but more troublesome)
    Current algorithm averages X values
    Heads for center between two intersections of line with center row

## Slide 32: Problem: Follow the Line!
…that means don’t follow the square.
A possible solution: Shape Recognition
  Feature Extraction
  Describe regions
FAILURE!

## Slide 33: In the Future: Feature Extraction
Features easy to measure:
  Area
  Perimeter
  Granularity Measurement
And how can their measurements be combined  decision?
Hypothesis: AIBO should choose
  Largest
  Most elongated
  Least grainy
region in image.

## Slide 34: Elongation
Ratio of Perimeter to Area of region
In computer vision, called “Compactness”
C = (P^2) / A
Circle = most compact
Way to differentiate between
  more compact shapes
  and the line.

## Slide 35: Granularity Measurement
Purpose: distinguish between
  clear lines and grainy regions
From each pixel at the boundary of a region
  a ray extends until another pink pixel is encountered
Granularity Measurement = sum of all rays’ lengths

## Slide 36: Standardization
To pick the best region, one can combine the three measurements
    Largeness, Compactness, & Grainy Measure
All have their own scales  standardization necessary
Relevant  measurement for a region relative to all other regions.
www.neiu.edu/~lruecker/ smrm.htm
How different is this point?

## Slide 37: Performance vs. Complexity

## Slide 38: Live Demo

## Slide 39: How Different Walks Affect Line-Following
Low velocity vs. high velocity
Center of gravity affects slip potential
Camera level affects:
  Ease of getting lost
  Precision of line following

## Slide 40: Special Thanks to:
Ethan
Alok Ladsariya
Dr. David Touretzky
Greg Kesden
Sony
CMU School of Computer Science and Robotics Institute
Manuela Veloso & CMU RoboCup
PMatt

## Slide 41: Bye!

## Slide 42: Image Sources
www.dai.ed.ac.uk/HIPR2/hough.htm
www.dai.ed.ac.uk/CVonline/LOCAL_COPIES/MARBLE/medium/contours/feature.htm
www.physik.uni-osnabrueck.de/nonlinop/Hough/LineHough.html
www.ri.cmu.edu/labs/lab_60.html
www.nynatur.dk/artikler/artikel_tekster/robo_pets.html
www003.upp.so_net.ne.jp/studio_mm/kameo/kameo.html
www.opus.co.jp/products/aibo/
www.generation5.org/aibo.shtml
www.ohta-kyoko.com/aibo/aibo.html
www.vdelnevo.co.uk/
www.d2.dion.ne.jp/~narumifu/diary.html
www.21stcentury.co.uk/robotics/aibo.asp
digitalcamera.gr.jp/html/HotNews/backno/HotNews001001-31.ht
www.seaple.icc.ne.jp/~somari/aibo.htm
www-2.cs.cmu.edu/afs/cs/project/robosoccer/www/legged/legged-team.html#publications
ccrma-www.stanford.edu/CCRMA/Courses/252/sensors/node9.html
http://www.icaen.uiowa.edu/~dip/LECTURE/Shape3.html#scalar