## Slide 1: Maker Culture in CMU SCS Part I: Overview & Laser Cutter
Dave Touretzky
November, 2013
http://www.cs.cmu.edu/~dst/Maker

## Slide 2: What Is Maker Culture?
“Do it yourself” meets high technology and open source movements.
The high tech part:
  CAD software
  Laser cutters, 3D printing, CNC machining
Why is this good?
  Rapid prototyping: hold your ideas in your hand!
  Extreme customization / personalization
  New modes of artistic expression

## Slide 3: Laser cutter / Water jet
Fast
Precise
Cheap
Wide choice of materials
Parts are only 2D (but assemblies can be 3D)

## Slide 4: Cheap 3D Printing
Slow
Less precise
More expensive
Limited materials
Support material may be required
Complex 3D structures!

## Slide 5: High End 3D Printing
Precise
Multicolor
Complex materials
Slow
Expensive

## Slide 6: SCS Maker Culture Experiment
Funded by Jeannette Wing and Matt Mason
Laser cutters:
  Laser cutter time is $10-$15 per hour at the CMC
  CSD/RI will pay for your laser cutter time
  You purchase your own materials (except today)
3D printer:
  SCS now has a public 3D printer in GHC 9206
  Frank & Matt are paying for the plastic – for now
  Heavy users should purchase their own plastic cartridges ($50 each from Cubify.com)

## Slide 7: CAD Software
AutoCAD
SolidWorks
  DraftSight
Google SketchUp
Blender (open source)
Alibre/Cubify Design
SIMI (Sketch It, Make It)
Many, many more…

## Slide 8: Plan For Today
Learn SolidWorks basics
Design something
Other useful stuff you’ll need to know
Visit the Collaborative Machining Center
  Doherty Hall B211: Larry Hayhurst’s shop
  3 laser cutters plus milling machines, lathes, etc.
Cut some plastic

## Slide 9: SolidWorks
CMU has a 500 seat license (Windows version)
SCS has purchased 50 seats
Contact Help@cs.cmu.edu to install on your workstation or laptop.
Runs on Macs under Boot Camp, Parallels, or VmWare.
No Linux version.
Student version for $25 at CMU bookstore.
The built-in tutorials are excellent.

## Slide 10: Four Modes + 1 Post-Processing Step
Assembly: a collection of mated parts
Part: a collection of features
  Often instantiated more than once
  Example: identical sides for a jewelry box
Sketch: a 2D representation of a shape
  Used to construct features of parts
Drawing: 2D layout of the required parts
DXF file: post-processed drawing that is sent to the laser cutter. (Drawing eXchange Format)

## Slide 11: Getting Started
Log in using your Andrew id
Create a folder named Maker
Download and unzip these files in your Maker folder:
  http://www.cs.cmu.edu/~dst/Maker/PenHolder.zip
  http://www.cs.cmu.edu/~dst/Maker/PhoneStand.zip
Go to Start > Program Files and run SolidWorks
Open Maker/PenHolder/PenHolder.SLDASM

## Slide 12: Exploring the Pen Holder Assembly
Changing the view:
  Middle button to rotate
  Scroll wheel to zoom
  Control-middle button to translate
  Left button to select
  View menu icon
  Section view icon; how to exit section view
The object tree
  Click for basic operations
  Right click for full context menu
Press ‘Escape’ to cancel a selection or mode

## Slide 13: Exploring Deeper
Open “Front” to examine the part
Open “Extruded Boss”:
  Opening a feature
  Exiting the feature dialog
  Opening the associated sketch
  Exiting the sketch editor
Open PenHolder.SLDDRW to examine the drawing
Use DraftSight to open PenHolder.DXF

## Slide 14: Let’s Design Something!
Phone Stand
Mobile
Holiday decoration
Name plate
Roughly one sheet of acrylic per person, but share amongst yourselves so you can have multiple colors if you need them.

## Slide 15: Phone Stand: One Part
Set extrusion thickness to 4.75 mm

## Slide 16: Making the Slot for the Phone Stand
Make two assemblies; add complementary extruded cuts 4.75 mm wide.

## Slide 17: How to Make a DXF File
Lay out your parts in a SolidWorks drawing.
Save as a SLDDRW file so you can make changes later.
Do “Save As” and choose “DXF” file format.
Open the DXF file with DraftSight (just double click on it).
Click on the “Student version” disclaimer text and hit Delete.
Type control-A to select all.
Set the color to red. (Use blue for engraving.)
Line should be “Continuous” (it is by default)
Set the line width to 0.0
Hit Escape to cancel selection.
Save as R2004-2006 ASCII Drawing DXF
Copy the DXF file to your USB drive.

## Slide 18: Assembling Your Creation
Press-fit (if you’re careful about tolerances)
Superglue or acrylic cement
Nuts and bolts; screws; hinges
Wire
What About Post-Processing?
  Recessed well; threaded hole; cutting a slot; etc.
  Larry can do machining to order (hourly charge)
  Make friends with someone in the RI machine shop

## Slide 19: Where to Buy Supplies
McMaster-Carr: www.mcmaster.com
  Acrylic and ABS plastic sheets
  All manner of hardware fasteners
  Rubber feet, etc.
AmazonSupply.com
Jameco, Pololu, SparkFun, Tower Hobbies, Trossen Robotics, LynxMotion
  Electronic components (LEDs, switches, battery cables, servos, etc.)

## Slide 20: Maker Culture
Make Magazine
  Makezine.com
Hacker spaces; TechShop
LaserSaur: open source laser cutter
Makerbot and open source 3D printers
Thingiverse & similar sites: marketplaces for 3D models (many are free)

## Slide 21: Sending Work Out
3D Systems makes the Cube but also offers printing services on high-end machines that offer multiple colors and tighter tolerances.
Shapeways and Ponoko do 3D printing in many types of materials, including metal and ceramics.
Big Blue Saw does water jet and CNC machining.
E-MachineShop will make anything (but they’re expensive).
MFG.com lets you put jobs out for bid

## Slide 22: What To Do In The Coming Week
Get SolidWorks running on your machine
  Also get DraftSight: it’s a free download
Do some SolidWorks tutorials for practice
Finish designing your holiday ornament or killer attack robot
Go see Larry to cut some plastic