## Slide 1: Maker Culture in CMU SCS Part II: 3D Printing
Dave Touretzky
November, 2013
http://www.cs.cmu.edu/~dst/Maker

## Slide 2: 3D Printing vs. Laser Cutter
Slower
Less precise
More expensive
Limited materials
Support material may be required
Complex 3D structures!

## Slide 3: Low Cost 3D Printers
RepRap: 2005 onward
  Adrian Bowyer, University of Bath (UK)
  Goal: open source 3D printer that can replicate itself
  4 generations: Darwin, Mendel, Prusa Mendel, Huxley
  Spawned many start-ups
Makerbot
  Evolved from RepRap; initially was open source
  Cupcake, Thing-o-Matic, Makerbot2, Replicator
Solidoodle ($500)
Cube
Many, many more…

## Slide 4: Cube Components
Material cartridge
“Cube tube”
Extruder
Print pad
USB port for
flash drive
Touch panel display and power button

## Slide 5: 2nd Generation Cube
Prints ABS (acrylonitrile butadiene styrene) or PLA (polylactic acid).
Faster than original cube.
Better precision (200 microns vs. 250 for original model.)
No heated bed: saves time.
Can print “hollow” or “solid” objects.
Same cost as the original: $1300.
Buy it at Staples, or at Cubify.com.

## Slide 6: Inside the Cartridge
Chip in cartridge tracks how much material used.
No actual sensing.

## Slide 7: Changing Cartridges
Takes several minutes for the extruder to heat.
Never yank filament out of the extruder!
  Can damage the mechanism.
  If a piece breaks off, the extruder will clog.
  Once it heats up, the filament comes out easily.
Always reinstall the thumbscrew to protect the cartridge.

## Slide 8: The Cube Extruder
Heated section
Image from cubifyfans.blogspot.com

## Slide 9: Cutting the Filament
A simple 45o cut will help to prevent jams in the extruder.
Image from cubifyfans.blogspot.com

## Slide 10: Preparing to Print
Check the extruder gap?
Coat the print pad with the “cube stick”.
  Not too thick a layer, but aim for uniformity.
  Keeps the object from shifting or warping.
Insert flash drive with your Cubify Print file.
  Flash drive must be FAT32 (Windows95) format.
Select your file using the Print menu.
If print bed doesn’t rise within 30 seconds, cancel and start again (software glitch).
5 minute warm-up before printing starts.
  Extruder becomes very hot!

## Slide 11: After Printing
Brief cool-down period for the extruder.
  20 minute cooldown on 1st generation (heated bed).
Your object needs to cool as well.
Printer will announce when cool-down done.
Object might not come easily off the bed.
  Soak in water to dissolve the glue.
Run the bed under the faucet in the kitchen sink to get all the glue off.
Dry the bed and reinstall on the printer.

## Slide 12: Post-Processing Steps
Wash any residual glue off the object.
Snap off any supports or raft.
  Cutting tools are in the cabinet.
Use a hot knife to remove stray material and retouch plastic that turned white.
Sanding or filing might also be helpful.
Machining? Painting? Gluing? Fake fur?
  It’s up to you!

## Slide 13: Designing for the Cube

## Slide 14: Symmetry and Precision
Dimension tool
Sketch relations
Centerlines

## Slide 15: Production Steps for Cube
Design in SolidWorks or some other tool.
Export an STL file.
Load the STL file into the Cubify Client program.
Set print parameters:
  Orientation and scale.
  Material: ABS or PLA?
  Do you want supports?
  Do you want a raft?
Click “Build” to produce a Cubify Print file.
Check the print file for reasonableness.
Save to flash drive and send to the printer.

## Slide 16: Designing 3D Shapes In SolidWorks
Extruded base (from previous session)
Extruded cut
Make a chalice:
  Revolved base
  Filleting
Swept base
  Planes
  Profile sketch, guide sketch
Make a hammer (SolidWorks tutorial):
  Planes
  Lofts
  Flex

## Slide 17: Design Rules
Shafts will be slightly thicker than intended.
Holes will be narrower than intended.
Do you want a 2.5 mm hole? On a 1st generation Cube:
  Use 3.0 mm for a horizontal hole.
  Use 3.7 mm for a vertical hole.
Minimum widths for walls?

## Slide 18: Test Object (Mike Taylor)
Compare requested size vs. actual.

## Slide 19: Coarse vs. Fine STL Triangulation
Too coarse can lose detail, but too fine can also cause features to be lost.
  SolidWorks “fine” seems to be okay, but don’t go to “custom” and crank up resolution to the max.

## Slide 20: Use of a Raft
Why use a raft?
  Stable base of support for tall, skinny parts.
  Prevents warping of big smooth parts (like cases) by reducing surface contact with heated bed (1st gen. Cubes only).
Why avoid a raft?
  Ruins the part finish (get out your sandpaper).
  Takes more time and more plastic to print.

## Slide 21: Cubify Client Program
Windows or Mac; you can install it yourself
Turns STL files into Cube Print files
Workflow: Import Heal  Orient/Scale  Center  Build
Settings:
  ABS or PLA
  Strong/Hollow/Solid
  2nd Generation (not Original cube)
  Support on/off
  Raft on/off
Import the Cube Print file to check supports.

## Slide 22: Cubify Client
Left button: orbit
Right button: translate
Scroll wheel: zoom

## Slide 23: Part Orientation
Choose your part orientation to avoid the need for supports if possible.
Don’t put supports where they will be difficult to remove.
Remember: supports leave a rough surface.

## Slide 24: Hollow, Strong, and Solid Modes
Image from cubify.com

## Slide 25: Setting Print Mode

## Slide 26: When the Bed Isn’t Perfectly Level

## Slide 27: Cubify Client Annoyances
Needs write access to its own directory, so you must fix the directory permissions if not running as Administrator.
  C:\Program Files (x86)\3D Systems Corporation\Cubify
Tells Windows that all STL files are “Cubify 3D Model” files.
Creates a bunch of auxiliary files with every Cubify Print file.
  VMF file has triangulation information

## Slide 28: When Things Go Wrong

## Slide 29: CubeX
Up to three print heads.
Can use PLA as dissolvable support material to make complex ABS parts.
Faster, better precision than Cube
$4400 for three-headed version; $1450 for ultrasonic tank.
Released in 2013; still needs some fine tuning.

## Slide 30: Where to Learn More
Cubify.com to learn about Cube and CubeX
cubifyfans.blogspot.com has lots of useful info about these printers.
User’s Guide, Cubify Client software, and demo objects can be downloaded from: www.cs.cmu.edu/~dst/Maker/Cube (only visible to CMU IP addresses)

## Slide 31: Alternative CAD Software Choices
Google SketchUp
  Fast drawing/dragging/moving.
  Requires plug-in to export STL files.
Cubify Invent
  Built on Alibre; similar to SolidWorks; $49
Sculptris: 3D sculpting
Sketch It/Make It (CMU spinoff)
  Quick designs for laser cutter
  Requires a WACOM tablet.
  Looking for beta testers.

## Slide 32: Alternative Printing Choices
Objet printer in Larry Hayhurst’s shop.
  Finer resolution, smoother finish.
  Can print dissolvable support material.
  Pay by the cubic centimeter.
TechShop in Bakery Square
  Makerbot Replicator and Replicator II (dual head)
  Multiple laser cutters, and a water jet machine.
Shapeways
  High end 3D printing service; many materials.
  Library of models and applications.
  8 day turn-around; fast shipping.