## Slide 1: Manipulation By Pushing
15-494 Cognitive Robotics
David S. Touretzky &
Ethan Tira-Thompson
Carnegie Mellon
Spring 2008

## Slide 2: Introduction
Affordances are where we want to be
Kinematics are where we are
How do we get from basic kinematics to actually doing something?

## Slide 3: Introduction
How do we get from basic kinematics to actually doing something?
  Configuration Space vs. Work Space
  Constraints
    Form Closure vs. Force Closure
    Grasp Analysis (Reuleaux’s Method)
  Path Planning
    Cspace, visibility graph, best first, RRT

## Slide 4: Configuration Space vs. Work Space
Consider a 2-link arm, with joint constraints: 0° <0 < 90° , -90° < 1 < 90°
Configuration Space: robot’s internal state space (e.g. joint angles)
Work Space: set of all possible end-effector positions

## Slide 5: Constraints
Constraints can be your friend!
  Upside: Use the environment and the object itself to your advantage.
  Downside: Requires planning and accurate modeling
Example: Part Orientation
  Can position/orient an ‘L’ shaped part with unknown initial configuration using nothing more than an actuated tray — no sensors!

## Slide 6: Constraints Are Your Friend
Example: Part Orientation
Fujimori, T., Development of Flexible Assembly System “SMART”
Video of Sony SMART Cell demo system by Wes Huang
CMU Manipulation Lab

## Slide 7: Constraints Are Your Friend
Example: Throwing (Kevin Lynch)

## Slide 8: Constraints Are Your Friend
A Turn and Two Topples
Tom A. Scharfeld
Kevin M. Lynch
December 2, 1998
2 DOF Arm over a conveyor belt (2JOC)

## Slide 9: Constraints Are Your Friend
Example: Hinge Assembly
Pingle, K., Paul, R., Bolles, R., "Programmable Assembly, Three Short Examples," Film,
Stanford Artificial Intelligence Laboratory, October 1974.

## Slide 10: Constraint Taxonomy
Bilateral - expressed by equality (e.g. y = 0)
Unilateral - expressed by inequality (e.g. y > 0)
Scleronomic - independent of time (static)
Rheonomic - changes over time (e.g. θ=2πt)
Holonomic - all constraints are independent of rate of change and bilateral (direct mapping between configuration space and work space)

## Slide 11: Holonomic vs. Non-Holonomic
Holonomic: robotic arms, unsteered mobile robots, omni-directional mobile robots
  can define configuration space such that returning to a configuration point implies returning to consistent point in work space
Non-Holonomic: commonly, mobile robots with constraints on their instantaneous motion, e.g. unicycles, steered carts (Ackerman steering) can’t go sideways

## Slide 12: Grasping
What does it mean to “hold” something?
  Form closure: object is “secure” — can’t move without moving a contact point
  Force closure: can apply any desired force
Not necessarily the same thing — depends on your friction model (next lecture)
No friction:
Form closure, but no force closure
With friction:
Force closure, but no form closure

## Slide 13: Grasping
Form closure is defined in increasing orders: position, velocity, acceleration, etc.
Force closure does not have orders (you have it or you don’t)
Frictionless force closure equates to first-order (positional) form closure
Example grasp with both force closure and first-order form closure, regardless of frictional model

## Slide 14: Grasping
  Original examples do not have force closure
  Left figure can be moved infinitesimally up or down, although cannot be in motion vertically (so it has second-order form closure)
With no friction,
neither example has force closure nor
first-order form closure

## Slide 15: Grasping
What does it mean to “hold” something?
  Form closure: object is “secure” — can’t move without moving a contact point
  Force closure: can apply any desired force
  Equilibrium: can resist environmental forces (gravity)
  Stablity: how much variance from the environment can be tolerated and still maintain equilibrium

## Slide 16: Taxonomy of Contacts
Figure 4.8 - Mason, Mechanics Of Robotic Manipulation

## Slide 17: Grasp Analysis: Reuleaux’s Method
For each constraint, divide the plane into areas which can hold positive or negative centers of rotation (IC’s - instantaneous centers)
+
–
±

## Slide 18: Grasp Analysis: Reuleaux’s Method
Intersect common regions
+
–

## Slide 19: Grasp Analysis: Reuleaux’s Method
Intersect common regions
+
–

## Slide 20: Grasp Analysis: Reuleaux’s Method
Another example:
Is this completely constrained?

## Slide 21: Grasp Analysis: Reuleaux’s Method
Another example:
Can spin counter-clockwise around area in the middle — but not clockwise!
+

## Slide 22: Grasp Analysis: Reuleaux’s Method
How about now?
Common intersections may indicate, but do not guarantee, that rotation is possible

## Slide 23: Grasp Analysis: Reuleaux’s Method
Reuleaux’s Method is good for humans, not so good for machines
Doesn’t extend to three dimensions
Analytical solution would require a lecture unto itself
  16-741: Mechanics of Manipulation
  Learn about screws, twists, wrenches, and moments

## Slide 24: Motion Path Planning
The Cspace Transform: the set of configuration points around obstacles which would cause a collision
Robot
Obstacle
Cspace from defining origin at red point
Notice how the Cspace formed by defining the origin of the robot in its center (red dot and outline) is merely a translated version of the Cspace formed by placing the origin at one of the robot’s corners (blue dot and outline).
Cspace from defining origin at blue point

## Slide 25: Motion Path Planning
The Cspace Transform: the area around obstacles which would cause a collision with the robot
Robot
Obstacle
Cspace
Figure 4.4 - Mason, Mechanics Of Robotic Manipulation

## Slide 26: Motion Path Planning
The Cspace Transform is not just for mobile robots’ outer hulls!
Figure 4.5 - Mason, Mechanics Of Robotic Manipulation

## Slide 27: Motion Path Planning
So, we know where we can’t go, but how do we avoid it?
Approach 1: Visibility Graph
  Connect visible corners together, search the graph of connected edges
Figure 4.1 - Mason, Mechanics Of Robotic Manipulation

## Slide 28: Motion Path Planning: Visibility Graph
Great for 2 dimensions, but not for more
Voronoi graphs are similar, and have been generalized to higher dimensions (Choset)
  Instead of a graph of tangents between obstacles, use a graph of the midpoints
  Fast search, safe path, but suboptimal distance
G
S
Voronoi Graph

## Slide 29: Motion Path Planning: Best First Search (& Friends)
Don’t explicitly solve all of Cspace before searching
Basically, keep a priority queue of unevaluated nodes, sorted by “score” (e.g. distance to goal, or distance to goal plus distance so far)
Each iteration, expand the current “best” node
Choice of scoring heuristic (if you have a choice!) can make tradeoffs between search speed and optimality of solution found.

## Slide 30: Motion Path Planning: Best First Search (& Friends)
S
G

## Slide 31: Motion Path Planning: Rapidly Exploring Random Trees
  LaValle 1998
  Repeat K times:
    Pick a random configuration point P
    Find N, the closest tree node to P
    Add new node N', some distance Δ from N toward P
  Back to exploring entire configuration space?
  Not necessarily — bias the random target to pick the goal more often

## Slide 32: Motion Path Planning: Rapidly Exploring Random Trees
http://msl.cs.uiuc.edu/rrt/treemovie.gif

## Slide 33: Motion Path Planning: Potential Fields
So far we’ve been assuming we already know the environment, and there aren’t other agents changing things around!
Constant replanning is costly
  replan only when something is amiss
  replan only affected parts of existing plan (open research problem!)
Or… don’t make a plan in the first place

## Slide 34: Motion Path Planning: Potential Fields
Define a function f mapping from a specified configuration to a score value
  e.g. distance to goal plus distance to obstacles
Essentially just running heuristic from before:
  Evaluate each of the currently available moves
  Pick the one which maximizes score (or in example above, minimizes cost)

## Slide 35: Motion Path Planning: Potential Fields
Downside: can get stuck in local minima
Workaround: follow edges (“bug” method)
Upside: extremely quick and reactive
  Popular in robosoccer for navigating to ball
G
S

## Slide 36: Motion Path Planning: Summary
Known Environment, Deterministic Actions
  Road Maps (Visibility, Voronoi), A*, RRT, brushfire
Unknown Environment, Deterministic Actions
  Potential Field, “Bug”, D*
Non-Deterministic and/or Unknown Environment
  MDP, POMDP

## Slide 37: Getting Back to the AIBO
Under-actuated manipulators
  use the ground and other objects to help
Don’t get hung up on grasp closure
  we’re not handling nuclear waste — equilibrium is enough for our purposes!

## Slide 38: Getting Back to the AIBO: Where we want to go
Develop larger library of motion primitives
  How to push a banana? One leg? Two legs? Head nuzzle?
  Each strategy has advantages, but have to quantify these capabilities so planners can choose among them
Learn models of the environment from experience

## Slide 39: Next Time:
Dynamics!
  Friction, Forces, and Control
Thanks to:
16-741: Mechanics of Manipulation (Mason)
16-830: Planning, Execution, and Learning (Rizzi, Veloso)