## Slide 1: Manipulation with Friction
15-494 Cognitive Robotics
David S. Touretzky &
Ethan Tira-Thompson
Carnegie Mellon
Spring 2007

## Slide 2: Introduction
Friction
Jacobians
Dynamics
Control (P, PD, PID)

## Slide 3: Friction: Coulomb’s Law
Figure 6.1 - Mason, Mechanics Of Robotic Manipulation
Pulling force
Static friction force balances pulling force, up to maximum specified by static friction coefficient
Friction Force
Once object begins moving, frictional force drops to constant value, called sliding friction or kinetic friction

## Slide 4: Friction: Coulomb’s Law
For common tasks, independent of velocity and surface area
  With extreme pressures, coefficient rises
  With extreme velocities, coefficient drops
Coefficients of friction are different for every pair of surfaces — table lookup
  also differ for every change in temperature, humidity, dust/dirt, vibration, celestial alignment, etc. — not terribly accurate

## Slide 5: Friction within Joints
Static friction is a headache for fine motor control
  motor has to ramp up power to overcome static friction within gears, but as soon as it succeeds in doing so, it’s now providing too much power and will “jump” to life.
  this is the fundamental reason you see the Aibo’s joints twitch from time to time
  the higher the gear ratio, the bigger the problem

## Slide 6: Computing with Forces
Forces are defined by a line through space, and a magnitude
  usually represented by a vector and a point
  but the point is not unique — any point along the vector is equally valid (“line of action”)
Figure 5.1 - Mason,
Mechanics Of Robotic Manipulation

## Slide 7: Friction with Objects
Now we can define a friction cone:
  Edges of the cone define maximum angle allowed for forces without slippage
  If you break applied force into normal force fn and tangental force ft, friction cone is defined as |ft| ≤ µ|fn|, with interior angle 2 tan-1µ
lL
lR
ft
fn

## Slide 8: Friction with Objects
Remember Reuleaux’s Method?
  Works with friction cones as well
Now we’re analyzing forces, not displacements, a different interpretation! (be careful about trying to mix them...)
Only forces which agree with the all of the contacts’ constraints can be applied by the contact(s):
lL
lR
+
–
+
–

## Slide 9: Combining Forces
Adding multiple contacts allows you to apply any force in the linear span of their friction cones
Remember that forces act along a line through space
  slide forces along line of action to intersection
  Resultant force is the vector sum of the two forces, acting through common intersection
f1
f2
f1 + f2

## Slide 10: Friction with Objects: Examples
–
NO
NO
NO
YES
YES
YES
NO
+
YES
YES
Don’t actually care about
the object itself once contacts
have been analyzed
+
–
For reference:

## Slide 11: Center of Friction
Similar to center of mass, center of friction is the integrated pressure over the support region
Allows you to treat the interaction as a single contact
Hard to model — with a rigid body, small variances completely throw off pressure distribution
  Ever play Jenga?

## Slide 12: Applying Friction & Forces
Use weight to flip brick
Use wall to direct ball (extra arm)
Get ball away from wall
Use wall to align/direct brick
Stand bone upright
Insert objects without jamming or wedging

## Slide 13: The Jacobian Matrix
One of the most important tools in analyzing and controlling robot motion!
Provides the instantaneous velocity in each of the 6 freedoms (translation and orientation along/around each of x, y, and z) as a function of each of the robot’s links
= Jacobian (6×n) — a function of
current joint positions (q)
= joint velocity vector (length n)
= workspace velocity vector (length 6)

## Slide 14: The Jacobian Matrix: Usage
Find current workspace velocity/force
Determine contribution of individual joints
Analyze rank to detect singularities (for better or worse)
  a singularity occurs when joints become aligned, causing a loss in effector mobility (but increased strength along that axis!)
  under-actuated robots always have incomplete rank
Full (planar) mobility
Singularity: cannot move along y axis, but also don’t have to do any work to resist forces along it

## Slide 15: The Jacobian Matrix: Usage
Things to watch out for at/near singularities:
  Small workspace movements/forces may require instantaneous joint motion (infinite motor torque!)
  Usually occur at workspace limits
  May have infinite inverse kinematic solutions
Test for configuration “quality”:
Swap J(q) and JT(q) if under-actuated (i.e. J(q) is less than full rank)
M(q) becomes zero at singularities

## Slide 16: The Jacobian Matrix: Composition
= Position component (sometimes )
= Orientation component
= Linear velocity vector of end effector
= Angular velocity vector of end effector
Jacobian is split into two components:

## Slide 17: The Jacobian Matrix: Position Component
If Joint i is prismatic:
If Joint i is revolute:
Where:
zi = z axis of joint i
p = position of the end effector
pi = position of joint i’s origin
(all relative to base frame)
Remember that a joint’s z axis is always defined to point along its axis of motion

## Slide 18: The Jacobian Matrix: Orientation Component
If Joint i is prismatic:
If Joint i is revolute:

## Slide 19: The Jacobian Matrix: Example
A planar RRR arm
These are all given to you by the forward kinematics: each joint’s transformation matrix holds the current z vector in the 3rd column and the current position in the 4th column

## Slide 20: The Jacobian Matrix: Example
A planar RRR arm
Notation:
s1 = sin(θ1)
c123 = cos(θ1+θ2+θ3)

## Slide 21: The Jacobian Matrix: Example
A planar RRR arm
Notation:
s1 = sin(θ1)
c123 = cos(θ1+θ2+θ3)

## Slide 22: Dynamics
How will joints move as power is applied?
  Ideally, the robot manufacturer tells you:
    Inertia Tensor ( , 3×3 matrix) for each link: angular momentum can then be found:
    Motor properties for each joint: rotor inertia (Im), gear ratio, viscous and coulomb friction
  Sony isn’t ideal – we don’t have these parameters
  Aibo doesn’t give direct control over torque anyway (we specify position, it computes power)

## Slide 23: Control
So then, how does it compute the power for each joint?
We want to move the joint to a specified position, and hold it there
  Sounds easy, right? Harder than it sounds:
    there may be other forces acting on the joint (e.g. gravity, inertia, etc.)
    you’re controlling acceleration, two derivatives away from position — go fast, but don’t oscillate

## Slide 24: Proportional Control
Here’s an idea:
  take the current position error (e(t) = x(t) - xtgt)
  multiply e(t) by some parameter kp
  use this value as the new power output output = -kp· e(t)
Should work, right? Farther away means more power. As we get closer, reduce power.

## Slide 25: Proportional Control
Here’s the resulting graph of position over time:
Whoa, look at that oscillation, and it isn’t even oscillating around the right value!
  One thing at a time buckaroo – oscillation first

## Slide 26: PD Control
The oscillation is caused because there’s nothing to cause it to slow down as it’s approaching the target — inertia will keep the link moving and blow right past the target
  if you have significant friction or little inertia (with a speed limit), this may not be a problem
Add a braking factor kd, multiplied by the current error derivative ∂e(t) output = -(kp· e(t)) - (kd· ∂e(t))

## Slide 27: PD Control
Here’s a new graph of position over time:
Closer! Now, let’s take care of that offset.

## Slide 28: PID Control
That offset is caused by external forces, like gravity. We need another term to handle its constant input to our system.
Use an integral of the error term, and multiply it by a new coefficient ki: output = -(kp· e(t)) - (ki· ∫e(t)dt) - (kd· ∂e(t))
Actual implementations vary in the parameterization, many use: output = -kp· (e(t) + (ki· ∫e(t)dt) + (kd· ∂e(t)))

## Slide 29: PID Control
Now look at the graph:
Ta-da!

## Slide 30: PID Control
We’ve put an Excel spreadsheet for this simulation online so you can play with it

## Slide 31: Qualifications
The graphs shown previously were based on a system with inertia
If the system you are controlling does not have inertia, or equivalently, you are controlling velocity directly (not force), proportional control may be all you need!
  Proportional control often used as a potential field function for steering mobile robots...

## Slide 32: Downside of the I Parameter
If grasping an object with several manipulators, any error in the manipulator’s position will cause gradually increasing internal strain
This is why the Aibo will sometimes shutdown with a joint overload error, simply from standing idly on the ground

## Slide 33: The Dirty Little Secret
How do we pick the P, I, and D parameters?
  Hard way: lots of math (a lecture unto itself)
    Read up on: Laplace Transforms, characteristic equations, pole placement, bode plots
  Easy way: play with them until you get something you like
    be careful not to make big changes at a time — don’t want to get into unstable feedback loops
  Smart way: adaptive self-tuning

## Slide 34: Intuitive PID Tuning Advice
In our notation (which I believe the AIBO uses)
  Scaling all the parameters together will scale maximum power output without changing control style (very much) — in the alternative formulation, only P can be scaled this way.
  P tends to have the biggest impact — higher P means more power , but more oscillation
  D balances oscillation, but reduces top speed
  I balances final errors (remember joint twitching?)

## Slide 35: Pulse-Width Modulation (PWM)
Finally, one last trick: servos are not controlled with analog power levels
Instead, power is “pulsed” on and off at high frequency
The portion of the period during which the power is turned on is called the duty cycle
Generally, this is a transparent effect, but knowing this allows you to interpret the “duty cycle” feedback given by each joint

## Slide 36: Getting Power From Position
So, now that we have some understanding of how power is computed from desired position, we should be able to invert it to compute a target position which will result in a desired force!
Make life easy for yourself: set ki and kd to 0, and specify an offset from current joint position as the target — force will be directly proportional to your offset (and kp)