## Slide 1: Manipulation
15-494 Cognitive Robotics
David S. Touretzky &
Ethan Tira-Thompson
Carnegie Mellon

## Slide 2: Constraints
Constraints can be your friend!
  Upside: Use the environment and the object itself to your advantage.
  Downside: Requires planning and accurate modeling
Example: Part Orientation
  Can position/orient an ‘L’ shaped part with unknown initial configuration using nothing more than an actuated tray — no sensors!

## Slide 3: Constraints Are Your Friend
Example: Part Orientation
Fujimori, T., Development of Flexible Assembly System “SMART”
Video of Sony SMART Cell demo system by Wes Huang
CMU Manipulation Lab

## Slide 4: Constraints Are Your Friend
Example: Throwing (Kevin Lynch)

## Slide 5: Constraints Are Your Friend
A Turn and Two Topples
Tom A. Scharfeld
Kevin M. Lynch
December 2, 1998
2 DOF Arm over a conveyor belt (2JOC)

## Slide 6: Constraints Are Your Friend
Example: Hinge Assembly
Pingle, K., Paul, R., Bolles, R., "Programmable Assembly, Three Short Examples," Film,
Stanford Artificial Intelligence Laboratory, October 1974.

## Slide 7: Grasping
What does it mean to “hold” something?
  Form closure: object is “secure” — can’t move without moving a contact point
  Force closure: can apply any desired force
Not necessarily the same thing — depends on your friction model (next lecture)
No friction:
Form closure, but no force closure
With friction:
Force closure, but no form closure

## Slide 8: Grasping
Form closure is defined in increasing orders: position, velocity, acceleration, etc.
Force closure does not have orders (you have it or you don’t)
Frictionless force closure equates to first-order (positional) form closure
Example grasp with both force closure and first-order form closure, regardless of frictional model

## Slide 9: Grasping
  Original examples do not have force closure
  Left figure can be moved infinitesimally up or down, although cannot be in motion vertically (so it has second-order form closure)
With no friction,
neither example has force closure nor
first-order form closure

## Slide 10: Grasping
What does it mean to “hold” something?
  Form closure: object is “secure” — can’t move without moving a contact point
  Force closure: can apply any desired force
  Equilibrium: can resist environmental forces (gravity)
  Stablity: how much variance from the environment can be tolerated and still maintain equilibrium

## Slide 11: Taxonomy of Contacts
Figure 4.8 - Mason, Mechanics Of Robotic Manipulation

## Slide 12: Grasp Analysis: Reuleaux’s Method
For each constraint, divide the plane into areas which can hold positive or negative centers of rotation (IC’s - instantaneous centers)
+
–
±

## Slide 13: Grasp Analysis: Reuleaux’s Method
Intersect common regions
+
–

## Slide 14: Grasp Analysis: Reuleaux’s Method
Intersect common regions
+
–

## Slide 15: Grasp Analysis: Reuleaux’s Method
Another example:
Is this completely constrained?

## Slide 16: Grasp Analysis: Reuleaux’s Method
Another example:
Can spin counter-clockwise around area in the middle — but not clockwise!
+

## Slide 17: Grasp Analysis: Reuleaux’s Method
How about now?
Common intersections may indicate, but do not guarantee, that rotation is possible

## Slide 18: Grasp Analysis: Reuleaux’s Method
Reuleaux’s Method is good for humans, not so good for machines
Doesn’t extend to three dimensions
Analytical solution would require a lecture unto itself
  16-741: Mechanics of Manipulation
  Learn about screws, twists, wrenches, and moments

## Slide 19: Friction: Coulomb’s Law
Figure 6.1 - Mason, Mechanics Of Robotic Manipulation
Pulling force
Static friction force balances pulling force, up to maximum specified by static friction coefficient
Friction Force
Once object begins moving, frictional force drops to constant value, called sliding friction or kinetic friction

## Slide 20: Friction: Coulomb’s Law
For common tasks, independent of velocity and surface area
  With extreme pressures, coefficient rises
  With extreme velocities, coefficient drops
Coefficients of friction are different for every pair of surfaces — table lookup
  also differ for every change in temperature, humidity, dust/dirt, vibration, celestial alignment, etc. — not terribly accurate

## Slide 21: Friction within Joints
Static friction is a headache for fine motor control
  motor has to ramp up power to overcome static friction within gears, but as soon as it succeeds in doing so, it’s now providing too much power and will “jump” to life.
  this is the fundamental reason you see the Aibo’s joints twitch from time to time
  the higher the gear ratio, the bigger the problem

## Slide 22: Computing with Forces
Forces are defined by a line through space, and a magnitude
  usually represented by a vector and a point
  but the point is not unique — any point along the vector is equally valid (“line of action”)
Figure 5.1 - Mason,
Mechanics Of Robotic Manipulation

## Slide 23: Friction with Objects
Now we can define a friction cone:
  Edges of the cone define maximum angle allowed for forces without slippage
  If you break applied force into normal force fn and tangental force ft, friction cone is defined as |ft| ≤ µ|fn|, with interior angle 2 tan-1µ
lL
lR
ft
fn

## Slide 24: Friction with Objects
Remember Reuleaux’s Method?
  Works with friction cones as well
Now we’re analyzing forces, not displacements, a different interpretation! (be careful about trying to mix them...)
Only forces which agree with the all of the contacts’ constraints can be applied by the contact(s):
lL
lR
+
–
+
–

## Slide 25: Combining Forces
Adding multiple contacts allows you to apply any force in the linear span of their friction cones
Remember that forces act along a line through space
  slide forces along line of action to intersection
  Resultant force is the vector sum of the two forces, acting through common intersection
f1
f2
f1 + f2

## Slide 26: Friction with Objects: Examples
–
NO
NO
NO
YES
YES
YES
NO
+
YES
YES
Don’t actually care about
the object itself once contacts
have been analyzed
+
–
For reference:

## Slide 27: Center of Friction
Similar to center of mass, center of friction is the integrated pressure over the support region
Allows you to treat the interaction as a single contact
Hard to model — with a rigid body, small variances completely throw off pressure distribution
  Ever play Jenga?

## Slide 28: Applying Friction & Forces
Use weight to flip brick
Use wall to direct ball (extra arm)
Get ball away from wall
Use wall to align/direct brick
Stand bone upright
Insert objects without jamming or wedging