## Slide 1: Future of Computing: Moore’s Law & Its Implications + High-Performance Computing 15-213: Introduction to Computer Systems 27th Lecture, Nov. 30, 2017
Instructors:
Randy Bryant

## Slide 2: Moore’s Law Origins
April 19, 1965

## Slide 3: Moore’s Law Origins
Moore’s Thesis
  Minimize price per device
  Optimum number of devices / chip increasing 2x / year
Later
  2x / 2 years
  “Moore’s Prediction”
1965: 50
1970: 1000

## Slide 4: Moore’s Law: 50 Years
Sample of
129 processor chips
Chart: Transistor Count by Year
| 1976.0 | 1976.0 | 1978.0 | 1979.0 | 1982.0 | 1982.0 | 1984.0 | 1985.0 | 1986.0 | 1986.0 | 1989.0 | 1991.0 | 1993.0 | 1996.0 | 1997.0 | 1997.0 | 1998.0 | 1999.0 | 1999.0 | 1999.0 | 1999.0 | 2000.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2006.0 | 2007.0 | 2007.0 | 2008.0 | 2008.0 | 2008.0 | 2011.0 | 2012.0 | 2012.0 | 2014.0 | 2015.0
Desktop | 6500 | 8500 | 29000 | 68000 | 55000 | 134000 | 190000 | 275000 | 25000 | 25000 | 1180235 | 1350000 | 3100000 | 4300000 | 7500000 | 8800000 | 7500000 | 9500000 | 27400000 | 21300000 | 22000000 | 21000000 | 42000000 | 45000000 | 55000000 | 54300000 | 105900000 | 112000000 | 169000000 | 184000000 | 291000000 | 169000000 | 411000000 | 230000000 | 731000000 | 758000000 | 1160000000 | 1303000000 | 1400000000 | 1400000000 | 1900000000
Embedded | 2300 | 3500 | 4100 | 4500 | 5000 | 3510 | 9000 | 11500 | 25000000 | 47000000 | 1000000000 | 3000000000 | 2000000000 | 3300000000 | 4300000000
GPU | 3500000 | 8000000 | 23000000 | 20000000 | 25000000 | 30000000 | 57000000 | 60000000 | 63000000 | 107000000 | 117000000 | 135000000 | 160000000 | 222000000 | 303000000 | 321000000 | 241000000 | 384000000 | 681000000 | 700000000 | 754000000 | 959000000 | 1400000000 | 2154000000 | 2640000000 | 3200000000 | 3000000000 | 4312711873 | 3540000000 | 7080000000 | 5000000000 | 6300000000 | 5200000000 | 8100000000 | 8900000000 | 8900000000 | 15300000000 | 15300000000 | 7000000000 | 21100000000 | 12500000000
Server | 5500000 | 220000000 | 410000000 | 592000000 | 1700000000 | 463000000 | 789000000 | 1900000000 | 904000000 | 1000000000 | 1170000000 | 1200000000 | 1400000000 | 2000000000 | 2300000000 | 2270000000 | 2600000000 | 1200000000 | 2100000000 | 2750000000 | 3100000000 | 1860000000 | 4200000000 | 2600000000 | 4310000000 | 5000000000 | 5560000000 | 3990000000 | 7200000000 | 6100000000 | 4800000000 | 8000000000
General Trend | 969.507 | 13045873366.0275
Moore's Prediction | 282.8427 | 3355443200

## Slide 5: What Moore’s Law Has Meant
1976 Cray 1
  250 M Ops/second
  ~170,000 chips
  0.5B transistors
  5,000 kg, 115 KW
  $9M
  80 manufactured
2017 iPhone X
  > 10 B Ops/second
  16 chips
  4.3B transistors (CPU only)
  174 g, < 5 W
  $999
  ~3 million sold in first 3 days

## Slide 6: What Moore’s Law Has Meant
1965 Consumer Product
2017 Consumer Product
Apple A11 Processor
4.3B transistors

## Slide 7: Visualizing Moore’s Law to Date
Intel 4004
1970
2,300 transistors
Apple A11
2017
4.3 B transistors
If transistors were the size of a grain of sand
0.1 g
189 kg

## Slide 8: Moore’s Law Economics
Capital +
R&D Investment
New Technology
Product
Design
Sales $$
Better
Products
Consumer products sustain the
$300B semiconductor industry

## Slide 9: What Moore’s Law Has Meant
12 generations of iPhone since 2007

## Slide 10: What Moore’s Law Could Mean
2017 Consumer Product
2065 Consumer Product
  Portable
  Low power
  Will drive markets & innovation
?

## Slide 11: Requirements for Future Technology
Must be suitable for portable, low-power operation
  Consumer products
  Internet of Things components
  Not cryogenic, not quantum
Must be inexpensive to manufacture
  Comparable to current semiconductor technology
    O(1) cost to make chip with O(N) devices
Need not be based on transistors
  Memristors, carbon nanotubes, DNA transcription, ...
  Possibly new models of computation
  But, still want lots of devices in an integrated system

## Slide 12: Moore’s Law: 100 Years
1017 devices!
Chart: Device Count by Year
| 1976.0 | 1976.0 | 1978.0 | 1979.0 | 1982.0 | 1982.0 | 1984.0 | 1985.0 | 1986.0 | 1986.0 | 1989.0 | 1991.0 | 1993.0 | 1996.0 | 1997.0 | 1997.0 | 1998.0 | 1999.0 | 1999.0 | 1999.0 | 1999.0 | 2000.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2006.0 | 2007.0 | 2007.0 | 2008.0 | 2008.0 | 2008.0 | 2011.0 | 2012.0 | 2012.0 | 2014.0 | 2015.0
Desktop | 6500 | 8500 | 29000 | 68000 | 55000 | 134000 | 190000 | 275000 | 25000 | 25000 | 1180235 | 1350000 | 3100000 | 4300000 | 7500000 | 8800000 | 7500000 | 9500000 | 27400000 | 21300000 | 22000000 | 21000000 | 42000000 | 45000000 | 55000000 | 54300000 | 105900000 | 112000000 | 169000000 | 184000000 | 291000000 | 169000000 | 411000000 | 230000000 | 731000000 | 758000000 | 1160000000 | 1303000000 | 1400000000 | 1400000000 | 1900000000
Embedded | 2300 | 3500 | 4100 | 4500 | 5000 | 3510 | 9000 | 11500 | 25000000 | 47000000 | 1000000000 | 3000000000 | 2000000000 | 3300000000 | 4300000000
GPU | 3500000 | 8000000 | 23000000 | 20000000 | 25000000 | 30000000 | 57000000 | 60000000 | 63000000 | 107000000 | 117000000 | 135000000 | 160000000 | 222000000 | 303000000 | 321000000 | 241000000 | 384000000 | 681000000 | 700000000 | 754000000 | 959000000 | 1400000000 | 2154000000 | 2640000000 | 3200000000 | 3000000000 | 4312711873 | 3540000000 | 7080000000 | 5000000000 | 6300000000 | 5200000000 | 8100000000 | 8900000000 | 8900000000 | 15300000000 | 15300000000 | 7000000000 | 21100000000 | 12500000000
Server | 5500000 | 220000000 | 410000000 | 592000000 | 1700000000 | 463000000 | 789000000 | 1900000000 | 904000000 | 1000000000 | 1170000000 | 1200000000 | 1400000000 | 2000000000 | 2300000000 | 2270000000 | 2600000000 | 1200000000 | 2100000000 | 2750000000 | 3100000000 | 1860000000 | 4200000000 | 2600000000 | 4310000000 | 5000000000 | 5560000000 | 3990000000 | 7200000000 | 6100000000 | 4800000000 | 8000000000
General Trend | 969.507 | 13045873366.0275 | 2.4893e+17
Moore's Prediction | 282.8427 | 3355443200 | 56294995342131200

## Slide 13: Visualizing 1017 Devices
0.1 m3
3.5 X 109 grains
1 million m3
0.35 X 1017 grains
If devices were the size of a grain of sand

## Slide 14: Increasing Transistor Counts
Chips have gotten bigger
  1 area doubling / 10 years
Transistors have gotten smaller
  4 density doublings / 10 years
Will these trends continue?

## Slide 15: Chips Have Gotten Bigger
Intel 4004
1970
2,300 transistors
12 mm2
Apple A11
2017
4.3 B transistors
89 mm2
NVIDIA GV100 Volta
2017
21.1 B transistors
815 mm2

## Slide 16: Chip Size Trend
2x every 9.8 years
Chart: Area by Year
| 1976.0 | 1976.0 | 1978.0 | 1979.0 | 1982.0 | 1982.0 | 1984.0 | 1985.0 | 1986.0 | 1986.0 | 1989.0 | 1991.0 | 1993.0 | 1996.0 | 1997.0 | 1997.0 | 1998.0 | 1999.0 | 1999.0 | 1999.0 | 1999.0 | 2000.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2006.0 | 2007.0 | 2007.0 | 2008.0 | 2008.0 | 2008.0 | 2011.0 | 2012.0 | 2012.0 | 2014.0 | 2015.0
Desktop | 20 | 18 | 33 | 44 | 60 | 49 | 85 | 104 | 50 | 30 | 173 | 213 | 294 | 251 | 195 | 162 | 113 | 128 | 180 | 118 | 184 | 80 | 217 | 81 | 145 | 101 | 193 | 110 | 143 | 90 | 143 | 111 | 107 | 83 | 263 | 258 | 216 | 246 | 160 | 177 | 133
Embedded | 12 | 14 | 16 | 20 | 27 | 21 | 21 | 6 | 50 | 24 | 102 | 128 | 89 | 125 | 89
GPU | 90 | 70 | 111 | 65 | 81 | 97 | 128 | 68 | 142 | 218 | 218 | 207 | 297 | 305 | 333 | 288 | 221 | 352 | 480 | 420 | 324 | 282 | 576 | 334 | 389 | 526 | 520 | 365 | 294 | 561 | 363 | 438 | 398 | 601 | 596 | 596 | 610 | 610 | 360 | 815 | 484
Server | 307 | 421 | 374 | 432 | 596 | 283 | 341 | 503 | 346 | 377 | 240 | 567 | 512 | 699 | 684 | 434 | 512 | 315 | 567 | 597 | 544 | 256 | 650 | 355 | 541 | 541 | 661 | 678 | 456 | 696 | 192 | 695
Trend | 17.2782 | 486.7304

## Slide 17: Chip Size Extrapolation
147 cm2
Chart: Area by Year
| 1976.0 | 1976.0 | 1978.0 | 1979.0 | 1982.0 | 1982.0 | 1984.0 | 1985.0 | 1986.0 | 1986.0 | 1989.0 | 1991.0 | 1993.0 | 1996.0 | 1997.0 | 1997.0 | 1998.0 | 1999.0 | 1999.0 | 1999.0 | 1999.0 | 2000.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2006.0 | 2007.0 | 2007.0 | 2008.0 | 2008.0 | 2008.0 | 2011.0 | 2012.0 | 2012.0 | 2014.0 | 2015.0
Desktop | 20 | 18 | 33 | 44 | 60 | 49 | 85 | 104 | 50 | 30 | 173 | 213 | 294 | 251 | 195 | 162 | 113 | 128 | 180 | 118 | 184 | 80 | 217 | 81 | 145 | 101 | 193 | 110 | 143 | 90 | 143 | 111 | 107 | 83 | 263 | 258 | 216 | 246 | 160 | 177 | 133
Embedded | 12 | 14 | 16 | 20 | 27 | 21 | 21 | 6 | 50 | 24 | 102 | 128 | 89 | 125 | 89
GPU | 90 | 70 | 111 | 65 | 81 | 97 | 128 | 68 | 142 | 218 | 218 | 207 | 297 | 305 | 333 | 288 | 221 | 352 | 480 | 420 | 324 | 282 | 576 | 334 | 389 | 526 | 520 | 365 | 294 | 561 | 363 | 438 | 398 | 601 | 596 | 596 | 610 | 610 | 360 | 815 | 484
Server | 307 | 421 | 374 | 432 | 596 | 283 | 341 | 503 | 346 | 377 | 240 | 567 | 512 | 699 | 684 | 434 | 512 | 315 | 567 | 597 | 544 | 256 | 650 | 355 | 541 | 541 | 661 | 678 | 456 | 696 | 192 | 695
Trend | 17.2782 | 486.7304 | 14720.5667

## Slide 18: Extrapolation: The iPhone XXX
Apple A111
2065
1017 transistors
147 cm2

## Slide 19: Transistors Have Gotten Smaller
  Area A
  N devices
  Linear Scale L
L

## Slide 20: Linear Scaling Trend
Chart: Linear Spacing by Year
| 1976.0 | 1976.0 | 1978.0 | 1979.0 | 1982.0 | 1982.0 | 1984.0 | 1985.0 | 1986.0 | 1986.0 | 1989.0 | 1991.0 | 1993.0 | 1996.0 | 1997.0 | 1997.0 | 1998.0 | 1999.0 | 1999.0 | 1999.0 | 1999.0 | 2000.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2006.0 | 2007.0 | 2007.0 | 2008.0 | 2008.0 | 2008.0 | 2011.0 | 2012.0 | 2012.0 | 2014.0 | 2015.0
Desktop | 55470.0196 | 46017.8993 | 33733.2334 | 25437.351 | 33028.913 | 19122.5428 | 21151.0856 | 19446.8974 | 44721.3595 | 34641.0162 | 12107.0631 | 12560.9625 | 9738.5168 | 7640.1632 | 5099.0195 | 4290.5817 | 3881.5804 | 3670.6517 | 2563.073 | 2353.7005 | 2891.9952 | 1951.8001 | 2273.0303 | 1341.6408 | 1623.6883 | 1363.8317 | 1349.9904 | 991.0312 | 919.8662 | 699.3786 | 701.0057 | 810.4349 | 510.2359 | 600.7242 | 599.8176 | 583.4119 | 431.517 | 434.5056 | 338.0617 | 355.568 | 264.5751
Embedded | 72231.5119 | 63245.5532 | 62469.5048 | 66666.6667 | 73484.6923 | 77349.2468 | 48304.5892 | 22841.6096 | 1414.2136 | 714.5896 | 319.3744 | 206.5591 | 210.9502 | 194.6247 | 143.8669
GPU | 5070.9255 | 2958.0399 | 2196.8357 | 1802.7756 | 1800 | 1798.1472 | 1498.5373 | 1064.5813 | 1501.3222 | 1427.3693 | 1365.0084 | 1238.2784 | 1362.4427 | 1172.1237 | 1048.3367 | 947.2044 | 957.6077 | 957.4271 | 839.551 | 774.5967 | 655.5213 | 542.2696 | 641.427 | 393.777 | 383.86 | 405.4319 | 416.3332 | 290.9184 | 288.1854 | 281.4912 | 269.4439 | 263.6737 | 276.6559 | 272.3922 | 258.7785 | 258.7785 | 199.6729 | 199.6729 | 226.7787 | 196.5339 | 196.774
Server | 7471.1567 | 1383.3425 | 955.0891 | 854.2422 | 592.1049 | 781.8127 | 657.4136 | 514.5258 | 618.6626 | 614.0033 | 452.9108 | 687.3864 | 604.7432 | 591.1853 | 545.336 | 437.2521 | 443.7602 | 512.3475 | 519.6152 | 465.9302 | 418.908 | 370.9911 | 393.3979 | 369.5111 | 354.2909 | 328.9377 | 344.7969 | 412.2194 | 251.6611 | 337.7845 | 200 | 294.7457
Trend | 133497.7743 | 193.1558
1/2x every 5 years 
2x transistor density every 2.5 years

## Slide 21: Decreasing Feature Sizes
Intel 4004
1970
2,300 transistors
L = 72,000 nm
Apple A11
2017
4.3 B transistors
L = 144 nm

## Slide 22: Linear Scaling Trend
Chart: Linear Spacing by Year
| 1976.0 | 1976.0 | 1978.0 | 1979.0 | 1982.0 | 1982.0 | 1984.0 | 1985.0 | 1986.0 | 1986.0 | 1989.0 | 1991.0 | 1993.0 | 1996.0 | 1997.0 | 1997.0 | 1998.0 | 1999.0 | 1999.0 | 1999.0 | 1999.0 | 2000.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2006.0 | 2007.0 | 2007.0 | 2008.0 | 2008.0 | 2008.0 | 2011.0 | 2012.0 | 2012.0 | 2014.0 | 2015.0
Desktop | 55470.0196 | 46017.8993 | 33733.2334 | 25437.351 | 33028.913 | 19122.5428 | 21151.0856 | 19446.8974 | 44721.3595 | 34641.0162 | 12107.0631 | 12560.9625 | 9738.5168 | 7640.1632 | 5099.0195 | 4290.5817 | 3881.5804 | 3670.6517 | 2563.073 | 2353.7005 | 2891.9952 | 1951.8001 | 2273.0303 | 1341.6408 | 1623.6883 | 1363.8317 | 1349.9904 | 991.0312 | 919.8662 | 699.3786 | 701.0057 | 810.4349 | 510.2359 | 600.7242 | 599.8176 | 583.4119 | 431.517 | 434.5056 | 338.0617 | 355.568 | 264.5751
Embedded | 72231.5119 | 63245.5532 | 62469.5048 | 66666.6667 | 73484.6923 | 77349.2468 | 48304.5892 | 22841.6096 | 1414.2136 | 714.5896 | 319.3744 | 206.5591 | 210.9502 | 194.6247 | 143.8669
GPU | 5070.9255 | 2958.0399 | 2196.8357 | 1802.7756 | 1800 | 1798.1472 | 1498.5373 | 1064.5813 | 1501.3222 | 1427.3693 | 1365.0084 | 1238.2784 | 1362.4427 | 1172.1237 | 1048.3367 | 947.2044 | 957.6077 | 957.4271 | 839.551 | 774.5967 | 655.5213 | 542.2696 | 641.427 | 393.777 | 383.86 | 405.4319 | 416.3332 | 290.9184 | 288.1854 | 281.4912 | 269.4439 | 263.6737 | 276.6559 | 272.3922 | 258.7785 | 258.7785 | 199.6729 | 199.6729 | 226.7787 | 196.5339 | 196.774
Server | 7471.1567 | 1383.3425 | 955.0891 | 854.2422 | 592.1049 | 781.8127 | 657.4136 | 514.5258 | 618.6626 | 614.0033 | 452.9108 | 687.3864 | 604.7432 | 591.1853 | 545.336 | 437.2521 | 443.7602 | 512.3475 | 519.6152 | 465.9302 | 418.908 | 370.9911 | 393.3979 | 369.5111 | 354.2909 | 328.9377 | 344.7969 | 412.2194 | 251.6611 | 337.7845 | 200 | 294.7457
Trend | 133497.7743 | 193.1558
Submillimeter
Submicrometer

## Slide 23: Submillimeter Dimensions
1 micrometer (μm)
10-3
10-4
10-5
10-6
5μm: Spider silk thickness
72μm: Intel 4004 linear scale
50μm: Average size of cell in human body
500μm: Length of amoeba
10μm: Thickness of sheet of plastic food wrap
2μm: E coli bacterium length
1 millimeter (mm)

## Slide 24: Submicrometer Dimensions
1 micrometer (μm)
1 nanometer (nm)
10-6
10-7
10-8
10-9
1nm: Carbon nanotube diameter
2nm: DNA helix diameter
9nm: Cell membrane thickness
144nm: Apple A11 linear scale
30nm: Minimum cooking oil smoke particle diameter
400-700nm: Visible light wavelengths

## Slide 25: Linear Scaling Extrapolation
Chart: Linear Spacing by Year
| 1976.0 | 1976.0 | 1978.0 | 1979.0 | 1982.0 | 1982.0 | 1984.0 | 1985.0 | 1986.0 | 1986.0 | 1989.0 | 1991.0 | 1993.0 | 1996.0 | 1997.0 | 1997.0 | 1998.0 | 1999.0 | 1999.0 | 1999.0 | 1999.0 | 2000.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2006.0 | 2007.0 | 2007.0 | 2008.0 | 2008.0 | 2008.0 | 2011.0 | 2012.0 | 2012.0 | 2014.0 | 2015.0
Desktop | 55470.0196 | 46017.8993 | 33733.2334 | 25437.351 | 33028.913 | 19122.5428 | 21151.0856 | 19446.8974 | 44721.3595 | 34641.0162 | 12107.0631 | 12560.9625 | 9738.5168 | 7640.1632 | 5099.0195 | 4290.5817 | 3881.5804 | 3670.6517 | 2563.073 | 2353.7005 | 2891.9952 | 1951.8001 | 2273.0303 | 1341.6408 | 1623.6883 | 1363.8317 | 1349.9904 | 991.0312 | 919.8662 | 699.3786 | 701.0057 | 810.4349 | 510.2359 | 600.7242 | 599.8176 | 583.4119 | 431.517 | 434.5056 | 338.0617 | 355.568 | 264.5751
Embedded | 72231.5119 | 63245.5532 | 62469.5048 | 66666.6667 | 73484.6923 | 77349.2468 | 48304.5892 | 22841.6096 | 1414.2136 | 714.5896 | 319.3744 | 206.5591 | 210.9502 | 194.6247 | 143.8669
GPU | 5070.9255 | 2958.0399 | 2196.8357 | 1802.7756 | 1800 | 1798.1472 | 1498.5373 | 1064.5813 | 1501.3222 | 1427.3693 | 1365.0084 | 1238.2784 | 1362.4427 | 1172.1237 | 1048.3367 | 947.2044 | 957.6077 | 957.4271 | 839.551 | 774.5967 | 655.5213 | 542.2696 | 641.427 | 393.777 | 383.86 | 405.4319 | 416.3332 | 290.9184 | 288.1854 | 281.4912 | 269.4439 | 263.6737 | 276.6559 | 272.3922 | 258.7785 | 258.7785 | 199.6729 | 199.6729 | 226.7787 | 196.5339 | 196.774
Server | 7471.1567 | 1383.3425 | 955.0891 | 854.2422 | 592.1049 | 781.8127 | 657.4136 | 514.5258 | 618.6626 | 614.0033 | 452.9108 | 687.3864 | 604.7432 | 591.1853 | 545.336 | 437.2521 | 443.7602 | 512.3475 | 519.6152 | 465.9302 | 418.908 | 370.9911 | 393.3979 | 369.5111 | 354.2909 | 328.9377 | 344.7969 | 412.2194 | 251.6611 | 337.7845 | 200 | 294.7457
Trend | 133497.7743 | 193.1558 | 0.24318
243 pm

## Slide 26: Subnanometer Dimensions
1 nanometer (nm)
1 picometer (pm)
10-9
10-10
10-11
10-12
2.4pm: Electron wavelength (Compton wavelength)
53pm: Electron-proton spacing in hydrogen (Bohr radius)
1nm: Carbon nanotube diameter
543pm: Silicon crystal lattice spacing
74pm: Spacing between atoms in hydrogen molecule
243pm: 2065 linear scale projection

## Slide 27: Reaching 2065 Goal
Target
  1017 devices
  400 mm2
  L = 63 pm
Is this possible?
No!
Not with 2-d
fabrication

## Slide 28: Fabricating in 3 Dimensions
Parameters
  1017 devices
  100,000 logical layers
    Each 50 nm thick
    ~1,000,000 physical layers
      To provide wiring and isolation
  L = 20 nm
    10x smaller than today
2065 mm3
20 mm
20 mm
5 mm
2000 mm3

## Slide 29: 3D Fabrication Challenges
Yield
  How to avoid or tolerate flaws
Cost
  High cost of lithography
Power
  Keep power consumption within acceptable limits
  Limited energy available
  Limited ability to dissipate heat

## Slide 30: Photolithography
  Pattern entire chip in one step
  Modern chips require ~60 lithography steps
  Fabricate N transistor system with O(1) steps

## Slide 31: Fabrication Costs
Stepper
  Most expensive equipment in fabrication facility
  Rate limiting process step
    18s / wafer
  Expose 858 mm2 per step
    1.2% of chip area

## Slide 32: Fabrication Economics
Currently
  Fixed number of lithography steps
  Manufacturing cost $10–$20 / chip
    Including amortization of facility
Fabricating 1,000,000 physical layers
  Cannot do lithography on every step
Options
  Chemical self assembly
    Devices generate themselves via chemical processes
  Pattern multiple layers at once

## Slide 33: Samsung V-Nand Flash Example
  Build up layers of unpatterned material
  Then use lithography to slice, drill, etch, and deposit material across all layers
  ~30 total masking steps
  64 layers of memory cells (soon to be 96)
  Exploits particular structure of flash memory circuits

## Slide 34: Meeting Power Constraints
  4.3 B transistors
  2.3 GHz operation
  1—5 W
  64 B neurons
  100 Hz operation
  15—25 W
    Liquid cooling
    Up to 25% body’s total energy consumption
Can we increase number of devices by 23,000,000x without increasing power requirement?

## Slide 35: Challenges to Moore’s Law: Economic
Growing Capital Costs
  State of art fab line ~$20B
  Must have very high volumes to amortize investment
  Has led to major consolidations

## Slide 36: Dennard Scaling
  Due to Robert Dennard, IBM, 1974
  Quantifies benefits of Moore’s Law
How to shrink an IC Process
  Reduce horizontal and vertical dimensions by k
  Reduce voltage by k
Outcomes
  Devices / chip increase by k2
  Clock frequency increases by k
  Power / chip constant
Significance
  Increased capacity and performance
  No increase in power

## Slide 37: End of Dennard Scaling
What Happened?
  Can’t drop voltage below ~1V
  Reached limit of power / chip in 2004
  More logic on chip (Moore’s Law), but can’t make them run faster
    Response has been to increase cores / chip

## Slide 38: Some Thoughts about Technology
Compared to future, past 50 years will seem fairly straightforward
  50 years of using photolithography to pattern transistors on two-dimensional surface
Questions about future integrated systems
  Can we build them?
  What will be the technology?
  Are they commercially viable?
  Can we keep power consumption low?
  What will we do with them?
  How will we program / customize them?

## Slide 39: High-Performance Computing

## Slide 40: Comparing Two Large-Scale Systems
Oakridge Titan
  Monolithic supercomputer (4th fastest in world)
  Designed for compute-intensive applications
Google Data Center
  Servers to support millions of customers
  Designed for data collection, storage, and analysis

## Slide 41: Computing Landscape
Computational Intensity
Personal
Computing
Cloud
Services
Data Intensity
Modeling &
Simulation-Driven
Science &
Engineering
Traditional Supercomputing
Web search
Mapping / directions
Language translation
Video streaming
Google Data Center
Oakridge Titan
Internet-Scale
Computing

## Slide 42: Supercomputing Landscape
Computational Intensity
Personal
Computing
Data Intensity
Modeling &
Simulation-Driven
Science &
Engineering
Traditional Supercomputing
Oakridge Titan

## Slide 43: Supercomputer Applications
Simulation-Based Modeling
  System structure + initial conditions + transition behavior
  Discretize time and space
  Run simulation to see what happens
Requirements
  Model accurately reflects actual system
  Simulation faithfully captures model
Science
Industrial Products
Public Health

## Slide 44: Titan Hardware
Each Node
  AMD 16-core processor
  nVidia Graphics Processing Unit
  38 GB DRAM
  No disk drive
Overall
  7MW, $200M
Local Network
CPU
Node 1
CPU
Node 2
CPU
Node 18,688
• • •
GPU
GPU
GPU

## Slide 45: Titan Node Structure: CPU
CPU
  16 cores sharing common memory
  Supports multithreaded programming
  ~0.16 x 1012 floating-point operations per second (FLOPS) peak performance
DRAM
Memory

## Slide 46: Titan Node Structure: GPU
Kepler GPU
  14 multiprocessors
  Each with 12 groups of 16 stream processors
    14 X 12 X 16 = 2688
  Single-Instruction, Multiple-Data parallelism
    Single instruction controls all processors in group
  4.0 x 1012 FLOPS peak performance

## Slide 47: Titan Programming: Principle
Solving Problem Over Grid
  E.g., finite-element system
  Simulate operation over time
Bulk Synchronous Model
  Partition into Regions
    p regions for p-node machine
  Map Region per Processor

## Slide 48: Titan Programming: Principle (cont)
Bulk Synchronous Model
  Map Region per Processor
  Alternate
    All nodes compute behavior of region
      Perform on GPUs
    All nodes communicate values at boundaries
P1
P2
P3
P4
P5
Communicate
Communicate
Communicate
Compute
Compute
Compute

## Slide 49: Bulk Synchronous Performance
  Limited by performance of slowest processor
Strive to keep perfectly balanced
  Engineer hardware to be highly reliable
  Tune software to make as regular as possible
  Eliminate “noise”
    Operating system events
    Extraneous network activity
P1
P2
P3
P4
P5
Communicate
Communicate
Communicate
Compute
Compute
Compute

## Slide 50: Titan Programming: Reality
System Level
  Message-Passing Interface (MPI) supports node computation, synchronization and communication
Node Level
  OpenMP supports thread-level operation of node CPU
  CUDA programming environment for GPUs
    Performance degrades quickly if don’t have perfect balance among memories and processors
Result
  Single program is complex combination of multiple programming paradigms
  Tend to optimize for specific hardware configuration

## Slide 51: My GPU Experience
Multiply two 1024 x 1024 matrices (MM)
  2 X 109 floating point operations
  Express performance in Giga FLOPS
  Program in CUDA and map onto nVidia GPU
Chart: Giga FLOPS
| simple | transpose | block | tblock | fblock | cosimple | csimple | ctranspose | coblock | cblock | csblock | cqblock
 | 0.93 | 2.25 | 2.07 | 2 | 2.1 | 11.06 | 87.25 | 10.97 | 69.89 | 381.58 | 25.77 | 777.31

## Slide 52: Matrix Multiplication Progress
Versions
  Naive 1
  Simple parallel 11
  Blocking 70
  nVidia Example Code 388
  Reorient memory accesses 382
  Packed data access 777
Observations
  Progress is very nonlinear
    Not even monotonic
  Requires increased understanding of how program maps onto hardware
  Becomes more specialized to specific hardware configuration

## Slide 53: Supercomputer Programming Model
  Program on top of bare hardware
Performance
  Low-level programming to maximize node performance
  Keep everything globally synchronized and balanced
Reliability
  Single failure causes major delay
  Engineer hardware to minimize failures
Hardware
Machine-Dependent
Programming Model
Software
Packages
Application
Programs

## Slide 54: Data-Intensive Computing Landscape
Computational Intensity
Personal
Computing
Cloud
Services
Data Intensity
Web search
Mapping / directions
Language translation
Video streaming
Google Data Center
Internet-Scale
Computing

## Slide 55: Internet Computing
Web Search
  Aggregate text data from across WWW
  No definition of correct operation
  Do not need real-time updating
Mapping Services
  Huge amount of (relatively) static data
  Each customer requires individualized computation
Online Documents
  Must be stored reliably
  Must support real-time updating
  (Relatively) small data volumes

## Slide 56: Other Data-Intensive Computing Applications
Wal-Mart
  267 million items/day, sold at 6,000 stores
  HP built them 4 PB data warehouse
  Mine data to manage supply chain, understand market trends, formulate pricing strategies
LSST
  Chilean telescope will scan entire sky every 3 days
  A 3.2 gigapixel digital camera
  Generate 30 TB/day of image data

## Slide 57: Data-Intensive Application Characteristics
Diverse Classes of Data
  Structured & unstructured
  High & low integrity requirements
Diverse Computing Needs
  Localized & global processing
  Numerical & non-numerical
  Real-time & batch processing

## Slide 58: Google Data Centers
Dalles, Oregon
  Hydroelectric power @ 2¢ / KW Hr
  50 Megawatts
    Enough to power 60,000 homes
  Engineered for low cost, modularity & power efficiency
  Container: 1160 server nodes, 250KW
Notes: One of the biggest users of cluster computing is Google. They have set up dozens of data centers around the world, containing more computer power than just about anyone else.
Here’s a picture of their data center in Dalles, Oregon. It cost them $600M and requires around 50 megawatts of power. (For reference, that much power would supply the residential electricity needs of 6,000 households in the U.S.). They located the data center near the Columbia River to take advantage of low-cost electricity.
Imagine what our intelligence sources could do if they had facilities on this scale to store and process satellite imagery, voice signals, and feeds from media outlets.

## Slide 59: Google Cluster
  Typically 1,000−2,000 nodes
Node Contains
  2 multicore CPUs
  2 disk drives
  DRAM
Local Network
CPU
Node 1
CPU
Node 2
CPU
Node n
• • •

## Slide 60: Hadoop Project
File system with files distributed across nodes
  Store multiple (typically 3 copies of each file)
    If one node fails, data still available
  Logically, any node has access to any file
    May need to fetch across network
Map / Reduce programming environment
  Software manages execution of tasks on nodes
Local Network
CPU
Node 1
CPU
Node 2
CPU
Node n
• • •

## Slide 61: Map/Reduce Programming Model
  Map computation across many objects
    E.g., 1010 Internet web pages
  Aggregate results in many different ways
  System deals with issues of resource allocation & reliability
M
x1
M
x2
M
x3
M
xn
k1
Map
Reduce
k1
kr
  
  
Key-Value
Pairs
Dean & Ghemawat: “MapReduce: Simplified Data Processing on Large Clusters”, OSDI 2004

## Slide 62: Cluster Programming Model
  Application programs written in terms of high-level operations on data
  Runtime system controls scheduling, load balancing, …
Scaling Challenges
  Centralized scheduler forms bottleneck
  Copying to/from disk very costly
  Hard to limit data movement
    Significant performance factor
Hardware
Machine-Independent
Programming Model
Runtime
System
Application
Programs

## Slide 63: Recent Programming Systems
Spark Project
  at U.C., Berkeley
  Grown to have large open source community
GraphLab
  Started as project at CMU by Carlos Guestrin
  Environment for describing machine-learning algorithms
    Sparse matrix structure described by graph
    Computation based on updating of node values

## Slide 64: Computing Landscape Trends
Computational Intensity
Data Intensity
Modeling &
Simulation-Driven
Science &
Engineering
Traditional
Supercomputing
Mixing simulation
with data analysis

## Slide 65: Combining Simulation with Real Data
Limitations
  Simulation alone: Hard to know if model is correct
  Data alone: Hard to understand causality & “what if”
Combination
  Check and adjust model during simulation

## Slide 66: Real-Time Analytics
Millenium XXL Simulation (2010)
  3 X 109 particles
  Simulation run of 9.3 days on 12,228 cores
  700TB total data generated
    Save at only 4 time points
    70 TB
  Large-scale simulations generate large data sets
What If?
  Could perform data analysis while simulation is running
Simulation
Engine
Analytic
Engine

## Slide 67: Computing Landscape Trends
Computational Intensity
Internet-Scale
Computing
Data Intensity
Google Data Center
Sophisticated
data analysis

## Slide 68: Example Analytic Applications
Classifier
Image
Description
Microsoft Project Adam
Transducer
English
Text
German
Text

## Slide 69: Data Analysis with Deep Neural Networks
Task:
  Compute classification of set of input signals
Training
  Use many training samples of form input / desired output
  Compute weights that minimize classification error
Operation
  Propagate signals from input to output

## Slide 70: DNN Application Example
Facebook DeepFace Architecture

## Slide 71: Training DNNs
Characteristics
  Iterative numerical algorithm
  Regular data organization
Project Adam Training
  2B connections
  15M images
  62 machines
  10 days
Chart: 
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Chart: 
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0
 | 0 | 1 | 4 | 9 | 16 | 25 | 36 | 49 | 64 | 81 | 100 | 121 | 144 | 169 | 196 | 225 | 256 | 289 | 324 | 361 | 400
Chart: 
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
×

Model Size
Training Data
Training Effort

## Slide 72: Trends
Computational Intensity
Internet-Scale
Computing
Data Intensity
Modeling &
Simulation-Driven
Science &
Engineering
Traditional
Supercomputing
Google Data Center
Sophisticated
data analysis
Mixing simulation
with real-world data
Convergence?

## Slide 73: Challenges for Convergence
Supercomputers
  Customized
  Optimized for reliability
  Source of “noise”
  Static scheduling
  Low-level, processor-centric model
Data Center Clusters
  Consumer grade
  Optimized for low cost
  Provides reliability
  Dynamic allocation
  High level, data-centric model
Hardware
Run-Time System
Application Programming

## Slide 74: Summary: Computation/Data Convergence
Two Important Classes of Large-Scale Computing
  Computationally intensive supercomputing
  Data intensive processing
    Internet companies + many other applications
Followed Different Evolutionary Paths
  Supercomputers: Get maximum performance from available hardware
  Data center clusters: Maximize cost/performance over variety of data-centric tasks
  Yielded different approaches to hardware, runtime systems, and application programming
A Convergence Would Have Important Benefits
  Computational and data-intensive applications
  But, not clear how to do it