## Slide 2: Thread-Level Parallelism 15-213 / 18-213 / 14-513 / 15-513: Introduction to Computer Systems 26th Lecture, November 27, 2018

## Slide 3: Today
Parallel Computing Hardware
  Multicore
    Multiple separate processors on single chip
  Hyperthreading
    Efficient execution of multiple threads on single core
Consistency Models
  What happens when multiple threads are reading & writing shared state
Thread-Level Parallelism
  Splitting program into independent tasks
    Example: Parallel summation
    Examine some performance artifacts
  Divide-and conquer parallelism
    Example: Parallel quicksort

## Slide 4: Typical Multicore Processor
Multiple processors operating with coherent view of memory
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core n-1
…
L3 unified cache
(shared by all cores)
Main memory

## Slide 5: Out-of-Order Processor Structure
Instruction control dynamically converts program into stream of operations
Operations mapped onto functional units to execute in parallel
Functional Units
Int
Arith
Int
Arith
FP
Arith
Load /
Store
Instruction Control
Registers
Instruction Decoder
Op. Queue
Data Cache
Instruction
Cache
PC

## Slide 6: Hyperthreading Implementation
Replicate instruction control to process K instruction streams
K copies of all registers
Share functional units
Functional Units
Int
Arith
Int
Arith
FP
Arith
Load /
Store
Instruction Control
Reg B
Instruction Decoder
Op. Queue B
Data Cache
Instruction
Cache
Reg A
Op. Queue A
PC A
PC B

## Slide 7: Benchmark Machine
Get data about machine from /proc/cpuinfo
Shark Machines
  Intel Xeon E5520 @ 2.27 GHz
  Nehalem, ca. 2010
  8 Cores
  Each can do 2x hyperthreading

## Slide 8: Exploiting parallel execution
So far, we’ve used threads to deal with I/O delays
  e.g., one thread per client to prevent one from delaying another
Multi-core CPUs offer another opportunity
  Spread work over threads executing in parallel on N cores
  Happens automatically, if many independent tasks
    e.g., running many applications or serving many clients
  Can also write code to make one big task go faster
    by organizing it as multiple parallel sub-tasks
Shark machines can execute 16 threads at once
  8 cores, each with 2-way hyperthreading
  Theoretical speedup of 16X
    never achieved in our benchmarks

## Slide 9: Memory Consistency
What are the possible values printed?
  Depends on memory consistency model
  Abstract model of how hardware handles concurrent accesses
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);

## Slide 10: Non-Coherent Cache Scenario
Write-back caches, without coordination between them
Main Memory
a:1
b:100
Thread1 Cache
a: 2
Thread2 Cache
b:200
a:1
print 1
b:100
print 100
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);
At later points, a:2 and b:200
are written back to main memory

## Slide 11: Memory Consistency
What are the possible values printed?
  Depends on memory consistency model
  Abstract model of how hardware handles concurrent accesses
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);
Wa
Rb
Wb
Ra
Thread consistency
constraints

## Slide 12: Memory Consistency
What are the possible values printed?
  Depends on memory consistency model
  Abstract model of how hardware handles concurrent accesses
Sequential consistency
  As if only one operation at a time, in an order consistent with the order of operations within each thread
  Thus, overall effect consistent with each individual thread but otherwise allows an arbitrary interleaving
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);
Wa
Rb
Wb
Ra
Thread consistency
constraints

## Slide 13: Sequential Consistency Example
Impossible outputs
  100, 1 and 1, 100
  Would require reaching both Ra and Rb before Wa and Wb
Wa
Rb
Wb
Ra
Wb
Rb
Ra
Ra
Rb
Wb
Ra
Wa
Rb
Wa
Ra
Rb
Rb
Ra
100, 2
200, 2
2, 200
1, 200
2, 200
200, 2
Wa
Rb
Wb
Ra
Thread consistency
constraints
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);

## Slide 14: Non-Coherent Cache Scenario
Write-back caches, without coordination between them
Main Memory
a:1
b:100
Thread1 Cache
a: 2
Thread2 Cache
b:200
a:1
print 1
b:100
print 100
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);
Sequentially consistent?
No!

## Slide 15: Non-Sequentially Consistent Scenario
Coherent caches, but thread consistency constraints violated due to out-of-order execution
Main Memory
a:1
b:100
Thread1 Cache
a:2
Thread2 Cache
b:200
a:1
print 1
b:100
print 100
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);
Fix: Add SFENCE instructions between Wa & Rb and Wb & Ra
1
2
3
4

## Slide 16: Snoopy Caches
Tag each cache block with state
  Invalid Cannot use value
  Shared Readable copy
  Exclusive Writeable copy
Main Memory
a:1
b:100
Thread1 Cache
Thread2 Cache
a: 2
E
b:200
E
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);

## Slide 17: Snoopy Caches
Tag each cache block with state
  Invalid Cannot use value
  Shared Readable copy
  Exclusive Writeable copy
Main Memory
a:1
b:100
Thread1 Cache
Thread2 Cache
a: 2
E
b:200
E
print 200
b:200
S
b:200
S
print 2
a:2
S
a: 2
S
int a = 1;
int b = 100;
Thread1:
Wa: a = 2;
Rb: print(b);
Thread2:
Wb: b = 200;
Ra: print(a);
When cache sees request for one of its E-tagged blocks
  Supply value from cache (Note: value in memory may be stale)
  Set tag to S

## Slide 18: Memory Models
Sequentially Consistent:
  Each thread executes in proper order, any interleaving
To ensure, requires
  Proper cache/memory behavior
  Proper intra-thread ordering constraints

## Slide 19: Today
Parallel Computing Hardware
  Multicore
    Multiple separate processors on single chip
  Hyperthreading
    Efficient execution of multiple threads on single core
Consistency Models
  What happens when multiple threads are reading & writing shared state
Thread-Level Parallelism
  Splitting program into independent tasks
    Example: Parallel summation
    Examine some performance artifacts
  Divide-and conquer parallelism
    Example: Parallel quicksort

## Slide 20: Summation Example
Sum numbers 0, …, N-1
  Should add up to (N-1)*N/2
Partition into K ranges
  N/K values each
  Each of the t threads processes 1 range
  Accumulate leftover values serially
Method #1: All threads update single global variable
  1A: No synchronization
  1B: Synchronize with pthread semaphore
  1C: Synchronize with pthread mutex
    “Binary” semaphore. Only values 0 & 1

## Slide 21: Accumulating in Single Global Variable: Declarations
typedef unsigned long data_t;
/* Single accumulator */
volatile data_t global_sum;
/* Mutex & semaphore for global sum */
sem_t semaphore;
pthread_mutex_t mutex;
/* Number of elements summed by each thread */
size_t nelems_per_thread;
/* Keep track of thread IDs */
pthread_t tid[MAXTHREADS];
/* Identify each thread */
int myid[MAXTHREADS];

## Slide 22: Accumulating in Single Global Variable: Declarations
typedef unsigned long data_t;
/* Single accumulator */
volatile data_t global_sum;
/* Mutex & semaphore for global sum */
sem_t semaphore;
pthread_mutex_t mutex;
/* Number of elements summed by each thread */
size_t nelems_per_thread;
/* Keep track of thread IDs */
pthread_t tid[MAXTHREADS];
/* Identify each thread */
int myid[MAXTHREADS];

## Slide 23: Accumulating in Single Global Variable: Declarations
typedef unsigned long data_t;
/* Single accumulator */
volatile data_t global_sum;
/* Mutex & semaphore for global sum */
sem_t semaphore;
pthread_mutex_t mutex;
/* Number of elements summed by each thread */
size_t nelems_per_thread;
/* Keep track of thread IDs */
pthread_t tid[MAXTHREADS];
/* Identify each thread */
int myid[MAXTHREADS];

## Slide 24: Accumulating in Single Global Variable: Operation
nelems_per_thread = nelems / nthreads;
/* Set global value */
global_sum = 0;
/* Create threads and wait for them to finish */
for (i = 0; i < nthreads; i++) {
myid[i] = i;
Pthread_create(&tid[i], NULL, thread_fun, &myid[i]);
}
for (i = 0; i < nthreads; i++)
Pthread_join(tid[i], NULL);
result = global_sum;
/* Add leftover elements */
for (e = nthreads * nelems_per_thread; e < nelems; e++)
result += e;
Thread ID
Thread routine
Thread arguments
(void *p)

## Slide 25: Thread Function: No Synchronization
void *sum_race(void *vargp)
{
int myid = *((int *)vargp);
size_t start = myid * nelems_per_thread;
size_t end = start + nelems_per_thread;
size_t i;
for (i = start; i < end; i++) {
global_sum += i;
}
return NULL;
}

## Slide 26: Unsynchronized Performance
N = 230
Best speedup = 2.86X
Gets wrong answer when > 1 thread!
Why?

## Slide 27: Thread Function: Semaphore / Mutex
void *sum_sem(void *vargp)
{
int myid = *((int *)vargp);
size_t start = myid * nelems_per_thread;
size_t end = start + nelems_per_thread;
size_t i;
for (i = start; i < end; i++) {
sem_wait(&semaphore);
global_sum += i;
sem_post(&semaphore);
}
return NULL;
}
sem_wait(&semaphore);
global_sum += i;
sem_post(&semaphore);
pthread_mutex_lock(&mutex);
global_sum += i;
pthread_mutex_unlock(&mutex);
Semaphore
Mutex

## Slide 28: Semaphore / Mutex Performance
Terrible Performance
  2.5 seconds  ~10 minutes
Mutex 3X faster than semaphore
Clearly, neither is successful
What is main reason for poor performance?

## Slide 29: Separate Accumulation
Method #2: Each thread accumulates into separate variable
  2A: Accumulate in contiguous array elements
  2B: Accumulate in spaced-apart array elements
  2C: Accumulate in registers
/* Partial sum computed by each thread */
data_t psum[MAXTHREADS*MAXSPACING];
/* Spacing between accumulators */
size_t spacing = 1;

## Slide 30: Separate Accumulation: Operation
nelems_per_thread = nelems / nthreads;
/* Create threads and wait for them to finish */
for (i = 0; i < nthreads; i++) {
myid[i] = i;
psum[i*spacing] = 0;
Pthread_create(&tid[i], NULL, thread_fun, &myid[i]);
}
for (i = 0; i < nthreads; i++)
Pthread_join(tid[i], NULL);
result = 0;
/* Add up the partial sums computed by each thread */
for (i = 0; i < nthreads; i++)
result += psum[i*spacing];
/* Add leftover elements */
for (e = nthreads * nelems_per_thread; e < nelems; e++)
result += e;

## Slide 31: Thread Function: Memory Accumulation
void *sum_global(void *vargp)
{
int myid = *((int *)vargp);
size_t start = myid * nelems_per_thread;
size_t end = start + nelems_per_thread;
size_t i;
size_t index = myid*spacing;
psum[index] = 0;
for (i = start; i < end; i++) {
psum[index] += i;
}
return NULL;
}
Where is the mutex?

## Slide 32: Memory Accumulation Performance
Clear threading advantage
  Adjacent speedup: 5 X
  Spaced-apart speedup: 13.3 X (Only observed speedup > 8)
Why does spacing the accumulators apart matter?

## Slide 33: False Sharing
Coherency maintained on cache blocks
To update psum[i], thread i must have exclusive access
  Threads sharing common cache block will keep fighting each other for access to block
…
…
0
7
8
15
Cache Block m
Cache Block m+1
psum

## Slide 34: False Sharing Performance
  Best spaced-apart performance 2.8 X better than best adjacent
Demonstrates cache block size = 64
  8-byte values
  No benefit increasing spacing beyond 8

## Slide 35: Thread Function: Register Accumulation
void *sum_local(void *vargp)
{
int myid = *((int *)vargp);
size_t start = myid * nelems_per_thread;
size_t end = start + nelems_per_thread;
size_t i;
size_t index = myid*spacing;
data_t sum = 0;
for (i = start; i < end; i++) {
sum += i;
}
psum[index] = sum;
return NULL;
}

## Slide 36: Register Accumulation Performance
Clear threading advantage
  Speedup = 7.5 X
2X better than fastest memory accumulation
Beware the speedup metric!

## Slide 37: Lessons learned
Sharing memory can be expensive
  Pay attention to true sharing
  Pay attention to false sharing
Use registers whenever possible
  (Remember cachelab)
  Use local cache whenever possible
Deal with leftovers
When examining performance, compare to best possible sequential implementation

## Slide 38: Quiz Time!
Check out:
https://canvas.cmu.edu/courses/5835

## Slide 39: A More Substantial Example: Sort
Sort set of N random numbers
Multiple possible algorithms
  Use parallel version of quicksort
Sequential quicksort of set of values X
  Choose “pivot” p from X
  Rearrange X into
    L: Values  p
    R: Values  p
  Recursively sort L to get L
  Recursively sort R to get R
  Return L : p : R

## Slide 40: Sequential Quicksort Visualized
X
p
L
p
R
p2
L2
R2
p2



L

## Slide 41: Sequential Quicksort Visualized
X
p
R
p3
L3
R3
p3
L



R
p
L
R

## Slide 42: Sequential Quicksort Code
Sort nele elements starting at base
  Recursively sort L or R if has more than one element
void qsort_serial(data_t *base, size_t nele) {
if (nele <= 1)
return;
if (nele == 2) {
if (base[0] > base[1])
swap(base, base+1);
return;
}
/* Partition returns index of pivot */
size_t m = partition(base, nele);
if (m > 1)
qsort_serial(base, m);
if (nele-1 > m+1)
qsort_serial(base+m+1, nele-m-1);
}

## Slide 43: Parallel Quicksort
Parallel quicksort of set of values X
  If N  Nthresh, do sequential quicksort
  Else
    Choose “pivot” p from X
    Rearrange X into
      L: Values  p
      R: Values  p
    Recursively spawn separate threads
      Sort L to get L
      Sort R to get R
    Return L : p : R

## Slide 44: Parallel Quicksort Visualized
X
p
L
p
R
p2
p3
p2
L2
R2
L3
R3
p3
p



L



R
p

## Slide 45: Thread Structure: Sorting Tasks
Task: Sort subrange of data
  Specify as:
    base: Starting address
    nele: Number of elements in subrange
Run as separate thread
X
  
Task Threads

## Slide 46: Small Sort Task Operation
Sort subrange using serial quicksort
X
  
Task Threads

## Slide 47: Large Sort Task Operation
X
  
p
L
R
X
  
p
L
R
Partition Subrange
Spawn 2 tasks

## Slide 48: Top-Level Function (Simplified)
Sets up data structures
Calls recursive sort routine
Keeps joining threads until none left
Frees data structures
void tqsort(data_t *base, size_t nele) {
init_task(nele);
global_base = base;
global_end = global_base + nele - 1;
task_queue_ptr tq = new_task_queue();
tqsort_helper(base, nele, tq);
join_tasks(tq);
free_task_queue(tq);
}

## Slide 49: Recursive sort routine (Simplified)
Small partition: Sort serially
Large partition: Spawn new sort task
/* Multi-threaded quicksort */
static void tqsort_helper(data_t *base, size_t nele,
task_queue_ptr tq) {
if (nele <= nele_max_sort_serial) {
/* Use sequential sort */
qsort_serial(base, nele);
return;
}
sort_task_t *t = new_task(base, nele, tq);
spawn_task(tq, sort_thread, (void *) t);
}

## Slide 50: Sort task thread (Simplified)
Get task parameters
Perform partitioning step
Call recursive sort routine on each partition
/* Thread routine for many-threaded quicksort */
static void *sort_thread(void *vargp) {
sort_task_t *t = (sort_task_t *) vargp;
data_t *base = t->base;
size_t nele = t->nele;
task_queue_ptr tq = t->tq;
free(vargp);
size_t m = partition(base, nele);
if (m > 1)
tqsort_helper(base, m, tq);
if (nele-1 > m+1)
tqsort_helper(base+m+1, nele-m-1, tq);
return NULL;
}

## Slide 51: Parallel Quicksort Performance
Serial fraction: Fraction of input at which do serial sort
Sort 227 (134,217,728) random values
Best speedup = 6.84X

## Slide 52: Parallel Quicksort Performance
Good performance over wide range of fraction values
  F too small: Not enough parallelism
  F too large: Thread overhead + run out of thread memory

## Slide 53: Amdahl’s Law
Overall problem
  T Total sequential time required
  p Fraction of total that can be sped up (0  p  1)
  k Speedup factor
Resulting Performance
  Tk = pT/k + (1-p)T
    Portion which can be sped up runs k times faster
    Portion which cannot be sped up stays the same
  Maximum possible speedup
    k = 
    T = (1-p)T

## Slide 54: Amdahl’s Law Example
Overall problem
  T = 10 Total time required
  p = 0.9 Fraction of total which can be sped up
  k = 9 Speedup factor
Resulting Performance
  T9 = 0.9 * 10/9 + 0.1 * 10 = 1.0 + 1.0 = 2.0
  Maximum possible speedup
    T = 0.1 * 10.0 = 1.0

## Slide 55: Amdahl’s Law & Parallel Quicksort
Sequential bottleneck
  Top-level partition: No speedup
  Second level:  2X speedup
  kth level:  2k-1X speedup
Implications
  Good performance for small-scale parallelism
  Would need to parallelize partitioning step to get large-scale parallelism
    Parallel Sorting by Regular Sampling
      H. Shi & J. Schaeffer, J. Parallel & Distributed Computing, 1992

## Slide 56: Parallelizing Partitioning Step
p
L1
R1
X1
X2
X3
X4
L2
R2
L3
R3
L4
R4
Parallel partitioning based on global p
L1
R1
L2
R2
L3
R3
L4
R4
Reassemble into partitions

## Slide 57: Experience with Parallel Partitioning
Could not obtain speedup
Speculate: Too much data copying
  Could not do everything within source array
  Set up temporary space for reassembling partition

## Slide 58: Lessons Learned
Must have parallelization strategy
  Partition into K independent parts
  Divide-and-conquer
Inner loops must be synchronization free
  Synchronization operations very expensive
Watch out for hardware artifacts
  Need to understand processor & memory structure
  Sharing and false sharing of global data
Beware of Amdahl’s Law
  Serial code can become bottleneck
You can do it!
  Achieving modest levels of parallelism is not difficult
  Set up experimental framework and test multiple strategies