## Slide 1: Future of Computing: Moore’s Law & Its Implications + High-Performance Computing 15-213: Introduction to Computer Systems 27th Lecture, Nov. 29, 2018

## Slide 2: Moore’s Law Origins
April 19, 1965

## Slide 3: Moore’s Law Origins
Moore’s Thesis
  Minimize price per device
  Optimum number of devices / chip increasing 2x / year
Later
  2x / 2 years
  “Moore’s Prediction”
1965: 50
1970: 1000

## Slide 4: Moore’s Law: 50+ Years
Sample of
130 processor chips
Wikipedia:
Transistor_count
Chart: Transistor Count by Year
| 1976 | 1976 | 1978 | 1979 | 1982 | 1982 | 1984 | 1985 | 1986 | 1986 | 1989 | 1991 | 1993 | 1996 | 1997 | 1997 | 1998 | 1999 | 1999 | 1999 | 1999 | 2000 | 2000 | 2001 | 2002 | 2003 | 2003 | 2004 | 2005 | 2006 | 2006 | 2007 | 2007 | 2008 | 2008 | 2008 | 2011 | 2012 | 2012 | 2014 | 2015
Desktop | 6500 | 8500 | 29000 | 68000 | 55000 | 134000 | 190000 | 275000 | 25000 | 25000 | 1180235 | 1350000 | 3100000 | 4300000 | 7500000 | 8800000 | 7500000 | 9500000 | 21300000 | 22000000 | 27400000 | 21000000 | 42000000 | 45000000 | 55000000 | 54300000 | 105900000 | 112000000 | 169000000 | 184000000 | 291000000 | 169000000 | 411000000 | 230000000 | 731000000 | 758000000 | 1160000000 | 1303000000 | 1400000000 | 1400000000 | 1900000000
Embedded | 2300 | 3500 | 4100 | 4500 | 5000 | 3510 | 9000 | 11500 | 25000000 | 47000000 | 1000000000 | 2000000000 | 3000000000 | 3300000000 | 4300000000 | 6900000000
GPU | 3500000 | 8000000 | 23000000 | 20000000 | 25000000 | 30000000 | 57000000 | 60000000 | 63000000 | 107000000 | 117000000 | 135000000 | 160000000 | 222000000 | 303000000 | 321000000 | 241000000 | 384000000 | 681000000 | 700000000 | 754000000 | 959000000 | 1400000000 | 2154000000 | 2640000000 | 3000000000 | 3200000000 | 4312711873 | 3540000000 | 7080000000 | 5000000000 | 6300000000 | 5200000000 | 8100000000 | 8900000000 | 15300000000 | 7000000000 | 12500000000 | 21100000000
Server | 5500000 | 220000000 | 410000000 | 592000000 | 1700000000 | 463000000 | 789000000 | 1900000000 | 904000000 | 1000000000 | 1170000000 | 1200000000 | 1400000000 | 2000000000 | 2300000000 | 2270000000 | 2600000000 | 1200000000 | 2100000000 | 2750000000 | 3100000000 | 1860000000 | 4200000000 | 2600000000 | 4310000000 | 5000000000 | 5560000000 | 3990000000 | 7200000000 | 4800000000 | 6100000000 | 8000000000 | 19200000000
General Trend | 981.366 | 18278006823.8039
Moore's Prediction | 282.8427 | 4745313281.2126

## Slide 5: Moore’s Law Benefits
1976 Cray 1
  250 M Ops/second
  ~170,000 chips
  0.5B transistors
  5,000 kg, 115 KW
  $9M
  80 manufactured
2018 iPhone XS
  > 10 B Ops/second
  8 chips
  6.9 B transistors (CPU only)
  177 g, < 5 W
  $999
  ~9 million sold in first 7 days

## Slide 6: What Moore’s Law Has Meant
1965 Consumer Product
2018 Consumer Product
Apple A12
6.9 B transistors
(not to scale)

## Slide 7: Visualizing Moore’s Law to Date
Intel 4004
1970
2,300 transistors
Apple A12
2018
6.9 B transistors
If transistors were the size of a grain of sand
0.1 g
300 kg

## Slide 8: What Does 6.9 Billion Transistors Provide?
4 CPUs
  2 high performance
  4 low power
4 GPUs
  Graphics/image/video processing
Neural Engine
  For AI applications
Lots of specialized logic
  Video encode / decode
  Image stitching

## Slide 9: Moore’s Law Economics
Capital +
R&D Investment
New Technology
Product
Design
Sales $$
Better
Products
Consumer products sustain the
$300B semiconductor industry

## Slide 10: What Moore’s Law Has Meant
20 versions of iPhone since 2007

## Slide 11: What Moore’s Law Could Mean
2018 Consumer Product
2065 Consumer Product
  Portable
  Low power
  Will drive markets & innovation
?

## Slide 12: Requirements for Future Technology
Must be suitable for portable, low-power operation
  Consumer products
  Internet of Things components
  Not cryogenic, not quantum
Must be inexpensive to manufacture
  Comparable to current semiconductor technology
    O(1) cost to make chip with O(N) devices
Need not be based on transistors
  Memristors, carbon nanotubes, DNA transcription, ...
  Possibly new models of computation
  But, still want lots of devices in an integrated system

## Slide 13: Moore’s Law: 100 Years
1017 devices!
Chart: Device Count by Year
| 1976 | 1976 | 1978 | 1979 | 1982 | 1982 | 1984 | 1985 | 1986 | 1986 | 1989 | 1991 | 1993 | 1996 | 1997 | 1997 | 1998 | 1999 | 1999 | 1999 | 1999 | 2000 | 2000 | 2001 | 2002 | 2003 | 2003 | 2004 | 2005 | 2006 | 2006 | 2007 | 2007 | 2008 | 2008 | 2008 | 2011 | 2012 | 2012 | 2014 | 2015
Desktop | 6500 | 8500 | 29000 | 68000 | 55000 | 134000 | 190000 | 275000 | 25000 | 25000 | 1180235 | 1350000 | 3100000 | 4300000 | 7500000 | 8800000 | 7500000 | 9500000 | 21300000 | 22000000 | 27400000 | 21000000 | 42000000 | 45000000 | 55000000 | 54300000 | 105900000 | 112000000 | 169000000 | 184000000 | 291000000 | 169000000 | 411000000 | 230000000 | 731000000 | 758000000 | 1160000000 | 1303000000 | 1400000000 | 1400000000 | 1900000000
Embedded | 2300 | 3500 | 4100 | 4500 | 5000 | 3510 | 9000 | 11500 | 25000000 | 47000000 | 1000000000 | 2000000000 | 3000000000 | 3300000000 | 4300000000 | 6900000000
GPU | 3500000 | 8000000 | 23000000 | 20000000 | 25000000 | 30000000 | 57000000 | 60000000 | 63000000 | 107000000 | 117000000 | 135000000 | 160000000 | 222000000 | 303000000 | 321000000 | 241000000 | 384000000 | 681000000 | 700000000 | 754000000 | 959000000 | 1400000000 | 2154000000 | 2640000000 | 3000000000 | 3200000000 | 4312711873 | 3540000000 | 7080000000 | 5000000000 | 6300000000 | 5200000000 | 8100000000 | 8900000000 | 15300000000 | 7000000000 | 12500000000 | 21100000000
Server | 5500000 | 220000000 | 410000000 | 592000000 | 1700000000 | 463000000 | 789000000 | 1900000000 | 904000000 | 1000000000 | 1170000000 | 1200000000 | 1400000000 | 2000000000 | 2300000000 | 2270000000 | 2600000000 | 1200000000 | 2100000000 | 2750000000 | 3100000000 | 1860000000 | 4200000000 | 2600000000 | 4310000000 | 5000000000 | 5560000000 | 3990000000 | 7200000000 | 4800000000 | 6100000000 | 8000000000 | 19200000000
General Trend | 981.366 | 18278006823.8039 | 2.402e+17
Moore's Prediction | 282.8427 | 4745313281.2126 | 56294995342131200

## Slide 14: Visualizing 1017 Devices
0.1 m3
3.5 X 109 grains
1 million m3
0.35 X 1017 grains
If devices were the size of a grain of sand

## Slide 15: Increasing Transistor Counts
Chips have gotten bigger
  1 area doubling / 10 years
Transistors have gotten smaller
  4 density doublings / 10 years
Will these trends continue?

## Slide 16: Chips Have Gotten Bigger
Intel 4004
1970
2,300 transistors
12 mm2
Apple A12
6.9 B transistors
83 mm2
NVIDIA GV100 Volta
2017
21.1 B transistors
815 mm2

## Slide 17: Chip Size Trend
2x every 9.8 years
Chart: Area by Year
| 1976 | 1976 | 1978 | 1979 | 1982 | 1982 | 1984 | 1985 | 1986 | 1986 | 1989 | 1991 | 1993 | 1996 | 1997 | 1997 | 1998 | 1999 | 1999 | 1999 | 1999 | 2000 | 2000 | 2001 | 2002 | 2003 | 2003 | 2004 | 2005 | 2006 | 2006 | 2007 | 2007 | 2008 | 2008 | 2008 | 2011 | 2012 | 2012 | 2014 | 2015
Desktop | 20 | 18 | 33 | 44 | 60 | 49 | 85 | 104 | 50 | 30 | 173 | 213 | 294 | 251 | 195 | 162 | 113 | 128 | 118 | 184 | 180 | 80 | 217 | 81 | 145 | 101 | 193 | 110 | 143 | 90 | 143 | 111 | 107 | 83 | 263 | 258 | 216 | 246 | 160 | 177 | 133
Embedded | 12 | 14 | 16 | 20 | 27 | 21 | 21 | 6 | 50 | 24 | 102 | 89 | 128 | 125 | 89 | 83.27
GPU | 90 | 70 | 111 | 65 | 81 | 97 | 128 | 68 | 142 | 218 | 218 | 207 | 297 | 305 | 333 | 288 | 221 | 352 | 480 | 420 | 324 | 282 | 576 | 334 | 389 | 520 | 526 | 365 | 294 | 561 | 363 | 438 | 398 | 601 | 596 | 610 | 360 | 484 | 815
Server | 307 | 421 | 374 | 432 | 596 | 283 | 341 | 503 | 346 | 377 | 240 | 567 | 512 | 699 | 684 | 434 | 512 | 315 | 567 | 597 | 544 | 256 | 650 | 355 | 541 | 541 | 661 | 678 | 456 | 192 | 696 | 695 | 768
Trend | 17.2782 | 522.5587

## Slide 18: Chip Size Extrapolation
147 cm2
Chart: Area by Year
| 1976 | 1976 | 1978 | 1979 | 1982 | 1982 | 1984 | 1985 | 1986 | 1986 | 1989 | 1991 | 1993 | 1996 | 1997 | 1997 | 1998 | 1999 | 1999 | 1999 | 1999 | 2000 | 2000 | 2001 | 2002 | 2003 | 2003 | 2004 | 2005 | 2006 | 2006 | 2007 | 2007 | 2008 | 2008 | 2008 | 2011 | 2012 | 2012 | 2014 | 2015
Desktop | 20 | 18 | 33 | 44 | 60 | 49 | 85 | 104 | 50 | 30 | 173 | 213 | 294 | 251 | 195 | 162 | 113 | 128 | 118 | 184 | 180 | 80 | 217 | 81 | 145 | 101 | 193 | 110 | 143 | 90 | 143 | 111 | 107 | 83 | 263 | 258 | 216 | 246 | 160 | 177 | 133
Embedded | 12 | 14 | 16 | 20 | 27 | 21 | 21 | 6 | 50 | 24 | 102 | 89 | 128 | 125 | 89 | 83.27
GPU | 90 | 70 | 111 | 65 | 81 | 97 | 128 | 68 | 142 | 218 | 218 | 207 | 297 | 305 | 333 | 288 | 221 | 352 | 480 | 420 | 324 | 282 | 576 | 334 | 389 | 520 | 526 | 365 | 294 | 561 | 363 | 438 | 398 | 601 | 596 | 610 | 360 | 484 | 815
Server | 307 | 421 | 374 | 432 | 596 | 283 | 341 | 503 | 346 | 377 | 240 | 567 | 512 | 699 | 684 | 434 | 512 | 315 | 567 | 597 | 544 | 256 | 650 | 355 | 541 | 541 | 661 | 678 | 456 | 192 | 696 | 695 | 768
Trend | 17.2782 | 522.5587 | 14720.5667

## Slide 19: Extrapolation: The iPhone XXX
Apple A111
2065
1017 transistors
147 cm2

## Slide 20: Transistors Have Gotten Smaller
  Area A
  N devices
  Linear Scale L
L

## Slide 21: Linear Scaling Trend
Chart: Linear Spacing by Year
| 1976 | 1976 | 1978 | 1979 | 1982 | 1982 | 1984 | 1985 | 1986 | 1986 | 1989 | 1991 | 1993 | 1996 | 1997 | 1997 | 1998 | 1999 | 1999 | 1999 | 1999 | 2000 | 2000 | 2001 | 2002 | 2003 | 2003 | 2004 | 2005 | 2006 | 2006 | 2007 | 2007 | 2008 | 2008 | 2008 | 2011 | 2012 | 2012 | 2014 | 2015
Desktop | 55470.0196 | 46017.8993 | 33733.2334 | 25437.351 | 33028.913 | 19122.5428 | 21151.0856 | 19446.8974 | 44721.3595 | 34641.0162 | 12107.0631 | 12560.9625 | 9738.5168 | 7640.1632 | 5099.0195 | 4290.5817 | 3881.5804 | 3670.6517 | 2353.7005 | 2891.9952 | 2563.073 | 1951.8001 | 2273.0303 | 1341.6408 | 1623.6883 | 1363.8317 | 1349.9904 | 991.0312 | 919.8662 | 699.3786 | 701.0057 | 810.4349 | 510.2359 | 600.7242 | 599.8176 | 583.4119 | 431.517 | 434.5056 | 338.0617 | 355.568 | 264.5751
Embedded | 72231.5119 | 63245.5532 | 62469.5048 | 66666.6667 | 73484.6923 | 77349.2468 | 48304.5892 | 22841.6096 | 1414.2136 | 714.5896 | 319.3744 | 210.9502 | 206.5591 | 194.6247 | 143.8669 | 109.855
GPU | 5070.9255 | 2958.0399 | 2196.8357 | 1802.7756 | 1800 | 1798.1472 | 1498.5373 | 1064.5813 | 1501.3222 | 1427.3693 | 1365.0084 | 1238.2784 | 1362.4427 | 1172.1237 | 1048.3367 | 947.2044 | 957.6077 | 957.4271 | 839.551 | 774.5967 | 655.5213 | 542.2696 | 641.427 | 393.777 | 383.86 | 416.3332 | 405.4319 | 290.9184 | 288.1854 | 281.4912 | 269.4439 | 263.6737 | 276.6559 | 272.3922 | 258.7785 | 199.6729 | 226.7787 | 196.774 | 196.5339
Server | 7471.1567 | 1383.3425 | 955.0891 | 854.2422 | 592.1049 | 781.8127 | 657.4136 | 514.5258 | 618.6626 | 614.0033 | 452.9108 | 687.3864 | 604.7432 | 591.1853 | 545.336 | 437.2521 | 443.7602 | 512.3475 | 519.6152 | 465.9302 | 418.908 | 370.9911 | 393.3979 | 369.5111 | 354.2909 | 328.9377 | 344.7969 | 412.2194 | 251.6611 | 200 | 337.7845 | 294.7457 | 200
Trend | 133497.7743 | 168.0704
1/2x every 5 years 
2x transistor density every 2.5 years

## Slide 22: Decreasing Feature Sizes
Intel 4004
1970
2,300 transistors
L = 72,000 nm
Apple A12
2018
6.9 B transistors
L = 110 nm

## Slide 23: Linear Scaling Trend
Chart: Linear Spacing by Year
| 1976 | 1976 | 1978 | 1979 | 1982 | 1982 | 1984 | 1985 | 1986 | 1986 | 1989 | 1991 | 1993 | 1996 | 1997 | 1997 | 1998 | 1999 | 1999 | 1999 | 1999 | 2000 | 2000 | 2001 | 2002 | 2003 | 2003 | 2004 | 2005 | 2006 | 2006 | 2007 | 2007 | 2008 | 2008 | 2008 | 2011 | 2012 | 2012 | 2014 | 2015
Desktop | 55470.0196 | 46017.8993 | 33733.2334 | 25437.351 | 33028.913 | 19122.5428 | 21151.0856 | 19446.8974 | 44721.3595 | 34641.0162 | 12107.0631 | 12560.9625 | 9738.5168 | 7640.1632 | 5099.0195 | 4290.5817 | 3881.5804 | 3670.6517 | 2353.7005 | 2891.9952 | 2563.073 | 1951.8001 | 2273.0303 | 1341.6408 | 1623.6883 | 1363.8317 | 1349.9904 | 991.0312 | 919.8662 | 699.3786 | 701.0057 | 810.4349 | 510.2359 | 600.7242 | 599.8176 | 583.4119 | 431.517 | 434.5056 | 338.0617 | 355.568 | 264.5751
Embedded | 72231.5119 | 63245.5532 | 62469.5048 | 66666.6667 | 73484.6923 | 77349.2468 | 48304.5892 | 22841.6096 | 1414.2136 | 714.5896 | 319.3744 | 210.9502 | 206.5591 | 194.6247 | 143.8669 | 109.855
GPU | 5070.9255 | 2958.0399 | 2196.8357 | 1802.7756 | 1800 | 1798.1472 | 1498.5373 | 1064.5813 | 1501.3222 | 1427.3693 | 1365.0084 | 1238.2784 | 1362.4427 | 1172.1237 | 1048.3367 | 947.2044 | 957.6077 | 957.4271 | 839.551 | 774.5967 | 655.5213 | 542.2696 | 641.427 | 393.777 | 383.86 | 416.3332 | 405.4319 | 290.9184 | 288.1854 | 281.4912 | 269.4439 | 263.6737 | 276.6559 | 272.3922 | 258.7785 | 199.6729 | 226.7787 | 196.774 | 196.5339
Server | 7471.1567 | 1383.3425 | 955.0891 | 854.2422 | 592.1049 | 781.8127 | 657.4136 | 514.5258 | 618.6626 | 614.0033 | 452.9108 | 687.3864 | 604.7432 | 591.1853 | 545.336 | 437.2521 | 443.7602 | 512.3475 | 519.6152 | 465.9302 | 418.908 | 370.9911 | 393.3979 | 369.5111 | 354.2909 | 328.9377 | 344.7969 | 412.2194 | 251.6611 | 200 | 337.7845 | 294.7457 | 200
Trend | 133497.7743 | 168.0704
Submillimeter
Submicrometer

## Slide 24: Submillimeter Dimensions
1 micrometer (μm)
10-3
10-4
10-5
10-6
5μm: Spider silk thickness
72μm: Intel 4004 linear scale
50μm: Average size of cell in human body
500μm: Length of amoeba
10μm: Thickness of sheet of plastic food wrap
2μm: E coli bacterium length
1 millimeter (mm)

## Slide 25: Submicrometer Dimensions
1 micrometer (μm)
1 nanometer (nm)
10-6
10-7
10-8
10-9
1nm: Carbon nanotube diameter
2nm: DNA helix diameter
9nm: Cell membrane thickness
110nm: Apple A12 linear scale
30nm: Minimum cooking oil smoke particle diameter
400-700nm: Visible light wavelengths

## Slide 26: Linear Scaling Extrapolation
Chart: Linear Spacing by Year
| 1976 | 1976 | 1978 | 1979 | 1982 | 1982 | 1984 | 1985 | 1986 | 1986 | 1989 | 1991 | 1993 | 1996 | 1997 | 1997 | 1998 | 1999 | 1999 | 1999 | 1999 | 2000 | 2000 | 2001 | 2002 | 2003 | 2003 | 2004 | 2005 | 2006 | 2006 | 2007 | 2007 | 2008 | 2008 | 2008 | 2011 | 2012 | 2012 | 2014 | 2015
Desktop | 55470.0196 | 46017.8993 | 33733.2334 | 25437.351 | 33028.913 | 19122.5428 | 21151.0856 | 19446.8974 | 44721.3595 | 34641.0162 | 12107.0631 | 12560.9625 | 9738.5168 | 7640.1632 | 5099.0195 | 4290.5817 | 3881.5804 | 3670.6517 | 2353.7005 | 2891.9952 | 2563.073 | 1951.8001 | 2273.0303 | 1341.6408 | 1623.6883 | 1363.8317 | 1349.9904 | 991.0312 | 919.8662 | 699.3786 | 701.0057 | 810.4349 | 510.2359 | 600.7242 | 599.8176 | 583.4119 | 431.517 | 434.5056 | 338.0617 | 355.568 | 264.5751
Embedded | 72231.5119 | 63245.5532 | 62469.5048 | 66666.6667 | 73484.6923 | 77349.2468 | 48304.5892 | 22841.6096 | 1414.2136 | 714.5896 | 319.3744 | 210.9502 | 206.5591 | 194.6247 | 143.8669 | 109.855
GPU | 5070.9255 | 2958.0399 | 2196.8357 | 1802.7756 | 1800 | 1798.1472 | 1498.5373 | 1064.5813 | 1501.3222 | 1427.3693 | 1365.0084 | 1238.2784 | 1362.4427 | 1172.1237 | 1048.3367 | 947.2044 | 957.6077 | 957.4271 | 839.551 | 774.5967 | 655.5213 | 542.2696 | 641.427 | 393.777 | 383.86 | 416.3332 | 405.4319 | 290.9184 | 288.1854 | 281.4912 | 269.4439 | 263.6737 | 276.6559 | 272.3922 | 258.7785 | 199.6729 | 226.7787 | 196.774 | 196.5339
Server | 7471.1567 | 1383.3425 | 955.0891 | 854.2422 | 592.1049 | 781.8127 | 657.4136 | 514.5258 | 618.6626 | 614.0033 | 452.9108 | 687.3864 | 604.7432 | 591.1853 | 545.336 | 437.2521 | 443.7602 | 512.3475 | 519.6152 | 465.9302 | 418.908 | 370.9911 | 393.3979 | 369.5111 | 354.2909 | 328.9377 | 344.7969 | 412.2194 | 251.6611 | 200 | 337.7845 | 294.7457 | 200
Trend | 133497.7743 | 168.0704 | 0.24318
243 pm

## Slide 27: Subnanometer Dimensions
1 nanometer (nm)
1 picometer (pm)
10-9
10-10
10-11
10-12
2.4pm: Electron wavelength (Compton wavelength)
53pm: Electron-proton spacing in hydrogen (Bohr radius)
1nm: Carbon nanotube diameter
543pm: Silicon crystal lattice spacing
74pm: Spacing between atoms in hydrogen molecule
243pm: 2065 linear scale projection

## Slide 28: Reaching 2065 Goal
Target
  1017 devices
  400 mm2
  L = 63 pm
Is this possible?
No!
Not with 2-d
fabrication

## Slide 29: Fabricating in 3 Dimensions
Parameters
  1017 devices
  100,000 logical layers
    Each 50 nm thick
    ~1,000,000 physical layers
      To provide wiring and isolation
  L = 20 nm
    10x smaller than today
2065 mm3
20 mm
20 mm
5 mm
2000 mm3

## Slide 30: 3D Fabrication Challenges
Yield
  How to avoid or tolerate flaws
Cost
  High cost of lithography
Power
  Keep power consumption within acceptable limits
  Limited energy available
  Limited ability to dissipate heat

## Slide 31: Photolithography
  Pattern entire chip in one step
  Modern chips require ~60 lithography steps
  Fabricate N transistor system with O(1) steps

## Slide 32: Fabrication Costs
Stepper
  Most expensive equipment in fabrication facility
  Rate limiting process step
    18s / wafer
  Expose 858 mm2 per step
    1.2% of chip area

## Slide 33: Fabrication Economics
Currently
  Fixed number of lithography steps
  Manufacturing cost $10–$20 / chip
    Including amortization of facility
Fabricating 1,000,000 physical layers
  Cannot do lithography on every step
Options
  Chemical self assembly
    Devices generate themselves via chemical processes
  Pattern multiple layers at once

## Slide 34: Samsung V-Nand Flash Example
  Build up layers of unpatterned material
  Then use lithography to slice, drill, etch, and deposit material across all layers
  ~30 total masking steps
  64 layers of memory cells (soon to be 96)
  Exploits particular structure of flash memory circuits

## Slide 35: Meeting Power Constraints
  6.9 B transistors
  2.5 GHz operation
  1—5 W
  64 B neurons
  100 Hz operation
  15—25 W
    Liquid cooling
    Up to 25% body’s total energy consumption
Can we increase number of devices by 10,000,000x without increasing power requirement?

## Slide 36: Challenges to Moore’s Law: Economic
Growing Capital Costs
  State of art fab line ~$20B
  Must have very high volumes to amortize investment
  Has led to major consolidations
  2018: Global Foundaries won’t attempt 7nm fabrication

## Slide 37: Dennard Scaling
  Due to Robert Dennard, IBM, 1974
  Quantifies benefits of Moore’s Law
How to shrink an IC Process
  Reduce horizontal and vertical dimensions by k
  Reduce voltage by k
Outcomes
  Devices / chip increase by k2
  Clock frequency increases by k
  Power / chip constant
Significance
  Increased capacity and performance
  No increase in power

## Slide 38: End of Dennard Scaling
What Happened?
  Can’t drop voltage below ~1V
  Reached limit of power / chip in 2004
  More logic on chip (Moore’s Law), but can’t make them run faster
    Response has been to increase cores / chip

## Slide 39: Some Thoughts about Technology
Compared to future, past 50 years will seem fairly straightforward
  50 years of using photolithography to pattern transistors on two-dimensional surface
Questions about future integrated systems
  Can we build them?
  What will be the technology?
  Are they commercially viable?
  Can we keep power consumption low?
  What will we do with them?
  How will we program / customize them?

## Slide 40: High-Performance Computing

## Slide 41: Comparing Two Large-Scale Systems
Oakridge Summit
  Monolithic supercomputer (fastest in world)
  Designed for compute-intensive applications
Google Data Center
  Servers to support millions of customers
  Designed for data collection, storage, and analysis

## Slide 42: Computing Landscape
Computational Intensity
Personal
Computing
Cloud
Services
Data Intensity
Modeling &
Simulation-Driven
Science &
Engineering
Traditional Supercomputing
Web search
Mapping / directions
Language translation
Video streaming
Google Data Center
Internet-Scale
Computing
Oakridge
Summit

## Slide 43: Supercomputing Landscape
Computational Intensity
Personal
Computing
Data Intensity
Modeling &
Simulation-Driven
Science &
Engineering
Traditional Supercomputing
Oakridge
Summit

## Slide 44: Traditional Supercomputer Applications
Simulation-Based Modeling
  System structure + initial conditions + transition behavior
  Discretize time and space
  Run simulation to see what happens
Requirements
  Model accurately reflects actual system
  Simulation faithfully captures model
Science
Industrial Products
Public Health

## Slide 45: Summit Hardware
Each Node
  2 IBM 22-core POWER9 processors
  6 nVidia Graphics Processing Units
  608 GB DRAM
  1600 GB Flash
Overall
  13MW water cooled
  $325 M for two machines
Local Network
Node 1
Node 2
Node 4,608
• • •
CPU
GPU
GPU
GPU
CPU
GPU
GPU
GPU
CPU
GPU
GPU
GPU
CPU
GPU
GPU
GPU
CPU
GPU
GPU
GPU
CPU
GPU
GPU
GPU

## Slide 46: Summit Node Structure

## Slide 47: Summit Node Structure: CPU
CPU
  22 cores sharing common memory
  Supports multithreaded programming
  Connects to three GPUs
  Connects to interconnection network
DRAM
Memory
GPU
GPU
GPU
Interconnection
Network

## Slide 48: Summit Node Structure: GPU
Tesla V100 GPU
  80 streaming multiprocessors (SMs)
  Each with multiple execution units: 64 double-precision, 32 single-precision, 32 integer
  Single-Instruction, Multiple-Data parallelism
    Single instruction controls all processors in group
  7 x 1012 FLOPS peak performance

## Slide 49: Supercomputer Programming: Principle
Solving Problem Over Grid
  E.g., finite-element system
  Simulate operation over time
Bulk Synchronous Model
  Partition into Regions
    p regions for p-node machine
  Map Region per Processor

## Slide 50: Supercomputer Programming: (cont)
Bulk Synchronous Model
  Map Region per Processor
  Alternate
    All nodes compute behavior of region
      Perform on GPUs
    All nodes communicate values at boundaries
P1
P2
P3
P4
P5
Communicate
Communicate
Communicate
Compute
Compute
Compute

## Slide 51: Bulk Synchronous Performance
  Limited by performance of slowest processor
Strive to keep perfectly balanced
  Engineer hardware to be highly reliable
  Tune software to make as regular as possible
  Eliminate “noise”
    Operating system events
    Extraneous network activity
P1
P2
P3
P4
P5
Communicate
Communicate
Communicate
Compute
Compute
Compute

## Slide 52: Summit Programming: Reality
System Level
  Message-Passing Interface (MPI) supports node computation, synchronization and communication
Node Level
  OpenMP supports thread-level operation of node CPU
  CUDA programming environment for GPUs
    Performance degrades quickly if don’t have perfect balance among memories and processors
Result
  Single program is complex combination of multiple programming paradigms
  Tend to optimize for specific hardware configuration

## Slide 53: My GPU Experience
Multiply two 1024 x 1024 matrices (MM)
  2 X 109 floating point operations
  Express performance in Giga FLOPS
  Program in CUDA and map onto nVidia GPU
Chart: Giga FLOPS
| simple | transpose | block | tblock | fblock | cosimple | csimple | ctranspose | coblock | cblock | csblock | cqblock
 | 0.93 | 2.25 | 2.07 | 2 | 2.1 | 11.06 | 87.25 | 10.97 | 69.89 | 381.58 | 25.77 | 777.31

## Slide 54: Matrix Multiplication Progress
Versions
  Naive 1
  Simple parallel 11
  Blocking 70
  nVidia Example Code 388
  Reorient memory accesses 382
  Packed data access 777
Observations
  Progress is very nonlinear
    Not even monotonic
  Requires increased understanding of how program maps onto hardware
  Becomes more specialized to specific hardware configuration

## Slide 55: Supercomputer Programming Model
  Program on top of bare hardware
Performance
  Low-level programming to maximize node performance
  Keep everything globally synchronized and balanced
Reliability
  Single failure causes major delay
  Engineer hardware to minimize failures
Hardware
Machine-Dependent
Programming Model
Software
Packages
Application
Programs

## Slide 56: Data-Intensive Computing Landscape
Computational Intensity
Personal
Computing
Cloud
Services
Data Intensity
Web search
Mapping / directions
Language translation
Video streaming
Google Data Center
Internet-Scale
Computing

## Slide 57: Internet Computing
Web Search
  Aggregate text data from across WWW
  No definition of correct operation
  Do not need real-time updating
Mapping Services
  Huge amount of (relatively) static data
  Each customer requires individualized computation
Online Documents
  Must be stored reliably
  Must support real-time updating
  (Relatively) small data volumes

## Slide 58: Other Data-Intensive Computing Applications
Wal-Mart
  267 million items/day, sold at 6,000 stores
  HP built them 4 PB data warehouse
  Mine data to manage supply chain, understand market trends, formulate pricing strategies
LSST
  Chilean telescope will scan entire sky every 3 days
  A 3.2 gigapixel digital camera
  Generate 30 TB/day of image data

## Slide 59: Data-Intensive Application Characteristics
Diverse Classes of Data
  Structured & unstructured
  High & low integrity requirements
Diverse Computing Needs
  Localized & global processing
  Numerical & non-numerical
  Real-time & batch processing

## Slide 60: Google Data Centers
Dalles, Oregon
  Hydroelectric power @ 2¢ / KW Hr
  50 Megawatts
    Enough to power 60,000 homes
  Engineered for low cost, modularity & power efficiency
  Container: 1160 server nodes, 250KW
Notes: One of the biggest users of cluster computing is Google. They have set up dozens of data centers around the world, containing more computer power than just about anyone else.
Here’s a picture of their data center in Dalles, Oregon. It cost them $600M and requires around 50 megawatts of power. (For reference, that much power would supply the residential electricity needs of 6,000 households in the U.S.). They located the data center near the Columbia River to take advantage of low-cost electricity.
Imagine what our intelligence sources could do if they had facilities on this scale to store and process satellite imagery, voice signals, and feeds from media outlets.

## Slide 61: Google Cluster
  Typically 1,000−2,000 nodes
Node Contains
  2 multicore CPUs
  2 disk drives (or Flash)
  DRAM
Local Network
CPU
Node 1
CPU
Node 2
CPU
Node n
• • •

## Slide 62: Hadoop Project
File system with files distributed across nodes
  Store multiple (typically 3 copies of each file)
    If one node fails, data still available
  Logically, any node has access to any file
    May need to fetch across network
Map / Reduce programming environment
  Software manages execution of tasks on nodes
Local Network
CPU
Node 1
CPU
Node 2
CPU
Node n
• • •

## Slide 63: Map/Reduce Programming Model
  Map computation across many objects
    E.g., 1010 Internet web pages
  Aggregate results in many different ways
  System deals with issues of resource allocation & reliability
M
x1
M
x2
M
x3
M
xn
k1
Map
Reduce
k1
kr
  
  
Key-Value
Pairs
Dean & Ghemawat: “MapReduce: Simplified Data Processing on Large Clusters”, OSDI 2004

## Slide 64: Cluster Programming Model
  Application programs written in terms of high-level operations on data
  Runtime system controls scheduling, load balancing, …
Scaling Challenges
  Centralized scheduler forms bottleneck
  Copying to/from disk very costly
  Hard to limit data movement
    Significant performance factor
Hardware
Machine-Independent
Programming Model
Runtime
System
Application
Programs

## Slide 65: Recent Programming Systems
Spark Project
  at U.C., Berkeley
  Grown to have large open source community
GraphLab
  Started as project at CMU by Carlos Guestrin
  Environment for describing machine-learning algorithms
    Sparse matrix structure described by graph
    Computation based on updating of node values

## Slide 66: Computing Landscape Trends
Computational Intensity
Data Intensity
Modeling &
Simulation-Driven
Science &
Engineering
Traditional
Supercomputing
Mixing simulation
with data analysis
Oakridge
Summit

## Slide 67: Combining Simulation with Real Data
Limitations
  Simulation alone: Hard to know if model is correct
  Data alone: Hard to understand causality & “what if”
Combination
  Check and adjust model during simulation

## Slide 68: Real-Time Analytics
Millenium XXL Simulation (2010)
  3 X 109 particles
  Simulation run of 9.3 days on 12,228 cores
  700TB total data generated
    Save at only 4 time points
    70 TB
  Large-scale simulations generate large data sets
What If?
  Could perform data analysis while simulation is running
Simulation
Engine
Analytic
Engine

## Slide 69: Computing Landscape Trends
Computational Intensity
Internet-Scale
Computing
Data Intensity
Google Data Center
Sophisticated
data analysis

## Slide 70: Example Analytic Applications
Classifier
Image
Description
Microsoft Project Adam
Transducer
English
Text
German
Text

## Slide 71: Data Analysis with Deep Neural Networks
Task:
  Compute classification of set of input signals
Training
  Use many training samples of form input / desired output
  Compute weights that minimize classification error
Operation
  Propagate signals from input to output

## Slide 72: DNN Application Example
Facebook DeepFace Architecture

## Slide 73: Training DNNs
Characteristics
  Iterative numerical algorithm
  Regular data organization
Project Adam Training
  2B connections
  15M images
  62 machines
  10 days
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
 | 0 | 1 | 4 | 9 | 16 | 25 | 36 | 49 | 64 | 81 | 100 | 121 | 144 | 169 | 196 | 225 | 256 | 289 | 324 | 361 | 400
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
×

Model Size
Training Data
Training Effort

## Slide 74: Trends
Computational Intensity
Internet-Scale
Computing
Data Intensity
Modeling &
Simulation-Driven
Science &
Engineering
Traditional
Supercomputing
Google Data Center
Sophisticated
data analysis
Mixing simulation
with real-world data
Convergence?

## Slide 75: Challenges for Convergence
Supercomputers
  Customized
  Optimized for reliability
  Source of “noise”
  Static scheduling
  Low-level, processor-centric model
Data Center Clusters
  Consumer grade
  Optimized for low cost
  Provides reliability
  Dynamic allocation
  High level, data-centric model
Hardware
Run-Time System
Application Programming

## Slide 76: Summary: Computation/Data Convergence
Two Important Classes of Large-Scale Computing
  Computationally intensive supercomputing
  Data intensive processing
    Internet companies + many other applications
Followed Different Evolutionary Paths
  Supercomputers: Get maximum performance from available hardware
  Data center clusters: Maximize cost/performance over variety of data-centric tasks
  Yielded different approaches to hardware, runtime systems, and application programming
A Convergence Would Have Important Benefits
  Computational and data-intensive applications
  But, not clear how to do it

## Slide 77: Overall Summary
Consumer products and supercomputers share technology
  CMOS integrated circuits
  Flash memory
Both are power limited
  Heat / cooling
  Battery life or utilities
Until recently, technology followed predictable trends
But, these are harder to sustain
  Both technology and cost