## Slide 1: The Memory Hierarchy January 21, 2002
Topics
  Storage technologies and trends
  Locality of reference
  Caching in the memory hierarchy
  Reading: 6.1 – 6.4
  Problems: 6.21, 6.23, 6.24
class12.ppt
15-213

## Slide 2: Random-Access Memory (RAM)
Key features
  RAM is packaged as a chip.
  Basic storage unit is a cell (one bit per cell).
  Multiple RAM chips form a memory.
Static RAM (SRAM)
  Each cell stores bit with a six-transistor circuit.
  Retains value indefinitely, as long as it is kept powered.
  Relatively insensitive to disturbances such as electrical noise.
  Faster and more expensive than DRAM.
Dynamic RAM (DRAM)
  Each cell stores bit with a capacitor and transistor.
  Value must be refreshed every 10-100 ms.
  Sensitive to disturbances.
  Slower and cheaper than SRAM.

## Slide 3: SRAM vs DRAM summary
Tran. Access
per bit time Persist? Sensitive? Cost Applications
SRAM 6 1X Yes No 100x cache memories
DRAM 1 10X No Yes 1X Main memories,
frame buffers

## Slide 4: Conventional DRAM organization
d x w DRAM:
  dw total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
memory
controller
(to CPU)

## Slide 5: Reading DRAM supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2.
Step 1(b): Row 2 copied from DRAM array to row buffer.
RAS = 2
cols
rows
0
1
2
3
0
1
2
3
internal row buffer
16 x 8 DRAM chip
row 2
addr
data
2
/
8
/
memory
controller

## Slide 6: Reading DRAM supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1.
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU.
internal buffer
supercell
(2,1)
cols
rows
0
1
2
3
0
1
2
3
internal row buffer
16 x 8 DRAM chip
CAS = 1
addr
data
2
/
8
/
memory
controller

## Slide 7: Memory modules
: supercell (i,j)
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit doubleword at main memory address A
addr (row = i, col = j)
data
64 MB
memory module
consisting of
eight 8Mx8 DRAMs
Memory
controller
bits
0-7
DRAM 7
DRAM 0
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit doubleword to CPU chip

## Slide 8: Enhanced DRAMs
All enhanced DRAMs are built around the conventional DRAM core.
  Fast page mode DRAM (FPM DRAM)
    Access contents of row with [RAS, CAS, CAS, CAS, CAS] instead of [(RAS,CAS), (RAS,CAS), (RAS,CAS), (RAS,CAS)].
  Extended data out DRAM (EDO DRAM)
    Enhanced FPM DRAM with more closely spaced CAS signals.
  Synchronous DRAM (SDRAM)
    Driven with rising clock edge instead of asynchronous control signals.
  Double data-rate synchronous DRAM (DDR SDRAM)
    Enhancement of SDRAM that uses both clock edges as control signals.
  Video RAM (VRAM)
    Like FPM DRAM, but output is produced by shifting row buffer
    Dual ported (allows concurrent reads and writes)

## Slide 9: Nonvolatile memories
DRAM and SRAM are volatile memories
  Lose information if powered off.
Nonvolatile memories retain value even if powered off.
  Generic name is read-only memory (ROM).
  Misleading because some ROMs can be read and modified.
Types of ROMs
  Programmable ROM (PROM)
  Eraseable programmable ROM (EPROM)
  Electrically eraseable PROM (EEPROM)
  Flash memory
Firmware
  Program stored in a ROM
    Boot time code, BIOS (basic input/ouput system)
    graphics cards, disk controllers.

## Slide 10: Bus structure connecting CPU and memory
A bus is a collection of parallel wires that carry address, data, and control signals.
Buses are typically shared by multiple devices.
main
memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus

## Slide 11: Memory read transaction (1)
ALU
register file
bus interface
A
0
A
x
main memory
I/O bridge
%eax
Load operation: movl A, %eax
CPU places address A on the memory bus.

## Slide 12: Memory read transaction (2)
Main memory reads A from the memory bus, retreives word x, and places it on the bus.
ALU
register file
bus interface
x
0
A
x
main memory
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 13: Memory read transaction (3)
CPU read word x from the bus and copies it into register %eax.
x
ALU
register file
bus interface
x
main memory
0
A
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 14: Memory write transaction (1)
CPU places address A on bus. Main memory reads it and waits for the corresponding data word to arrive.
y
ALU
register file
bus interface
A
main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 15: Memory write transaction (2)
CPU places data word y on the bus.
y
ALU
register file
bus interface
y
main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 16: Memory write transaction (3)
Main memory read data word y from the bus and stores it at address A.
y
ALU
register file
bus interface
y
main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 17: Disk geometry
Disks consist of platters, each with two surfaces.
Each surface consists of concentric rings called tracks.
Each track consists of sectors separated by gaps.
spindle
surface
tracks
track k
sectors
gaps

## Slide 18: Disk geometry (muliple-platter view)
Aligned tracks form a cylinder.
surface 0
surface 1
surface 2
surface 3
surface 4
surface 5
cylinder k
spindle
platter 0
platter 1
platter 2

## Slide 19: Disk capacity
Capacity: maximum number of bits that can be stored.
  Vendors express capacity in units of gigabytes (GB), where 1 GB = 10^6.
Capacity is determined by these technology factors:
  Recording density (bits/in): number of bits that can be squeezed into a 1 inch segment of a track.
  Track density (tracks/in): number of tracks that can be squeezed into a 1 inch radial segment.
  Areal density (bits/in2): product of recording and track density.
Modern disks partition tracks into disjoint subsets called recording zones
  Each track in a zone has the same number of sectors, determined by the circumference of innermost track.
  Each zone has a different number of sectors/track

## Slide 20: Computing disk capacity
Capacity = (# bytes/sector) x (avg. # sectors/track) x
(# tracks/surface) x (# surfaces/platter) x
(# platters/disk)
Example:
  512 bytes/sector
  300 sectors/track (on average)
  20,000 tracks/surface
  2 surfaces/platter
  5 platters/disk
Capacity = 512 x 300 x 20000 x 2 x 5
= 30,720,000,000
= 30.72 GB

## Slide 21: Disk operation (single-platter view)
By moving radially, the arm can position the read/write head over any track.
spindle
The disk surface
spins at a fixed
rotational rate
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.

## Slide 22: Disk operation (multi-platter view)
arm
read/write heads
move in unison
from cylinder to cylinder
spindle

## Slide 23: Disk access time
Average time to access some target sector approximated by :
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time
  Time to position heads over cylinder containing target sector.
  Typical Tavg seek = 9 ms
Rotational latency
  Time waiting for first bit of target sector to pass under r/w head.
  Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min
Transfer time
  Time to read the bits in the target sector.
  Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min.

## Slide 24: Disk access time example
Given:
  Rotational rate = 7,200 RPM
  Average seek time = 9 ms.
  Avg # sectors/track = 400.
Derived:
  Tavg rotation = 1/2 x (60 secs/7200 RPM) x 1000 ms/sec = 4 ms.
  Tavg transfer = 60/7200 RPM x 1/400 secs/track x 1000 ms/sec = 0.02 ms
  Taccess = 9 ms + 4 ms + 0.02 ms
Important points:
  Access time dominated by seek time and rotational latency.
  First bit in a sector is the most expensive, the rest are free.
  SRAM access time is about 4ns/doubleword, DRAM about 60 ns
    Disk is about 40,000 times slower than SRAM,
    2,500 times slower then DRAM.

## Slide 25: Logical disk blocks
Modern disks present a simpler abstract view of the complex sector geometry:
  The set of available sectors is modeled as a sequence of b-sized logical blocks (0, 1, 2, ...)
Mapping between logical blocks and actual (physical) sectors
  Maintained by hardware/firmware device called disk controller.
  Converts requests for logical blocks into (surface,track,sector) triples.
Allows controller to set aside spare cylinders for each zone.
  Accounts for the difference in “formatted capacity” and “maximum capacity”.

## Slide 26: Bus structure connecting I/O and CPU
main
memory
I/O
bridge
bus interface
ALU
register file
CPU chip
system bus
memory bus
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
Expansion slots for
other devices such
as network adapters.

## Slide 27: Reading a disk sector (1)
main
memory
ALU
register file
CPU chip
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
bus interface
CPU initiates a disk read by writing a command, logical block number, and destination memory address to a port (address) associated with disk controller.

## Slide 28: Reading a disk sector (2)
main
memory
ALU
register file
CPU chip
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
bus interface
Disk controller reads the sector and performs a direct memory access (DMA) transfer into main memory.

## Slide 29: Reading a disk sector (3)
main
memory
ALU
register file
CPU chip
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
bus interface
When the DMA transfer completes, the disk controller notifies the CPU with an interrupt (i.e., asserts a special “interrupt” pin on the CPU)

## Slide 30: Storage trends
(Culled from back issues of Byte and PC Magazine)
metric 1980 1985 1990 1995 2000 2000:1980
$/MB 8,000 880 100 30 1 8,000
access (ns) 375 200 100 70 60 6
typical size(MB) 0.064 0.256 4 16 64 1,000
DRAM
metric 1980 1985 1990 1995 2000 2000:1980
$/MB 19,200 2,900 320 256 100 190
access (ns) 300 150 35 15 2 100
SRAM
metric 1980 1985 1990 1995 2000 2000:1980
$/MB 500 100 8 0.30 0.05 10,000
access (ms) 87 75 28 10 8 11
typical size(MB) 1 10 160 1,000 9,000 9,000
Disk

## Slide 31: CPU clock rates
1980 1985 1990 1995 2000 2000:1980
processor 8080 286 386 Pent P-III
clock rate(MHz) 1 6 20 150 750 750
cycle time(ns) 1,000 166 50 6 1.6 750

## Slide 32: The CPU-Memory Gap
The increasing gap between DRAM, disk, and CPU speeds.

## Slide 33: Locality of Reference
Principle of Locality:
  Programs tend to reuse data and instructions near those they have used recently, or that were recently referenced themselves.
  Temporal locality: Recently referenced items are likely to be referenced in the near future.
  Spatial locality: Items with nearby addresses tend to be referenced close together in time.
Locality Example:
  Data
    Reference array elements in succession (spatial)
  Instructions
    Reference instructions in sequence (spatial)
    Cycle through loop repeatedly (temporal)
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;

## Slide 34: Locality example
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Does this function have good locality?
int sumarrayrows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum
}

## Slide 35: Locality example
Does this function have good locality?
int sumarraycols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum
}

## Slide 36: Locality example
Permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good locality)
int sumarray3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum
}

## Slide 37: Memory hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte and have less capacity.
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
Suggest an approach for organizing memory and storage systems known as a “memory hierarchy”.

## Slide 38: An example memory hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
remote secondary storage
(distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers.
Main memory holds disk
blocks retrieved from local
disks.
off-chip L2
cache (SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from cache memory.
L2 cache holds cache lines retrieved from memory.
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices

## Slide 39: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
  Net effect: A large pool of memory that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 40: Caching in a memory hierarchy
4
9
14
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Larger, slower, cheaper storage
device at level k+1 is partitioned
into blocks.
Smaller, faster, more expensive
device at level k caches a
subset of the blocks from level k+1
Data is copied between
levels in block-sized transfer units
Level k:
Level k+1:

## Slide 41: General caching concepts
Program needs object d, which is stored in some block b.
Cache hit
  Program finds b in the cache at level k. E.g. block 14.
Cache miss
  b is not at level k, so level k cache must fetch it from level k+1. E.g. block 12.
  If level k cache is full, then some current block must be replaced (evicted).
  Which one? Determined by replacement policy. E.g. evict least recently used block.
4
9
14
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level k:
Level k+1:

## Slide 42: General caching concepts
Types of cache misses:
  Cold (compulsary) miss
    Cold misses occur because the cache is empty.
  Conflict miss
    Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    E.g. Block i at level k+1 must be placed in block (i mod 4) at level k+1.
    Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.
  Capacity miss
    Occurs when the set of active cache blocks (working set) is larger than the cache.

## Slide 43: Examples of caching in the hierarchy
Hardware
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB page
32-byte block
32-byte block
4-byte word
What Cached
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
1
On-Chip L1
Hardware
10
Off-Chip L2
AFS/NFS client
10,000,000
Local disk
Hardware+OS
100
Main memory
Compiler
0
CPU registers
Managed By
Latency (cycles)
Where Cached