## Slide 1: Cache Memories February 28, 2002
Topics
  Generic cache memory organization
  Direct mapped caches
  Set associative caches
  Impact of caches on performance
  Reading: 6.5-6.7
  Problems: 6.25, 6.26. 6.27
class14.ppt
15-213

## Slide 2: Cache memories
main
memory
I/O
bridge
bus interface
L2 cache
ALU
register file
CPU chip
cache bus
system bus
memory bus
L1
cache
Cache memories are small, fast SRAM-based memories managed automatically in hardware.
  Hold frequently accessed blocks of main memory
CPU looks first for data in L1, then in L2, then in main memory.
Typical bus structure:

## Slide 3: Inserting an L1 cache between the CPU and main memory
a b c d
block 10
p q r s
block 21
...
...
w x y z
block 30
...
The big slow main memory
has room for many 4-word
blocks.
The small fast L1 cache has room
for two 4-word blocks.
The tiny, very fast CPU register file
has room for four 4-byte words.
The transfer unit between
the cache and main
memory is a 4-word block
(16 bytes).
The transfer unit between
the CPU register file and
the cache is a 4-byte block.
line 0
line 1

## Slide 4: General organization of a cache memory
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set 0:
B = 2b bytes
per cache block
E lines
per set
S = 2s sets
t tag bits
per line
1 valid bit
per line
Cache size: C = B x E x S data bytes
• • •
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set 1:
• • •
• • •
B–1
1
0
• • •
B–1
1
0
valid
valid
tag
tag
set S-1:
• • •
• • •
Cache is an array
of sets.
Each set contains
one or more lines.
Each line holds a
block of data.

## Slide 5: Addressing caches
t bits
s bits
b bits
0
m-1
<tag>
<set index>
<block offset>
Address A:
• • •
B–1
1
0
• • •
B–1
1
0
v
v
tag
tag
set 0:
• • •
• • •
B–1
1
0
• • •
B–1
1
0
v
v
tag
tag
set 1:
• • •
• • •
B–1
1
0
• • •
B–1
1
0
v
v
tag
tag
set S-1:
• • •
• • •
The word at address A is in the cache if
the tag bits in one of the <valid> lines in
set <set index> match <tag>.
The word contents begin at offset
<block offset> bytes from the beginning
of the block.

## Slide 6: Direct-mapped cache
Simplest kind of cache
Characterized by exactly one line per set.
valid
valid
valid
tag
tag
tag
• • •
set 0:
set 1:
set S-1:
E=1 lines per set
cache block
cache block
cache block

## Slide 7: Accessing direct-mapped caches
valid
valid
valid
tag
tag
tag
• • •
set 0:
set 1:
set S-1:
t bits
s bits
0 0 0 0 1
0
m-1
b bits
tag
set index
block offset
selected set
cache block
cache block
cache block
Set selection
  Use the set index bits to determine the set of interest.

## Slide 8: Accessing direct-mapped caches
Line matching and word selection
  find a valid line in the selected set with a matching tag (line matching)
  then extract the word (word selection)
1
t bits
s bits
100
i
0110
0
m-1
b bits
tag
set index
block offset
selected set (i):
=1?
= ?
(3) If (1) and (2), then
cache hit,
and block offset
selects
starting byte.
(1) The valid bit must be set
(2) The tag bits in the cache
line must match the
tag bits in the address
0110
w3
w0
w1
w2
3
0
1
2
7
4
5
6

## Slide 9: Direct-mapped cache simulation
M=16 byte addresses, B=2 bytes/block, S=4 sets, E=1 entry/set
Address trace (reads):
0 [0000] 1 [0001] 13 [1101] 8 [1000] 0 [0000]
x
t=1
s=2
b=1
xx
x
1
0
m[1] m[0]
v
tag
data
0 [0000] (miss)
(1)
1
0
m[1] m[0]
v
tag
data
1
1
m[13] m[12]
13 [1101] (miss)
(2)
1
1
m[9] m[8]
v
tag
data
8 [1000] (miss)
(3)
1
0
m[1] m[0]
v
tag
data
1
1
m[13] m[12]
0 [0000] (miss)
(4)

## Slide 10: Why use middle bits as index?
High-Order Bit Indexing
  Adjacent memory lines would map to same cache entry
  Poor use of spatial locality
Middle-Order Bit Indexing
  Consecutive memory lines map to different cache lines
  Can hold C-byte region of address space in cache at one time
4-line Cache
High-Order
Bit Indexing
Middle-Order
Bit Indexing
00
01
10
11
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111

## Slide 11: Set associative caches
Characterized by more than one line per set
valid
tag
set 0:
E=2 lines per set
set 1:
set S-1:
• • •
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block
valid
tag
cache block

## Slide 12: Accessing set associative caches
Set selection
  identical to direct-mapped cache
valid
valid
tag
tag
set 0:
valid
valid
tag
tag
set 1:
valid
valid
tag
tag
set S-1:
• • •
t bits
s bits
0 0 0 0 1
0
m-1
b bits
tag
set index
block offset
Selected set
cache block
cache block
cache block
cache block
cache block
cache block

## Slide 13: Accessing set associative caches
Line matching and word selection
  must compare the tag in each valid line in the selected set.
1
0110
w3
w0
w1
w2
1
1001
t bits
s bits
100
i
0110
0
m-1
b bits
tag
set index
block offset
selected set (i):
=1?
= ?
(3) If (1) and (2), then
cache hit, and
block offset selects
starting byte.
(2) The tag bits in one
of the cache lines must
match the tag bits in
the address
(1) The valid bit must be set.
3
0
1
2
7
4
5
6

## Slide 14: Multi-level caches
size:
speed:
$/Mbyte:
line size:
200 B
3 ns
8 B
8-64 KB
3 ns
32 B
128 MB DRAM
60 ns
$1.50/MB
8 KB
30 GB
8 ms
$0.05/MB
larger, slower, cheaper
Memory
disk
TLB
L1 Icache
L1 Dcache
regs
L2
Cache
Processor
1-4MB SRAM
6 ns
$100/MB
32 B
larger line size, higher associativity, more likely to write back
Options: separate data and instruction caches, or a unified cache

## Slide 15: Intel Pentium cache hierarchy
Processor Chip
L1 Data
1 cycle latency
16KB
4-way assoc
Write-through
32B lines
L1 Instruction
16KB, 4-way
32B lines
Regs.
L2 Unified
128KB--2 MB
4-way assoc
Write-back
Write allocate
32B lines
Main
Memory
Up to 4GB

## Slide 16: Cache performance metrics
Miss Rate
  fraction of memory references not found in cache (misses/references)
  Typical numbers:
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  time to deliver a line in the cache to the processor (includes time to determine whether the line is in the cache)
  Typical numbers:
    1 clock cycle for L1
    3-8 clock cycles for L2
Miss Penalty
  additional time required because of a miss
    Typically 25-100 cycles for main memory

## Slide 17: Writing cache friendly code
Repeated references to variables are good (temporal locality)
Stride-1 reference patterns are good (spatial locality)
Example
  cold cache, 4-byte words, 4-word cache blocks
int sumarrayrows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
int sumarraycols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Miss rate =
Miss rate =

## Slide 18: The Memory Mountain

## Slide 19: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain
  Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 20: Memory mountain test function
/* The test function */
void test(int elems, int stride) {
int i, result = 0;
volatile int sink;
for (i = 0; i < elems; i += stride)
result += data[i];
sink = result; /* So compiler doesn't optimize away the loop */
}
/* Run test(elems, stride) and return read throughput (MB/s) */
double run(int size, int stride, double Mhz)
{
double cycles;
int elems = size / sizeof(int);
test(elems, stride); /* warm up the cache */
cycles = fcyc2(test, elems, stride, 0); /* call test(elems,stride) */
return (size / stride) / (cycles / Mhz); /* convert cycles to MB/s */
}

## Slide 21: Memory mountain main routine
/* mountain.c - Generate the memory mountain. */
#define MINBYTES (1 << 10) /* Working set size ranges from 1 KB */
#define MAXBYTES (1 << 23) /* ... up to 8 MB */
#define MAXSTRIDE 16 /* Strides range from 1 to 16 */
#define MAXELEMS MAXBYTES/sizeof(int)
int data[MAXELEMS]; /* The array we'll be traversing */
int main()
{
int size; /* Working set size (in bytes) */
int stride; /* Stride (in array elements) */
double Mhz; /* Clock frequency */
init_data(data, MAXELEMS); /* Initialize each element in data to 1 */
Mhz = mhz(0); /* Estimate the clock frequency */
for (size = MAXBYTES; size >= MINBYTES; size >>= 1) {
for (stride = 1; stride <= MAXSTRIDE; stride++)
printf("%.1f\t", run(size, stride, Mhz));
printf("\n");
}
exit(0);
}

## Slide 22: The Memory Mountain

## Slide 23: Ridges of temporal locality
Slice through the memory mountain with stride=1
  illuminates read throughputs of different caches and memory

## Slide 24: A slope of spatial locality
Slice through memory mountain with size=256KB
  shows cache block size.

## Slide 25: Matrix multiplication example
Major Cache Effects to Consider
  Total cache size
    Exploit temporal locality and keep the working set small (e.g., by using blocking)
  Block size
    Exploit spatial locality
Description:
  Multiply N x N matrices
  O(N3) total operations
  Accesses
    N reads per source element
    N values summed per destination
      but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register

## Slide 26: Miss rate analysis for matrix multiply
Assume:
  Line size = 32B (big enough for 4 64-bit words)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
C
A
k
i
B
k
j
i
j

## Slide 27: Layout of arrays in memory
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
  if block size (B) > 4 bytes, exploit spatial locality
    compulsory miss rate = 4 bytes / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    compulsory miss rate = 1 (i.e. 100%)

## Slide 28: Matrix multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  0.25 1.0 0.0

## Slide 29: Matrix multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  0.25 1.0 0.0

## Slide 30: Matrix multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  0.0 0.25 0.25

## Slide 31: Matrix multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  0.0 0.25 0.25

## Slide 32: Matrix multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column -
wise
Column-
wise
Fixed
Misses per Inner Loop Iteration:
  A B C
  1.0 0.0 1.0

## Slide 33: Matrix multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per Inner Loop Iteration:
  A B C
  1.0 0.0 1.0

## Slide 34: Summary of matrix multiplication
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
ijk (& jik):
  2 loads, 0 stores
  misses/iter = 1.25
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
kij (& ikj):
  2 loads, 1 store
  misses/iter = 0.5
jki (& kji):
  2 loads, 1 store
  misses/iter = 2.0

## Slide 35: Pentium matrix multiply performance
Notice that miss rates are helpful but not perfect predictors.
    Code scheduling matters, too.

## Slide 36: Improving temporal locality by blocking
C11 = A11B11 + A12B21 C12 = A11B12 + A12B22
C21 = A21B11 + A22B21 C22 = A21B12 + A22B22
A11 A12
A21 A22
B11 B12
B21 B22
X
=
C11 C12
C21 C22
Key idea: Sub-blocks (i.e., Axy) can be treated just like scalars.
Example: Blocked matrix multiplication
  “block” (in this context) does not mean “cache block”.
  Instead, it mean a sub-block within the matrix.
  Example: N = 8; sub-block size = 4

## Slide 37: Blocked matrix multiply (bijk)
for (jj=0; jj<n; jj+=bsize) {
for (i=0; i<n; i++)
for (j=jj; j < min(jj+bsize,n); j++)
c[i][j] = 0.0;
for (kk=0; kk<n; kk+=bsize) {
for (i=0; i<n; i++) {
for (j=jj; j < min(jj+bsize,n); j++) {
sum = 0.0
for (k=kk; k < min(kk+bsize,n); k++) {
sum += a[i][k] * b[k][j];
}
c[i][j] += sum;
}
}
}
}

## Slide 38: Blocked matrix multiply analysis
A
B
C
block reused n times in succession
row sliver accessed
bsize times
Update successive
elements of sliver
i
i
kk
kk
jj
jj
for (i=0; i<n; i++) {
for (j=jj; j < min(jj+bsize,n); j++) {
sum = 0.0
for (k=kk; k < min(kk+bsize,n); k++) {
sum += a[i][k] * b[k][j];
}
c[i][j] += sum;
}
  Innermost loop pair multiplies a 1 X bsize sliver of A by a bsize X bsize block of B and accumulates into 1 X bsize sliver of C
  Loop over i steps through n row slivers of A & C, using same B
Innermost
Loop Pair

## Slide 39: Pentium blocked matrix multiply performance
Blocking (bijk and bikj) improves performance by a factor of two over unblocked versions (ijk and jik)
  relatively insensitive to array size.

## Slide 40: Concluding observations
Programmer can optimize for cache performance
  How data structures are organized
  How data accessed
    Nested loop structure
    Blocking (see text) is a general technique
All machines like “cache friendly code”
  Getting absolute optimum performance very platform specific
    Cache sizes, line sizes, associativities, etc.
  Can get most of the advantage with generic code
    Keep working set reasonably small (temporal locality)
    Use small strides (spatial locality)