## Slide 1
Randal E. Bryant
Carnegie Mellon University
CS:APP2e
CS:APP Chapter 4
Computer Architecture
Logic Design
http://csapp.cs.cmu.edu

## Slide 2: Overview of Logic Design
Fundamental Hardware Requirements
  Communication
    How to get values from one place to another
  Computation
  Storage
Bits are Our Friends
  Everything expressed in terms of values 0 and 1
  Communication
    Low or high voltage on wire
  Computation
    Compute Boolean functions
  Storage
    Store bits of information

## Slide 3: Digital Signals
  Use voltage thresholds to extract discrete values from continuous signal
  Simplest version: 1-bit signal
    Either high range (1) or low range (0)
    With guard range between them
  Not strongly affected by noise or low quality circuit elements
    Can make circuits simple, small, and fast
Voltage
Time
0
1
0

## Slide 4: Computing with Logic Gates
  Outputs are Boolean functions of inputs
  Respond continuously to changes in inputs
    With some, small delay
Voltage
Time
a
b
a && b
Rising Delay
Falling Delay

## Slide 5: Combinational Circuits
Acyclic Network of Logic Gates
  Continously responds to changes on primary inputs
  Primary outputs become (after some delay) Boolean functions of primary inputs
Acyclic Network
Primary
Inputs
Primary
Outputs

## Slide 6: Bit Equality
  Generate 1 if a and b are equal
Hardware Control Language (HCL)
  Very simple hardware description language
    Boolean operations have syntax similar to C logical operations
  We’ll use it to describe control logic for processors
Bit equal
a
b
eq
bool eq = (a&&b)||(!a&&!b)
HCL Expression

## Slide 7: Word Equality
  32-bit word size
  HCL representation
    Equality operation
    Generates Boolean value
b31
Bit equal
a31
eq31
b30
Bit equal
a30
eq30
b1
Bit equal
a1
eq1
b0
Bit equal
a0
eq0
Eq
=
B
A
Eq
Word-Level Representation
bool Eq = (A == B)
HCL Representation

## Slide 8: Bit-Level Multiplexor
  Control signal s
  Data signals a and b
  Output a when s=1, b when s=0
Bit MUX
b
s
a
out
bool out = (s&&a)||(!s&&b)
HCL Expression

## Slide 9: Word Multiplexor
  Select input word A or B depending on control signal s
  HCL representation
    Case expression
    Series of test : value pairs
    Output value for first successful test
Word-Level Representation
HCL Representation
b31
s
a31
out31
b30
a30
out30
b0
a0
out0
int Out = [
s : A;
1 : B;
];
s
B
A
Out
MUX

## Slide 10: HCL Word-Level Examples
  Find minimum of three input words
  HCL case expression
  Final case guarantees match
A
Min3
MIN3
B
C
int Min3 = [
A < B && A < C : A;
B < A && B < C : B;
1 : C;
];
D0
D3
Out4
s0
s1
MUX4
D2
D1
  Select one of 4 inputs based on two control bits
  HCL case expression
  Simplify tests by assuming sequential matching
int Out4 = [
!s1&&!s0: D0;
!s1 : D1;
!s0 : D2;
1 : D3;
];
Minimum of 3 Words
4-Way Multiplexor

## Slide 11: Arithmetic Logic Unit
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
  Combinational logic
    Continuously responding to inputs
  Control signal selects function computed
    Corresponding to 4 arithmetic/logical operations in Y86
  Also computes values for condition codes
A
L
U
Y
X
X + Y
0
A
L
U
Y
X
X - Y
1
A
L
U
Y
X
X & Y
2
A
L
U
Y
X
X ^ Y
3
A
B
A
B
A
B
A
B

## Slide 12: Storing 1 Bit
Bistable Element
Q+
Q–
q
!q
q = 0 or 1
Vin
V1
V2

## Slide 13: Storing 1 Bit (cont.)
Bistable Element
Q+
Q–
q
!q
q = 0 or 1
Vin
V1
V2
Vin
V1
V2
Vin = V2
Stable 0
Stable 1
Metastable

## Slide 14: Physical Analogy
Stable 0
Stable 1
Metastable
.
Stable left
.
Stable right
.
Metastable

## Slide 15: Storing and Accessing 1 Bit
Q+
Q–
R
S
R-S Latch
Resetting
1
0
1
0
0
1
Setting
0
1
0
1
1
0
Storing
0
0
!q
q
q
!q
Bistable Element
Q+
Q–
q
!q
q = 0 or 1

## Slide 16: 1-Bit Latch
D Latch
Q+
Q–
R
S
D
C
Data
Clock
Latching
1
d
!d
!d
!d
d
d
d
!d
0
Storing
d
!d
q
!q
!q
q
0
0

## Slide 17: Transparent 1-Bit Latch
  When in latching mode, combinational propogation from D to Q+ and Q–
  Value latched depends on value of D as C falls
Latching
1
d
!d
!d
!d
d
d
d
!d
C
D
Q+
Time
Changing D

## Slide 18: Edge-Triggered Latch
  Only in latching mode for brief period
    Rising clock edge
  Value latched depends on data as clock rises
  Output remains stable at all other times
Q+
Q–
R
S
D
C
Data
Clock
T
Trigger
C
D
Q+
Time
T

## Slide 19: Registers
  Stores word of data
    Different from program registers seen in assembly code
  Collection of edge-triggered latches
  Loads input on rising edge of clock
I
O
Clock
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
i7
i6
i5
i4
i3
i2
i1
i0
o7
o6
o5
o4
o3
o2
o1
o0
Clock
Structure

## Slide 20: Register Operation
  Stores data bits
  For most of time acts as barrier between input and output
  As clock rises, loads input
State = x
Rising
clock

Output = x
Input = y
x

State = y
Output = y
y

## Slide 21: State Machine Example
  Accumulator circuit
  Load or accumulate on each cycle
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load
x0
x1
x2
x3
x4
x5
x0
x0+x1
x0+x1+x2
x3
x3+x4
x3+x4+x5
Clock
Load
In
Out

## Slide 22: Random-Access Memory
  Stores multiple words of memory
    Address input specifies which word to read or write
  Register file
    Holds values of program registers
    %eax, %esp, etc.
    Register identifier serves as address
      ID 15 (0xF) implies no read or write performed
  Multiple Ports
    Can read and/or write multiple words in one cycle
      Each has separate address and data input/output
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Read ports
Write port
Clock

## Slide 23: Register File Timing
Reading
  Like combinational logic
  Output data generated based on input address
    After some delay
Writing
  Like register
  Update only as clock rises
Register
file
A
B
srcA
valA
srcB
valB
y
2
Register
file
W
dstW
valW
Clock
x
2
Rising
clock


Register
file
W
dstW
valW
Clock
y
2
x
2
x
2

## Slide 24: Hardware Control Language
  Very simple hardware description language
  Can only express limited aspects of hardware operation
    Parts we want to explore and modify
Data Types
  bool: Boolean
    a, b, c, …
  int: words
    A, B, C, …
    Does not specify word size---bytes, 32-bit words, …
Statements
  bool a = bool-expr ;
  int A = int-expr ;

## Slide 25: HCL Operations
  Classify by type of value returned
Boolean Expressions
  Logic Operations
    a && b, a || b, !a
  Word Comparisons
    A == B, A != B, A < B, A <= B, A >= B, A > B
  Set Membership
    A in { B, C, D }
      Same as A == B || A == C || A == D
Word Expressions
  Case expressions
    [ a : A; b : B; c : C ]
    Evaluate test expressions a, b, c, … in sequence
    Return word expression A, B, C, … for first successful test

## Slide 26: Summary
Computation
  Performed by combinational logic
  Computes Boolean functions
  Continuously reacts to input changes
Storage
  Registers
    Hold single words
    Loaded as clock rises
  Random-access memories
    Hold multiple words
    Possible multiple read or write ports
    Read word when address input changes
    Write word as clock rises