## Slide 1
Randal E. Bryant
Carnegie Mellon University
CS:APP3e
CS:APP Chapter 4
Computer Architecture
Sequential
Implementation
http://csapp.cs.cmu.edu

## Slide 2: Y86-64 Instruction Set #1
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9

## Slide 3: Y86-64 Instruction Set #2
0
1
2
3
4
5
6
7
8
9
V
D
D
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
rmmovq rA, D(rB)
4
0
rA
rB
mrmovq D(rB), rA
5
0
rA
rB
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
rrmovq
7
0
cmovle
7
1
cmovl
7
2
cmove
7
3
cmovne
7
4
cmovge
7
5
cmovg
7
6

## Slide 4: Y86-64 Instruction Set #3
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
addq
6
0
subq
6
1
andq
6
2
xorq
6
3

## Slide 5: Y86-64 Instruction Set #4
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6

## Slide 6: Building Blocks
Combinational Logic
  Compute Boolean functions of inputs
  Continuously respond to input changes
  Operate on data and implement control
Storage Elements
  Store bits
  Addressable memories
  Non-addressable registers
  Loaded only as clock rises
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Clock
A
L
U
fun
A
B
MUX
0
1
=
Clock

## Slide 7: Hardware Control Language
  Very simple hardware description language
  Can only express limited aspects of hardware operation
    Parts we want to explore and modify
Data Types
  bool: Boolean
    a, b, c, …
  int: words
    A, B, C, …
    Does not specify word size---bytes, 32-bit words, …
Statements
  bool a = bool-expr ;
  int A = int-expr ;

## Slide 8: HCL Operations
  Classify by type of value returned
Boolean Expressions
  Logic Operations
    a && b, a || b, !a
  Word Comparisons
    A == B, A != B, A < B, A <= B, A >= B, A > B
  Set Membership
    A in { B, C, D }
      Same as A == B || A == C || A == D
Word Expressions
  Case expressions
    [ a : A; b : B; c : C ]
    Evaluate test expressions a, b, c, … in sequence
    Return word expression A, B, C, … for first successful test

## Slide 9: SEQ Hardware Structure
State
  Program counter register (PC)
  Condition code register (CC)
  Register File
  Memories
    Access same memory space
    Data: for reading/writing program data
    Instruction: for reading instructions
Instruction Flow
  Read instruction at address specified by PC
  Process through stages
  Update program counter
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Cnd
valE
Addr
, Data
valM
PC
valE
,
valM
newPC

## Slide 10: SEQ Stages
Fetch
  Read instruction from instruction memory
Decode
  Read program registers
Execute
  Compute value or address
Memory
  Read or write data
Write Back
  Write program registers
PC
  Update program counter
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Cnd
valE
Addr
, Data
valM
PC
valE
,
valM
newPC

## Slide 11: Instruction Decoding
Instruction Format
  Instruction byte icode:ifun
  Optional register byte rA:rB
  Optional constant word valC
5
0
rA
rB
D
icode
ifun
rA
rB
valC
Optional
Optional

## Slide 12: Executing Arith./Logical Operation
Fetch
  Read 2 bytes
Decode
  Read operand registers
Execute
  Perform operation
  Set condition codes
Memory
  Do nothing
Write back
  Update register
PC Update
  Increment PC by 2
OPq rA, rB
6
fn
rA
rB

## Slide 13: Stage Computation: Arith/Log. Ops
  Formulate instruction execution as sequence of simple steps
  Use same general form for all instructions
OPq rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB OP valA
Set CC
Execute
Perform ALU operation
Set condition code register
Memory
R[rB]  valE
Write
back
Write back result
PC  valP
PC update
Update PC

## Slide 14: Executing rmmovq
Fetch
  Read 10 bytes
Decode
  Read operand registers
Execute
  Compute effective address
Memory
  Write to memory
Write back
  Do nothing
PC Update
  Increment PC by 10
rmmovq rA, D(rB)
4
0
rA
rB
D

## Slide 15: Stage Computation: rmmovq
  Use ALU for address computation
rmmovq rA, D(rB)
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
Fetch
Read instruction byte
Read register byte
Read displacement D
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB + valC
Execute
Compute effective address
M8[valE]  valA
Memory
Write value to memory
Write
back
PC  valP
PC update
Update PC

## Slide 16: Executing popq
Fetch
  Read 2 bytes
Decode
  Read stack pointer
Execute
  Increment stack pointer by 8
Memory
  Read from old stack pointer
Write back
  Update stack pointer
  Write result to register
PC Update
  Increment PC by 2
popq rA
b
0
rA
8

## Slide 17: Stage Computation: popq
  Use ALU to increment stack pointer
  Must update two registers
    Popped value
    New stack pointer
popq rA
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[%rsp]
valB  R[%rsp]
Decode
Read stack pointer
Read stack pointer
valE  valB + 8
Execute
Increment stack pointer
valM  M8[valA]
Memory
Read from stack
R[%rsp]  valE
R[rA]  valM
Write
back
Update stack pointer
Write back result
PC  valP
PC update
Update PC

## Slide 18: Executing Conditional Moves
Fetch
  Read 2 bytes
Decode
  Read operand registers
Execute
  If !cnd, then set destination register to 0xF
Memory
  Do nothing
Write back
  Update register (or not)
PC Update
  Increment PC by 2
cmovXX rA, rB
2
fn
rA
rB

## Slide 19: Stage Computation: Cond. Move
  Read register rA and pass through ALU
  Cancel move by setting destination register to 0xF
    If condition codes & move condition indicate no move
cmovXX rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[rA]
valB  0
Decode
Read operand A
valE  valB + valA
If ! Cond(CC,ifun) rB  0xF
Execute
Pass valA through ALU
(Disable register update)
Memory
R[rB]  valE
Write
back
Write back result
PC  valP
PC update
Update PC

## Slide 20: Executing Jumps
Fetch
  Read 9 bytes
  Increment PC by 9
Decode
  Do nothing
Execute
  Determine whether to take branch based on jump condition and condition codes
Memory
  Do nothing
Write back
  Do nothing
PC Update
  Set PC to Dest if branch taken or to incremented PC if not branch
jXX Dest
7
fn
Dest
XX
XX
fall thru:
XX
XX
target:
Not taken
Taken

## Slide 21: Stage Computation: Jumps
  Compute both addresses
  Choose based on setting of condition codes and branch condition
jXX Dest
icode:ifun  M1[PC]
valC  M8[PC+1]
valP  PC+9
Fetch
Read instruction byte
Read destination address
Fall through address
Decode
Cnd  Cond(CC,ifun)
Execute
Take branch?
Memory
Write
back
PC  Cnd ? valC : valP
PC update
Update PC

## Slide 22: Executing call
Fetch
  Read 9 bytes
  Increment PC by 9
Decode
  Read stack pointer
Execute
  Decrement stack pointer by 8
Memory
  Write incremented PC to new value of stack pointer
Write back
  Update stack pointer
PC Update
  Set PC to Dest
call Dest
8
0
Dest
XX
XX
return:
XX
XX
target:

## Slide 23: Stage Computation: call
  Use ALU to decrement stack pointer
  Store incremented PC
call Dest
icode:ifun  M1[PC]
valC  M8[PC+1]
valP  PC+9
Fetch
Read instruction byte
Read destination address
Compute return point
valB  R[%rsp]
Decode
Read stack pointer
valE  valB + –8
Execute
Decrement stack pointer
M8[valE]  valP
Memory
Write return value on stack
R[%rsp]  valE
Write
back
Update stack pointer
PC  valC
PC update
Set PC to destination

## Slide 24: Executing ret
Fetch
  Read 1 byte
Decode
  Read stack pointer
Execute
  Increment stack pointer by 8
Memory
  Read return address from old stack pointer
Write back
  Update stack pointer
PC Update
  Set PC to return address
ret
9
0
XX
XX
return:

## Slide 25: Stage Computation: ret
  Use ALU to increment stack pointer
  Read return address from memory
ret
icode:ifun  M1[PC]
Fetch
Read instruction byte
valA  R[%rsp]
valB  R[%rsp]
Decode
Read operand stack pointer
Read operand stack pointer
valE  valB + 8
Execute
Increment stack pointer
valM  M8[valA]
Memory
Read return address
R[%rsp]  valE
Write
back
Update stack pointer
PC  valM
PC update
Set PC to return address

## Slide 26: Computation Steps
  All instructions follow same general pattern
  Differ in what gets computed on each step
OPq rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
[Read constant word]
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB OP valA
Set CC
Execute
Perform ALU operation
Set/use cond. code reg
Memory
[Memory read/write]
R[rB]  valE
Write
back
Write back ALU result
[Write back memory result]
PC  valP
PC update
Update PC
icode,ifun
rA,rB
valC
valP
valA, srcA
valB, srcB
valE
Cond code
valM
dstE
dstM
PC

## Slide 27: Computation Steps
  All instructions follow same general pattern
  Differ in what gets computed on each step
call Dest
Fetch
Decode
Execute
Memory
Write
back
PC update
icode,ifun
rA,rB
valC
valP
valA, srcA
valB, srcB
valE
Cond code
valM
dstE
dstM
PC
icode:ifun  M1[PC]
valC  M8[PC+1]
valP  PC+9
valB  R[%rsp]
valE  valB + –8
M8[valE]  valP
R[%rsp]  valE
PC  valC
Read instruction byte
[Read register byte]
Read constant word
Compute next PC
[Read operand A]
Read operand B
Perform ALU operation
[Set /use cond. code reg]
Memory read/write
Write back ALU result
[Write back memory result]
Update PC

## Slide 28: Computed Values
Fetch
  icode Instruction code
  ifun Instruction function
  rA Instr. Register A
  rB Instr. Register B
  valC Instruction constant
  valP Incremented PC
Decode
  srcA Register ID A
  srcB Register ID B
  dstE Destination Register E
  dstM Destination Register M
  valA Register value A
  valB Register value B
Execute
  valE ALU result
  Cnd Branch/move flag
Memory
  valM Value from memory

## Slide 29: SEQ Hardware
Key
  Blue boxes: predesigned hardware blocks
    E.g., memories, ALU
  Gray boxes: control logic
    Describe in HCL
  White ovals: labels for signals
  Thick lines: 64-bit word values
  Thin lines: 4-8 bit values
  Dotted lines: 1-bit values

## Slide 30: Fetch Logic
Predefined Blocks
  PC: Register containing PC
  Instruction memory: Read 10 bytes (PC to PC+9)
    Signal invalid address
  Split: Divide instruction byte into icode and ifun
  Align: Get fields for rA, rB, and valC
Instruction
memory
PC
increment
rB
icode
ifun
rA
PC
valC
valP
Need
regids
Need
valC
Instr
valid
Align
Split
Bytes 1-9
Byte 0
imem_error
icode
ifun

## Slide 31: Fetch Logic
Control Logic
  Instr. Valid: Is this instruction valid?
  icode, ifun: Generate no-op if invalid address
  Need regids: Does this instruction have a register byte?
  Need valC: Does this instruction have a constant word?
Instruction
memory
PC
increment
rB
icode
ifun
rA
PC
valC
valP
Need
regids
Need
valC
Instr
valid
Align
Split
Bytes 1-9
Byte 0
imem_error
icode
ifun

## Slide 32: Fetch Control Logic in HCL
# Determine instruction code
int icode = [
imem_error: INOP;
1: imem_icode;
];
# Determine instruction function
int ifun = [
imem_error: FNONE;
1: imem_ifun;
];
Instruction
memory
PC
Split
Byte 0
imem_error
icode
ifun

## Slide 33: Fetch Control Logic in HCL
bool need_regids =
icode in { IRRMOVQ, IOPQ, IPUSHQ, IPOPQ,
IIRMOVQ, IRMMOVQ, IMRMOVQ };
bool instr_valid = icode in
{ INOP, IHALT, IRRMOVQ, IIRMOVQ, IRMMOVQ, IMRMOVQ,
IOPQ, IJXX, ICALL, IRET, IPUSHQ, IPOPQ };
popq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
8
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0

## Slide 34: Decode Logic
Register File
  Read ports A, B
  Write ports E, M
  Addresses are register IDs or 15 (0xF) (no access)
Control Logic
  srcA, srcB: read port addresses
  dstE, dstM: write port addresses
rB
dstE
dstM
srcA
srcB
Register
file
A
B
M
E
dstE
dstM
srcA
srcB
icode
rA
valB
valA
valE
valM
Cnd
Signals
  Cnd: Indicate whether or not to perform conditional move
    Computed in Execute stage

## Slide 35: A Source
int srcA = [
icode in { IRRMOVQ, IRMMOVQ, IOPQ, IPUSHQ } : rA;
icode in { IPOPQ, IRET } : RRSP;
1 : RNONE; # Don't need register
];
cmovXX rA, rB
valA  R[rA]
Decode
Read operand A
rmmovq rA, D(rB)
valA  R[rA]
Decode
Read operand A
popq rA
valA  R[%rsp]
Decode
Read stack pointer
jXX Dest
Decode
No operand
call Dest
valA  R[%rsp]
Decode
Read stack pointer
ret
Decode
No operand
OPq rA, rB
valA  R[rA]
Decode
Read operand A

## Slide 36: E Desti- nation
int dstE = [
icode in { IRRMOVQ } && Cnd : rB;
icode in { IIRMOVQ, IOPQ} : rB;
icode in { IPUSHQ, IPOPQ, ICALL, IRET } : RRSP;
1 : RNONE; # Don't write any register
];
None
R[%rsp]  valE
Update stack pointer
None
R[rB]  valE
cmovXX rA, rB
Write-back
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
Write-back
Write-back
Write-back
Write-back
Write-back
Conditionally write back result
R[%rsp]  valE
Update stack pointer
R[%rsp]  valE
Update stack pointer
R[rB]  valE
OPq rA, rB
Write-back
Write back result

## Slide 37: Execute Logic
Units
  ALU
    Implements 4 required functions
    Generates condition code values
  CC
    Register with 3 condition code bits
  cond
    Computes conditional jump/move flag
Control Logic
  Set CC: Should condition code register be loaded?
  ALU A: Input A to ALU
  ALU B: Input B to ALU
  ALU fun: What function should ALU compute?
CC
ALU
ALU
A
ALU
B
ALU
fun.
Cnd
icode
ifun
valC
valB
valA
valE
Set
CC
cond

## Slide 38: ALU A Input
int aluA = [
icode in { IRRMOVQ, IOPQ } : valA;
icode in { IIRMOVQ, IRMMOVQ, IMRMOVQ } : valC;
icode in { ICALL, IPUSHQ } : -8;
icode in { IRET, IPOPQ } : 8;
# Other instructions don't need ALU
];
valE  valB + –8
Decrement stack pointer
No operation
valE  valB + 8
Increment stack pointer
valE  valB + valC
Compute effective address
valE  0 + valA
Pass valA through ALU
cmovXX rA, rB
Execute
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
Execute
Execute
Execute
Execute
Execute
valE  valB + 8
Increment stack pointer
valE  valB OP valA
Perform ALU operation
OPq rA, rB
Execute

## Slide 39: ALU Oper- ation
int alufun = [
icode == IOPQ : ifun;
1 : ALUADD;
];
valE  valB + –8
Decrement stack pointer
No operation
valE  valB + 8
Increment stack pointer
valE  valB + valC
Compute effective address
valE  0 + valA
Pass valA through ALU
cmovXX rA, rB
Execute
rmmovl rA, D(rB)
popq rA
jXX Dest
call Dest
ret
Execute
Execute
Execute
Execute
Execute
valE  valB + 8
Increment stack pointer
valE  valB OP valA
Perform ALU operation
OPl rA, rB
Execute

## Slide 40: Memory Logic
Memory
  Reads or writes memory word
Control Logic
  stat: What is instruction status?
  Mem. read: should word be read?
  Mem. write: should word be written?
  Mem. addr.: Select address
  Mem. data.: Select data
Data
memory
Mem.
read
Mem.
addr
read
write
data out
Mem.
data
valE
valM
valA
valP
Mem.
write
data in
icode
Stat
dmem_error
instr_valid
imem_error
stat

## Slide 41: Instruction Status
Control Logic
  stat: What is instruction status?
Data
memory
Mem.
read
Mem.
addr
read
write
data out
Mem.
data
valE
valM
valA
valP
Mem.
write
data in
icode
Stat
dmem_error
instr_valid
imem_error
stat
## Determine instruction status
int Stat = [
imem_error || dmem_error : SADR;
!instr_valid: SINS;
icode == IHALT : SHLT;
1 : SAOK;
];

## Slide 42: Memory Address
OPq rA, rB
Memory
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
No operation
M8[valE]  valA
Memory
Write value to memory
valM  M8[valA]
Memory
Read from stack
M8[valE]  valP
Memory
Write return value on stack
valM  M8[valA]
Memory
Read return address
Memory
No operation
int mem_addr = [
icode in { IRMMOVQ, IPUSHQ, ICALL, IMRMOVQ } : valE;
icode in { IPOPQ, IRET } : valA;
# Other instructions don't need address
];

## Slide 43: Memory Read
OPq rA, rB
Memory
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
No operation
M8[valE]  valA
Memory
Write value to memory
valM  M8[valA]
Memory
Read from stack
M8[valE]  valP
Memory
Write return value on stack
valM  M8[valA]
Memory
Read return address
Memory
No operation
bool mem_read = icode in { IMRMOVQ, IPOPQ, IRET };

## Slide 44: PC Update Logic
New PC
  Select next value of PC
New
PC
Cnd
icode
valC
valP
valM
PC

## Slide 45: PC Update
OPq rA, rB
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
PC  valP
PC update
Update PC
PC  valP
PC update
Update PC
PC  valP
PC update
Update PC
PC  Cnd ? valC : valP
PC update
Update PC
PC  valC
PC update
Set PC to destination
PC  valM
PC update
Set PC to return address
int new_pc = [
icode == ICALL : valC;
icode == IJXX && Cnd : valC;
icode == IRET : valM;
1 : valP;
];

## Slide 46: SEQ Operation
State
  PC register
  Cond. Code register
  Data memory
  Register file
  All updated as clock rises
Combinational Logic
  ALU
  Control logic
  Memory reads
    Instruction memory
    Register file
    Data memory
Combinational
logic
Data
memory
Register
file
%rbx = 0x100
PC
0x014
CC
100
Read
ports
Write
ports
Read
Write

## Slide 47: SEQ Operation #2
  state set according to second irmovq instruction
  combinational logic starting to react to state changes
0x014: addq %rdx,%rbx # %rbx <-- 0x300 CC <-- 000
0x016: je dest # Not taken
0x01f: rmmovq %rbx,0(%rdx) # M[0x200] <-- 0x300
Cycle 3:
Cycle 4:
Cycle 5:
0x00a: irmovq $0x200,%rdx # %rdx <-- 0x200
Cycle 2:
0x000: irmovq $0x100,%rbx # %rbx <-- 0x100
Cycle 1:
Clock
Cycle 1
j
l
m
k
Cycle 2
Cycle 3
Cycle 4
Combinational
logic
Data
memory
Register
file
%rbx = 0x100
PC
0x014
CC
100
Read
ports
Write
ports
Read
Write

## Slide 48: SEQ Operation #3
  state set according to second irmovq instruction
  combinational logic generates results for addq instruction
Combinational
logic
Data
memory
Register
file
%rbx = 0x100
PC
0x014
CC
100
Read
ports
Write
ports
0x016
000
%rbx
<--
0x300
Read
Write
0x014: addq %rdx,%rbx # %rbx <-- 0x300 CC <-- 000
0x016: je dest # Not taken
0x01f: rmmovq %rbx,0(%rdx) # M[0x200] <-- 0x300
Cycle 3:
Cycle 4:
Cycle 5:
0x00a: irmovq $0x200,%rdx # %rdx <-- 0x200
Cycle 2:
0x000: irmovq $0x100,%rbx # %rbx <-- 0x100
Cycle 1:
Clock
Cycle 1
j
l
m
k
Cycle 2
Cycle 3
Cycle 4
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write

## Slide 49: SEQ Operation #4
  state set according to addq instruction
  combinational logic starting to react to state changes
0x014: addq %rdx,%rbx # %rbx <-- 0x300 CC <-- 000
0x016: je dest # Not taken
0x01f: rmmovq %rbx,0(%rdx) # M[0x200] <-- 0x300
Cycle 3:
Cycle 4:
Cycle 5:
0x00a: irmovq $0x200,%rdx # %rdx <-- 0x200
Cycle 2:
0x000: irmovq $0x100,%rbx # %rbx <-- 0x100
Cycle 1:
Clock
Cycle 1
j
l
m
k
Cycle 2
Cycle 3
Cycle 4
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write

## Slide 50: SEQ Operation #5
  state set according to addq instruction
  combinational logic generates results for je instruction
0x014: addq %rdx,%rbx # %rbx <-- 0x300 CC <-- 000
0x016: je dest # Not taken
0x01f: rmmovq %rbx,0(%rdx) # M[0x200] <-- 0x300
Cycle 3:
Cycle 4:
Cycle 5:
0x00a: irmovq $0x200,%rdx # %rdx <-- 0x200
Cycle 2:
0x000: irmovq $0x100,%rbx # %rbx <-- 0x100
Cycle 1:
Clock
Cycle 1
j
l
m
k
Cycle 2
Cycle 3
Cycle 4
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
0x01f
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
0x01f
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
0x01f
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
0x01f
Read
Write

## Slide 51: SEQ Summary
Implementation
  Express every instruction as series of simple steps
  Follow same general flow for each instruction type
  Assemble registers, memories, predesigned combinational blocks
  Connect with control logic
Limitations
  Too slow to be practical
  In one cycle, must propagate through instruction memory, register file, ALU, and data memory
  Would need to run clock very slowly
  Hardware units only active for fraction of clock cycle