## Slide 1
Randal E. Bryant
Carnegie Mellon University
CS:APP3e
CS:APP Chapter 4
Computer Architecture
Pipelined
Implementation
Part II
http://csapp.cs.cmu.edu

## Slide 2: Overview
  Make the pipelined processor work!
Data Hazards
  Instruction having register R as source follows shortly after instruction having register R as destination
  Common condition, don’t want to slow down pipeline
Control Hazards
  Mispredict conditional branch
    Our design predicts all branches as being taken
    Naïve pipeline executes two extra instructions
  Getting return address for ret instruction
    Naïve pipeline executes three extra instructions
Making Sure It Really Works
  What if multiple special cases happen simultaneously?

## Slide 3: Pipeline Stages
Fetch
  Select current PC
  Read instruction
  Compute incremented PC
Decode
  Read program registers
Execute
  Operate ALU
Memory
  Read or write data memory
Write Back
  Update register file

## Slide 4: PIPE- Hardware
  Pipeline registers hold intermediate values from instruction execution
Forward (Upward) Paths
  Values passed from one stage to next
  Cannot jump past stages
    e.g., valC passes through decode

## Slide 5: Data Dependencies: 2 Nop’s
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
F
D
E
M
W
0x014:
nop
F
D
E
M
W
F
D
E
M
W
0x015:
nop
F
D
E
M
W
F
D
E
M
W
0x016:
addq
%
rdx
,%
rax
F
D
E
M
W
F
D
E
M
W
0x018: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-h2.ys
W
R[
%
rax
]
f
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
•
•
•
W
R[
%
rax
]
f
3
W
R[
%
rax
]
f
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
•
•
•
Cycle 6
Error

## Slide 6: Data Dependencies: No Nop
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
F
D
E
M
W
0x014:
addq
%
rdx
,%
rax
F
D
E
M
W
0x016: halt
# demo-h0.ys
E
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
Cycle 4
Error
M
M_
valE
= 10
M_
dstE
=
%
rdx
e_
valE
f
0 + 3 = 3
E_
dstE
=
%
rax

## Slide 7: Stalling for Data Dependencies
  If instruction follows too closely after one that writes register, slow it down
  Hold instruction in decode
  Dynamically inject nop into execute stage
0x000: irmovq $10,%rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x00a: irmovq $3,%rax
F
D
E
M
W
0x014: nop
F
D
E
M
W
bubble
F
E
M
W
0x016: addq %rdx,%rax
D
D
E
M
W
0x018: halt
F
D
E
M
W
10
# demo-h2.ys
F
F
D
E
M
W
0x015: nop
11

## Slide 8: Stall Condition
Source Registers
  srcA and srcB of current instruction in decode stage
Destination Registers
  dstE and dstM fields
  Instructions in execute, memory, and write-back stages
Special Case
  Don’t stall for register ID 15 (0xF)
    Indicates absence of register operand
    Or failed cond. move

## Slide 9: Detecting Stall Condition
0x000: irmovq $10,%rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x00a: irmovq $3,%rax
F
D
E
M
W
0x014: nop
F
D
E
M
W
bubble
F
E
M
W
0x016: addq %rdx,%rax
D
D
E
M
W
0x018: halt
F
D
E
M
W
10
# demo-h2.ys
F
F
D
E
M
W
0x015: nop
11
Cycle 6
W
D
•
•
•
W_dstE = %rax
W_valE = 3
srcA = %rdx
srcB = %rax

## Slide 10: Stalling X3
0x000: irmovq $10,%rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
0x00a: irmovq $3,%rax
F
D
E
M
W
bubble
F
E
M
W
bubble
D
E
M
W
0x014: addq %rdx,%rax
D
D
E
M
W
0x016: halt
F
D
E
M
W
10
# demo-h0.ys
F
F
D
F
E
M
W
bubble
11
Cycle 4
•
•
•
W
W_dstE = %rax
D
srcA = %rdx
srcB = %rax
•
•
•
M
M_dstE = %rax
D
srcA = %rdx
srcB = %rax
E
e_dstE = %rax
D
srcA = %rdx
srcB = %rax
Cycle 5
Cycle 6

## Slide 11: What Happens When Stalling?
  Stalling instruction held back in decode stage
  Following instruction stays in fetch stage
  Bubbles injected into execute stage
    Like dynamically generated nop’s
    Move through later stages
0x000: irmovq $10,%rdx
0x00a: irmovq $3,%rax
0x014: addq %rdx,%rax
Cycle 4
0x016: halt
0x000: irmovq $10,%rdx
0x00a: irmovq $3,%rax
0x014: addq %rdx,%rax
# demo-h0.ys
0x016: halt
0x000: irmovq $10,%rdx
0x00a: irmovq $3,%rax
bubble
0x014: addq %rdx,%rax
Cycle 5
0x016: halt
0x00a: irmovq $3,%rax
bubble
0x014: addq %rdx,%rax
bubble
Cycle 6
0x016: halt
bubble
bubble
0x014: addq %rdx,%rax
bubble
Cycle 7
0x016: halt
bubble
bubble
Cycle 8
0x014: addq %rdx,%rax
0x016: halt
Write Back
Memory
Execute
Decode
Fetch

## Slide 12: Implementing Stalling
Pipeline Control
  Combinational logic detects stall condition
  Sets mode signals for how pipeline registers should update
Pipeline
control
logic
Pipeline
control
logic
Pipeline
control
logic
Pipeline
control
logic

## Slide 13: Pipeline Register Modes
Rising
clock
Rising
clock
_
_
Output = y
y
y
Rising
clock
Rising
clock
_
_
Output = x
x
x
x
x
n
o
p
Rising
clock
Rising
clock
_
_
Output =
nop
Output = x
Input = y
stall
= 0
bubble
= 0
x
x
Normal
Output = x
Input = y
stall
= 1
bubble
= 0
x
x
Stall
Output = x
Input = y
stall
= 0
bubble
= 1
Bubble

## Slide 14: Data Forwarding
Naïve Pipeline
  Register isn’t written until completion of write-back stage
  Source operands read from register file in decode stage
    Needs to be in register file at start of stage
Observation
  Value generated in execute or memory stage
Trick
  Pass value directly from generating instruction to decode stage
  Needs to be available at end of decode stage

## Slide 15: Data Forwarding Example
  irmovq in write-back stage
  Destination value in W pipeline register
  Forward as valB for decode stage
0x000:
irmovq
$10,%
rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x00a:
irmovq
$3,%
rax
F
D
E
M
W
F
D
E
M
W
0x014:
nop
F
D
E
M
W
F
D
E
M
W
0x015:
nop
F
D
E
M
W
F
D
E
M
W
0x016:
addq
%
rdx
,%
rax
F
D
E
M
W
F
D
E
M
W
0x018: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-h2.ys
Cycle 6
W
R[
%
rax
]
f
3
D
valA
f
R[
%
rdx
]
=
10
valB
f
W_
valE
=
3
•
•
•
W_
dstE
=
%
rax
W_
valE
= 3
srcA
=
%
rdx
srcB
=
%
rax

## Slide 16: Bypass Paths
Decode Stage
  Forwarding logic selects valA and valB
  Normally from register file
  Forwarding: get valA or valB from later pipeline stage
Forwarding Sources
  Execute: valE
  Memory: valE, valM
  Write back: valE, valM

## Slide 17: Data Forwarding Example #2
Register %rdx
  Generated by ALU during previous cycle
  Forward from memory as valA
Register %rax
  Value just generated by ALU
  Forward from execute as valB
0x000: irmovq $10,%rdx
1
2
3
4
5
6
7
8
F
D
E
M
W
0x00a: irmovq $3,%rax
F
D
E
M
W
F
D
E
M
W
0x014: addq %rdx,%rax
F
D
E
M
W
0x016: halt
# demo-h0.ys
Cycle 4
M
D
valA f M_valE = 10
valB f e_valE = 3
M_dstE = %rdx
M_valE = 10
srcA = %rdx
srcB = %rax
E
E_dstE = %rax
e_valE f 0 + 3 = 3

## Slide 18: Forwarding Priority
Multiple Forwarding Choices
  Which one should have priority
  Match serial semantics
  Use matching value from earliest pipeline stage
0x000: irmovq $1, %rax
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x00a: irmovq $2, %rax
F
D
E
M
W
F
D
E
M
W
0x014: irmovq $3, %rax
F
D
E
M
W
F
D
E
M
W
0x01e: rrmovq %rax, %rdx
F
D
E
M
W
F
D
E
M
W
0x020: halt
F
D
E
M
W
F
D
E
M
W
10
# demo-priority.ys
W
R[
%
rax
]
f
3
W
R[
%
rax
]
f
1
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
%
rax
]
=
0
D
valA
f
R[
%
rdx
]
=
10
valB
f
R[
D
valA
f
R[
%
rax
]
=
?
valB
f
0
Cycle 5
W
R[
%
rax
]
f
3
M
R[
%
rax
]
f
2
W
R[
%
rax
]
f
3
E
R[
%
rax
]
f
3

## Slide 19: Implementing Forwarding
  Add additional feedback paths from E, M, and W pipeline registers into decode stage
  Create logic blocks to select from multiple sources for valA and valB in decode stage

## Slide 20: Implementing Forwarding
## What should be the A value?
int d_valA = [
# Use incremented PC
D_icode in { ICALL, IJXX } : D_valP;
# Forward valE from execute
d_srcA == e_dstE : e_valE;
# Forward valM from memory
d_srcA == M_dstM : m_valM;
# Forward valE from memory
d_srcA == M_dstE : M_valE;
# Forward valM from write back d_srcA == W_dstM : W_valM;
# Forward valE from write back
d_srcA == W_dstE : W_valE;
# Use value read from register file
1 : d_rvalA;
];

## Slide 21: Limitation of Forwarding
Load-use dependency
  Value needed by end of decode stage in cycle 7
  Value read from memory in memory stage of cycle 8

## Slide 22: Avoiding Load/Use Hazard
  Stall using instruction for one cycle
  Can then pick up loaded value by forwarding from memory stage

## Slide 23: Detecting Load/Use Hazard
Condition | Trigger
Load/Use Hazard | E_icode in { IMRMOVQ, IPOPQ } && E_dstM in { d_srcA, d_srcB }

## Slide 24: Control for Load/Use Hazard
  Stall instructions in fetch and decode stages
  Inject bubble into execute stage
0x000:
irmovq
$128,%
rdx
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
0x00a:
irmovq
$3,%
rcx
F
D
E
M
W
F
D
E
M
W
0x014:
rmmovq
%
rcx
, 0(%
rdx
)
F
D
E
M
W
F
D
E
M
W
0x01e:
irmovq
$10,%
ebx
F
D
E
M
W
F
D
E
M
W
0x028:
mrmovq
0(%
rdx
),
%
rax
# Load %
rax
F
D
E
M
W
F
D
E
M
W
# demo
-
luh
.
ys
0x032:
addq
%
ebx
,
%
rax
# Use %
rax
0x034: halt
F
D
E
M
W
E
M
W
10
D
D
E
M
W
11
bubble
F
D
E
M
W
F
F
12
Condition | F | D | E | M | W
Load/Use Hazard | stall | stall | bubble | normal | normal

## Slide 25: Branch Misprediction Example
  Should only execute first 8 instructions
0x000: xorq %rax,%rax
0x002: jne t # Not taken
0x00b: irmovq $1, %rax # Fall through
0x015: nop
0x016: nop
0x017: nop
0x018: halt
0x019: t: irmovq $3, %rdx # Target
0x023: irmovq $4, %rcx # Should not execute
0x02d: irmovq $5, %rdx # Should not execute
demo-j.ys

## Slide 26: Handling Misprediction
Predict branch as taken
  Fetch 2 instructions at target
Cancel when mispredicted
  Detect branch not-taken in execute stage
  On following cycle, replace instructions in execute and decode by bubbles
  No side effects have occurred yet

## Slide 27: Detecting Mispredicted Branch
Condition | Trigger
Mispredicted Branch | E_icode = IJXX & !e_Cnd

## Slide 28: Control for Misprediction
Condition | F | D | E | M | W
Mispredicted Branch | normal | bubble | bubble | normal | normal

## Slide 29: Return Example
0x000: irmovq Stack,%rsp # Intialize stack pointer
0x00a: call p # Procedure call
0x013: irmovq $5,%rsi # Return point
0x01d: halt
0x020: .pos 0x20
0x020: p: irmovq $-1,%rdi # procedure
0x02a: ret
0x02b: irmovq $1,%rax # Should not be executed
0x035: irmovq $2,%rcx # Should not be executed
0x03f: irmovq $3,%rdx # Should not be executed
0x049: irmovq $4,%rbx # Should not be executed
0x100: .pos 0x100
0x100: Stack: # Stack: Stack pointer
  Previously executed three additional instructions
demo-retb.ys

## Slide 30: Correct Return Example
0x026: ret
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
0x013:
irmovq
$5,%
rsi
# Return
F
D
E
M
W
# demo
-
retb
F
D
E
M
W
F
valC
f
5
rB
f
%
esi
F
valC
f
5
rB
f
%
rsi
W
valM
=
0x0b
W
valM
=
0x013
•
•
•
  As ret passes through pipeline, stall at fetch stage
    While in decode, execute, and memory stage
  Inject bubble into decode stage
  Release stall when reach write-back stage

## Slide 31: Detecting Return
Condition | Trigger
Processing ret | IRET in { D_icode, E_icode, M_icode }

## Slide 32: Control for Return
0x026: ret
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
bubble
F
D
E
M
W
0x014:
irmovq
$5,%
rsi
# Return
F
D
E
M
W
# demo
-
retb
F
D
E
M
W
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal

## Slide 33: Special Control Cases
Detection
Action (on next cycle)
Condition | Trigger
Processing ret | IRET in { D_icode, E_icode, M_icode }
Load/Use Hazard | E_icode in { IMRMOVQ, IPOPQ } && E_dstM in { d_srcA, d_srcB }
Mispredicted Branch | E_icode = IJXX & !e_Cnd
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Mispredicted Branch | normal | bubble | bubble | normal | normal

## Slide 34: Implementing Pipeline Control
  Combinational logic generates pipeline control signals
  Action occurs at start of following cycle

## Slide 35: Initial Version of Pipeline Control
bool F_stall =
# Conditions for a load/use hazard
E_icode in { IMRMOVQ, IPOPQ } && E_dstM in { d_srcA, d_srcB } ||
# Stalling at fetch while ret passes through pipeline
IRET in { D_icode, E_icode, M_icode };
bool D_stall =
# Conditions for a load/use hazard
E_icode in { IMRMOVQ, IPOPQ } && E_dstM in { d_srcA, d_srcB };
bool D_bubble =
# Mispredicted branch
(E_icode == IJXX && !e_Cnd) ||
# Stalling at fetch while ret passes through pipeline
IRET in { D_icode, E_icode, M_icode };
bool E_bubble =
# Mispredicted branch
(E_icode == IJXX && !e_Cnd) ||
# Load/use hazard
E_icode in { IMRMOVQ, IPOPQ } && E_dstM in { d_srcA, d_srcB };

## Slide 36: Control Combinations
  Special cases that can arise on same clock cycle
Combination A
  Not-taken branch
  ret instruction at branch target
Combination B
  Instruction that reads from memory to %rsp
  Followed by ret instruction

## Slide 37: Control Combination A
  Should handle as mispredicted branch
  Stalls F pipeline register
  But PC selection logic will be using M_valM anyhow
JXX
E
D
M
Mispredict
JXX
E
D
M
Mispredict
E
ret
D
M
ret
1
E
ret
D
M
ret
1
E
ret
D
M
ret
1
Combination A
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Mispredicted Branch | normal | bubble | bubble | normal | normal
Combination | stall | bubble | bubble | normal | normal

## Slide 38: Control Combination B
  Would attempt to bubble and stall pipeline register D
  Signaled by processor as pipeline error
Load
E
Use
D
M
Load/use
E
ret
D
M
ret
1
E
ret
D
M
ret
1
E
ret
D
M
ret
1
Combination B
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Combination | stall | bubble + stall | bubble | normal | normal

## Slide 39: Handling Control Combination B
  Load/use hazard should get priority
  ret instruction should be held in decode stage for additional cycle
Load
E
Use
D
M
Load/use
E
ret
D
M
ret
1
E
ret
D
M
ret
1
E
ret
D
M
ret
1
Combination B
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Combination | stall | stall | bubble | normal | normal

## Slide 40: Corrected Pipeline Control Logic
  Load/use hazard should get priority
  ret instruction should be held in decode stage for additional cycle
Condition | F | D | E | M | W
Processing ret | stall | bubble | normal | normal | normal
Load/Use Hazard | stall | stall | bubble | normal | normal
Combination | stall | stall | bubble | normal | normal
bool D_bubble =
# Mispredicted branch
(E_icode == IJXX && !e_Cnd) ||
# Stalling at fetch while ret passes through pipeline
IRET in { D_icode, E_icode, M_icode }
# but not condition for a load/use hazard
&& !(E_icode in { IMRMOVQ, IPOPQ }
&& E_dstM in { d_srcA, d_srcB });

## Slide 41: Pipeline Summary
Data Hazards
  Most handled by forwarding
    No performance penalty
  Load/use hazard requires one cycle stall
Control Hazards
  Cancel instructions when detect mispredicted branch
    Two clock cycles wasted
  Stall fetch stage while ret passes through pipeline
    Three clock cycles wasted
Control Combinations
  Must analyze carefully
  First version had subtle bug
    Only arises with unusual instruction combination