## Slide 1: Directory-Based Cache Coherence
Lecture 13:

## Slide 2: Today you will learn…
What limits the scalability of snooping-based approaches to cache coherence
How a directory-based scheme avoids these problems
How the storage overhead of the directory structure be reduced (and at what cost)
How the interconnection network (bus, point-to-point, ring) affect scalability and design choices

## Slide 3: Implementing cache coherence
Processor
Local Cache
Processor
Local Cache
Processor
Local Cache
Processor
Local Cache
Interconnect
Memory
I/O
The snooping cache coherence protocols from the last lecture relied on broadcasting coherence information to all processors over the chip interconnect.
Every time a cache miss occurred, the triggering cache communicated with all other caches!
Notes: I actually didn’t tell you how to implement the broadcast, but I will in a later lecture
We really only talked about what information needs to be communicated

## Slide 4: Scaling problems with snoopy coherence
How does performance scale with number of processors?
Communication limited to one message at a time
Even a scalable point-to-point interconnect requires P messages per memory request (occupying each cache)
Fundamentally, all-to-all broadcast will not scale.
Processor
Local Cache
Processor
Local Cache
Processor
Local Cache
Processor
Local Cache
Interconnect
Memory
I/O
Processor
Local Cache
Processor
Local Cache
Processor
Local Cache
Processor
Local Cache

## Slide 5: Scaling cache coherence to large machines
Processor
Local Cache
Memory
Processor
Local Cache
Memory
Processor
Local Cache
Memory
Processor
Local Cache
Memory
Interconnect
Recall non-uniform memory access (NUMA) shared memory systems
Idea: locating regions of memory near the processors increases scalability: it yields higher aggregate bandwidth and reduced latency (especially when there is locality in the application)
But... efficiency of NUMA system does little good if the coherence protocol can’t also be scaled!
Consider this case: processor accesses nearby memory (good...), but to ensure coherence still must broadcast to all other processors it is doing so (bad...)
Some terminology:
  cc-NUMA = “cache-coherent, non-uniform memory access”
  Distributed shared memory system (DSM): cache coherent, shared address space, but architecture implemented by physically distributed memories
Notes: scaling: the point of local data is for it to be local
if you have to broadcast
one technique to build a system that scales better is to distribute the memories.

## Slide 6: Scaling cache coherence in current multicores
ccNUMA typically refers to supercomputing/clusters
Same issues appear in multicores
  NUMA: Memory controllers distributed around chip
  NUCA (non-uniform cache access): L3 banks distributed around the chip too
Mem
Ctrl
Mem
Ctrl
Mem
Ctrl
Mem
Ctrl
Core
L3 Cache Bank

## Slide 7: Why did we need a bus?
Ordering
  Bus serializes requests, ordering some before others
  BUT: Coherence does not require ordering of requests to different addresses
    (More on this when we discuss consistency)
Communication
  Simple, fast (but not scalable) broadcast medium
  BUT: Coherence does not require broadcast
    Only need to communicate with sharers
    Most data is not shared by every cache

## Slide 8: One possible solution: hierarchical snooping
Processor
Local Cache
Processor
Local Cache
Processor
Local Cache
Processor
Local Cache
Interconnect
Processor
Local Cache
Processor
Local Cache
Processor
Local Cache
Processor
Local Cache
Interconnect
Interconnect
Use snooping coherence at each level
Memory
Advantages
Relatively simple to build (already must deal with similar issues due to multi-level caches)
Disadvantages
The root of the network can become a bottleneck
Larger latencies than direct communication
Does not apply to more general network topologies (meshes, cubes)

## Slide 9: Scalable cache coherence using directories
Snooping schemes broadcast coherence messages to determine the state of a line in the other caches
Alternative idea: avoid broadcast by storing information about the status of the line in one place: a “directory”
  The directory entry for a cache line contains information about the state of the cache line in all caches.
  Caches look up information from the directory as necessary
  Cache coherence is maintained by point-to-point messages between the caches on a “need to know” basis (not by broadcast mechanisms)
Notes: centralized location that holds information about the state of a line in a cache’s
DEMO: “hey dude, who’s got X?”

## Slide 10: A very simple directory
Scalable Interconnect
Processor
Local Cache
Directory
Memory
. . .
One line of memory
One directory entry per line of memory
P presence bits: indicate whether processor P has line in its cache
Dirty bit: indicates line is dirty in one of the processors’ caches
Line: A region of memory that would be cached as a single block (e.g., 64 bytes)
Notes: shows memory
and the directory

## Slide 11: So we’ve traded a bus bottleneck for a memory bottleneck?
Not quite; directories distributed across memory banks
  Different ordering points for different addresses
Can cache directory entries + avoid memory access
  Caches are much faster + higher bandwidth than memory

## Slide 12: A distributed directory in ccNUMA
Scalable Interconnect
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
“Home node” of a line: node with memory holding the corresponding data for the line
  Example: node 0 is the home node of the yellow line, node 1 is the home node of the blue line
“Requesting node”: node containing processor requesting line
Example: directory partition is co-located with memory it describes
Notes: if you thought about processor plus it’s local memory as a “node”

## Slide 13: A distributed directory in a multicore
As we shall see, directories really live in each L3 bank
Mem
Ctrl
Mem
Ctrl
Mem
Ctrl
Mem
Ctrl
Core
L3 Cache Bank
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir
Dir

## Slide 14: Example 1: read miss to clean line
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is not dirty
Read miss message sent to home node of the requested line
Home directory checks entry for line
1. Request: read miss msg
Scalable Interconnect
Notes: P1 wants to load the blue line
“TRAFFIC DIRECTOR”
YO, A WANT THE BLUE LINE

## Slide 15: Example 1: read miss to clean line
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is not dirty
Read miss message sent to home node of the requested line
Home directory checks entry for line
  If dirty bit for cache line is OFF, respond with contents from memory, set presence[0] to true
  (to indicate line is cached by processor 0)
2. Response (line of data from memory)
1. Request: read miss msg
Scalable Interconnect
Notes: Sets the presence bit
OKAY, HERE YOU GO
Q. WHAT IF THE DATA IS DIRTY?

## Slide 16: Example 2: read miss to dirty line
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contents in P2’s cache)
If dirty bit is ON, then data must be sourced by another processor (with the most up-to-date copy of the line)
Home node must tell requesting node where to find data
  Responds with message providing identity of line owner (“get it from P2”)
2. Response: owner id
1. Request: read miss msg
Scalable Interconnect
Notes: now, what if the line is dirty?
Explain figure. presence[2] and dirty bit is set
YO MAN, I DON’T HAVE THE DATA, GET IT FROM P2

## Slide 17: Example 2: read miss to dirty line
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contents in P2’s cache)
If dirty bit is ON, then data must be sourced by another processor
Home node responds with message providing identity of line owner
Requesting node requests data from owner
Owner changes state in cache to SHARED (read only), responds to requesting node
2. Response: owner id
1. Request: read miss msg
3. Request: data
4. Response: data
Scalable Interconnect
Notes: Q. WHAT DOES P2 DO TO LINE BEFORE RESPONDING to P0: it drops from M to S

## Slide 18: Example 2: read miss to dirty line
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contents in P2’s cache)
If dirty bit is ON, then data must be sourced by another processor
Home node responds with message providing identity of line owner
Requesting node requests data from owner
Owner responds to requesting node, changes state in cache to SHARED (read only)
Owner also responds to home node, home clears dirty, updates presence bits, updates memory
2. Response: owner id
1. Request: read miss msg
3. Request: data
4. Response: data
5. Response: data+dir revision
Scalable Interconnect
Notes: this is just one possible sequence of steps
Q. What is the state of the line in cache 0 (shared)
Q. Why did we send the data to P1? (because it reduces hops in the future)

## Slide 19: Example 3: write miss
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Write to memory by processor 0: line is clean, but resident in P1’s and P2’s caches
1. Request: write miss msg
Scalable Interconnect

## Slide 20: Example 3: write miss
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Write to memory by processor 0: line is clean, but resident in P1’s and P2’s caches
1. Request: write miss msg
2. Response: sharer ids + data
Scalable Interconnect

## Slide 21: Example 3: write miss
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Write to memory by processor 0: line is clean, but resident in P1’s and P2’s caches
1. Request: write miss msg
3. Request: invalidate (2 msgs)
2. Response: sharer ids + data
Scalable Interconnect

## Slide 22: Example 3: write miss
Scalable Interconnect
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Write to memory by processor 0: line is clean, but resident in P1’s and P2’s caches
1. Request: write miss msg
3. Request: invalidate (2 msgs)
2. Response: sharer ids + data
4a. Response: ack from P2
4b. Response: ack from P1
After receiving both invalidation acks, P0 can perform write
Notes: Need to acks because we have a network, and messages can get out of order

## Slide 23: Advantage of directories
On reads, directory tells requesting node exactly where to get the line from
  Either from home node (if the line is clean)
  Or from the owning node (if the line is dirty)
  Either way, retrieving data involves only point-to-point communication
On writes, the advantage of directories depends on the number of sharers
  In the limit, if all caches are sharing data, all caches must be communicated with (just like broadcast in a snooping protocol)
Notes: this second stat is the key one

## Slide 24: Cache invalidation patterns
64 processor system
Barnes-Hut
LU
Ocean
01234567
8 to 11
12 to 15
16 to 19
20 to 23
24 to 27
28 to 31
32 to 35
36 to 39
40 to 43
44 to 47
48 to 51
52 to 55
56 to 59
60 to 63
Graphs plot histogram of number of sharers of a line at the time of a write
In general only a few processors share the line (only a few processors must be told of writes)
Not shown here, but the expected number of sharers typically increases slowly with P (good!)
Number of sharers 
Notes: Let’s do a demo to talk about why this is the case!
If writes do occur often, it’s unlikely there will be a lot of sharers
If writes infrequent, overhead of invalidating everyone inefficiently isn’t that big of a deal

## Slide 25: In general, only a few sharers during a write
Access patterns
  “Mostly-read” objects: lots of sharers but writes are infrequent, so minimal impact on performance (e.g., root node in Barnes-Hut)
  Migratory objects (one processor reads/writes for while, then another, etc.): very few sharers, count does not scale with number of processors
  Frequently read/written objects: frequent invalidations, but sharer count is low because count cannot build up in short time between invalidations (e.g, shared task queue)
  Low-contention locks: infrequent invalidations, no performance problem
  High-contention locks: can be a challenge, because many readers present when lock released
Implication 1: directories are useful for limiting coherence traffic
  Don’t need a broadcast mechanism to “tell everyone”
Implication 2: lets us limit directory storage overhead (how?)
Notes: migratory objects = one processor manipulates, then another, etc.
frequently read... assume that writes occur frequently enough such that reader list can’t build up
high contention lock, if the lock is held long enough, the reader lists can build up (all other CPUs are spinning on the lock)

## Slide 26: Very simple directory storage requirements
Scalable Interconnect
Processor
Local Cache
Directory
Memory
. . .
One line of memory
One directory entry per line of memory
P presence bits: indicate whether processor P has line in its cache
Dirty bit: indicates line is dirty in one of the processors’ caches
Assume
  64 bytes / line
  P = 256 processors
  M = main memory size (bytes)
How big is directory?
Notes: Number of directory bits = M/64 * P
D = directory bytes = M/512 * P
When P = 256, D = M/2

## Slide 27: Full-map directory representation
Recall: one presence bit per node
Storage proportional to P x M
  P = number of nodes (e.g., processors)
  M = number of lines in memory
  # dir entries = M / 64B
  # bytes / dir entry = P / 8
   Dir size = P * M / 8
Storage overhead rises with P
  Assume 64 byte cache line size (512 bits)
  64 nodes (P=64) →12% overhead
  256 nodes (P=256) → 50% overhead
  1024 nodes (P=1024) → 200% overhead
. . .
P
M
. . .
Notes: 64 bytes = 512 bits
remember, this is a supercomputer. There’s a lot of memory, so 200% overhead is a nasty problem

## Slide 28: Reducing storage overhead of directory
Optimizations on full-map directory scheme
  Increase cache line size (reduce M term)
      What are the downsides of this approach? (consider graphs from last lecture)
  Group multiple processors into a single directory “node” (reduce P term)
      Need only one directory bit per node, not one bit per processor
      Hierarchical: could use snooping protocol to maintain coherence among processors in a node
      But hierarchical coherence is very complicated + adds latency
We will now discuss two alternative schemes
  Limited pointer schemes (reduce P)
  Sparse directories

## Slide 29: Limited directory
Most data has few sharers  Idea: Store only a few pointers in directory (we only need a list of the nodes holding a valid copy of the line!)
Ocean
Example: 1024 processor system
Full bit vector scheme needs 1024 bits per line
Instead, we can track most accesses with a few pointers to sharers
Each pointer is , so anything <100 pointers is a win!
(E.g., >99% of writes with just a five sharers in Ocean)
01234567
8 to 11
12 to 15
16 to 19
20 to 23
24 to 27
28 to 31
32 to 35
36 to 39
40 to 43
44 to 47
48 to 51
52 to 55
56 to 59
60 to 63
Notes: REALLY, WHAT IS THE BIT VECTOR? it’s a representation of a list of sharers
ring a bell with assignment 2?
Q. OVERFLOW?

## Slide 30: Managing overflow in limited pointer schemes
Fallback to broadcast
Replaces an existing sharer (invalidating its cache) with the new sharer
Coarse bit-vector
  Revert to bit vector representation
  Each bit corresponds to a cluster of K processors
  On write, invalidate all processors in the cluster
Many possible approaches
Notes: challenge is dealing with the situation where there’s high dynamic range of list sizes
when are these schemes bad?
broadcast: when there’s X + 1 sharers (or data is just sitting there in a processors cache’s and never touched)
no broadcast: like LRU, can construct an access pattern where always taking a miss
coarse: when the “spatial locality” of sharing does exist

## Slide 31: Optimize for the common case!
Limited pointer schemes are a great example of understanding and optimizing for the common case:
Workload-driven observation: in general the number of cache line sharers is low
Make the common case simple and fast: array of pointers for first N sharers
Uncommon case is still handled correctly, just with a slower, more complicated mechanism (the program still works!)
Extra expense of the complicated solution is tolerable, since it happens infrequently

## Slide 32: Limited pointer schemes: summary
Limited pointer schemes reduce directory storage overhead caused by large P
Most lines have few sharers, so this works well
But do we really even need to maintain a list of sharers for each line of data in memory?
. . .
P  k log P
M
. . .
Directory
Notes: rows where bit-vectors
there was a row for every memory line in the machine
one way to think about few sharers
increase cache line size
NOTE: Some students take issue with calling this reducing M, since there’s

## Slide 33: Limiting size of directory: sparse directories
Key observations: 1) The coherence protocol only needs sharing information for lines in some cache. 2) Most memory is NOT resident in cache.  Almost all directory entries are empty
E.g., 1 MB cache, 1 GB memory → ≥ 99.9% of entries are empty
Directory
. . .
One directory entry per line of memory held in some cache
{
Tag
Scaling:
Each cache holds C lines
P*C entries / processor
Notes: original implementation: data for all processors for all lines
limited pointer: most processors are not sharing (sparse sharing)
sparse directories: most lines are not in cache (sparse residency in cache)
But, possible to have case where large fraction of memory resident across set of caches

## Slide 34: Limiting size of directory: sparse directories
Key observations: 1) The coherence protocol only needs sharing information for lines in some cache. 2) Most memory is NOT resident in cache.  Almost all directory entries are empty
E.g., 1 MB cache, 1 GB memory → ≥ 99.9% of entries are empty
Interconnect
Processor
Local Cache
Directory
Memory
. . .
One line of memory
One directory entry per line of memory
Notes: original implementation: data for all processors for all lines
limited pointer: most processors are not sharing (sparse sharing)
sparse directories: most lines are not in cache (sparse residency in cache)
But, possible to have case where large fraction of memory resident across set of caches

## Slide 35: Sparse directories: Reducing directory entries
Key observations: 1) The coherence protocol only needs sharing information for lines in some cache. 2) Most memory is NOT resident in cache.  Almost all directory entries are empty
E.g., 1 MB cache, 1 GB memory → ≥ 99.9% of entries are empty
Interconnect
Processor
Local Cache
Directory
Memory
One line of memory
One directory entry per line of cache
Tag
Scaling:
Each cache holds C lines
P * C bits / processor
Directory scales with cache (not memory) size
Notes: original implementation: data for all processors for all lines
limited pointer: most processors are not sharing (sparse sharing)
sparse directories: most lines are not in cache (sparse residency in cache)
But, possible to have case where large fraction of memory resident across set of caches

## Slide 36: Sparse directories: Reducing directory entries
Key observations: 1) The coherence protocol only needs sharing information for lines in some cache. 2) Most memory is NOT resident in cache.  Almost all directory entries are empty
E.g., 1 MB cache, 1 GB memory → ≥ 99.9% of entries are empty
Interconnect
Processor
Local Cache
Directory
Memory
One line of memory
One directory entry per line of cache
Tag
Scaling:
Each cache holds C lines
P * C bits / processor
Directory scales with cache (not memory) size
Notes: original implementation: data for all processors for all lines
limited pointer: most processors are not sharing (sparse sharing)
sparse directories: most lines are not in cache (sparse residency in cache)
But, possible to have case where large fraction of memory resident across set of caches

## Slide 37: Sparse directories: Limiting entry size
Idea: Store sharers as a linked list
Directory at home node stores only 1 pointer to head of the list (not the full list)
Pointer to next node in list is stored with cache line (alongside the line’s tag, dirty bits, etc)
. . .
M
Processor cache: node 0
(last reader)
prev ptr
line data
Directory (home node for line)
Processor cache: node 1
next ptr
Processor cache: node 2
(last reader)
On read miss: add requesting node to head of list
On write miss: walk list to invalidate each sharer
One directory entry per cache line of memory held in some cache
On evict: need to patch up list (linked list removal)
Scaling:
Directory has C entries
Each entry is one pointer, or total = bits
Two pointers C cache lines = bits
Total: bits / processor
Notes: Questions:
O(1) read miss
O(sharers) write miss
O(1) evict with forward/back links

## Slide 38: Sparse directories: scaling properties
Good:
. . .
M
Processor cache: node 0
prev ptr
line data
Directory (home node for line)
Processor cache: node 1
next ptr
Processor cache: node 2
Bad:
  Low memory storage overhead
  Traffic on write is proportional to number of sharers (no broadcast fallback)
  Latency of write proportional to number of sharers (invalidation of lines is serial)
  Higher implementation complexity
Notes: Q. what’s the bad?
notice the difference between serial invalidation here, and parallel invalidation in basic bit vector scheme (see next slide)

## Slide 39: Recall: write miss in full bit vector scheme
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Memory
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Write to memory by processor 0: line is clean, but resident in P1’s and P2’s caches
1. Request: write miss msg
3. Request: invalidate (2 msgs)
2. Response: sharer ids + data
Original bit-vector scheme sends same number of invalidation messages as sparse directory approach, but invalidation messages can be sent to all processors in parallel
Scalable Interconnect
Notes: hold this idea (path versus traffic)
dependencies

## Slide 40: In-cache directories
In-cache directory: Add directory entries to shared L3 cache
Sparse directory: Add separately tagged structure to track L2 contents
In-cache directories are common in multicores today
Core
L1 Data Cache
L2 Cache
Shared L3 Cache
(One bank per core)
Interconnect
Core
L1 Data Cache
L2 Cache
Core
L1 Data Cache
L2 Cache
Core
L1 Data Cache
L2 Cache
Recall: Coherence implemented at shared-private boundary
Memory
Tag
Sharers
Data
add’l bits
L3 must be inclusive
add’l bits
L3 need not be inclusive
In-cache dir smaller if:

## Slide 41: Optimizing directory-based coherence
Reducing storage overhead of directory data structure
  Limited pointer schemes
  Sparse directories
Reducing number of messages sent to implement coherence protocol

## Slide 42
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s cache)
1. Request: read miss msg
Recall: read miss to dirty line
Scalable Interconnect
Notes: This for a read miss by P0 to dirty data owned by P2

## Slide 43: Recall: read miss to dirty line
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s cache) (Note: figure below shows final state of system after operation is complete)
Five network transactions in total
Four of the transactions are on the “critical path” (transactions 4 and 5 can be done in parallel)
  Critical path: sequence of dependent operations that must occur to complete operation
2. Response: owner id
1. Request: read miss msg
3. Request: data
4. Response: data
5. Response: data+dir revision
Scalable Interconnect
Notes: NOTE: before you built the slide. This is the end result
CAN WE DO BETTER?

## Slide 44: Intervention forwarding
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s cache)
1. Request: read miss msg
Scalable Interconnect

## Slide 45: Intervention forwarding
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s cache)
1. Request: read miss msg
3. Response: data+dir revision
2. Request: intervention read
Home node requests data from owner node (processor 2)
Owning node responds
Scalable Interconnect
Notes: Message 2: Hey can you give me the data. (flush)

## Slide 46: Intervention forwarding
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s cache)
1. Request: read miss msg
3. Response: data+dir revision
2. Request: intervention read
4. Response: data
Home node updates directory, and responds to requesting node with data
Four network transactions in total (less traffic)
But all four of the transactions are on the “critical path.” Can we do better?
Scalable Interconnect
Notes: Q. Can we do better?

## Slide 47: Request forwarding
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s cache)
1. Request: read miss msg
Scalable Interconnect

## Slide 48: Request forwarding
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s cache)
1. Request: read miss msg
2. Request: send data to requestor
Scalable Interconnect

## Slide 49: Request forwarding
Memory
Processor 0
Local Cache
Memory
Directory
. . .
Processor 1
Local Cache
Directory
. . .
Processor 2
Local Cache
Memory
Directory
. . .
Read from main memory by processor 0 of the blue line: line is dirty (contained in P2’s cache)
1. Request: read miss msg
2. Request: send data to requestor
3/4. Response: data
(2 msgs: sent to both home node and requestor)
Four network transactions in total
Only three of the transactions are on the critical path (transactions 3 and 4 can be done in parallel)
Note: system is no longer pure request/response (since P0 sent request to P1, but receives response from P2)
Scalable Interconnect
Notes: no longer purely request-response: requestor get a response from a node that it didn’t request data from
complex

## Slide 50: Directory coherence in Intel Core i7 CPU
L3 hosts in-cache directory (and is inclusive)
Directory maintains list of L2 caches containing line
Instead of broadcasting coherence traffic to all L2’s, only send coherence messages to L2’s that contain the line
(Core i7 interconnect is a ring, it is not a bus)
Directory dimensions:
  P=4
  M = number of L3 cache lines
Core
L1 Data Cache
L2 Cache
Shared L3 Cache
(One bank per core)
Ring Interconnect
Core
L1 Data Cache
L2 Cache
Core
L1 Data Cache
L2 Cache
Core
L1 Data Cache
L2 Cache
Notes: SINGLE-CHIP directory-based coherence
inclusion: if it’s in an L2, that means there can be coherence traffic, directory entry guaranteed to exist in L3 ***
find the directory entry by finding the line in the L3
Since P is so small, clearly a bit-vector based scheme

## Slide 51: Coherence in multi-socket Intel systems
Core
L1
L2
L3 Cache
Core
L1
L2
Core
L1
L2
Core
L1
L2
Core
L1
L2
L3 Cache
Core
L1
L2
Core
L1
L2
Core
L1
L2
Cache Agent
Cache Agent
Memory Controller
Memory Controller
Home Agent
Home Agent
QuickPath Interconnect
(QPI)
to DRAM…
(with in memory directory)
Dir cache (16KB)
Dir cache (16KB)
to DRAM…
(in memory directory)
L3 directory reduces on-chip coherence traffic (previous slide)
In-memory directory (cached by home agent/memory controller) reduces coherence traffic between cores
Notes: SINGLE-CHIP directory-based coherence
inclusion: if it’s in an L2, that means there can be coherence traffic, directory entry guaranteed to exist in L3 ***
find the directory entry by finding the line in the L3
Since P is so small, clearly a bit-vector based scheme

## Slide 52: Xeon Phi
Intel’s NUMA on a chip
Many (50+) x86 cores
  Ours have 61
  “Knight’s Corner”
  4-way hyper threading
  Each with 1–2 vector units
Cache-coherent memory system
Knight’s Corner overall system:
  Max. 8GB memory
  Max. 2 TFLOPS
  0.004 bytes/flop
    not balanced
  300 Watts
Prototype / internal names include:
Larrabee, Knight’s Ferry, Knight’s Corner, Knight’s Landing, Knight’s Hill
China’s Tianhe-2 has 48,000 Knight’s Corner chips

## Slide 53: Knight’s Corner Xeon Phi Cache Coherence
  512KB L2 caches
  8 memory controllers
    Total 8GB max.
Prototype / internal names include:
Larrabee, Knight’s Ferry, Knight’s Corner, Knight’s Landing, Knight’s Hill

## Slide 54: KC Xeon Phi Ring Communication
Messages sent around bidirectional ring
  Having everything on single chip enables very wide communication paths
  Can get effect of broadcast by circulating message around entire ring
    Advantage over point-to-point

## Slide 55: KC Xeon Phi Directory Structure
Directory keeps track of which lines are resident in local L2
  Same as with single-node system
Worst-case memory read or write by P:
  Check local cache
  Circulate request around ring for line in some cache
  Send request around ring to memory controller
Notes: More like a bus-based cache system, due to broadcast capabilities of ring

## Slide 56: Next Generation Xeon Phi
“Knight’s Landing”
72 cores
  Each with 4-way hyper threading
  Each with 2 vector units
Grouped into pairs to give 36 compute nodes
Peak 6 SP TFLOPS
16 GB on package RAM
Access to up to 384 GB off-package RAM

## Slide 57: Knight’s Landing Xeon Phi Cache Coherence
  Nodes organized as 2-D mesh
    Some for computation
    Some for memory interfaces
  Use X/Y routing to send messages
  Must use more traditional directory-based scheme

## Slide 58: Summary: directory-based coherence
Primary observation: broadcast doesn’t scale, but luckily we don’t need to broadcast to ensure coherence because often the number of caches containing a copy of a line is small
Instead of snooping, just store the list of sharers in a “directory” and check the list as necessary
One challenge: reducing overhead of directory storage
  Use hierarchies of processors or larger line sizes
  Limited pointer schemes: exploit fact the most processors not sharing line
  Sparse directory schemes: exploit fact that most lines are not in cache
Another challenge: reducing the number of messages sent (traffic) and critical path (latency) of message chains needed to implement coherence operations
Ring-based schemes can be much simpler than point-to-point communication