## Slide 1: Interconnection Networks
Lecture 15:
Credit: some slides created by Michael Papamichael, others based on slides from Onur Mutlu’s 18-742

## Slide 2: Basic system design from previous lectures
Cache
Processor
Interconnect (shared bus)
Cache
Processor
Memory
Bus interconnect:
All nodes connected by a shared set of wires
Request bus:
cmd + address
Response bus:
data
e.g., 256 bits
3 bits
Response tag
e.g., 40 bits
Bus clients (interconnect nodes)
Bus
Arbitrator

## Slide 3: Today: modern interconnect designs
Cache
Processor
Interconnection Network
Cache
Processor
Memory
Interconnect nodes
Today’s topics: the basic ideas of building a high-performance interconnection network in a parallel processor.
(think: “a network-on-a-chip”)

## Slide 4: What are interconnection networks used for?
To connect:
  Processor cores with other cores
  Processors and memories
  Processor cores and caches
  Caches and caches
  I/O devices

## Slide 5: Why is the design of the interconnection network important?
System scalability
  How large of a system can be built?
  How easy is it to add more nodes (e.g., cores)
System performance and energy efficiency
  How fast can cores, caches, memory communicate
  How long is latency to memory?
  How much energy is spent on communication?

## Slide 6: With increasing core counts…
Tilera GX 64-core chip
Intel Xeon Phi (72-core x86)
Intel core i7 (4-CPU cores, + GPU)
Scalability of on-chip interconnection network becomes increasingly important
Tegra K1: 4 + 1 ARM cores + GPU cores

## Slide 7: Interconnect terminology

## Slide 8: Terminology
Network node: a network endpoint connected to a router/switch
  Examples: processor caches, the memory controller
Network interface:
  Connects nodes to the network
Switch/router:
  Connects a fixed number of input links to a fixed number of output links
Link:
  A bundle of wires carrying a signal
0
1
2
3
Node
Link
Switch
Network interface
Notes: describe iconography

## Slide 9: Design issues
Topology: how switches are connected via links - Affects routing, throughput, latency, complexity/cost of implementation
Routing: how a message gets from its source to its destination in the network
  - Can be static (messages take a predetermined path) or adaptive based on load
Buffering and flow control
  What data are stored in the network? packets, partial packets? etc.
  How does the network manage buffer space?

## Slide 10: Properties of interconnect topology
Routing distance
  Number of links (“hops”) along a route between two nodes
Diameter: the maximum routing distance
Average distance: average routing distance over all valid routes
Example:
diameter = 6

## Slide 11: Properties of interconnect topology
Direct vs. indirect networks
  Direct network: endpoints sit “inside” the network
  e.g., mesh is direct network: every node is both an endpoint and a switch
Direct network
Indirect network

## Slide 12: Properties of an interconnect topology
Bisection bandwidth:
  Common metric of performance for recursive topologies
  Cut network in half, sum bandwidth of all severed links
  Warning: can be misleading as it does not account for switch and routing efficiencies
Blocking vs. non-blocking:
  If connecting any pairing of nodes is possible, network is non-blocking (otherwise, it’s blocking)
Notes: The bisection bandwidth is the bandwidth across the minimum cut which divides the network into two equal partitions.

## Slide 13: Example: blocking vs. non-blocking
Is this network blocking or non-blocking?
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Consider simultaneous messages from 0-to-1 and 3-to-7.
Note: in this network illustration, each node is drawn twice for clarity (at left and at right)

## Slide 14: Example: blocking vs. non-blocking
Is this network blocking or non-blocking?
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Conflict
Consider simultaneous messages from 0-to-1 and 3-to-7.
Consider simultaneous messages from 1-to-6 and 3-to-7. Blocking!!!
Note: in this network illustration, each node is drawn twice for clarity (at left and at right)

## Slide 15: Load-latency behavior of network
Latency
Load - Offered Traffic (bits/sec)
Min latency given by topology
Min latency given by routing algorithm
Zero load or idle latency
(topology+routing+flow control)
Throughput given by topology
Throughput given by routing
Saturation throughput
(given by flow control)
General rule: latency increases with load (throughput)

## Slide 16: Interconnect topologies

## Slide 17: Many possible network topologies
Bus
Crossbar
Ring
Tree
Omega
Hypercube
Mesh
Torus
Butterfly
…

## Slide 18: Bus interconnect
Good:
  Simple design
  Cost effective for a small number of nodes
  Easy to implement coherence (via snooping)
Bad:
  Contention: all nodes contend for shared bus
  Limited bandwidth: all nodes communicate over same wires (one communication at a time)
  High electrical load = low frequency, high power
0
1
2
3
4
0
1
2
3
4
Physical Structure
Logical Structure

## Slide 19: Crossbar interconnect
Every node is connected to every other node (non-blocking, indirect)
Switch i,j provides direct connection from node i to node j
Good:
  O(1) latency and high bandwidth
Bad:
  Not scalable: O(N2) switches
  High cost
  Difficult to arbitrate at scale
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Note: in this network illustration, each node is drawn twice for clarity (at left and at top)
8-node crossbar network (N=8)
Crossbar scheduling algorithms / efficient hardware implementations are still active research areas.
Notes: non-buffering switches

## Slide 20: Crossbar interconnect
Horizontal/Vertical lines
  Continuous wires
Circles
  Optionally connect horizontal wire to vertical
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
(Here is a more verbose illustration than that on previous slide)

## Slide 21: Crossbar Logical Structure
For each possible sender:
  Can connect to any set of receivers simultaneously
  Very general, but very expensive
0
1
2
3
4
5
6
7

## Slide 22: Crossbars were used in recent multi-core processing from Oracle (previously Sun)
Note that crossbar (CCX) occupies about the same chip area as a core
Sun SPARC T2 (8 cores, 8 L2 cache banks)
Oracle SPARC T5 (16 cores, 8 L3 cache banks)
Notes: point out area of chip dedicated to crossbar

## Slide 23: Ring
Good:
  Simple
  Cheap: O(N) cost
Bad:
  High latency: O(N)
  Bisection bandwidth remains constant as nodes are added (scalability issue)
Used in recent Intel architectures
  Core i7
Also used in IBM CELL Broadband Engine (9 cores)
0
1
2
3

## Slide 24: Intel’s ring interconnect
Introduced in Sandy Bridge microarchitecture
L3 cache slice
(2 MB)
L3 cache slice
(2 MB)
L3 cache slice
(2 MB)
L3 cache slice
(2 MB)
System Agent
Graphics
Four rings
  request
  snoop
  Ack
  data (32 bytes)
Six interconnect nodes: four “slices” of L3 cache + system agent + graphics
Each bank of L3 connected to ring bus twice
Theoretical peak BW from cores to L3 at 3.4 GHz is approx. 435 GB/sec
  When each core is accessing its local slice
Core
Core
Core
Core
Notes: unidirectional ring, but connected twice

## Slide 25: Mesh
Direct network
Echoes locality in grid-based applications
O(N) cost
Average latency: O(sqrt(N))
Easy to lay out on chip: fixed-length links
Path diversity: many ways for message to travel from one node to another
Used by:
  Tilera processors
  Prototype Intel chips
2D Mesh
Notes: Q. what’s a potential problem with a mesh network?
A. average node-to-node latency highly variable depending on where node is on grid
say you were processor, and you had to choose a position on a grid to minimize communication latency
near a corner there’s trouble. Middle is better.

## Slide 26: Xeon Phi (Knights Landing)
72 cores, arranged as 6 x 6 mesh of tiles (2 cores/tile)
YX routing of messages:
  Move in Y
  “Turn”
  Move in X
Notes: 72 cores, paired up, so 36 caches / nodes, 6x6

## Slide 27: Torus
Characteristics of mesh topology are different based on whether node is near edge or middle of network (torus topology introduces new links to avoid this problem)
Still O(N) cost, but higher cost than 2D grid
Higher path diversity and bisection BW than mesh
Higher complexity
  Difficult to layout on chip
  Unequal link lengths
2D Torus

## Slide 28: Folded Torus
Interleaving rows & columns eliminates need for long connections
All connections doubled in length
Torus
Folded Torus
16
16
00
30
10
20
01
31
11
21
03
33
13
23
02
32
12
22
00
10
20
30
01
11
21
31
02
12
22
32
03
13
23
33

## Slide 29: Hypercube
Low latency: O(lg N)
Radix: O(lg N)
Number of links O(N lg N)
6D hypercube used in 64-core Cosmic Cube computer developed at Caltech in the 80s
SGI Origin used a hypercube
0000
0101
0100
0001
0011
0010
0110
0111
1000
1101
1100
1001
1011
1010
1110
1111
Notes: bisection is N/2

## Slide 30: Generalizing Torii and Hypercubes
k-ary n-cube
  Rings of k nodes
  Connected in n dimensions
(10,1)
(5,2)
(3,3)
(2,0)
(2,1)
(2,2)
(2,3)
(2,4)

## Slide 31: Trees
Planar, hierarchical topology
Like mesh/torus, good when traffic has locality
Latency: O(lg N)
Use “fat trees” to alleviate root bandwidth problem (higher bandwidth links near root)
0
1
2
3
4
5
6
7
Fat Tree
H-Tree
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Notes: Q. What’s the latency
Q. What’s the problem with a tree (think: bisection BW)
Solution: fat trees
The Fat Tree network was invented by MIT Prof. Charles Leiserson and was used as the interconnection network in the Thinking Machines CM-5 supercomputer developed in the 90s. A CM-5 was featured in the movie Jurassic Park.

## Slide 32: Tree Routing
Getting from 1 to 2:
  1 = 0012
  2 = 0102
Getting from 3 to 6:
  3 = 0112
  6 = 1102
0
1
2
3
4
5
6
7
Upward:
Until have common ancestor
Downward:
0  left, 1  right

## Slide 33: Fat Tree
Charles Leiserson, 1985
Increase bandwidth between nodes as move upward
O(N) bisection bandwidth
Routing:
  Like tree routing, but randomly choose when multiple links possible
0
1
2
3
4
5
6
7

## Slide 34: Constant-Width Fat Tree
Sometimes called “Folded Clos Network”
All nodes fixed degree
  Simpler hardware design
Used in Infiniband networks
0
1
2
3
4
5
6
7

## Slide 35: Data Center Networks
Requirements
  Provide connectivity between 1K–10K nodes in data center
  High bisection bandwidth
  Low cost
Traditional Design: Hierarchy of Ethernet Switches

## Slide 36: Clos/Fat-Tree Networks for Data Centers
Many copies of identical switches
More tolerant of failures
Can implement with IP-based protocols

## Slide 37: Generalizing Clos Network
k-ary fat tree
  Basic unit is k-ported switch
  E.g., k = 6:
  Connect k3/4 hosts with 5k2/4 switches
  Bisection bandwidth = k3/4

## Slide 38: Supercomputer Networks
Oak Ridge Titan
  Fastest Computer in 2013
  3D Torus Network
  18,688 nodes
    ~ 26 x 26 x 28
Oak Ridge Summit
  Fastest in 2018
  3-level fat tree
  4,608 nodes
  ~ k = 28

## Slide 39: Multi-stage logarithmic
Indirect network with multiple switches between terminals
Cost: O(N lg N)
Latency: O(lg N)
Many variations: Omega, butterfly, etc…
0
1
2
3
4
5
6
7
000
001
010
011
100
101
110
111
0
1
2
3
4
5
6
7
000
001
010
011
100
101
110
111
Omega Network
Notes: log n steps
cost is n lg n because lg n steps * n/2 each step
how do you route to …
bit pattern tells you how to route (each stage, look at corresponding bit in destination)

## Slide 40: Multi-stage logarithmic Routing
Route from 1 to 6
  6 = 1102
  1  down, 0  up
0
1
2
3
4
5
6
7
000
001
010
011
100
101
110
111
0
1
2
3
4
5
6
7
000
001
010
011
100
101
110
111
Omega Network
Notes: log n steps
cost is n lg n because lg n steps * n/2 each step
how do you route to …
bit pattern tells you how to route (each stage, look at corresponding bit in destination)

## Slide 41: Review: network topologies
Topology
Direct/Indirect
Blocking/ Non-blocking
Cost
Latency
Crossbar Indirect Non-blocking O(N2)
O(1)
Multi-stage log. Indirect Blocking (one discussed in class is, others are not)
O(N lg N) O(lg N)
Mesh Direct Blocking
O(N) O(sqrt(N)) (average)
Notes: bisection: mesh (sqrt(N)), torus 2 x mesh

## Slide 42: Buffering and flow control

## Slide 43: Circuit switching vs. packet switching
Circuit switching sets up a full path (acquires all resources) between sender and receiver prior to sending a message
  Establish route (reserve links) then send all data for message
  Higher bandwidth transmission (no per-packet link mgmt overhead)
  Does incur overhead to set up/tear down path
  Reserving links can result in low utilization
Packet switching makes routing decisions per packet
  Route each packet individually (possibly over different network links)
  Opportunity to use link for a packet whenever link is idle
  Overhead due to dynamic switching logic during transmission
  No setup/tear down overhead
Notes: how many of you have taken a networking class
once again, infringement on other topics

## Slide 44: Granularity of communication
Message
  Unit of transfer between network clients (e.g., cores, memory)
  Can be transmitted using many packets
Packet
  Unit of transfer for network
  Can be transmitted using multiple flits (will discuss later)
Flit (flow control unit)
  Packets broken into smaller units called “flits”
  Flit: (“flow control unit”) a unit of flow control in the network
  Flits become minimum granularity of routing/buffering

## Slide 45: Packet format
A packet consists of:
  Header:
    Contains routing and control information
    At start of packet to router can start forwarding early
  Payload/body: containing the data to be sent
  Tail
    Contains control information, e.g., checksum code for error detection
    Generally located at end of packet so it can be generated “on the way out”
    (sender computes checksum, appends it to end of packet)
Header
Tail
Payload/body
Packet

## Slide 46: Handling contention
Packet 1
Packet 2
Scenario: two packets need to be routed onto the same outbound link at the same time
Options:
  Buffer one packet, send it over link later
  Drop one packet
  Reroute one packet (deflection)
In this lecture: we only consider buffering *
* But recent research has looked at using bufferless networks with deflection routing
as a power-efficient interconnect for chip multiprocessors.
Notes: Q. what can we do?
Q. what happens if we drop one and try again?
Q. why doesn’t this happen in a circuit switched network

## Slide 47: Circuit-switched routing
High-granularity resource allocation
  Main idea: pre-allocate all resources (links across multiple switches) along entire network path for a message (“setup a flow”)
Costs
  Needs setup phase (“probe”) to set up the path (and to tear it down and release the resources when message complete)
  Lower link utilization. Transmission of two messages cannot share same link (even if some resources on a preallocated path are no longer utilized during a transmission)
Benefits
  No contention during transmission due to preallocation, so no need for buffering
  Arbitrary message sizes (once path is set up, send data until done)
Dest
Source
Reserved
Link
Reserved
Link
Reserved
Link
Notes: costs are setup and tear down
but once you’re ready, you’re ready

## Slide 48: Store-and-forward (packet-based routing)
Packet copied entirely into network switch before moving to next node
Flow control unit is an entire packet
  Different packets from the same message can take different routes, but all data in a packet is transmitted over the same route
Requires buffering for entire packet in each router
Source
Destination
One packet
Packet Buffer
Packet Buffer
Packet Buffer
Packet Buffer
Packet Buffer
Packet Buffer
Busy Link
Busy Link
Busy Link
Note to students: in lecture this slide was animated and the final build shown here is not illustrative of store-and-forward routing concept (please refer to lecture video)
High per-packet latency (latency = packet transmission time on link x network distance)
Notes: Q. problem: latency
Q. Can we do better on latency?

## Slide 49: Cut-through flow control (also packet-based)
Switch starts forwarding data on next link as soon as packet header is received (header determines how much link bandwidth packet requires + where to route)
Result: reduced transmission latency
  Cut-through routing reduces to store-and-forward under high contention. Why?
Source
Destination
One Packet
Packet Buffer
Packet Buffer
Packet Buffer
Packet Buffer
Packet Buffer
Packet Buffer
Busy Link
Busy Link
Busy Link
Store and forward solution from previous slide: 3 hops x 4 units of time to transmit packet over a single link = 12 units of time
Cut-through solution: 3 steps of latency for head of packet to get to destination + 3 units of time for rest of packet = 6 units of time
Note to students: in lecture this slide was animated and the final build shown here is not illustrative of the cut-through routing concept (please refer to lecture video or Powerpoint version)
Notes: Go back through steps (store and forward= 12 steps (3 hops * 4)
Here: 8 steps. (5 latency + 3 rest of packet)
Q. What if link not available?
NOTE: ALL THIS DONE AT PACKET GRANULARITY. THE OPERATION IS JUST SEND PACKET

## Slide 50: Cut-through flow control
If output link is blocked (cannot transmit head), transmission of tail can continue
  Worst case: entire message is absorbed into a buffer in a switch (cut-through flow control degenerates to store-and-forward in this case)
  Requires switches to have buffering for entire packet, just like store-and-forward

## Slide 51: Wormhole flow control
Flit (flow control unit)
  Packets broken into smaller units called “flits”
  Flit: (“flow control unit”) a unit of flow control in the network
  Flits become minimum granularity of routing/buffering
    Recall: up until now, packets were the granularity of transfer AND flow control and buffering (store-and-forward, cut-through routing)
Head
Flit
Tail
Flit
Flit
Flit
Flit
Flit
Flit
Flit
Packet
Head
Flit
Tail
Flit
Flit
Flit
Flit
Flit
Flit
Flit
Packet
Message

## Slide 52: Wormhole flow control
Routing information only in head flit
Body flits follows head, tail flit flows body
If head flit blocks, rest of packet stops
Completely pipelined transmission
  For long messages, latency is almost entirely independent of network distance. Why?
Source
Destination
Flit Buffer
Flit Buffer
Flit Buffer
Flit Buffer
Flit Buffer
Flit Buffer
Busy Link
Busy Link
Busy Link
Head flit
Tail flit
Body flits (2 in this example)
Example:
Four-flit packet sent using wormhole flow control
H
T
B0
B1
B1
B0
H
T
Notes: wait for head

## Slide 53: Problem: head-of-line blocking
Flit Buffer
Flit Buffer
Flit Buffer
Flit Buffer
Flit Buffer
Flit Buffer
Idle link
(reserved)
Idle link
(reserved)
Idle link
(reserved)
Head flit for gray packet:
(blocked waiting for this busy link)
Flit Buffer
Flit Buffer
Flit Buffer
Head flit for blue packet:(route is free, but blocked behind gray packet in buffer)
Blue flits to be routed this way to their dest (this link is free)
Notes: two flows here
first describe gray

## Slide 54: Virtual channel flow control
Multiplex multiple operations over single physical channel
Divide switch’s input buffer into multiple buffers sharing a single physical channel
Reduces head-of-line blocking
Buf 0
Buf 1
Buf 0
Buf 1
Packet in flow 0: transmitting
Packet in flow 1: Blocked waiting for this link
See “Virtual Channel Flow Control,” [Dally ISCA 1990]

## Slide 55: Other uses of virtual channels
Deadlock avoidance
  Can be used to break cyclic dependency of resources
  Prevent cycles by ensuring requests and responses use different virtual channels
  “Escape” VCs: retain at least one virtual channel that uses deadlock-free routing
Prioritization of traffic classes
  Provide quality-of-service guarantees
  Some virtual channels have higher priority than others

## Slide 56: Current research topics
Energy efficiency of interconnections
  Interconnect can be energy intensive (~35% of total chip power in MIT RAW research processor)
  Bufferless networks
  Other techniques: turn on/off regions of network, use fast and slow networks
Prioritization and quality-of-service guarantees
  Prioritize packets to improve multi-processor performance (e.g., some applications may be more sensitive to network performance than others)
  Throttle endpoints (e.g., cores) based on network feedback
New/emerging technologies
  Die stacking (3D chips)
  Photonic networks-on-chip (use optical waveguides instead of wires)
  Reconfigurable devices (FPGAs): create custom interconnects tailored to application (see CMU projects: CONNECT, CoRAM, Shrinkwrap)

## Slide 57: Summary
The performance of the interconnection network in a modern multi-processor is critical to overall system performance
  Buses do not scale to many nodes
  Historically interconnect was off-chip network connecting sockets, boards, racks
  Today, all these issues apply to the design of on-chip networks
Network topologies differ in performance, cost, complexity tradeoffs
  e.g., crossbar, ring, mesh, torus, multi-stage network, fat tree, hypercube
Challenge: efficiently routing data through network
  Interconnect is a precious resource (communication is expensive!)
  Flit-based flow control: fine-grained flow control to make good use of available link bandwidth
  If interested, much more to learn about (not discussed in this class): ensuring quality-of-service, prioritization, reliability, deadlock, livelock, etc.
Notes: now think about last time when we went through many steps to issue a load instruction. We didn’t even talk about the network