## Slide 1: Heterogeneous Parallelism and Hardware Specialization
Lecture 21:

## Slide 2: Let’s begin this lecture by reminding you…
That we observed in assignment 1 that a well-optimized parallel implementation of a compute-bound application was about 44 times faster than single-threaded C code compiled with gcc -O3, running on the same processor

## Slide 3: You need to buy a new computer…

## Slide 4: You need to buy a computer system
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Processor A
4 cores
Each core has sequential performance P
Processor B
16 cores
Each core has sequential performance P/2
All other components of the system are equal.
Which do you pick?
Notes: everything else is equal

## Slide 5: Amdahl’s law revisited
f = fraction of program that is parallelizable
n = parallel processors
Assumptions:
Parallelizable work distributes perfectly onto n processors of equal capability
Notes: f/n because this fraction of work is parallelized perfectly onto n processors

## Slide 6: Rewrite Amdahl’s law in terms of resource limits
f = fraction of program that is parallelizable
n = total processing resources (e.g., transistors on a chip)
r = resources dedicated to each processing core,
 each of the n/r cores has sequential performance perf(r)
Two examples where n=16
rA = 4
rB = 1
Relative to processor with 1 unit of resources, n=1. Assume perf(1) = 1
[Hill and Marty 08] Amdahl’s Law in the Multicore Era
More general form of Amdahl’s Law in terms of f, n, r
Notes: NOTE: rewrite amdahl’s law in terms of resources N and not cores. (If r=1 then it’s the same as original version)
terms in the denominator are time. (amount of work / rate)
sequential: perf is perf(r)
parallel: perf is perf(r) * (n/r)
this slide assumes perf(1) = 1
\mathrm{speedup}(f,n,r) = \frac{1}{\frac{1-f}{\textrm{perf}(r)} + \frac{f}{\textrm{perf}(r)\cdot\frac{n}{r}}}

## Slide 7: Speedup (relative to n=1)
X-axis = r (chip with many small cores to left, fewer “fatter” cores to right)
Each line corresponds to a different workload
Each graph plots performance as resource allocation changes, but total chip resources resources kept the same (constant n per graph)
perf(r) modeled as
Up to 16 cores (n=16)
Up to 256 cores (n=256)
[Figure credit: Hill and Marty 08]
1
1
Notes: left fig: left, 16 cores, each /w performance=1. RIGHT, 1 core, performance=sqrt(16)
MOST LINES (LOOK AT RED), performance decreases as more powerful cores are used
BLUE LINE, performance ***increases*** as more powerful cores are used (left: 2, right 4)
But there’s a mixture of sequential work AND parallel WORK
THINK ABOUT GAMUT OF WORKLOADS (X=1, good for one but not the other)

## Slide 8: Asymmetric set of processing cores
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Example: n=16
One core: r = 4
Other 12 cores: r = 1
(of heterogeneous processor with n resources, relative to uniprocessor with one unit worth of resources, n=1)
one perf(r) processor + (n-r) perf(1)=1 processors
[Hill and Marty 08]
Notes: parallelize onto all the cores, assuming perfect speedup
perf r for the big core, perf 1 for the other n-r cores (so perf(r) + n - r)
\mathrm{speedup}(f,n,r) = \frac{1}{\frac{1-f}{\textrm{perf}(r)} + \frac{f}{\textrm{perf}(r) + (n-r)}}

## Slide 9: Speedup (relative to n=1)
X-axis for asymmetric architectures gives r for the single “fat” core (assume rest of cores are r = 1)
X-axis for symmetric architectures gives r for all cores (many small cores to left, few “fat” cores to right)
(chip from prev. slide)
[Source: Hill and Marty 08]
Notes: top graphs are what I showed you before
idea: sacrifice a bit on best max performance for better performance in the middle
ONE WAY TO THINK ABOUT IS, TAKE A LARGE SPEEDUP IN SERIAL SECTION FOR PERCENTAGE SLOWDOWN IN PARALLEL SECTION (run blue line well, and use rest of resources to keep red lines high up there… but a little loss)

## Slide 10: Heterogeneous processing
Observation: most “real world” applications have complex workload characteristics *
They have components that can be widely parallelized.
And components that are difficult to parallelize.
They have components that are amenable to wide SIMD execution.
And components that are not.
(divergent control flow)
They have components with predictable data access
And components with unpredictable access (but those accesses might cache well).
* You will likely make a similar observation during your projects
Idea: the most efficient processor is a heterogeneous mixture of resources (“use the most efficient tool for the job”)

## Slide 11: Example: Intel “Skylake" (2015)
(6th Generation Core i7 architecture)
4 CPU cores + graphics cores + media accelerators
CPU
core
CPU
core
CPU
core
CPU
core
Integrated
Gen9 GPU
graphics + media
Shared LLC
System
Agent
(display,
memory,
I/O
controllers)

## Slide 12: Example: Intel “Skylake" (2015)
CPU cores and graphics cores share same memory system
Also share LLC (L3 cache)
  Enables, low-latency, high-bandwidth communication between CPU and integrated GPU
Graphics cores cache coherent with CPU
(6th Generation Core i7 architecture)
CPU
core
CPU
core
CPU
core
CPU
core
Integrated
Gen9 GPU
graphics + media
Shared LLC
System
Agent
(display,
memory,
I/O)

## Slide 13: More heterogeneity: add discrete GPU
High-end discrete GPU
(AMD or NVIDIA)
PCIe x16 bus
DDR5 Memory
Keep discrete (power hungry) GPU turned off unless needed for graphics-intensive applications
Use integrated, low power graphics for basic graphics/window manager/UI
Memory controller
L3 cache (8 MB)
Ring interconnect
DDR3 Memory
CPU Core 0
CPU Core 3
…
Gen9 Graphics

## Slide 14: 15in Macbook Pro 2011 (two GPUs)
From ifixit.com teardown
AMD Radeon HD GPU
Quad-core Intel Core i7 CPU
(contains integrated GPU)
Notes: for kicks, lets go through some examples
this is my laptop, and like about every computing device there are two main processors in it the CPU.
And a GPU for 3D graphics

## Slide 15: Mobile heterogeneous processors
Apple A9 (2015)
> 2 B transistors
Dual Core 64 bit CPU
GPU PowerVR GT6700 (6 “core”) GPU
NVIDIA Tegra X1
Four ARM Cortex A57 CPU cores for applications
Four low performance (low power) ARM A53 CPU cores
One Maxwell SMM (256 “CUDA” cores)
A9 image credit Chipworks, obtained from
http://www.anandtech.com/show/9686/the-apple-iphone-6s-and-iphone-6s-plus-review/3
Notes: Why 4+4?

## Slide 16: Smartphone Processor
Apple A12, 2018
  6.9 billion transistors
Processors
  2 high-power CPUs
    7-wide issue
  4 low-power CPUs
    3-wide issue
  4-core GPU
  Neural engine
    for deep neural network evaluation
Specialized hardware
  Video encode/decode
  GPS
  Encryption/Decryption
  ...
Neural Engine
  Fixed sequence of arithmetic operations
  8-bit FP
  8-wide parallelism
  5 x 1012 ops/second

## Slide 17: Supercomputers use heterogeneous processing
Los Alamos National Laboratory: Roadrunner
Fastest US supercomputer in 2008, first to break Petaflop barrier: 1.7 PFLOPS
Unique at the time due to use of two types of processing elements
(IBM’s Cell processor served as “accelerator” to achieve desired compute density)
  6,480 AMD Opteron dual-core CPUs (12,960 cores)
  12,970 IBM Cell Processors (1 CPU + 8 accelerator cores per Cell = 116,640 cores)
  2.4 MWatt (about 2,400 average US homes)
Notes: first
data-parallel programming for CELL (proprietary)
OpenMP, on Opterons
MPI across chips

## Slide 18: GPU-accelerated supercomputing
Oak Ridge Summit
  World’s most powerful computer
Each Node
  2 IBM 22-core POWER9 processors
  6 nVidia Graphics Processing Units
  608 GB DRAM
  1600 GB Flash
Overall
  13MW water cooled
  $325 M for two machines
* Source: NPR
Local Network
Node 1
Node 2
Node 4,608
• • •
CPU
GPU
GPU
GPU
CPU
GPU
GPU
GPU
CPU
GPU
GPU
GPU
CPU
GPU
GPU
GPU
CPU
GPU
GPU
GPU
CPU
GPU
GPU
GPU

## Slide 19: Intel Xeon Phi (Knights Landing)
72 “simple” x86 cores (1.1 Ghz, derived from Intel Atom)
16-wide vector instructions (AVX-512), four threads per core
Targeted as an accelerator for supercomputing applications

## Slide 20: Heterogeneous architectures for supercomputing
Source: Top500.org Fall 2018 rankings
Xeon Phi
NVIDIA GPU
NVIDIA GPU
NVIDIA GPU
NVIDIA GPU
NVIDIA GPU
Xeon Phi
Notes: Tianhe-2 is 208 MFlops/Watt

## Slide 21: Green500: most energy efficient supercomputers
Source: Green500 Fall 2018 rankings
Efficiency metric: MFLOPS per Watt

## Slide 22: Research: ARM + GPU Supercomputer
Observation: the heavy lifting in supercomputing applications is the data-parallel part of workload
  Less need for “beefy” sequential performance cores
Idea: build supercomputer out of power-efficient building blocks
  ARM CPUs (for control/scheduling) + GPU cores (primary compute engine)
Project underway at Barcelona Supercomputing Center
  www.montblanc-project.eu

## Slide 23: Energy-constrained computing
Supercomputers are energy constrained
  Due to shear scale
  Overall cost to operate (power for machine and for cooling)
Datacenters are energy constrained
  Reduce cost of cooling
  Reduce physical space requirements
Mobile devices are energy constrained
  Limited battery life
  Heat dissipation

## Slide 24: Limits on chip power consumption
General mobile processing rule: the longer a task runs the less power it can use
  Processor’s power consumption is limited by heat generated (efficiency is required for more than just maximizing battery life)
Power
Time
Electrical limit: max power that can be supplied to chip
Die temp: (junction temp -- Tj): chip becomes unreliable above this temp (chip can run at high power for short period of time until chip heats to Tj)
Case temp: mobile device gets too hot for user to comfortably hold
(chip is at suitable operating temp, but heat is dissipating into case)
Battery life: chip and case are cool, but want to reduce power consumption to sustain long battery life for given task
Slide credit: adopted from original slide from M. Shebanow: HPG 2013 keynote
iPhone 6 battery: 7 watt-hours
9.7in iPad Pro battery: 28 watt-hours
15in Macbook Pro: 99 watt-hours
Notes: current I = Q/t (change per unit time)
Energy is spent moving charge through a voltage difference
power P = energy/t = (QV)/t = (Q/t)V = IV = (I^2)R (applying Olm’s Law: V=IR)
Since P=IV, fixing power and increasing voltage reduces current, which results lost energy from resistance

## Slide 25: Efficiency benefits of compute specialization
Rules of thumb: compared to high-quality C code on CPU...
Throughput-maximized processor architectures: e.g., GPU cores
  Approximately 10x improvement in perf / watt
  Assuming code maps well to wide data-parallel execution and is compute bound
Fixed-function ASIC (“application-specific integrated circuit”)
  Can approach 100-1000x or greater improvement in perf/watt
  Assuming code is compute bound and
  and is not floating-point math
[Source: Chung et al. 2010 , Dally 08]
[Figure credit Eric Chung]

## Slide 26: Hardware specialization increases efficiency
[Chung et al. MICRO 2010]
lg2(N) (data set size)
FPGA
GPUs
FPGA
GPUs
lg2(N) (data set size)
ASIC delivers same performance as one CPU core with ~ 1/1000th the chip area.
GPU cores: ~ 5-7 times more area efficient than CPU cores.
ASIC delivers same performance as one CPU core with only ~ 1/100th the power.

## Slide 27: Benefits of increasing efficiency
Run faster for a fixed period of time
  Run at higher clock, use more cores (reduce latency of critical task)
  Do more at once
Run at a fixed level of performance for longer
  e.g., video playback
  Achieve “always-on” functionality that was previously impossible
Moto X:
Always listening for “ok, google now”
Device contains ASIC for detecting this audio pattern.
iPhone:
Siri activated by button press or holding phone up to ear
Google Glass: ~40 min recording per charge (nowhere near “always on”)
Notes: fundamentally different interaction with the device
Just not possible

## Slide 28: Example: iPad Air (2013)
DRAM
Flash memory
Dual-core 64-bit ARM CPU
Imagination
PowerVR
GPU
Video
Encode/Decode
Image
Processor
4MB L3
Core
Core
Motion co-processor
(accelerometer, gyro, compass, etc.)
Touchscreen controllers
Image Credit: ifixit.com
Apple A7 Processor

## Slide 29: Original iPhone touchscreen controller
From US Patent Application 2006/0097991
Separate digital signal processor to interpret raw signal from capacitive touch sensor (do not burden main CPU)

## Slide 30: Modern computing: efficiency often matters more than in the past, not less
Steve Jobs’ “Thoughts on Flash”, 2010
http://www.apple.com/hotnews/thoughts-on-flash/
(Justification for why Apple won’t support Adobe Flash)

## Slide 31: Example: image processing on a Nikon D7000
Process 16 MPixel RAW data from sensor to obtain JPG image:
On camera: ~ 1/6 sec per image
Adobe Lightroom a quad-core Macbook Pro laptop: 1-2 sec per image
This is a older camera: much, much faster image processing performance on a modern smart phone (burst mode)

## Slide 32: Qualcomm Hexagon Digital Signal Processor
Originally used for audio/LTE support on Qualcomm SoCs
Multi-threaded, VLIW DSP
Third major programmable unit on Qualcomm SoCs
  Multi-core CPU
  Multi-core GPU (Adreno)
  Hexagon DSP

## Slide 33: Up next? application programmable image signal processors
All modern systems have fixed-function support for common image processing tasks: image/video encode/decode, sensor to image conversion, etc.
Computational photography: use of advanced algorithms to make better photographs and videos
  Large space of (rapidly evolving techniques)
High Dynamic Range (HDR) and low light enhancement
Automatic panoramas
Remove camera shake

## Slide 34: Anton supercomputer
Supercomputer highly specialized for molecular dynamics
  Simulates time evolution of proteins
ASIC for computing particle-particle interactions (512 of them in machine)
Throughput-oriented subsystem for efficient fast-Fourier transforms
  Custom, low-latency communication network designed for communication patterns of N-body simulations
[Developed by DE Shaw Research]

## Slide 35: GPUs are heterogeneous multi-core processors
GPU
GPU
Memory
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Cache
SIMD
Exec
Texture
Texture
Texture
Texture
Clip/Cull
Rasterize
Clip/Cull
Rasterize
Clip/Cull
Rasterize
Clip/Cull
Rasterize
Tessellate
Tessellate
Tessellate
Tessellate
Zbuffer /
Blend
Zbuffer /
Blend
Zbuffer /
Blend
Zbuffer /
Blend
Zbuffer /
Blend
Zbuffer /
Blend
Scheduler / Work Distributor
Compute resources your CUDA programs used in assignment 2
Graphics-specific, fixed-function compute resources

## Slide 36
Rasterization:
Determining what pixels a triangle overlaps
Example graphics tasks performed in fixed-function HW
Texture mapping:
Warping/filtering images to apply detail to surfaces
Geometric tessellation:
computing fine-scale geometry from coarse geometry

## Slide 37: FPGAs (Field Programmable Gate Arrays)
Middle ground between an ASIC and a processor
FPGA chip provides array of logic blocks, connected by interconnect
Programmer-defined logic implemented directly by FGPA
Programmable lookup table (LUT)
Flip flop (a register)
Image credit: Bai et al. 2014

## Slide 38: Project Catapult
Microsoft Research investigation of use of FPGAs to accelerate datacenter workloads
Demonstrated offload of part of Bing Search’s document ranking logic
Now widely used to accelerate DNNs across Microsoft services
1U server (Dual socket CPU + FPGA connected via PCIe bus)
[Putnam et al. ISCA 2014]
FPGA board

## Slide 39: Summary: choosing the right tool for the job
Energy-optimized CPU
Throughput-oriented
processor (GPU)
~10X more efficient
Credit Pat Hanrahan for this taxonomy
ASIC
~100-1000X
more efficient
Video encode/decode,
Audio playback,
Camera RAW processing,
neural nets (future?)
Programmable DSP
FPGA/Future
reconfigurable logic
~100X???
(jury still out)
Easiest to program
Difficult to program
(making it easier is active area of research)
Not programmable +
costs 10-100’s millions of dollars to design / verify / create

## Slide 40: Challenges of heterogeneous designs

## Slide 41: Challenges of heterogeneity
So far in this course:
  Homogeneous system: every processor can be used for every task
  To get best speedup vs. sequential execution, “keep all processors busy all the time” (this is hard to achieve)
Heterogeneous system: use preferred processor for each task
  Challenge for system designer: what is the right mixture of resources to meet performance, cost, and energy goals?
  Too few throughput-oriented resources (lower peak performance/efficiency for parallel workloads -- should have used resources for more throughput cores)
  Too few sequential processing resources (get bitten by Amdahl’s Law)
  How much chip area should be dedicated to a specific function, like video?
    (these resources are taken away from general-purpose processing)
Implication: increased pressure to understand workloads accurately at chip design time

## Slide 42: Pitfalls of heterogeneous designs
Say 10% of the workload is rasterization
Let’s say you under-provision the fixed-function rasterization unit on GPU:
Chose to dedicate 1% of chip area used for rasterizer, really needed 20% more throughput: 1.2% of chip area
Problem: rasterization is now the bottleneck, so the expensive programmable processors (99% of chip) are idle waiting on rasterization. 99% of the chip runs at 80% efficiency!
 Tendency is to be conservative, and over-provision fixed-function components (diminishing their advantage)
[Molnar 2010]
Notes: 1% of the chip is rasterizer
it’s a pipeline

## Slide 43: Challenges of heterogeneity
Heterogeneous system: preferred processor for each task
  Challenge for hardware designer: what is the right mixture of resources?
  Too few throughput oriented resources (lower peak throughput for parallel workloads)
  Too few sequential processing resources (limited by sequential part of workload)
  How much chip area should be dedicated to a specific function, like video? (these resources are taken away from general-purpose processing)
  Work balance must be anticipated at chip design time  System cannot adapt to changes in usage over time, new algorithms, etc.
Challenge to software developer: how to map programs onto a heterogeneous collection of resources?
  Challenge: “Pick the right tool for the job”: design algorithms that decompose well into components that each map well to different processing components of the machine
  The scheduling problem is more complex on a heterogeneous system
  Available mixture of resources can dictate choice of algorithm
  Software portability & maintenance nightmare (we’ll revisit this next class)

## Slide 44: Reducing energy consumption idea 1: use specialized processing Reducing energy consumption idea 2: move less data

## Slide 45: Data movement has high energy cost
Rule of thumb in mobile system design: always seek to reduce amount of data transferred from memory
  Earlier in class we discussed minimizing communication to reduce stalls (poor performance). Now, we wish to reduce communication to reduce energy consumption
“Ballpark” numbers
  Integer op: ~ 1 pJ *
  Floating point op: ~20 pJ *
  Reading 64 bits from small local SRAM (1mm away on chip): ~ 26 pJ
  Reading 64 bits from low power mobile DRAM (LPDDR): ~1200 pJ
Implications
  Reading 10 GB/sec from memory: ~1.6 watts
  Entire power budget for mobile GPU: ~1 watt (remember phone is also running CPU, display, radios, etc.)
  iPhone 6 battery: ~7 watt-hours (compare: Macbook Pro laptop: 99 watt-hour battery)
  Exploiting locality matters!!!
* Cost to just perform the logical operation, not counting overhead of instruction decode, load data from registers, etc.
[Sources: Bill Dally (NVIDIA), Tom Olson (ARM)]
Suggests that recomputing values, rather than storing and reloading them, is a better answer when optimizing code for energy efficiency!
Notes: exploit locality
compression hardware

## Slide 46: Three trends in energy-optimized computing
Compute less!
  Computing costs energy: parallel algorithms that do more work than sequential counterparts may not be desirable even if they run faster
  …But performance matters too, because processors burn energy whenever they are turned on (“static power”)
Specialize compute units:
  Heterogeneous processors: CPU-like cores + throughput-optimized cores (GPU-like cores)
  Fixed-function units: audio processing, “movement sensor processing” video decode/encode, image processing/computer vision?
  Specialized instructions: expanding set of AVX vector instructions, new instructions for accelerating AES encryption (AES-NI)
  Programmable soft logic: FPGAs
Reduce bandwidth requirements
  Exploit locality (restructure algorithms to reuse on-chip data as much as possible)
  Aggressive use of compression: perform extra computation to compress application data before transferring to memory (likely to see fixed-function HW to reduce overhead of general data compression/decompression)

## Slide 47: Summary
Heterogeneous parallel processing: use a mixture of computing resources that each fit with mixture of needs of target applications
  Latency-optimized sequential cores, throughput-optimized parallel cores, domain-specialized fixed-function processors
  Examples exist throughout modern computing: mobile processors, servers, supercomputers
Traditional rule of thumb in “good system design” is to design simple, general-purpose components
  This is not the case with emerging processing systems (optimized for perf/watt)
  Today: want collection of components that meet perf requirement AND minimize energy use
Challenge of using these resources effectively is pushed up to the programmer
  Current CS research challenge: how to write efficient, portable programs for emerging heterogeneous architectures?