## Slide 1: Lecture 12: I/O Introduction: Storage Devices, Metrics, & Productivity
Professor David A. Patterson
Computer Science 252
Spring 1998

## Slide 2: Motivation: Who Cares About I/O?
CPU Performance: 60% per year
I/O system performance limited by mechanical delays (disk I/O)
  < 10% per year (IO per sec or MB per sec)
Amdahl's Law: system speed-up limited by the slowest part!
  10% IO & 10x CPU => 5x Performance (lose 50%)
  10% IO & 100x CPU => 10x Performance (lose 90%)
I/O bottleneck:
  Diminishing fraction of time in CPU
  Diminishing value of faster CPUs
Notes: Ancestor of Java had no I/O
CPU vs. Peripheral
Primary vs. Secondary
What maks portable, PDA exciting?

## Slide 3: Storage System Issues: 1.5 weeks
Historical Context of Storage I/O
Secondary and Tertiary Storage Devices
Storage I/O Performance Measures
Processor Interface Issues
A Little Queuing Theory
Redundant Arrarys of Inexpensive Disks (RAID)
I/O Buses
ABCs of UNIX File Systems
I/O Benchmarks
Comparing UNIX File System Performance

## Slide 4: I/O Systems
Processor
Cache
Memory - I/O Bus
Main
Memory
I/O
Controller
Disk
Disk
I/O
Controller
I/O
Controller
Graphics
Network
interrupts

## Slide 5: Technology Trends
Disk Capacity
now doubles every
18 months; before
1990 every 36 motnhs
• Today: Processing Power Doubles Every 18 months
• Today: Memory Size Doubles Every 18 months(4X/3yr)
• Today: Disk Capacity Doubles Every 18 months
• Disk Positioning Rate (Seek + Rotate) Doubles Every Ten Years!
The I/O
GAP

## Slide 6: Storage Technology Drivers
Driven by the prevailing computing paradigm
  1950s: migration from batch to on-line processing
  1990s: migration to ubiquitous computing
    computers in phones, books, cars, video cameras, …
    nationwide fiber optical network with wireless tails
Effects on storage industry:
  Embedded storage
    smaller, cheaper, more reliable, lower power
  Data utilities
    high capacity, hierarchically managed storage

## Slide 7: Historical Perspective
1956 IBM Ramac — early 1970s Winchester
  Developed for mainframe computers, proprietary interfaces
  Steady shrink in form factor: 27 in. to 14 in.
1970s developments
  5.25 inch floppy disk formfactor (microcode into mainframe)
  early emergence of industry standard disk interfaces
    ST506, SASI, SMD, ESDI
Early 1980s
  PCs and first generation workstations
Mid 1980s
  Client/server computing
  Centralized storage on file server
    accelerates disk downsizing: 8 inch to 5.25 inch
  Mass market disk drives become a reality
    industry standards: SCSI, IPI, IDE
    5.25 inch drives for standalone PCs, End of proprietary interfaces

## Slide 8: Disk History
Data
density
Mbit/sq. in.
Capacity of
Unit Shown
Megabytes
1973:
1. 7 Mbit/sq. in
140 MBytes
1979:
7. 7 Mbit/sq. in
2,300 MBytes
source: New York Times, 2/23/98, page C3, “Makers of disk drives crowd even mroe data into even smaller spaces”

## Slide 9: Historical Perspective
Late 1980s/Early 1990s:
  Laptops, notebooks, (palmtops)
  3.5 inch, 2.5 inch, (1.8 inch formfactors)
  Formfactor plus capacity drives market, not so much performance
    Recently Bandwidth improving at 40%/ year
  Challenged by DRAM, flash RAM in PCMCIA cards
    still expensive, Intel promises but doesn’t deliver
    unattractive MBytes per cubic inch
  Optical disk fails on performace (e.g., NEXT) but finds niche (CD ROM)

## Slide 10: Disk History
1989:
63 Mbit/sq. in
60,000 MBytes
1997:
1450 Mbit/sq. in
2300 MBytes
source: New York Times, 2/23/98, page C3, “Makers of disk drives crowd even mroe data into even smaller spaces”
1997:
3090 Mbit/sq. in
8100 MBytes

## Slide 11: MBits per square inch: DRAM as % of Disk over time
source: New York Times, 2/23/98, page C3, “Makers of disk drives crowd even mroe data into even smaller spaces”
470 v. 3000 Mb/si
9 v. 22 Mb/si
0.2 v. 1.7 Mb/si

## Slide 12: Alternative Data Storage Technologies: Early 1990s
Cap BPI TPI BPI*TPI Data Xfer Access
Technology (MB) (Million) (KByte/s) Time
Conventional Tape:
Cartridge (.25") 150 12000 104 1.2 92 minutes
IBM 3490 (.5") 800 22860 38 0.9 3000 seconds
Helical Scan Tape:
Video (8mm) 4600 43200 1638 71 492 45 secs
DAT (4mm) 1300 61000 1870 114 183 20 secs
Magnetic & Optical Disk:
Hard Disk (5.25") 1200 33528 1880 63 3000 18 ms
IBM 3390 (10.5") 3800 27940 2235 62 4250 20 ms
Sony MO (5.25") 640 24130 18796 454 88 100 ms

## Slide 13: Devices: Magnetic Disks
Sector
Track
Cylinder
Head
Platter
Purpose:
  Long-term, nonvolatile storage
  Large, inexpensive, slow level in the storage hierarchy
Characteristics:
  Seek Time (~8 ms avg)
    positional latency
    rotational latency
Transfer rate
  About a sector per ms (5-15 MB/s)
  Blocks
Capacity
  Gigabytes
  Quadruples every 3 years (aerodynamics)
7200 RPM = 120 RPS => 8 ms per rev
ave rot. latency = 4 ms
128 sectors per track => 0.25 ms per sector
1 KB per sector => 16 MB / s
Response time
= Queue + Controller + Seek + Rot + Xfer
Service time

## Slide 14: Disk Device Terminology
Disk Latency = Queuing Time + Controller time +
Seek Time + Rotation Time + Xfer Time
Order of magnitude times for 4K byte transfers:
Seek: 8 ms or less
Rotate: 4.2 ms @ 7200 rpm
Xfer: 1 ms @ 7200 rpm

## Slide 15: Advantages of Small Formfactor Disk Drives
Low cost/MB
High MB/volume
High MB/watt
Low cost/Actuator
Cost and Environmental Efficiencies

## Slide 16: CS 252 Administrivia
Wed March 4 Quiz 1
  Pizza at LaVal’s 8:30 – 10PM
Email URL of initial project home page to TA?
  can share some knowledge gained with other projects
  allow faculty, TA to make suggestoins
  final “report” will be a URL
  Limit access to cs.berkeley for now
Upcoming events in CS 252
13-Mar Fri I/O 2: Queuing Theory and Busses
18-Mar Wed I/O 3: Tertiary Storage & Network Intro
20-Mar Fri Networks 2: Interface, Switches, Routing
23-Mar to 27-Mar Spring Break

## Slide 17: Tape vs. Disk
• Longitudinal tape uses same technology as
hard disk; tracks its density improvements
Disk head flies above surface, tape head lies on surface
Disk fixed, tape removable
• Inherent cost-performance based on geometries:
fixed rotating platters with gaps
(random access, limited area, 1 media / reader)
vs.
removable long strips wound on spool
(sequential access, "unlimited" length, multiple / reader)
• New technology trend:
Helical Scan (VCR, Camcoder, DAT)
Spins head at angle to tape to improve density

## Slide 18: Current Drawbacks to Tape
Tape wear out:
  Helical 100s of passes to 1000s for longitudinal
Head wear out:
  2000 hours for helical
Both must be accounted for in economic / reliability model
Long rewind, eject, load, spin-up times; not inherent, just no need in marketplace (so far)
Designed for archival

## Slide 19: Automated Cartridge System
STC 4400
6000 x 0.8 GB 3490 tapes = 5 TBytes in 1992 $500,000 O.E.M. Price
6000 x 10 GB D3 tapes = 60 TBytes in 1998
Library of Congress: all information in the world; in 1992, ASCII of all books = 30 TB
8 feet
10 feet

## Slide 20: Library vs. Storage
Getting books today as quaint as the way I learned to program
  punch cards, batch processing
  wander thru shelves, anticipatory purchasing
Cost $1 per book to check out
$30 for a catalogue entry
30% of all books never checked out
Write only journals?
Digital library can transform campuses
Will have lecture on getting electronic information

## Slide 21: Relative Cost of Storage Technology—Late 1995/Early 1996
Magnetic Disks
5.25” 9.1 GB $2129 $0.23/MB $1985 $0.22/MB
3.5” 4.3 GB $1199 $0.27/MB $999 $0.23/MB
2.5” 514 MB $299 $0.58/MB 1.1 GB $345 $0.33/MB
Optical Disks
5.25” 4.6 GB $1695+199 $0.41/MB $1499+189 $0.39/MB
PCMCIA Cards
Static RAM 4.0 MB $700 $175/MB
Flash RAM 40.0 MB $1300 $32/MB
175 MB $3600 $20.50/MB

## Slide 22: Lecture Outline
Historical Context of Storage I/O
Secondary and Tertiary Storage Devices
Storage I/O Performance Measures
Processor Interface Issues

## Slide 23: Disk I/O Performance
Response time = Queue + Device Service time
100%
Response
Time (ms)
Throughput
(% total BW)
0
100
200
300
0%
Proc
Queue
IOC
Device
Metrics:
Response Time
Throughput

## Slide 24: Response Time vs. Productivity
Interactive environments:
Each interaction or transaction has 3 parts:
  Entry Time: time for user to enter command
  System Response Time: time between user entry & system replies
  Think Time: Time from response until user begins next command
1st transaction
  2nd transaction
What happens to transaction time as shrink system response time from 1.0 sec to 0.3 sec?
  With Keyboard: 4.0 sec entry, 9.4 sec think time
  With Graphics: 0.25 sec entry, 1.6 sec think time

## Slide 25: Response Time & Productivity
0.7sec off response saves 4.9 sec (34%) and 2.0 sec (70%) total time per transaction => greater productivity
Another study: everyone gets more done with faster response, but novice with fast response = expert with slow

## Slide 26: Disk Time Example
Disk Parameters:
  Transfer size is 8K bytes
  Advertised average seek is 12 ms
  Disk spins at 7200 RPM
  Transfer rate is 4 MB/sec
Controller overhead is 2 ms
Assume that disk is idle so no queuing delay
What is Average Disk Access Time for a Sector?
  Ave seek + ave rot delay + transfer time + controller overhead
  12 ms + 0.5/(7200 RPM/60) + 8 KB/4 MB/s + 2 ms
  12 + 4.15 + 2 + 2 = 20 ms
Advertised seek time assumes no locality: typically 1/4 to 1/3 advertised seek time: 20 ms => 12 ms

## Slide 27: Lecture Outline
Historical Context of Storage I/O
Secondary and Tertiary Storage Devices
Storage I/O Performance Measures
Processor Interface Issues
Redundant Arrarys of Inexpensive Disks (RAID)

## Slide 28: Processor Interface Issues
Processor interface
  Interrupts
  Memory mapped I/O
I/O Control Structures
  Polling
  Interrupts
  DMA
  I/O Controllers
  I/O Processors
Capacity, Access Time, Bandwidth
Interconnections
  Busses

## Slide 29: I/O Interface
Independent I/O Bus
CPU
Interface
Interface
Peripheral
Peripheral
Memory
memory
bus
Seperate I/O instructions (in,out)
CPU
Interface
Interface
Peripheral
Peripheral
Memory
Lines distinguish between
I/O and memory transfers
common memory
& I/O bus
VME bus
Multibus-II
Nubus
40 Mbytes/sec
optimistically
10 MIP processor
completely
saturates the bus!

## Slide 30: Memory Mapped I/O
Single Memory & I/O Bus
No Separate I/O Instructions
CPU
Interface
Interface
Peripheral
Peripheral
Memory
ROM
RAM
I/O
$
CPU
L2 $
Memory Bus
Memory
Bus Adaptor
I/O bus

## Slide 31: Programmed I/O (Polling)
CPU
IOC
device
Memory
Is the
data
ready?
read
data
store
data
yes
no
done?
no
yes
busy wait loop
not an efficient
way to use the CPU
unless the device
is very fast!
but checks for I/O
completion can be
dispersed among
computationally
intensive code

## Slide 32: Interrupt Driven Data Transfer
CPU
IOC
device
Memory
add
sub
and
or
nop
read
store
...
rti
memory
user
program
(1) I/O
interrupt
(2) save PC
(3) interrupt
service addr
interrupt
service
routine
(4)
Device xfer rate = 10 MBytes/sec => 0 .1 x 10 sec/byte => 0.1 µsec/byte
=> 1000 bytes = 100 µsec
1000 transfers x 100 µsecs = 100 ms = 0.1 CPU seconds
-6
User program progress only halted during
actual transfer
1000 transfers at 1 ms each:
1000 interrupts @ 2 µsec per interrupt
1000 interrupt service @ 98 µsec each = 0.1 CPU seconds
Still far from device transfer rate! 1/2 in interrupt overhead

## Slide 33: Direct Memory Access
CPU
IOC
device
Memory
DMAC
Time to do 1000 xfers at 1 msec each:
1 DMA set-up sequence @ 50 µsec
1 interrupt @ 2 µsec
1 interrupt service sequence @ 48 µsec
.0001 second of CPU time
CPU sends a starting address,
direction, and length count to
DMAC. Then issues "start".
DMAC provides handshake signals for Peripheral
Controller, and Memory Addresses and handshake
signals for Memory.
0
ROM
RAM
Peripherals
DMAC
n
Memory
Mapped I/O

## Slide 34: Input/Output Processors
CPU
IOP
Mem
D1
D2
Dn
. . .
main memory
bus
I/O
bus
CPU
IOP
issues instruction to IOP
interrupts when done
(1)
memory
(2)
(3)
(4)
Device to/from memory
transfers are controlled
by the IOP directly.
IOP steals memory cycles.
OP Device Address
target device
where cmnds are
looks in memory for commands
OP Addr Cnt Other
what
to do
where
to put
data
how
much
special
requests

## Slide 35: Relationship to Processor Architecture
I/O instructions have largely disappeared
Interrupt vectors have been replaced by jump tables PC <- M [ IVA + interrupt number ] PC <- IVA + interrupt number
Interrupts:
  Stack replaced by shadow registers
  Handler saves registers and re-enables higher priority int's
  Interrupt types reduced in number; handler must query interrupt controller

## Slide 36: Relationship to Processor Architecture
Caches required for processor performance cause problems for I/O
  Flushing is expensive, I/O polutes cache
  Solution is borrowed from shared memory multiprocessors "snooping"
Virtual memory frustrates DMA
Load/store architecture at odds with atomic operations
  load locked, store conditional
Stateful processors hard to context switch

## Slide 37: Summary
Disk industry growing rapidly, improves:
  bandwidth 40%/yr ,
  areal density 60%/year, $/MB faster?
queue + controller + seek + rotate + transfer
Advertised average seek time benchmark much greater than average seek time in practice
Response time vs. Bandwidth tradeoffs
Value of faster response time:
  0.7sec off response saves 4.9 sec and 2.0 sec (70%) total time per transaction => greater productivity
  everyone gets more done with faster response, but novice with fast response = expert with slow
Processor Interface: today peripheral processors, DMA, I/O bus, interrupts

## Slide 38: Summary: Relationship to Processor Architecture
I/O instructions have disappeared
Interrupt vectors have been replaced by jump tables
Interrupt stack replaced by shadow registers
Interrupt types reduced in number
Caches required for processor performance cause problems for I/O
Virtual memory frustrates DMA
Load/store architecture at odds with atomic operations
Stateful processors hard to context switch

## Slide 39: Summary: Storage System Issues
Historical Context of Storage I/O
Secondary and Tertiary Storage Devices
Storage I/O Performance Measures
Processor Interface Issues
A Little Queuing Theory
Redundant Arrarys of Inexpensive Disks (RAID)
I/O Buses
ABCs of UNIX File Systems
I/O Benchmarks
Comparing UNIX File System Performance