## Slide 1: Lecture 13: I/O: A Little Queuing Theory, RAID
Professor David A. Patterson
Computer Science 252
Spring 1998

## Slide 2: Review: Disk Device Terminology
Disk Latency = Queuing Time + Seek Time + Rotation Time + Xfer Time
Order of magnitude times for 4K byte transfers:
Seek: 12 ms or less
Rotate: 4.2 ms @ 7200 rpm (8.3 ms @ 3600 rpm )
Xfer: 1 ms @ 7200 rpm (2 ms @ 3600 rpm)

## Slide 3: Review
Disk industry growing rapidly, improves:
  bandwidth 40%/yr ,
  areal density 60%/year, $/MB faster?
queue + controller + seek + rotate + transfer
Advertised average seek time benchmark much greater than average seek time in practice
Response time vs. Bandwidth tradeoffs
Value of faster response time:
  0.7sec off response saves 4.9 sec and 2.0 sec (70%) total time per transaction => greater productivity
  everyone gets more done with faster response, but novice with fast response = expert with slow
Processor Interface: today peripheral processors, DMA, I/O bus, interrupts

## Slide 4: Review: Storage System Issues
Historical Context of Storage I/O
Secondary and Tertiary Storage Devices
Storage I/O Performance Measures
Processor Interface Issues
A Little Queuing Theory
Redundant Arrarys of Inexpensive Disks (RAID)
I/O Buses
ABCs of UNIX File Systems
I/O Benchmarks
Comparing UNIX File System Performance

## Slide 5: Review: Disk I/O Performance
Response time = Queue + Device Service time
100%
Response
Time (ms)
Throughput
(% total BW)
0
100
200
300
0%
Proc
Queue
IOC
Device
Metrics:
Response Time
Throughput

## Slide 6: Introduction to Queueing Theory
More interested in long term, steady state than in startup => Arrivals = Departures
Little’s Law: Mean number tasks in system = arrival rate x mean reponse time
  Observed by many, Little was first to prove
Applies to any system in equilibrium, as long as nothing in black box is creating or destroying tasks
Arrivals
Departures
Notes: Old and New Testament by Kleirock
Regret skipping as grad student

## Slide 7: A Little Queuing Theory: Notation
Queuing models assume state of equilibrium: input rate = output rate
Notation:
r average number of arriving customers/second Tser average time to service a customer (tradtionally µ = 1/ Tser ) u server utilization (0..1): u = r x Tser (or u = r / Tser ) Tq average time/customer in queue Tsys average time/customer in system: Tsys = Tq + Tser Lq average length of queue: Lq = r x Tq Lsys average length of system: Lsys = r x Tsys
Little’s Law: Lengthsystem = rate x Timesystem (Mean number customers = arrival rate x mean service time)
Proc
IOC
Device
Queue
server
System
Notes: Sometimes Queue called waiting line, System called Queue

## Slide 8: A Little Queuing Theory
Service time completions vs. waiting time for a busy server: randomly arriving event joins a queue of arbitrary length when server is busy, otherwise serviced immediately
  Unlimited length queues key simplification
A single server queue: combination of a servicing facility that accomodates 1 customer at a time (server) + waiting area (queue): together called a system
Server spends a variable amount of time with customers; how do you characterize variability?
  Distribution of a random variable: histogram? curve?
Proc
IOC
Device
Queue
server
System
Notes: Characterize randomness
Request are random from processor
Nothing in queue gets immediate service

## Slide 9: A Little Queuing Theory
Server spends a variable amount of time with customers
  Weighted mean m1 = (f1 x T1 + f2 x T2 +...+ fn x Tn)/F (F=f1 + f2...)
  variance = (f1 x T12 + f2 x T22 +...+ fn x Tn2)/F – m12
    Must keep track of unit of measure (100 ms2 vs. 0.1 s2 )
  Squared coefficient of variance: C = variance/m12
    Unitless measure (100 ms2 vs. 0.1 s2)
Exponential distribution C = 1 : most short relative to average, few others long; 90% < 2.3 x average, 63% < average
Hypoexponential distribution C < 1 : most close to average, C=0.5 => 90% < 2.0 x average, only 57% < average
Hyperexponential distribution C > 1 : further from average C=2.0 => 90% < 2.8 x average, 69% < average
Proc
IOC
Device
Queue
server
System
Avg.

## Slide 10: A Little Queuing Theory: Variable Service Time
Server spends a variable amount of time with customers
  Weighted mean m1 = (f1xT1 + f2xT2 +...+ fnXTn)/F (F=f1+f2+...)
  Squared coefficient of variance C
Disk response times C ­ 1.5 (majority seeks < average)
Yet usually pick C = 1.0 for simplicity
Another useful value is average time must wait for server to complete task: m1(z)
  Not just 1/2 x m1 because doesn’t capture variance
  Can derive m1(z) = 1/2 x m1 x (1 + C)
  No variance => C= 0 => m1(z) = 1/2 x m1
Proc
IOC
Device
Queue
server
System
Notes: Power of queing theory
Would guess variance is 1/2 average
Gives a more realistic model
How well does it work; reserach papers WHY it works so well

## Slide 11: A Little Queuing Theory: Average Wait Time
Calculating average wait time in queue Tq
  If something at server, it takes to complete on average m1(z)
  Chance server is busy = u; average delay is u x m1(z)
  All customers in line must complete; each avg Tser
  Tq = u x m1(z) + Lq x Ts er= 1/2 x u x Tser x (1 + C) + Lq x Ts er Tq = 1/2 x u x Ts er x (1 + C) + r x Tq x Ts er Tq = 1/2 x u x Ts er x (1 + C) + u x Tq Tq x (1 – u) = Ts er x u x (1 + C) /2 Tq = Ts er x u x (1 + C) / (2 x (1 – u))
Notation:
r average number of arriving customers/second Tser average time to service a customer u server utilization (0..1): u = r x Tser Tq average time/customer in queue Lq average length of queue:Lq= r x Tq

## Slide 12: A Little Queuing Theory: M/G/1 and M/M/1
Assumptions so far:
  System in equilibrium
  Time between two successive arrivals in line are random
  Server can start on next customer immediately after prior finishes
  No limit to the queue: works First-In-First-Out
  Afterward, all customers in line must complete; each avg Tser
Described “memoryless” or Markovian request arrival (M for C=1 exponentially random), General service distribution (no restrictions), 1 server: M/G/1 queue
When Service times have C = 1, M/M/1 queue Tq = Tser x u x (1 + C) /(2 x (1 – u)) = Tser x u / (1 – u)
Tser average time to service a customer u server utilization (0..1): u = r x Tser Tq average time/customer in queue

## Slide 13: A Little Queuing Theory: An Example
processor sends 10 x 8KB disk I/Os per second, requests & service exponentially distrib., avg. disk service = 20 ms
On average, how utilized is the disk?
  What is the number of requests in the queue?
  What is the average time spent in the queue?
  What is the average response time for a disk request?
Notation:
r average number of arriving customers/second = 10 Tser average time to service a customer = 20 ms (0.02s) u server utilization (0..1): u = r x Tser= 10/s x .02s = 0.2 Tq average time/customer in queue = Tser x u / (1 – u) = 20 x 0.2/(1-0.2) = 20 x 0.25 = 5 ms (0 .005s) Tsys average time/customer in system: Tsys =Tq +Tser= 25 ms Lq average length of queue:Lq= r x Tq = 10/s x .005s = 0.05 requests in queue Lsys average # tasks in system: Lsys = r x Tsys = 10/s x .025s = 0.25

## Slide 14: CS 252 Administrivia
Email URL of initial project home page to TA?
Upcoming events in CS 252
18-Mar Wed I/O 3: Tertiary Storage & Network Intro
19-Mar Thu Send in Project Survey #2
20-Mar Fri Networks 2: Interface, Switches, Routing
23-Mar to 27-Mar Spring Break

## Slide 15: A Little Queuing Theory: Another Example
processor sends 20 x 8KB disk I/Os per sec, requests & service exponentially distrib., avg. disk service = 12 ms
On average, how utilized is the disk?
  What is the number of requests in the queue?
  What is the average time a spent in the queue?
  What is the average response time for a disk request?
Notation:
r average number of arriving customers/second= 20 Tser average time to service a customer= 12 ms u server utilization (0..1): u = r x Tser= /s x . s = Tq average time/customer in queue = Ts er x u / (1 – u) = x /( ) = x = ms Tsys average time/customer in system: Tsys =Tq +Tser= 16 ms Lq average length of queue:Lq= r x Tq = /s x s = requests in queue Lsys average # tasks in system : Lsys = r x Tsys = /s x s =

## Slide 16: A Little Queuing Theory: Another Example
processor sends 20 x 8KB disk I/Os per sec, requests & service exponentially distrib., avg. disk service = 12 ms
On average, how utilized is the disk?
  What is the number of requests in the queue?
  What is the average time a spent in the queue?
  What is the average response time for a disk request?
Notation:
r average number of arriving customers/second= 20 Tser average time to service a customer= 12 ms u server utilization (0..1): u = r x Tser= 20/s x .012s = 0.24 Tq average time/customer in queue = Ts er x u / (1 – u) = 12 x 0.24/(1-0.24) = 12 x 0.32 = 3.8 ms Tsys average time/customer in system: Tsys =Tq +Tser= 15.8 ms Lq average length of queue:Lq= r x Tq = 20/s x .0038s = 0.076 requests in queue Lsys average # tasks in system : Lsys = r x Tsys = 20/s x .016s = 0.32

## Slide 17: A Little Queuing Theory: Yet Another Example
Suppose processor sends 10 x 8KB disk I/Os per second, squared coef. var.(C) = 1.5, avg. disk service time = 20 ms
On average, how utilized is the disk?
  What is the number of requests in the queue?
  What is the average time a spent in the queue?
  What is the average response time for a disk request?
Notation:
r average number of arriving customers/second= 10 Tser average time to service a customer= 20 ms u server utilization (0..1): u = r x Tser= 10/s x .02s = 0.2 Tq average time/customer in queue = Tser x u x (1 + C) /(2 x (1 – u)) = 20 x 0.2(2.5)/2(1 – 0.2) = 20 x 0.32 = 6.25 ms Tsys average time/customer in system: Tsys = Tq +Tser= 26 ms Lq average length of queue:Lq= r x Tq = 10/s x .006s = 0.06 requests in queue Lsys average # tasks in system :Lsys = r x Tsys = 10/s x .026s = 0.26

## Slide 18: Pitfall of Not using Queuing Theory
1st 32-bit minicomputer (VAX-11/780)
How big should write buffer be?
  Stores 10% of instructions, 1 MIPS
Buffer = 1
=> Avg. Queue Length = 1 vs. low response time

## Slide 19: Review: Storage System Issues
Historical Context of Storage I/O
Secondary and Tertiary Storage Devices
Storage I/O Performance Measures
Processor Interface Issues
A Little Queuing Theory
Redundant Arrarys of Inexpensive Disks (RAID)
I/O Buses
ABCs of UNIX File Systems
I/O Benchmarks
Comparing UNIX File System Performance

## Slide 20: Network Attached Storage
Decreasing Disk Diameters
Increasing Network Bandwidth
Network File Services
High Performance
Storage Service
on a High Speed
Network
14" » 10" » 8" » 5.25" » 3.5" » 2.5" » 1.8" » 1.3" » . . .
high bandwidth disk systems based on arrays of disks
3 Mb/s » 10Mb/s » 50 Mb/s » 100 Mb/s » 1 Gb/s » 10 Gb/s
networks capable of sustaining high bandwidth transfers
Network provides
well defined physical
and logical interfaces:
separate CPU and
storage system!
OS structures
supporting remote
file access

## Slide 21: Manufacturing Advantages of Disk Arrays
14”
10”
5.25”
3.5”
3.5”
Disk Array: 1 disk design
Conventional: 4 disk designs
Low End
High End
Disk Product Families

## Slide 22: Replace Small # of Large Disks with Large # of Small Disks! (1988 Disks)
Data Capacity
Volume
Power
Data Rate
I/O Rate
MTTF
Cost
IBM 3390 (K)
20 GBytes
97 cu. ft.
3 KW
15 MB/s
600 I/Os/s
250 KHrs
$250K
IBM 3.5" 0061
320 MBytes
0.1 cu. ft.
11 W
1.5 MB/s
55 I/Os/s
50 KHrs
$2K
x70
23 GBytes
11 cu. ft.
1 KW
120 MB/s
3900 IOs/s
??? Hrs
$150K
Disk Arrays have potential for
large data and I/O rates
high MB per cu. ft., high MB per KW
reliability?

## Slide 23: Array Reliability
Reliability of N disks = Reliability of 1 Disk ÷ N
  50,000 Hours ÷ 70 disks = 700 hours
Disk system MTTF: Drops from 6 years to 1 month!
• Arrays (without redundancy) too unreliable to be useful!
Hot spares support reconstruction in parallel with
access: very high media availability can be achieved

## Slide 24: Redundant Arrays of Disks
• Files are "striped" across multiple spindles
• Redundancy yields high data availability
Disks will fail
Contents reconstructed from data redundantly stored in the array
Capacity penalty to store it
Bandwidth penalty to update
Mirroring/Shadowing (high capacity cost)
Horizontal Hamming Codes (overkill)
Parity & Reed-Solomon Codes
Failure Prediction (no capacity overhead!)
VaxSimPlus — Technique is controversial
Techniques:

## Slide 25: Redundant Arrays of Disks RAID 1: Disk Mirroring/Shadowing
• Each disk is fully duplicated onto its "shadow"
Very high availability can be achieved
• Bandwidth sacrifice on write:
Logical write = two physical writes
• Reads may be optimized
• Most expensive solution: 100% capacity overhead
Targeted for high I/O rate , high availability environments
recovery
group

## Slide 26: Redundant Arrays of Disks RAID 3: Parity Disk
P
10010011
11001101
10010011
. . .
logical record
1
0
0
1
0
0
1
1
1
1
0
0
1
1
0
1
1
0
0
1
0
0
1
1
0
0
1
1
0
0
0
0
Striped physical
records
• Parity computed across recovery group to protect against hard disk failures
33% capacity cost for parity in this configuration
wider arrays reduce capacity costs, decrease expected availability,
increase reconstruction time
• Arms logically synchronized, spindles rotationally synchronized
logically a single high capacity, high transfer rate disk
Targeted for high bandwidth applications: Scientific, Image Processing

## Slide 27: Redundant Arrays of Disks RAID 5+: High I/O Rate Parity
A logical write
becomes four
physical I/Os
Independent writes
possible because of
interleaved parity
Reed-Solomon
Codes ("Q") for
protection during
reconstruction
D0
D1
D2
D3
P
D4
D5
D6
P
D7
D8
D9
P
D10
D11
D12
P
D13
D14
D15
P
D16
D17
D18
D19
D20
D21
D22
D23
P
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Disk Columns
Increasing
Logical
Disk
Addresses
Stripe
Stripe
Unit
Targeted for mixed
applications

## Slide 28: Problems of Disk Arrays: Small Writes
D0
D1
D2
D3
P
D0'
+
+
D0'
D1
D2
D3
P'
new
data
old
data
old
parity
XOR
XOR
(1. Read)
(2. Read)
(3. Write)
(4. Write)
RAID-5: Small Write Algorithm
1 Logical Write = 2 Physical Reads + 2 Physical Writes

## Slide 29: Mirrored Large Disks vs. Arrayed Small Disks
RA90:
Ave. Seek: 18.5 ms
Rotation: 16.7 ms
Xfer Rate: 2.8 MB/s
Capacity: 1200 MB
IBM Small Disks:
Ave. Seek: 12.5 ms
Rotation: 14 ms
Xfer Rate: 2.4 MB/s
Capacity: 300 MB
Normal
Operating
Range of
Most
Existing
Systems
all writes
all reads
Mirrored RA90's
4+2 Array Group
IO/sec

## Slide 30: Subsystem Organization
host
array
controller
single board
disk
controller
single board
disk
controller
single board
disk
controller
single board
disk
controller
host
adapter
manages interface
to host, DMA
control, buffering,
parity logic
physical device
control
often piggy-backed
in small format devices
striping software off-loaded from
host to array controller
no applications modifications
no reduction of host performance

## Slide 31: System Availability: Orthogonal RAIDs
Array
Controller
String
Controller
String
Controller
String
Controller
String
Controller
String
Controller
String
Controller
. . .
. . .
. . .
. . .
. . .
. . .
Data Recovery Group: unit of data redundancy
Redundant Support Components: fans, power supplies, controller, cables
End to End Data Integrity: internal parity protected data paths

## Slide 32: System-Level Availability
Fully dual redundant
I/O Controller
I/O Controller
Array Controller
Array Controller
. . .
. . .
. . .
. . .
. . .
.
.
.
Recovery
Group
Goal: No Single
Points of
Failure
host
host
with duplicated paths, higher performance can be
obtained when there are no failures

## Slide 33: Review: Storage System Issues
Historical Context of Storage I/O
Secondary and Tertiary Storage Devices
Storage I/O Performance Measures
Processor Interface Issues
A Little Queuing Theory
Redundant Arrarys of Inexpensive Disks (RAID)
I/O Buses
ABCs of UNIX File Systems
I/O Benchmarks
Comparing UNIX File System Performance

## Slide 34: Interconnect Trends
Interconnect = glue that interfaces computer system components
High speed hardware interfaces + logical protocols
Networks, channels, backplanes
memory-mapped
wide pathways
centralized arb
message-based
narrow pathways
distributed arb

## Slide 35: Backplane Architectures
Distinctions begin to blur:
SCSI channel is like a bus
FutureBus is like a channel (disconnect/reconnect)
HIPPI forms links in high speed switching fabrics

## Slide 36: Bus-Based Interconnect
Bus: a shared communication link between subsystems
  Low cost: a single set of wires is shared multiple ways
  Versatility: Easy to add new devices & peripherals may even be ported between computers using common bus
Disadvantage
  A communication bottleneck, possibly limiting the maximum I/O throughput
Bus speed is limited by physical factors
  the bus length
  the number of devices (and, hence, bus loading).
  these physical limits prevent arbitrary bus speedup.

## Slide 37: Bus-Based Interconnect
Two generic types of busses:
  I/O busses: lengthy, many types of devices connected, wide range in the data bandwidth), and follow a bus standard (sometimes called a channel)
  CPU–memory buses: high speed, matched to the memory system to maximize memory–CPU bandwidth, single device (sometimes called a backplane)
  To lower costs, low cost (older) systems combine together
Bus transaction
  Sending address & receiving or sending data

## Slide 38: Bus Protocols
° ° °
Master
Slave
Control Lines
Address Lines
Data Lines
Multibus: 20 address, 16 data, 5 control, 50ns Pause
Bus Master: has ability to control the bus, initiates transaction
Bus Slave: module activated by the transaction
Bus Communication Protocol: specification of sequence of events and timing requirements in transferring information.
Asynchronous Bus Transfers: control lines (req., ack.) serve to orchestrate sequencing
Synchronous Bus Transfers: sequence relative to common clock

## Slide 39: Synchronous Bus Protocols
Address
Data
Read
Wait
Clock
Address
Data
Wait
Pipelined/Split transaction Bus Protocol
addr 1
data 0
addr 2
wait 1
data 1
addr 3
OK 1
data 2
begin read
Read complete

## Slide 40: Asynchronous Handshake
Address
Data
Read
Req.
Ack.
Master Asserts Address
Master Asserts Data
Next Address
Write Transaction
t0 t1 t2 t3 t4 t5
t0 : Master has obtained control and asserts address, direction, data
Waits a specified amount of time for slaves to decode target\
t1: Master asserts request line
t2: Slave asserts ack, indicating data received
t3: Master releases req
t4: Slave releases ack
4 Cycle Handshake

## Slide 41: Read Transaction
Address
Data
Read
Req
Ack
Master Asserts Address
Next Address
t0 t1 t2 t3 t4 t5
Time Multiplexed Bus: address and data share lines
t0 : Master has obtained control and asserts address, direction, data
Waits a specified amount of time for slaves to decode target\
t1: Master asserts request line
t2: Slave asserts ack, indicating ready to transmit data
t3: Master releases req, data received
t4: Slave releases ack
4 Cycle Handshake

## Slide 42: Bus Arbitration
Parallel (Centralized) Arbitration
Serial Arbitration (daisy chaining)
Polling
BR BG
M
BR BG
M
BR BG
M
M
BGi BGo
BR
M
BGi BGo
BR
M
BGi BGo
BR
BG
BR
A.U.
BR A C
M
BR A C
M
BR A C
M
BR
A
A.U.
Bus Request
Bus Grant

## Slide 43: Bus Options
Option High performance Low cost
Bus width Separate address Multiplex address & data lines & data lines
Data width Wider is faster Narrower is cheaper (e.g., 32 bits) (e.g., 8 bits)
Transfer size Multiple words has Single-word transfer less bus overhead is simpler
Bus masters Multiple Single master (requires arbitration) (no arbitration)
Split Yes—separate No—continuous transaction? Request and Reply connection is cheaper packets gets higher and has lower latency bandwidth (needs multiple masters)
Clocking Synchronous Asynchronous

## Slide 44: 1990 Bus Survey (P&H, 1st Ed)
VME FutureBus Multibus II IPI SCSI
Signals 128 96 96 16 8
Addr/Data mux no yes yes n/a n/a
Data width 16 - 32 32 32 16 8
Masters multi multi multi single multi
Clocking Async Async Sync Async either
MB/s (0ns, word) 25 37 20 25 1.5 (asyn)
5 (sync)
150ns word 12.9 15.5 10 = =
0ns block 27.9 95.2 40 = =
150ns block 13.6 20.8 13.3 = =
Max devices 21 20 21 8 7
Max meters 0.5 0.5 0.5 50 25
Standard IEEE 1014 IEEE 896.1 ANSI/IEEE ANSI X3.129 ANSI X3.131
1296

## Slide 45: VME
3 96-pin connectors
128 defined as standard, rest customer defined
  32 address
  32 data
  64 command & power/ground lines

## Slide 46: SCSI: Small Computer System Interface
Clock rate: 5 MHz / 10 MHz (fast) / 20 MHz (ultra)
Width: n = 8 bits / 16 bits (wide); up to n – 1 devices to communicate on a bus or “string”
Devices can be slave (“target”) or master(“initiator”)
SCSI protocol: a series of “phases”, during which specif- ic actions are taken by the controller and the SCSI disks
  Bus Free: No device is currently accessing the bus
  Arbitration: When the SCSI bus goes free, multiple devices may request (arbitrate for) the bus; fixed priority by address
  Selection: informs the target that it will participate (Reselection if disconnected)
  Command: the initiator reads the SCSI command bytes from host memory and sends them to the target
  Data Transfer: data in or out, initiator: target
  Message Phase: message in or out, initiator: target (identify, save/restore data pointer, disconnect, command complete)
  Status Phase: target, just before command complete

## Slide 47: SCSI “Bus”: Channel Architecture
peer-to-peer protocols
initiator/target
linear byte streams
disconnect/reconnect

## Slide 48: 1993 I/O Bus Survey (P&H, 2nd Ed)
Bus SBus TurboChannel MicroChannel PCI
Originator Sun DEC IBM Intel
Clock Rate (MHz) 16-25 12.5-25 async 33
Addressing Virtual Physical Physical Physical
Data Sizes (bits) 8,16,32 8,16,24,32 8,16,24,32,64 8,16,24,32,64
Master Multi Single Multi Multi
Arbitration Central Central Central Central
32 bit read (MB/s) 33 25 20 33
Peak (MB/s) 89 84 75 111 (222)
Max Power (W) 16 26 13 25

## Slide 49: 1993 MP Server Memory Bus Survey
Bus Summit Challenge XDBus
Originator HP SGI Sun
Clock Rate (MHz) 60 48 66
Split transaction? Yes Yes Yes?
Address lines 48 40 ??
Data lines 128 256 144 (parity)
Data Sizes (bits) 512 1024 512
Clocks/transfer 4 5 4?
Peak (MB/s) 960 1200 1056
Master Multi Multi Multi
Arbitration Central Central Central
Addressing Physical Physical Physical
Slots 16 9 10
Busses/system 1 1 2
Length 13 inches 12? inches 17 inches

## Slide 50: Communications Networks
Performance limiter is memory system, OS overhead
Send/receive queues in processor memories
Network controller copies back and forth via DMA
No host intervention needed
Interrupt host when message sent or received

## Slide 51: I/O Controller Architecture
Request/response block interface
Backdoor access to host memory

## Slide 52: I/O Data Flow
Impediment to high performance: multiple copies,
complex hierarchy

## Slide 53: Summary: A Little Queuing Theory
Queuing models assume state of equilibrium: input rate = output rate
Notation:
r average number of arriving customers/second Tser average time to service a customer (tradtionally µ = 1/ Tser ) u server utilization (0..1): u = r x Tser Tq average time/customer in queue Tsys average time/customer in system: Tsys = Tq + Tser Lq average length of queue: Lq = r x Tq Lsys average length of system : Lsys = r x Tsys
Little’s Law: Lengthsystem = rate x Timesystem (Mean number customers = arrival rate x mean service time)
Proc
IOC
Device
Queue
server
System

## Slide 54: Summary: Redundant Arrays of Disks (RAID) Techniques
• Disk Mirroring, Shadowing (RAID 1)
Each disk is fully duplicated onto its "shadow"
Logical write = two physical writes
100% capacity overhead
• Parity Data Bandwidth Array (RAID 3)
Parity computed horizontally
Logically a single high data bw disk
• High I/O Rate Parity Array (RAID 5)
Interleaved parity blocks
Independent reads and writes
Logical write = 2 reads + 2 writes
Parity + Reed-Solomon codes
1
0
0
1
0
0
1
1
1
1
0
0
1
1
0
1
1
0
0
1
0
0
1
1
0
0
1
1
0
0
1
0
1
0
0
1
0
0
1
1
1
0
0
1
0
0
1
1

## Slide 55: Review: Storage System Issues
Historical Context of Storage I/O
Secondary and Tertiary Storage Devices
Storage I/O Performance Measures
Processor Interface Issues
A Little Queuing Theory
Redundant Arrarys of Inexpensive Disks (RAID)
I/O Buses
ABCs of UNIX File Systems
I/O Benchmarks
Comparing UNIX File System Performance