## Slide 1: Lecture 14: I/O Benchmarks, Busses, and Automated Data Libraries
Professor David A. Patterson
Computer Science 252
Spring 1998

## Slide 2: Review: A Little Queuing Theory
Queuing models assume state of equilibrium: input rate = output rate
Notation:
r average number of arriving customers/second Tser average time to service a customer (tradtionally µ = 1/ Tser ) u server utilization (0..1): u = r x Tser Tq average time/customer in queue Tsys average time/customer in system: Tsys = Tq + Tser Lq average length of queue: Lq = r x Tq Lsys average length of system : Lsys = r x Tsys
Little’s Law: Lengthsystem = rate x Timesystem (Mean number customers = arrival rate x mean service time)
Proc
IOC
Device
Queue
server
System

## Slide 3: Review: Redundant Arrays of Disks (RAID) Techniques
• Disk Mirroring, Shadowing (RAID 1)
Each disk is fully duplicated onto its "shadow"
Logical write = two physical writes
100% capacity overhead
• Parity Data Bandwidth Array (RAID 3)
Parity computed horizontally
Logically a single high data bw disk
• High I/O Rate Parity Array (RAID 5)
Interleaved parity blocks
Independent reads and writes
Logical write = 2 reads + 2 writes
Parity + Reed-Solomon codes
1
0
0
1
0
0
1
1
1
1
0
0
1
1
0
1
1
0
0
1
0
0
1
1
0
0
1
1
0
0
1
0
1
0
0
1
0
0
1
1
1
0
0
1
0
0
1
1

## Slide 4: Review: RAID
RAID sales
1993: $3.4 billion on 214,667 arrays (­ $15,000 / RAID)
1996 forecast: $11 billion
1997 forecast: $13 billion on 837,155 units
  Source: DISK/TREND, 5/94 (415-961-6209)

## Slide 5: Review: Storage System Issues
Historical Context of Storage I/O
Secondary and Tertiary Storage Devices
Storage I/O Performance Measures
Processor Interface Issues
A Little Queuing Theory
Redundant Arrarys of Inexpensive Disks (RAID)
ABCs of UNIX File Systems
I/O Benchmarks
Comparing UNIX File System Performance
I/O Buses

## Slide 6: ABCs of UNIX File Systems
Key Issues
  File vs. Raw I/O
  File Cache Size Policy
  Write Policy
  Local Disk vs. Server Disk
File vs. Raw:
  File system access is the norm: standard policies apply
  Raw: alternate I/O system to avoid file system, used by data bases
File Cache Size Policy
  % of main memory dedicated to file cache is fixed at system generation (e.g., 10%)
  % of main memory for file cache varies depending on amount of file I/O (e.g., up to 80%)

## Slide 7: ABCs of UNIX File Systems
Write Policy
  File Storage should be permanent; either write immediately or flush file cache after fixed period (e.g., 30 seconds)
  Write Through with Write Buffer
  Write Back
  Write Buffer often confused with Write Back
    Write Through with Write Buffer, all writes go to disk
    Write Through with Write Buffer, writes are asynchronous, so processor doesn’t have to wait for disk write
    Write Back will combine multiple writes to same page; hence can be called Write Cancelling

## Slide 8: ABCs of UNIX File Systems
Local vs. Server
  Unix File systems have historically had different policies (and even file sytems) for local client vs. remote server
  NFS local disk allows 30 second delay to flush writes
  NFS server disk writes through to disk on file close
  Cache coherency problem if allow clients to have file caches in addition to server file cache
    NFS just writes through on file close Stateless protocol: periodically get new copies of file blocks
    Other file systems use cache coherency with write back to check state and selectively invalidate or update

## Slide 9: Network File Systems
local
accesses
remote
accesses

## Slide 10: Typical File Server Architecture
Limits to performance: data copying
read data staged from device to primary memory
copy again into network packet templates
copy yet again to network interface
No specialization for fast processing between network
and disk

## Slide 11: AUSPEX NS5000 File Server
Special hardware/software architecture for high performance NFS I/O
Functional multiprocessing
specialized for
protocol processing
I/O buffers
dedicated FS
software
UNIX
frontend
manages 10 SCSI
channels

## Slide 12: AUSPEX Software Architecture
Primary control flow
Primary data flow
Limited
control
interfaces

## Slide 13: Berkeley RAID-II Disk Array File Server
to
UltraNet
to 120 disk drives
Low latency transfers
mixed with high bandwidth
transfers
"Diskless Supercomputers"

## Slide 14: CS 252 Administrivia
Email URL of initial project home page to TA?
Upcoming events in CS 252
19-Mar Thu Send in Project Survey #2
20-Mar Fri Computer Pioneers and Pioneer Computers
(Video, Gordon Bell Host)
23-Mar to 27-Mar Spring Break

## Slide 15: I/O Benchmarks
For better or worse, benchmarks shape a field
  Processor benchmarks classically aimed at response time for fixed sized problem
  I/O benchmarks typically measure throughput, possibly with upper limit on response times (or 90% of response times)
What if fix problem size, given 60%/year increase in DRAM capacity?
Benchmark Size of Data % Time I/O Year
I/OStones 1 MB 26% 1990
Andrew 4.5 MB 4% 1988
  Not much time in I/O
  Not measuring disk (or even main memory)

## Slide 16: I/O Benchmarks
Alternative: self-scaling benchmark; automatically and dynamically increase aspects of workload to match characteristics of system measured
  Measures wide range of current & future
Describe three self-scaling benchmarks
  Transacition Processing: TPC-A, TPC-B, TPC-C
  NFS: SPEC SFS (LADDIS)
  Unix I/O: Willy

## Slide 17: I/O Benchmarks: Transaction Processing
Transaction Processing (TP) (or On-line TP=OLTP)
  Changes to a large body of shared information from many terminals, with the TP system guaranteeing proper behavior on a failure
  If a bank’s computer fails when a customer withdraws money, the TP system would guarantee that the account is debited if the customer received the money and that the account is unchanged if the money was not received
  Airline reservation systems & banks use TP
Atomic transactions makes this work
Each transaction => 2 to 10 disk I/Os & 5,000 and 20,000 CPU instructions per disk I/O
  Efficiency of TP SW & avoiding disks accesses by keeping information in main memory
Classic metric is Transactions Per Second (TPS)
  Under what workload? how machine configured?

## Slide 18: I/O Benchmarks: Transaction Processing
Early 1980s great interest in OLTP
  Expecting demand for high TPS (e.g., ATM machines, credit cards)
  Tandem’s success implied medium range OLTP expands
  Each vendor picked own conditions for TPS claims, report only CPU times with widely different I/O
  Conflicting claims led to disbelief of all benchmarks=> chaos
1984 Jim Gray of Tandem distributed paper to Tandem employees and 19 in other industries to propose standard benchmark
Published “A measure of transaction processing power,” Datamation, 1985 by Anonymous et. al
  To indicate that this was effort of large group
  To avoid delays of legal department of each author’s firm
  Still get mail at Tandem to author

## Slide 19: I/O Benchmarks: TP by Anon et. al
Proposed 3 standard tests to characterize commercial OLTP
  TP1: OLTP test, DebitCredit, simulates ATMs (TP1)
  Batch sort
  Batch scan
Debit/Credit:
  One type of transaction: 100 bytes each
  Recorded 3 places: account file, branch file, teller file + events recorded in history file (90 days)
    15% requests for different branches
  Under what conditions, how report results?

## Slide 20: I/O Benchmarks: TP1 by Anon et. al
DebitCredit Scalability: size of account, branch, teller, history function of throughput
  TPS Number of ATMs Account-file size
  10 1,000 0.1 GB
  100 10,000 1.0 GB
  1,000 100,000 10.0 GB
  10,000 1,000,000 100.0 GB
  Each input TPS =>100,000 account records, 10 branches, 100 ATMs
  Accounts must grow since a person is not likely to use the bank more frequently just because the bank has a faster computer!
Response time: 95% transactions take Š 1 second
Configuration control: just report price (initial purchase price + 5 year maintenance = cost of ownership)
By publishing, in public domain

## Slide 21: I/O Benchmarks: TP1 by Anon et. al
Problems
  Often ignored the user network to terminals
  Used transaction generator with no think time; made sense for database vendors, but not what customer would see
Solution: Hire auditor to certify results
  Auditors soon saw many variations of ways to trick system
Proposed minimum compliance list (13 pages); still, DEC tried IBM test on different machine with poorer results than claimed by auditor
Created Transaction Processing Performance Council in 1988: founders were CDC, DEC, ICL, Pyramid, Stratus, Sybase, Tandem, and Wang; 46 companies today
Led to TPC standard benchmarks in 1990, www.tpc.org

## Slide 22: I/O Benchmarks: Old TPC Benchmarks
TPC-A: Revised version of TP1/DebitCredit
  Arrivals: Random (TPC) vs. uniform (TP1)
  Terminals: Smart vs. dumb (affects instruction path length)
  ATM scaling: 10 terminals per TPS vs. 100
  Branch scaling: 1 branch record per TPS vs. 10
  Response time constraint: 90% Š2 seconds vs. 95% Š1
  Full disclosure, approved by TPC
  Complete TPS vs. response time plots vs. single point
TPC-B: Same as TPC-A but without terminals—batch processing of requests
  Response time makes no sense: plots tps vs. residence time (time of transaction resides in system)
These have been withdrawn as benchmarks

## Slide 23: I/O Benchmarks: TPC-C Complex OLTP
Models a wholesale supplier managing orders
Order-entry conceptual model for benchmark
Workload = 5 transaction types
Users and database scale linearly with throughput
Defines full-screen end-user interface
Metrics: new-order rate (tpmC) and price/performance ($/tpmC)
Approved July 1992

## Slide 24: I/O Benchmarks: TPC-D Complex Decision Support Workload
OLTP: business operation
Decision support: business analysis (historical)
Workload = 17 adhoc transactions
  e,g., Impact on revenue of eliminating company-wide discount?
Synthetic generator of data
Size determined by Scale Factor: 100 GB, 300 GB, 1 TB, 3 TB, 10 TB
Metrics: “Queries per Gigabyte Hour” Power (QppD@Size) = 3600 x SF / Geo. Mean of queries Throughput (QthD@Size) = 17 x SF / (time/3600) Price/Performance ($/QphD@Size) = $/ geo. mean(QppD@Size, QthD@Size)
Report time to load database (indices, stats) too
Approved April 1995

## Slide 25: I/O Benchmarks: TPC-W Transactional Web Benchmark
Represent any business (retail store, software distribution, airline reservation, electronic stock trades, etc.) that markets and sells over the Internet/ Intranet
Measure systems supporting users browsing, ordering, and conducting transaction oriented business activities.
Security (including user authentication and data encryption) and dynamic page generation are important
Before: processing of customer order by terminal operator working on LAN connected to database system
Today: customer accesses company site over Internet connection, browses both static and dynamically generated Web pages, and searches the database for product or customer information. Customer also initiate, finalize and check on product orders and deliveries.
Started 1/97; hope to release Fall, 1998

## Slide 26: TPC-C Performance tpm(c)
Rank Config tpmC $/tpmC Database
1 IBM RS/6000 SP (12 node x 8-way) 57,053.80 $147.40 Oracle8 8.0.4
2 HP HP 9000 V2250 (16-way) 52,117.80 $81.17 Sybase ASE
3 Sun Ultra E6000 c/s (2 node x 22-way) 51,871.62 $134.46 Oracle8 8.0.3
4 HP HP 9000 V2200 (16-way) 39,469.47 $94.18 Sybase ASE
5 Fujitsu GRANPOWER 7000 Model 800 34,116.93 $57,883.00 Oracle8
6 Sun Ultra E6000 c/s (24-way) 31,147.04 $108.90 Oracle8 8.0.3
7Digital AlphaS8400 (4 node x 8-way) 30,390.00 $305.00 Oracle7 V7.3
8 SGI Origin2000 Server c/s (28-way) 25,309.20 $139.04 INFORMIX
9 IBM AS/400e Server (12-way) 25,149.75 $128.00 DB2
10 Digital AlphaS8400 5/625 (10-way) 24,537.00 $110.48 Sybase SQL

## Slide 27: TPC-C Price/Performance $/tpm(c)
Rank Config $/tpmC tpmC Database
1 Acer AcerAltos 19000Pro4 $27.25 11,072.07 M/S SQL 6.5
2 Dell PowerEdge 6100 c/s $29.55 10,984.07 M/S SQL 6.5
3 Compaq ProLiant 5500 c/s $33.37 10,526.90 M/S SQL 6.5
4 ALR Revolution 6x6 c/s $35.44 13,089.30 M/S SQL 6.5
5 HP NetServer LX Pro $35.82 10,505.97 M/S SQL 6.5
6 Fujitsu teamserver M796i $37.62 13,391.13 M/S SQL 6.5
7 Fujitsu GRANPOWER 5000 Model 670 $37.62 13,391.13 M/S SQL 6.5
8 Unisys Aquanta HS/6 c/s $37.96 13,089.30 M/S SQL 6.5
9 Compaq ProLiant 7000 c/s $39.25 11,055.70 M/S SQL 6.5
10 Unisys Aquanta HS/6 c/s $39.39 12,026.07 M/S SQL 6.5

## Slide 28: TPC-D Performance/Price 300 GB
Rank Config. Qppd QthD $/QphD Database
1 NCR WorldMark 5150 9,260.0 3,117.0 2,172.00 Teradata
2 HP 9000 EPS22 (16 node) 5,801.2 2,829.0 1,982.00 Informix-XPS
3 DG AViiON AV20000 3,305.8 1,277.7 1,319.00 Oracle8 v8.0.4
4 Sun - Ultra Enterprise 6000 3,270.6 1,477.8 1,553.00 Informix-XPS
5 Sequent NUMA-Q 2000 (32 way) 3,232.3 1,097.8 3,283.00 Oracle8 v8.0.4
Rank Config. Qppd QthD $/QphD Database
1 DG AViiON AV20000 3,305.8 1,277.7 1,319.00 Oracle8 v8.0.4
2 Sun Ultra Enterprise 6000 3,270.6 1,477.8 1,553.00 Informix-XPS
3 HP 9000 EPS22 (16 node) 5,801.2 2,829.0 1,982.00 Informix-XPS
4 NCR WorldMark 5150 9,260.0 3,117.0 2,172.00 Teradata
5 Sequent NUMA-Q 2000 (32 way) 3,232.3 1,097.8 3,283.00 Oracle8 v8.0.4

## Slide 29: TPC-D Performance 1TB
Rank Config. Qppd QthD $/QphD Database
1 Sun Ultra E6000 (4 x 24-way) 12,931.9 5,850.3 1,353.00 Infomix Dyn
2 NCR WorldMark (32 x 4-way) 12,149.2 3,912.3 2103.00 Teradata
3 IBM RS/6000 SP (32 x 8-way) 7,633.0 5,155.4 2095.00 DB2 UDB, V5
NOTE: Inappropriate to compare results from different database sizes.

## Slide 30: TPC-D Performance 1TB
Rank Config. Qppd QthD $/QphD Database
1 Sun Ultra E6000 (4 x 24-way) 12,931.9 5,850.3 1,353.00 Infomix Dyn
2 NCR WorldMark (32 x 4-way) 12,149.2 3,912.3 2103.00 Teradata
3 IBM RS/6000 SP (32 x 8-way) 7,633.0 5,155.4 2095.00 DB2 UDB, V5

## Slide 31: SPEC SFS/LADDIS Predecessor: NFSstones
NFSStones: synthetic benchmark that generates series of NFS requests from single client to test server: reads, writes, & commands & file sizes from other studies
  Problem: 1 client could not always stress server
  Files and block sizes not realistic
  Clients had to run SunOS

## Slide 32: SPEC SFS/LADDIS
1993 Attempt by NFS companies to agree on standard benchmark: Legato, Auspex, Data General, DEC, Interphase, Sun. Like NFSstones but
  Run on multiple clients & networks (to prevent bottlenecks)
  Same caching policy in all clients
  Reads: 85% full block & 15% partial blocks
  Writes: 50% full block & 50% partial blocks
  Average response time: 50 ms
  Scaling: for every 100 NFS ops/sec, increase capacity 1GB
  Results: plot of server load (throughput) vs. response time & number of users
    Assumes: 1 user => 10 NFS ops/sec

## Slide 33: Example SPEC SFS Result: DEC Alpha
200 MHz 21064: 8KI + 8KD + 2MB L2; 512 MB; 1 Gigaswitch
DEC OSF1 v2.0
4 FDDI networks; 32 NFS Daemons, 24 GB file size
88 Disks, 16 controllers, 84 file systems
4817

## Slide 34: Willy
UNIX File System Benchmark that gives insight into I/O system behavior (Chen and Patterson, 1993)
Self scaling to automatically explore system size
Examines five parameters
  Unique bytes touched: ­ data size; locality via LRU
    Gives file cache size
  Percentage of reads: %writes = 1 – % reads; typically 50%
    100% reads gives peak throughput
  Average I/O Request Size: Bernoulli, C=1
  Percentage sequential requests: typically 50%
  Number of processes: concurrency of workload (number processes issuing I/O requests)
Fix four parameters while vary one parameter
Searches space to find high throughput

## Slide 35: Example Willy: DS 5000
Sprite Ultrix
Avg. Access Size 32 KB 13 KB
Data touched (file cache) 2MB, 15 MB 2 MB
Data touched (disk) 36 MB 6 MB
% reads = 50%, % sequential = 50%
DS 5000 32 MB memory
Ultrix: Fixed File Cache Size, Write through
Sprite: Dynamic File Cache Size, Write back (Write cancelling)

## Slide 36: Sprite's Log Structured File System
Large file caches effective in reducing disk reads
Disk traffic likely to be dominated by writes
Write-Optimized File System
Only representation on disk is log
Stream out files, directories, maps without seeks
Advantages:
Speed
Stripes easily across several disks
Fast recovery
Temporal locality
Versioning
Problems:
Random access retrieval
Log wrap
Disk space utilization

## Slide 37: Willy: DS 5000 Number Bytes Touched
Log Structured File System: effective write cache of LFS much smaller (5-8 MB) than read cache (20 MB)
  Reads cached while writes are not => 3 plateaus

## Slide 38: Summary: I/O Benchmarks
Scaling to track technological change
TPC: price performance as nomalizing configuration feature
Auditing to ensure no foul play
Througput with restricted response time is normal measure

## Slide 39: Review: Storage System Issues
Historical Context of Storage I/O
Secondary and Tertiary Storage Devices
Storage I/O Performance Measures
Processor Interface Issues
A Little Queuing Theory
Redundant Arrarys of Inexpensive Disks (RAID)
ABCs of UNIX File Systems
I/O Benchmarks
Comparing UNIX File System Performance
I/O Buses

## Slide 40: Interconnect Trends
Interconnect = glue that interfaces computer system components
High speed hardware interfaces + logical protocols
Networks, channels, backplanes
memory-mapped
wide pathways
centralized arb
message-based
narrow pathways
distributed arb

## Slide 41: Backplane Architectures
Distinctions begin to blur:
SCSI channel is like a bus
FutureBus is like a channel (disconnect/reconnect)
HIPPI forms links in high speed switching fabrics

## Slide 42: Bus-Based Interconnect
Bus: a shared communication link between subsystems
  Low cost: a single set of wires is shared multiple ways
  Versatility: Easy to add new devices & peripherals may even be ported between computers using common bus
Disadvantage
  A communication bottleneck, possibly limiting the maximum I/O throughput
Bus speed is limited by physical factors
  the bus length
  the number of devices (and, hence, bus loading).
  these physical limits prevent arbitrary bus speedup.

## Slide 43: Bus-Based Interconnect
Two generic types of busses:
  I/O busses: lengthy, many types of devices connected, wide range in the data bandwidth), and follow a bus standard (sometimes called a channel)
  CPU–memory buses: high speed, matched to the memory system to maximize memory–CPU bandwidth, single device (sometimes called a backplane)
  To lower costs, low cost (older) systems combine together
Bus transaction
  Sending address & receiving or sending data

## Slide 44: Bus Protocols
° ° °
Master
Slave
Control Lines
Address Lines
Data Lines
Multibus: 20 address, 16 data, 5 control, 50ns Pause
Bus Master: has ability to control the bus, initiates transaction
Bus Slave: module activated by the transaction
Bus Communication Protocol: specification of sequence of events and timing requirements in transferring information.
Asynchronous Bus Transfers: control lines (req., ack.) serve to orchestrate sequencing
Synchronous Bus Transfers: sequence relative to common clock

## Slide 45: Synchronous Bus Protocols
Address
Data
Read
Wait
Clock
Address
Data
Wait
Pipelined/Split transaction Bus Protocol
addr 1
data 0
addr 2
wait 1
data 1
addr 3
OK 1
data 2
begin read
Read complete

## Slide 46: Asynchronous Handshake
Address
Data
Read
Req.
Ack.
Master Asserts Address
Master Asserts Data
Next Address
Write Transaction
t0 t1 t2 t3 t4 t5
t0 : Master has obtained control and asserts address, direction, data
Waits a specified amount of time for slaves to decode target\
t1: Master asserts request line
t2: Slave asserts ack, indicating data received
t3: Master releases req
t4: Slave releases ack
4 Cycle Handshake

## Slide 47: Read Transaction
Address
Data
Read
Req
Ack
Master Asserts Address
Next Address
t0 t1 t2 t3 t4 t5
Time Multiplexed Bus: address and data share lines
t0 : Master has obtained control and asserts address, direction, data
Waits a specified amount of time for slaves to decode target\
t1: Master asserts request line
t2: Slave asserts ack, indicating ready to transmit data
t3: Master releases req, data received
t4: Slave releases ack
4 Cycle Handshake

## Slide 48: Bus Arbitration
Parallel (Centralized) Arbitration
Serial Arbitration (daisy chaining)
Polling
BR BG
M
BR BG
M
BR BG
M
M
BGi BGo
BR
M
BGi BGo
BR
M
BGi BGo
BR
BG
BR
A.U.
BR A C
M
BR A C
M
BR A C
M
BR
A
A.U.
Bus Request
Bus Grant

## Slide 49: Bus Options
Option High performance Low cost
Bus width Separate address Multiplex address & data lines & data lines
Data width Wider is faster Narrower is cheaper (e.g., 32 bits) (e.g., 8 bits)
Transfer size Multiple words has Single-word transfer less bus overhead is simpler
Bus masters Multiple Single master (requires arbitration) (no arbitration)
Split Yes—separate No—continuous transaction? Request and Reply connection is cheaper packets gets higher and has lower latency bandwidth (needs multiple masters)
Clocking Synchronous Asynchronous

## Slide 50: SCSI: Small Computer System Interface
Clock rate: 5 MHz / 10 MHz (fast) / 20 MHz (ultra)
Width: n = 8 bits / 16 bits (wide); up to n – 1 devices to communicate on a bus or “string”
Devices can be slave (“target”) or master(“initiator”)
SCSI protocol: a series of “phases”, during which specif- ic actions are taken by the controller and the SCSI disks
  Bus Free: No device is currently accessing the bus
  Arbitration: When the SCSI bus goes free, multiple devices may request (arbitrate for) the bus; fixed priority by address
  Selection: informs the target that it will participate (Reselection if disconnected)
  Command: the initiator reads the SCSI command bytes from host memory and sends them to the target
  Data Transfer: data in or out, initiator: target
  Message Phase: message in or out, initiator: target (identify, save/restore data pointer, disconnect, command complete)
  Status Phase: target, just before command complete

## Slide 51: SCSI “Bus”: Channel Architecture
peer-to-peer protocols
initiator/target
linear byte streams
disconnect/reconnect

## Slide 52: 1993 I/O Bus Survey (P&H, 2nd Ed)
Bus SBus TurboChannel MicroChannel PCI
Originator Sun DEC IBM Intel
Clock Rate (MHz) 16-25 12.5-25 async 33
Addressing Virtual Physical Physical Physical
Data Sizes (bits) 8,16,32 8,16,24,32 8,16,24,32,64 8,16,24,32,64
Master Multi Single Multi Multi
Arbitration Central Central Central Central
32 bit read (MB/s) 33 25 20 33
Peak (MB/s) 89 84 75 111 (222)
Max Power (W) 16 26 13 25

## Slide 53: 1993 MP Server Memory Bus Survey
Bus Summit Challenge XDBus
Originator HP SGI Sun
Clock Rate (MHz) 60 48 66
Split transaction? Yes Yes Yes?
Address lines 48 40 ??
Data lines 128 256 144 (parity)
Data Sizes (bits) 512 1024 512
Clocks/transfer 4 5 4?
Peak (MB/s) 960 1200 1056
Master Multi Multi Multi
Arbitration Central Central Central
Addressing Physical Physical Physical
Slots 16 9 10
Busses/system 1 1 2
Length 13 inches 12? inches 17 inches

## Slide 54: Summary: I/O Benchmarks
Scaling to track technological change
TPC: price performance as nomalizing configuration feature
Auditing to ensure no foul play
Throughput with restricted response time is normal measure