noise

---
noise: signal you don’t want
technical noise: sources we can control in the environment ... or at least we can imagine some powerful being could control them without violating the underlying fundamental laws of physics
fundamental noise: limits set by nature via temperature, quantization, and the laws of quantum mechanics (uncertainty principle)
understand that nature sets these limits but engineers usually do much worse
so ... learn good engineering and to do better

---
thermal / Nyquist / Johnson noise
theory by Nyquist: Phys Rev 32 110 (1928)
 adjacent experimental article by Johnson
applies to all devices
 easiest to discuss for resistors, so we will …
electrons moving randomly under influence of temperature generate a fluctuating voltage
time average voltage is (of course) zero
but power (~ V 2) can be delivered to another device at a lower temperature

---
origin of thermal noise
T2
voltage fluctuations (amplitude) are greater across the hotter device
net power flows from the hotter device to the colder device
eventually T2 = T1
net
power
flow
T2 > T1
T1

---
size of thermal noise
 any thermodynamic system stores
(at equilibrium) ½ kT energy per DoF
 bandwidth (f) characteristic of “receiver”
 Vnoise2/R = (½ kT) (f) (DoF/unit BW)
 2 DoF for 2 directions of energy transfer
 2 DoF for electric + magnetic fields
 2 DoF for arbitrary polarization direction
 gives 2 x 2 x 2 = 8 states

---
at room temperature kT ≈ (1/40) eV
e ≈ 1.6 x 10-19 coulomb/electron
so 4 kT ≈ 0.1 x 1.6 x 10-19 coulomb-volt
say f ≈ 300 kHz
(e.g., an FM radio station)
say R = 100 M
(e.g., an inexpensive digital voltmeter)
Vn ≈ (10-1 1.6x10-19 3x105 108 )1/2
 ≈ 7x10-4 volt
so RMS noise voltage ≈ 1 mV

---
assignment
 8) An inexpensive modern oscilloscope might have a signal bandwidth of 100 MHz; a typical pyroelectric “warm body sensor” has an output impedance around 100 M; what RMS noise voltage would you expect to see at room temperature, at 30 K, and at 3000 K?

---
shot noise
 statistical fluctuations in current originating with the quantization of electronic charge
moon phase
1991 Mar 10

---
current and electrons
current is not a continuum fluid … it is composed of a stream of individual electrons
when the current is small … or the sampling time is short … a typical sample may contain a relatively small number of electrons
the current corresponding to few thousand electrons/second is visible to a modern analog current measuring instrument
statistical fluctuations from sample-to-sample are then apparent as “shot noise”

---
 I ampere = I coulomb/second
 dN/dt = I/e (coulomb/s)/(coulomb/electron)
 e = 1.602 10-19 coulomb/electron
 (I/e) t = N electron (seen in t seconds)
 N = (I t/e)½ (standard deviation of the distribution of the values seen for N)
 I = e N/t (standard deviation of the distribution of the observed values of I
 I = (e/t) (I t /e)½ = (I e / t)½

---
but what to use for t ?
surely it depends on 1/bandwidth, but how exactly?
the “Nyquist sampling theorem”* says
that the right numerical factor is 1/2
so need to sample for t = (2 BW) -1
so I = (I e / t)½  (2 BW e I)½
if BW = 100 kHz and I = 10 mA then
I ≈ 18 nA, about 2 ppm of the signal
* you can reconstruct a continuous function perfectly from discrete samples at ≥ 2x its highest Fourier frequency

---
assignment
 9) What is the magnitude of the shot noise you would expect to see on a current measured at the highest sensitivity setting of a typical modern picoammeter in bandwidth 100 kHz?
(do a web search for “picoammeter” to find the specifications of a modern
off-the-shelf commercial instrument)

---
1/f noise
it is observed that noise power-per-unit-bandwidth increases with decreasing frequency, i.e., 1/f n, n ~ 1
called “pink” noise, in contrast to “white” noise character of Johnson and shot noise
its origin is still an active research topic: quantum mechanics, uncertainty, chaos, etc
but the phenomena is certainly ubiquitous and probably universal

---
to read more about 1/f noise:
http://www.nslij-genetics.org/wli/1fnoise

---
assignment
 10) Browse the given website on 1/f noise, select a subtopic and an article from the list “Specific Examples of 1/f Noise”, browse the article (or even just the abstract, if it is detailed enough: state the citation), and summarize what you read in ~ ½ page.
Mention at least: is the method theoretical, computational, or experimental? what is the observation that exhibits 1/f noise? how close to 1 is the observed exponent?