Using Microbenchmarks to Evaluate
                                System Performance

                                 Brian N. Bershad
                                 Richard P. Draves
                                 Alessandro Forin


                             School of Computer Science
                             Carnegie Mellon University
                                5000 Forbes Avenue
                               Pittsburgh, PA 15213



                1 Introduction

                It has become nearly impossible to write a paper about
                anything in operating systems without including some
                discussion of performance. Usually, the performance
                section concentrates on a few ``microbenchmarks'' which
                demonstrate that whatever it is which is being described
                in the paper can, has been, or might be, efficiently

                (0)This research was sponsored in part by the Defense
                Advanced Research Projects Agency, Information Science and
                Technology Office, under the title ``Research on Parallel
                Computing'', ARPA Order No. 7330, issued by DARPA/CMO
                under Contract MDA972-90-C-0035 and in part by the Open
                Software Foundation (OSF). Bershad was partially supported
                by a National Science Foundation Presidential Young
                Investigator Award. Draves was supported by a fellowship
                from the Fannie and John Hertz Foundation.
                  The views and conclusions contained in this document are
                those of the authors and should not be interpreted as
                representing the official policies, either expressed or
                implied, of DARPA, OSF, the Fannie and John Hertz
                Foundation, the NSF, or the U.S. government.
                 ()








                implemented. For example, the time to execute a null
                remote procedure call, a system trap, or to access a page
                of a mapped file have all been used at one time or another
                to show that the system implementing the function is
                either efficient (if it was built by the authors) or
                inefficient (if it was built by anybody else).

                Two implicit assumptions underlie the use of
                microbenchmarks. First, it is assumed that the time
                required for the microbenchmark to exercise the code path
                in question is the same as it is when the code path is
                used by real programs. Second, there is the assumption
                that a microbenchmark is actually representative of
                something which is either important in its own right, or
                which has a measurable impact on overall system
                performance. In this paper we point out the vulnerability
                of the first assumption by showing the significant
                variation that can occur with even simple microbenchmarks.
                Identifying weaknesses in the second assumption is
                something best done on a case by case basis.


                2 The Root of the Problem

                As Shakespeare once probably said, ``the fault, dear
                Brutus, lies not in our stars, but in our memory
                systems.'' High performance RISC processors live or die
                as a result of their memory system. Therefore, so do many
                microbenchmarks. In particular, (at least) two components
                of memory system design, the cache and the write buffer,
                must be considered when using microbenchmarks.


                2.1 Cache Effects

                The behavior of cache memory can distort the performance
                of a microbenchmark. Caches permit rapid access to memory
                locations which have been recently referenced. Cache
                collisions occur when a sequence of references resolve to
                the same cache line. The RISCier the processor, the
                simpler the cache structure, and the more vulnerable it is
                to collisions. The simplest caches, which are small (less
                than 64K) and direct mapped, present the greatest problem








                for microbenchmarks since they have little protection
                against collisions.

                Cache collisions can occur between memory in the same
                address space, or between memory in different address
                spaces. In the first case, the performance of a
                particular instance (that is, a linked binary) of the
                microbenchmark can be stable, but the performance of
                different versions of the same program can actually be
                quite variable. In the second case, when collisions occur
                between memories in separate address spaces, such as
                between the kernel and an application, then performance
                may be variable even from run to run, depending on how the
                system has allocated memory.

                When microbenchmark performance is used to tune pieces of
                the system by changing code and rerunning the
                microbenchmark to evaluate the change, the variability
                caused by cache effects can cause the wrong conclusions to
                be reached. It becomes difficult to say whether
                performance changed because of the tuning, or, say,
                because the linker assigned different addresses to object
                files.


                2.2 Write Buffers

                Many RISC processors have write buffers which are several
                entries deep. The write buffer allows the processor to
                proceed while previous stores complete asynchronously.
                Once the write buffer fills, however, subsequent stores
                slow the processor to memory speed. Often,
                microbenchmarks are structured to eliminate side effects
                which would normally occur during real applications of the
                code being tested. For example, a test to evaluate the
                performance of spinlocks might only acquire and release a
                lock in succession through a loop, rather than doing any
                real work (such as modifying a shared variable) inside the
                loop. Depending on the depth of the write buffer, a write
                stall could be avoided because nothing was computed inside
                the loop. In this case, the benchmark doesn't measure the
                true cost of the stores in the spinlock primitives.
                Consequently, the microbenchmark overestimates the actual








                performance of the primitives, since they would never be
                used in the way they were being tested.


                3 Some Real Examples

                A potential problem is different than one which occurs in
                real life. Our experiences with measuring operating
                system performance at CMU have shown that, in real life,
                microbenchmarks can be misleading. In this section we
                briefly describe two situations where microbenchmark
                results were, or could have been, affected by interactions
                with the memory system.


                3.1 The Null RPC -- Cache Interference Within the Kernel

                Mach is a ``small kernel'' operating system which provides
                support for fast cross-address space communication [Draves
                et al. 91]. On the DecStation 3100, which is a MIPS
                R2000-based system running at 16.67 MHz, null RPCs between
                two address spaces on the same machine typically take
                about 95 XXsecs, or about 1600 cycles.

                After one build of the system in which there were no
                changes to the kernel's RPC path, RPC times increased to
                about 160 XXsecs, or about 2650 cycles. The problem was
                that the machine-independent IPC code in one object file
                was colliding in the cache with machine-dependent
                functions in another object file. The collision occurred
                because of a change in the size of an unrelated object
                file. Since cache misses on the DecStation 3100 are
                resolved in 5 cycles, we concluded that about 215
                additional cache misses occurred on the newer system's RPC
                path. By rearranging the order of the object files for
                the kernel build, RPC times fell back to 95 XXsecs.

                If we had used the benchmark to tune the RPC path, to the
                exclusion of all other measurements, such as number of
                instructions executed, or number of memory accesses, then
                the variability could have lead to poor tuning decisions.
                If the application code itself had interfered with kernel
                code, then variability would have occurred from run to








                run.

                The best way to deal with the variability problem for
                tuning is to explicitly flush the cache during each
                iteration of the trial benchmark, and to then subtract off
                the cache flush overhead from the measured benchmark time.
                Although this technique will reveal worst case
                performance, the performance will at least be
                reproducible.

                Moreover, for tuning, it is important to count the number
                of loads and stores, rather than just instructions
                executed or microseconds measured during a run. As
                processor cycle times decreases, the major determinant of
                performance is the number of memory accesses which can not
                be satisfied by the cache. Many of the kinds of
                benchmarks which arise in operating system performance are
                stressing components of the system which are executed
                infrequently enough to make their long term presence in
                the cache unlikely. Therefore, performance profiles which
                reflect memory interaction are more likely to be good
                predictors of actual performance.


                3.2 The Simple Spinlock -- Failing to Fill the Write
                    Buffer

                Mach supports multiple threads of control per address
                space. Even on a uniprocessor, these threads use simple
                spinlocks to ensure mutual exclusion in the presence of
                interleaved execution. Some recent work at CMU focused on
                improving the performance of test-and-set primitives for
                architectures which do not have hardware support for
                atomic read-modify-write sequences [Bershad 91]. A simple
                microbenchmark evaluating the new locking primitives had
                the following form:








                     int i;
                     spinlock lock;

                     for (i = 0; i < GZILLION; i++) {
                           SPIN_LOCK(lock);
                           /* locked code fragment */
                           SPIN_UNLOCK(lock);
                     }


                On the DecStation 3100, the compiler generated a code
                sequence in which 8 instructions were executed during each
                pass of the loop. Within those 8 instructions were two
                memory stores --- one to acquire the lock and one to
                release it. The DecStation 3100 can complete one store
                every 6 cycles, but uses a four entry write buffer to
                allow the CPU to avoid stalling during writes. Multiple
                writes to the same address are coalesced in the write
                buffer, so the above loop can proceed at full speed -- the
                effective rate of writes is one per eight cycles.

                Unfortunately, the above loop will overestimate the
                performance of the locking primitives because, in reality,
                such primitives are always used in conjunction with writes
                to memory which is shared between multiple threads.
                Consequently, the above test is optimistic because it
                includes no writes to memory except the lock itself. If
                we include a store to shared memory within the loop, we
                add one instruction to the code path, for a total of nine
                instructions and two effective stores. Because the
                DecStation 3100 can retire only one store per six cycles,
                the augmented microbenchmark takes twelve cycles, not
                nine.

                This example motivates two conclusions. First, one can
                use microbenchmarks to predict baseline performance only
                if the measured behavior might really occur. In reality,
                no multithreaded program would ever acquire and then
                immediately release a spinlock. There would always be an
                intervening memory access, and this should be included in
                the measurements.

                Second, understanding the behavior and performance of a
                microbenchmark may often require understanding subtleties








                in the architectural implementation (e.g., depth of write
                buffer, ability to coalesce). It can sometimes be
                difficult to even discover these details, as they may be
                considered ``confidential and proprietary'' by industry.


                4 Conclusions

                Writing and interpreting microbenchmarks correctly can be
                difficult. The situation is only going to get worse as
                the gap between processing speed and memory speed widens.
                Microbenchmark performance may not be reflective of actual
                behavior, and even run-to-run results can have high
                variance. Flushing the cache while running a
                microbenchmark and counting memory accesses, rather than
                instructions, are two techniques for reducing the
                variability of results. Finally, it will become
                increasingly important to understand low-level details
                about architectural implementation when interpreting
                microbenchmarks.

                References

                [Bershad 91] Bershad, B. N. Mutual Exclusion for
                       Uniprocessors. Technical Report CMU-CS-91-116,
                       School of Computer Science, Carnegie Mellon
                       University, April 1991.
                [Draves et al. 91] Draves, R. P., Bershad, B. N., Rashid,
                       R. F., and Dean, R. W. Using Continuations to
                       Implement Thread Management and Communication in
                       Operating Systems. In Proceedings of the 13th ACM
                       Symposium on Operating Systems Principles, pages
                       122--136, October 1991.