A UNIX INTERFACE FOR SHARED MEMORY AND
                            MEMORY MAPPED FILES UNDER MACH



              Avadis Tevanian, Jr., Richard F. Rashid, Michael W. Young,
             David B. Golub, Mary R. Thompson, William Bolosky and Richar

                            Department of Computer Science
                              Carnegie-Mellon University
                                 Pittsburgh, PA 15213



                                       ABSTRACT

             This  paper  describes an approach to Unix shared memory and
             memory mapped files currently in use at CMU under  the  Mach
             Operating  System.    It  describes the rationale for Mach's
             memory sharing and file mapping primitives as well as  their
             impact   on   other   system   components   and  on  overall
             performance.

             1. Introduction

              The 4.2 BSD mapped file interface (mmap)  was  designed  to

             address two shortcomings of previous Unix systems: a lack of

             shared memory between processes and  the  need  to  simplify

             processing of file data.  Early Unix systems had provided no

             shared  memory  access  and  a  stylized  way  of  accessing

             sequential  file  data  through read and write system calls.

             Applications that desired random access to  data  would  use

             Unix's seek operation or buffer their data themselves, often

             incurring unwanted system overhead.  A mapped file  facility

             could  allow  a  user  to  treat  file data as normal memory

             without regard to buffering  or  concerns  about  sequential

             versus  random  access.    It  would also provide an obvious

             mechanism for sharing  memory  by  allowing  more  than  one

             process to map a file read/write simultaneously.


              The  BSD  file  mapping  facility  was proposed as early as

             1982.  Since then, similar mapped file interfaces have  been

             implemented by several vendors, both as part of 4.2 BSD Unix

             (e.g., Sequent Dynix [2]) and as part of a System V modified

             to contain 4.2 BSD enhancements (e.g., IBM's AIX).  A shared

             memory facility not based on mapped files  is  available  in

             AT&T's  System  V  and has also been adapted to a variety of

             4.2 BSD based systems  such  as  DEC's  Ultrix.    There  is

             currently a lively debate going on within the Unix community

             about the appropriate Unix interface to virtual  memory  and

             the  relationship  between  mapped files, memory sharing and

             other virtual memory concerns such as  copy-on-write  memory

             mapping.


              This  paper  describes  the  somewhat  atypical approach to

             shared memory and file mapping currently in use at CMU under

             the  Mach  Operating System.  It describes the rationale for

             Mach's memory sharing and  file  mapping  primitives,  their

             impact on other system components and on overall performance

             and the experiences of the Mach group  in  implementing  and

             using them.

             2. The Problems of a Mapped File Interface

              Despite its obvious convenience, the notion that all memory

             sharing should be channeled through a mapped file  interface

             presents a number of problems:

                1. A Unix file is (in principle) a permanent on-disk
                   data   structure   which   must   be   maintained
                   consistent  against  crashes.    The  use of disk
                   files to  exchange  temporary  data  can  put  an
                   unnecessary  I/O  load  on  the system and impact
                   performance.

                2. A mapped file facility must take into account the
                   sharing  of  remote (network) files.  In order to
                   handle remote file systems (e.g.  SUN  NFS),  the
                   operating  system  must be intimately involved in
                   maintaining network data consistency.   This  can
                   increase    its    complexity   considerably   by
                   introducing within the OS kernel many of the same
                   concerns  that  complicate transaction processing
                   systems.

                3. Sharing semantics are limited to  those  supplied
                   by  the  kernel.    In particular, an application
                   program cannot use domain specific  knowledge  to
                   allow  less  then  full  consistency  in  sharing
                   access  to  file  data.    This  can  result   in
                   inefficiency  in  the  handling  of  data sharing
                   across node boundaries.


              These problems typically have led  to  compromises  in  the

             actual  mapped  file  semantics  provided.  Most have either

             assumed that modifications to read/write  mapped  files  are

             not  guaranteed  to  be  consistent  in the face of multiple

             writers,  or  they  guarantee  consistency  only  for  those

             processes which share files on a single network node.

             3. The Uses of Shared Memory

              Many  of the potential uses of shared memory do not require

             a file mapping interface.  In fact, such  an  interface  may

             present  problems.    Memory sharing is often suggested as a

             way of overcoming traditional Unix deficiencies by providing

             for:

                - fine granularity multiprocessing,

                - ultra-fast IPC,

                - database management support and/or

                - reduced overhead file management.

             But  of  these  potential  uses  of  shared memory, only two

             require some kind of mapped file facility and of these  only

             one  fits  the  traditional  mmap  model  of file access and

             shared data consistency.



             3.1. Fine grain multiprocessing

              The need to support fine grain multiprocessing  has  forced

             several  multiprocessor  manufacturers to adopt some form of

             memory sharing in their  multiprocessor  versions  of  Unix,

             e.g.  in  Sequent's  Dynix [2]  and Encore's UMax [3].  This

             kind of shared memory often takes the form of  an  mmap-like

             primitive  which  acts  on  a  special device or file.  Fine

             grain multiprocessing is accomplished by  creating  as  many

             processes  as there are available processors which then mmap

             the shared memory object and synchronize through  it.    The

             only  reason  such  a  facility  would  want  a  mapped file

             interface is the benefit provided by using Unix's filesystem

             name  space  for referring to shared data.  There is no need

             for the shared data to be disk resident or permanent.

             3.2. Fast IPC

              Shared memory can be used  as  a  kind  of  ultra-fast  IPC

             facility,  especially  where large data structures are built

             in  shared  memory  by  one  process  and  then  managed  or

             manipulated  by  another.   An example of a potential use of

             this  kind  can  be  found  in  the   relationship   between

             multiphase program components such as the typical C language

             preprocessor and compiler.  Already such programs use  files

             or  pipes to accomplish their goals.  The advantages of such

             a fast IPC facility are actually diminished by tying it to a

             similar  shared file construct which would require some form

             of file system creation/destruction cost  as  well  as  disk

             I/O.



             3.3. Database management

              Designers   of  database  management  systems  have  argued

             against Unix at least partly because  of  its  inability  to

             share  data  between  potential database client programs and

             transaction  managers,  data  managers  and  recovery  logs.

             Systems of this sort need both sharing between processes and

             sharing of data pages in files  to  accomplish  their  ends.

             Unfortunately,  an  mmap-like construct does not, by itself,

             resolve  the  problems  posed  by  database  systems.    For

             example,  it  may be important for a database system to know

             when data is going to be moved from volatile storage to disk

             so  that  a  database  recovery  manager  can update crucial

             portions  of  the  recovery  log   in   advance [7]   (i.e.,

             write-ahead  logging).    In  addition,  the  consistency of

             shared memory must either be absolute,  or  the  consistency

             model must be well understood and manageable by the database

             transaction manager -- a fact  often  remarked  by  database

             builders  on  other systems with shared file constructs such

             as Apollo's Aegis [4].



             3.4. Efficient file access

              By far the most compelling  general  argument  for  linking

             shared  memory  with memory mapped files is the need in Unix

             for reducing  the  overhead  of  file  management.    Partly

             because  Unix was originally designed at a time when primary

             memory was a scarce commodity, traditional Unix programs are

             I/O  intensive.    Even  the  Unix  pipe  facility  was once

             implemented  as  file  I/O  to  conserve  memory.    As  the

             relationship  between  the  costs  of  memory  and secondary

             storage have changed, large memory Unix systems are  limited

             more  by  their  I/O capacity than by memory.  A mapped file

             facility  could  reduce  the  cost  of  I/O  operations   by

             eliminating  a  copy operation from the Unix buffer cache to

             process  memory  and  also   provide   for   better   memory

             utilization  by  allowing more than one process to share the

             same physical memory when accessing the same file.

             4. Mach Memory Primitives

              Rather than support sharing only through an mmap  model  of

             shared  memory  through shared files, Mach provides a number

             of  non-file  based  mechanisms  for  sharing   data   among

             computational entities:

                - Unrestricted,    fine    grain   sharing   between
                  processors in a tightly coupled multiprocessor can
                  be achieved by using the Mach notion of thread.  A
                  thread can be thought of as a lightweight  process
                  which   shares   an   address   space  with  other
                  lightweight processes.  The Unix notion of process
                  has  been  split  into  task  and  thread.  A task
                  defines an address space and  resource  domain  in
                  which  a number of program control flows (threads)
                  may coexist.  Using this multiple thread per  task
                  mechanism,  an  application  may  easily  share  a
                  single  address  space  among  separate  executing
                  entities.

                - In addition to unrestricted sharing using threads,
                  Mach allows tasks to  read/write  share  protected
                  ranges  of  virtual addresses through inheritance.
                  A Mach task can specify any portion of its address
                  space to be shared read/write with its children as
                  the result of a task_create operation.   The  fact
                  that  memory  is  shared  only through inheritance
                  guarantees  that  the  shared  memory  is   always
                  located  within a single host (or cluster within a
                  host).  This allows the kernel to guarantee  cache
                  consistency for such memory.  Another advantage of
                  this method of data sharing  is  that  it  ensures
                  that  shared  memory is always located at the same
                  virtual address in each  inheriting  task.    This
                  avoids  the  often  difficult programming problems
                  caused by pointer address aliasing in shared  data
                  structures.

                - Physical  memory  can  be  shared copy-on-write by
                  taking advantage of Mach's integration of IPC  and
                  virtual   memory  management.    Applications  not
                  requiring read/write memory sharing can  use  this
                  feature  to transfer large amounts of data between
                  tasks without actually copying data.  In effect, a
                  multiphase  application  can  effectively  forward
                  between  components  the  actual  physical  memory
                  containing  important data.  The sender in such an
                  exchange  is  always  protected  because  data  is
                  logically  sent  by  value. The kernel uses memory
                  management tricks  to  make  sure  that  the  same
                  physical  page  is  available  to  both sender and
                  receiver unless or until a write operation occurs.

                - Finally, applications may define their own sharing
                  semantics  within  a  distributed  system  of Mach
                  hosts using  the  Mach  external  pager  facility.
                  This    external   pager   mechanism   allows   an
                  application to control  many  aspects  of  virtual
                  memory  management  for regions of virtual memory.
                  An external pager  may  implement  fully  coherent
                  network shared memory, or a shared memory paradigm
                  that requires clients to maintain their own  cache
                  consistency  (if consistency is even desired).  It
                  allows a database recovery manager to  be  advised
                  of  the  kernel's  need  to  flush data to disk in
                  advance  and  thus  permit  efficient  write-ahead
                  logging.



             4.1. Mach virtual memory operations

              Table 4-1 lists the set of operations that can be performed

             on the virtual address space of a  task.    Mach  calls  are

             specified  to  act  on object handles called ports which are

             simplex communication channels on which messages  are  sent.

             A  more  complete  description  of  Mach  ports  and calling

             conventions can be found in [1].


              A task address space consists of an ordered  collection  of

             mappings  to memory objects; all threads within a task share

             access to that address space.  A Mach  memory  object  (also

             called  a  paging object) is a data repository, provided and

             managed by a server.   The  size  of  an  address  space  is
             limited   only   by   the  addressing  restrictions  of  the

                              Virtual Memory Operations
                
                   vm_allocate (task, address, size, anywhere)          A
                                                     virtual memory eithe
                                                     at a specified addre

                   vm_copy (task, src_addr, count, dst_addr)            V
                                                     from one address to

                   vm_deallocate (task, address, size)     Deallocate a r
                                                     i.e. make them no lo

                   vm_inherit (task, address, size, inheritance)        S
                                                     of an address range.

                   vm_protect (task, address, size, set_max, protection)
                                                     of an address range.

                   vm_read (task, address, size, data, data_count)      R
                                                     of a task's address

                   vm_regions (task, address, size, elements, elements_co
                                                     region of task's add

                   vm_statistics (task, vm_stats)    Return statistics ab
                                                     of memory by task.

                   vm_write (task, address, count, data, data_count)    W
                                                     of a task's address
                

                                     Table 4-1:

             All VM operations apply to a task (represented by a port) an
               but vm_statistics specify an address and size in bytes.
             anywhere is a boolean which indicates whether or not a vm_al
             allocates memory anywhere or at a location specified by addr

                


             underlying hardware.  For example, an IBM  RT  PC  task  can

             address  a  full 4 gigabytes of memory under Mach, while the

             VAX architecture allows at most 2 gigabytes of user  address

             space.


              The  basic  memory operations permit both copy-on-write and

             read/write  sharing  of  memory   regions   between   tasks.

             Copy-on-write sharing between unrelated tasks is usually the

             result of large message transfers. An entire  address  space

             may  be  sent  in  a single message with no actual data copy

             operations performed.  Read/write  shared  memory  within  a

             task  creation  tree  can  be created by allocating a memory

             region and setting its inheritance attribute.   Subsequently

             created  child  tasks  share  the  memory  of  their  parent

             according to its inheritance value.   The  only  restriction

             imposed  by  Mach  on  the nature of the regions that may be

             specified for virtual memory operations is that they must be

             aligned  on system page boundaries.  The system page size is

             a boot time parameter and can be any power of two that is  a

             multiple of the hardware page size.



             4.2. Managing external pagers

              The  basic  task  virtual  memory  operations  allow memory

             sharing through inheritance between tasks in the  same  task

             creation   subtree.      Read/write  shared  memory  between

             unrelated tasks  can  be  implemented  through  the  use  of

             external pagers -- tasks which allocate and manage secondary

             storage objects.


              The Mach interface for external pagers can best be  thought

             of  as  a message protocol used by a pager and the kernel to

             communicate with each other about the contents of  a  memory

             object.    The external pager interface to the kernel can be

             described in terms of operations  requested  by  the  kernel

             (messages  sent  to  a paging_object port) and calls made by

             the external pager on  the  kernel  (messages  sent  to  the

             kernel's   pager_request_port   associated   with  a  memory

             object).  Tables 4-2 and 4-3 describe these two interfaces.

                          Kernel to External Pager Interface
                  
                     pager_init (paging_object,  Initialize a memory obje
                          pager_request_port, pager_name)

                     pager_data_request (paging_object,              Requ
                          pager_request_port, offset,
                          length, desired_access)

                     pager_data_write (paging_object, offset         Writ
                          data, data_count)

                     pager_data_unlock (paging_object,               Requ
                          pager_request_port, offset,
                          length, desired_access)

                     pager_create (old_paging_object,                Acce
                          new_paging_object, new_request_port,
                          new_name)
                  

                                     Table 4-2:

             Calls made by Mach kernel to a task providing external pagin

                  


              A memory object may be mapped into the address space  of  a

             task  by  exercising  the  vm_allocate_with_pager primitive,

             specifying a paging object port.  This  port  will  then  be

             used by the kernel to refer to that object.  A single memory

             object may be mapped more than once (possibly  in  different

             tasks).    The Mach kernel provides consistent shared memory

             access to all mappings of the same memory object on the same

             uniprocessor  or  multiprocessor.  The role of the kernel in

             paging is primarily that of a physical  page  cache  manager

             for objects.


              When  asked  to map a memory object for the first time, the

             kernel responds by making a pager_init call  on  the  paging

             object port.  Included in this message are:

                - a  pager  request port, which the pager may use to
                  make cache management requests of the Mach kernel,

                - a pager name port, which the kernel  will  use  to
                  identify  this  memory  object  to  other tasks in
                  vm_regions calls.  (The paging object and  request
                  ports  cannot  be used for this purpose, as access
                  to those ports allows complete access to the  data
                  and management functions.)

             The Mach kernel holds send rights to the paging object port,

             and send,  receive,  and  ownership  rights  on  the  paging

             request and paging name ports.


              In  order  to  fulfill  a cache miss (i.e. page fault), the

             kernel issues a pager_data_request call specifying the range

             (usually  a  single page) desired.  The pager is expected to

             supply the requested data using the pager_data_provided call

             on  the  specified  paging  request port.  To flush modified

             cached data, the kernel performs  a  pager_data_write  call,
             including  the  data  to  be written and its location in the

             memory object.  When the pager  no  longer  needs  the  data

             (e.g.   it   has  been  successfully  written  to  secondary

             storage), it is expected to use the  vm_deallocate  call  to

             release the cache resources.


              Since  the  pager  may  have  external  constraints  on the

             consistency  of  its  memory  object,  the  Mach   interface

             provides  some functions to control caching; these calls are

             made using the pager request port provided at initialization

             time.

                          External Pager to Kernel Interface
                  
                     vm_allocate_with_pager (task, address,          Allo
                          size, anywhere, paging_object, offset)     addr

                     pager_data_provided (paging_object_request,     Supp
                          offset, data, data_count, lock_value)      of a

                     pager_data_lock (paging_object_request,         Prev
                          offset, length, lock_value)                data

                     pager_flush_request (paging_object_request,     Forc
                          offset, length)     to be destroyed.

                     pager_clean_request (paging_object_request,     Forc
                          offset, length)     to be written back to a mem

                     pager_cache (paging_object_request,             Noti
                          should_cache_object)                       know
                                              after all references to it 

                     pager_data_unavailable
                          (paging_object_request,                    Noti
                          offset, size)       available for that region o
                  

                                     Table 4-3:

             Calls made by a task on the kernel to allocate and and manag

                  


              A  pager_flush_request call causes the kernel to invalidate

             its cached copy  of  the  data  in  question,  writing  back

             modifications if necessary.  A pager_clean_request call asks

             the kernel to  write  back  modifications,  but  allows  the

             kernel  to  continue  to  use  the cached data.  A pager may

             restrict the use of cached data by issuing a pager_data_lock

             request,  specifying  the  types  of access (of read, write,

             execute) which may be permitted.  For example, a  pager  may

             wish  to  temporarily allow read-only access to cached data.

             The locking on  a  page  may  later  be  changed  as  deemed

             necessary by the pager.


              When  a  user  task  requires greater access to cached data

             (e.g.  a write fault on a read-only page) than the pager has

             permitted,  the kernel issues a pager_data_unlock call.  The

             pager is expected to respond by changing the locking on that

             data when it is able to do so.


              When  no  references  to  a  memory  object remain, and all

             modifications have been written back to  the  paging  object

             port,  the  kernel deallocates its rights to the three ports

             associated with that memory  object.    The  pager  receives

             notification  of the death of the request and name ports, at

             which time it can perform appropriate shutdown.


              In order to attain better cache performance,  a  pager  may

             permit  the data for a memory object to be cached even after

             all address map references are gone by calling  pager_cache.

             Permitting such caching is in no way binding; the kernel may

             choose to relinquish its access to the memory  object  ports

             as it deems necessary for its cache management.


              The  Mach  kernel may itself need to create memory objects,

             either to provide backing  storage  for  zero-filled  memory

             (vm_allocate),  or  to  implement  virtual  copy operations.

             These memory objects are managed by a  default  pager  task,

             which  is known to the kernel at system initialization time.

             When the kernel creates such a memory object, it performs  a

             pager_create  call (on the default pager port); this call is

             similar in form to pager_init.  Since  these  kernel-created

             objects  have  no  initial memory, the default pager may not

             have data to provide in response to  a  request.    In  this

             case, it should perform a pager_data_unavailable call.


              Since  interaction  with  pagers  is conducted only through

             ports, it is possible to map the  same  memory  object  into

             tasks  on  different  hosts  in a distributed system.  While

             each  kernel  keeps  its  own  uses  of  the   cached   data

             consistent,   the  pager  is  responsible  for  any  further

             coordination.    Since  each  Mach  kernel  will  perform  a

             pager_init  call  upon  its  first  use  of a memory object,

             including its own request and name ports, a pager can easily

             distinguish the various uses of its data.

             5. A Unix Interface for File Mapping

              Shared  memory  can  be obtained in Mach either through the

             use of memory inheritance or external pagers.   Given  these

             mechanisms  for  sharing  data, there is no need to overload

             the Unix filesystem  in  order  to  provide  shared  memory.

             Nevertheless, the potential performance advantages of mapped

             files make them desirable for Unix emulation under Mach.  In

             addition,  the  ease  of  programming associated with mapped

             files is attractive in both the Unix and Mach environments.


              At present, Mach provides a single new Unix  domain  system

             call for file mapping:

                 map_fd(fd, offset, addr, find_space, numbytes)
                         int             fd;
                         vm_offset_t     offset;
                         vm_offset_t     *addr;
                         boolean_t       find_space;
                         vm_size_t       numbytes;


              Map_fd is called with an open Unix file descriptor (fd) and

             if successful results in a virtual copy of the  file  mapped

             into  the address space of the calling Unix process.  Offset

             is the byte offset within the file at which  mapping  is  to

             begin.   The offset may be any byte offset in the file, page

             alignment is not required.  Addr is a pointer to the address

             in  the  address  space  of the calling process at which the

             mapped file should start.  This address, unlike the  offset,

             must  be  paged  aligned.  If find_space is TRUE, the kernel

             will select an unused address range and return it in  *addr.

             The number of bytes to be mapped is specified by numbytes.


              The   implementation   of   map_fd  was  a  straightforward

             application of internal Mach primitives for virtual  copying

             regions  of  memory  and  external  pagers [5, 8].    When a

             request is made for a file to be mapped into a user  address

             space, the kernel creates a temporary internal address space

             into which the file is mapped.  This mapping is accomplished

             with  the  vm_allocate_with_pager  primitive.    The  kernel

             specifies that new memory is to be allocated  and  that  the

             new  memory  will  be  backed  by  the internal kernel inode

             pager.  Then the file data is moved to the  process  address

             space  by  a call to vm_copy.  Once this is done, the kernel

             can deallocate the temporary map.

             6. Uses of Mapped Files in Mach

              Files mapped using map_fd can be used in a variety of ways.

             Mach  itself  uses  file  mapping  internally  to  implement

             program loading.   File  mapping  can  also  be  used  as  a

             replacement  for  buffer  management  in  the  standard  I/O

             library.



             6.1. File Mapping and Shared Libraries

              Mach uses the  mapped  file  interface  to  implement  both

             program  loading and a general form of shared libraries.  In

             the current Mach system, there  are  two  types  of  program

             loaders.    The  first program loader executes in the kernel

             and implements the Unix  exec  system  call.    This  loader

             handles  both  a.out and COFF format binary files for binary

             compatibility with existing  systems.    The  second  loader

             executes  in  a  user  task and handles MACH-O format binary

             files.  Both loaders use mapped files.


              The MACH-O format was devised to be flexible enough  to  be

             used  as  a  single file format for fully resolved binaries,

             unresolved object files, shared libraries and "core"  files.

             It provides enough backward compatibility with older formats

             (e.g., a.out) to salvage most existing  code  for  debuggers

             and related applications.


              The MACH-O format can roughly be though of as a sequence of

             commands to be executed by a program loader.  The layout  of

             a MACH-O file is summarized as:

                 start
                         header
                         command_id, command_info
                         command_id, command_info
                                 .
                                 .
                                 .
                         command_id, command_info
                 ENDMARKER


              Each command consists of a command identifier followed by a

             command-dependent number of arguments.  Some of the commands

             supported are:

                 READ_ONLY       Map  in  data  read-only  (e.g.  a  text
                                 segment).

                 WRITEABLE       Map in  data  read/write  (e.g.  a  data
                                 segment).

                 ZEROFILL        Allocate  zero-fill  memory  (e.g. a bss
                                 segment).

                 REGISTER        Create a thread in the task and set  its
                                 register state.

                 LOADFILE        Map  in  data  from another file (e.g. a
                                 shared library).

                 RELOCATE        Relocate a specified address.

                 END_LOAD        Loading complete.

              The  header  contains  a  magic  number  indicating  MACH-O

             format.    It also contains other useful information such as

             version information, and a machine-type specifier.  Finally,

             the  header  specifies  the  type  of file represented, e.g.

             executable, object file or shared library.


              The MACH-O program loader operates by scanning a load  file

             and  executing  commands as necessary.  In the typical case,

             it uses the map_fd call to map portions of  files  into  its

             address  space.   It then places the data in the image to be

             executed using the vm_write operation.  Since  copy-on-write

             is  used  at the base of the virtual memory primitives it is

             possible to share both code and writable data.    Each  task

             that writes data within a shared library will get a new copy

             as each page is written for the first time.  Pages that  are

             not written will be physically shared by all tasks.



             6.2. File Mapping and Standard I/O

              The Mach mapped file mechanism has been used to build a new

             version of the C library buffered I/O package.  When a  file

             is  fopened  it  is mapped in its entirety into the caller's

             address space.  The semantics of the  buffered  i/o  package

             are  not changed.  The existing stdio buffer has, in effect,

             been enlarged to the size of the file.  When a  write  takes

             place  only  the  data  buffer  is changed.  The file is not

             guaranteed to change on disk until a fflush or fclose  takes

             place.  As  with  normal buffered I/O, if two processes have

             the same file open for reading  and  writing,  there  is  no

             guarantee  how  the  reads and writes will intermix.  A read

             may get new information off the disk copy of the file, or it

             may use information that was already buffered.


              The   primary   rationale   for  this  change  is  improved

             performance.  Table 6-1 shows the time for  simple  buffered

             I/O  operations  both  with  and  without  the  change.   In

             addition to improved performance, the use  of  file  mapping

             also  has  the  effect  of  reducing  the memory load on the

             system.  In a traditional Unix  implementation  fopen  would

             allocate new memory to the calling process and copy the data

             from the Unix buffer cache into that new memory at the  time
             of  a  read.   Using this new package and Mach file mapping,

                  

                     Unmapped vs. Mapped Buffered I/O Performance
                   
                       Test program   First time     Second time
                                      user system elapsed
                  
                       old_read       6.1u   0.62s   0:08           

                       new_read       6.0u   0.71s   0:08           

                       map_read       2.8u   0.76s   0:04           
                  

                                     Table 6-1:

                 Time to read a 492544 byte file using standard I/O.
                         (Mach, 4K file system, MicroVAX II)

              old_read performs fopen followed by a loop of getc calls.
             new_read is identical to old_read with new mapped file packa
             map_read uses fmap and reads data by array reference, not ge

                  


             each new call  to  fopen  will  reuse  any  physical  memory

             containing  file  data  pages,  reducing  the  number of I/O

             operations.  (See table 6-2.)

                  

                         Multiple Access File I/O Performance
                   
                          Test program        user     system  elaps
                  
                          old_read[1]         25.4u     1.8s     1:2
                          old_read[2]         25.3u     2.0s     1:2
                          old_read[3]         25.1u     2.2s     1:2

                          new_read[1]         24.0u     1.6s     1:1
                          new_read[2]         24.0u     1.8s     1:1
                          new_read[3]         24.2u     1.6s     1:1
                  

                                     Table 6-2:

                 Time to read a 1970176 byte file using standard I/O.
                         (Mach, 4K file system, MicroVAX II)

             Each program is run 3 times in parallel and times are listed
                Instance numbers for each invocation are in brackets.
                 Each program accesses the same file simultaneously.

              old_read performs fopen followed by a loop of getc calls.
             new_read is identical to old_read with new mapped file packa

                  


              In addition to traditional buffered I/O calls,  the  mapped

             file  version of buffered I/O has had added to it a new call

             which allows an application program to directly  access  the

             mapped  file  data  and  thus further improve performance by

             eliminating the copying of data by fread and  fwrite.    The

             new  routine is called fmap and is a buffered I/O compatible

             version of map_fd.


              To read map a file with fmap the user calls:

                 stream = fopen("filename", "r");  /* existing call *
                 data = fmap(stream, size);        /* new call */

             where data is a pointer to a region of virtual memory  where

             the  file  contents  are buffered, and size is the suggested

             size for the data buffer; if that size  is  zero,  then  the

             implementation will choose a suitable size. As before,

                 bufsize = fbufsize(stream)

             returns the actual size of the buffer.  Once fmap is called,

             the user can reference file data by using the  data  pointer

             and  any  offset  less  than bufsize.  The user may also mix

             fseek, and fread calls with direct data  references.    Once

             the user is finished with the file the call

                 fclose(stream);                 /* existing call */

             should  be used to deallocate the virtual address space used

             by the mapped file.


              To write map a file the user would:

                 stream = fopen("filename", "w");/* existing call */
                 data = fmap(stream, size);      /* new call */

             where size is used as an initial buffer size; if  that  size

             is  zero,  the  implementation  will choose a suitable size.

             Initially, the buffer will be zero-filled.    Once  fmap  is

             called, the user may write into any part of the file with an

             offset less than bufsize.  An fwrite or fseek call  with  an

             offset  greater  than bufsize will cause an error. To expand

             the buffer size, the user may call fmap again with a  larger

             size parameter.  The calls

                 fflush(stream);                 /* existing call */
                 fclose(stream);                 /* existing call */

             continue  to  work  as  before.  Similarly, files opened for

             append and read/write may be fmaped.


              Table 6-3 shows the time advantage which can be  gained  by

             using fmap rather than conventional I/O.

                  

                     Unmapped vs. Mapped Buffered I/O Performance
                   
                       Test program   First time     Second time
                                      user system elapsed  I/O
                  
                       old_read       11.5u  3.1s    0:21  481io    

                       map_read       11.2u  2.9s    0:15  480io    
                  

                                     Table 6-3:

                          Time to read a 1970176 byte file.
                         (Mach, 4K file system, MicroVAX II)

             old_read performs open, mallocs buffer, calls read for whole
                     file and then reads data by array reference.

             map_read uses fopen and fmap and reads data by array referen

                  

             7. The Effect of Mach Memory Mapping on Performance

              File  mapping  is hardly free(Unless the output is going to

             /dev/null!). Even when a page is already in physical memory,

             a  page  fault  must be taken on the first process access to

             validate the corresponding hardware map entries.   Currently

             such  a  fault takes approximately 1.0-1.4 milliseconds on a

             MicroVAX II with a 4K page size.   There  are  also  several

             ways in which mapped files can adversely affect performance:

                - If  the file to be mapped is smaller than a single
                  page, file mapping will always result  in  a  full
                  page  being  allocated  in  physical  memory  with
                  excess data filled with zeroes.

                - Mapped files compete with program  text  and  data
                  for  physical  memory.    In  a  traditional  Unix
                  system,  user  programs  maintain   a   fixed-size
                  buffer,  so  the buffer cache limits the amount of
                  memory which can be consumed in accessing a file.


              Nevertheless, as the performance of the  new  standard  I/O

             library points out, useful performance gains can be achieved

             using Mach memory mapping.  In fact, because the Mach kernel

             uses  mapped  files  internally  to  implement exec, overall

             performance of vanilla 4.3 BSD programs  is  often  improved

             when  run  on  Mach. Particularly dramatic performance gains

             are seen on machines where  the  processor  speed  is  high,

             memory  is plentiful and disk is a bottleneck.  For example,

             performance gains of over 20% have been achieved  on  a  VAX

             8650.    Improvement  can  be  found, however, even on small

             memory systems with moderately heavy loads.   The  multiuser

             benchmark  load used to study the performance of the CMU ITC

             VICE/VIRTUE file system [6] ran  10-15%  faster  under  Mach

             than  a comparable BSD derived kernel on an IBM RT PC with 4

             megabytes of memory.


              These performance improvements  are  especially  surprising

             because  many  basic operating system overheads are actually

             larger in Mach than in 4.3 BSD.  The use of special  purpose

             scheduling instructions has, for example, been eliminated in

             the VAX version of Mach.  The Mach equivalent  of  the  Unix

             u-area  is  not  at  a fixed address so as to allow multiple

             threads of control. This increases  the  cost  of  task  and

             thread  data  structure  references  significantly [9].   In

             addition, VAX Mach is run as a multiprocessor system even on

             uniprocessors  at  CMU,  so  virtually all kernel operations

             have had their costs increased by locking concerns.

             8. Conclusion

              Mach's basic memory primitives  provide  applications  with

             several  mechanisms  for  sharing memory.  As such, a mapped

             file interface under Mach is not required for shared memory.

             Mach  does  provide a non-shared interface for mapped files.

             This interface is  not  only  appropriate  for  implementing

             various  applications  (e.g.  shared  libraries  and program

             loading),  but  has  increased  both  the  performance   and

             functionality of the system.


              The  internal  implementation  of Mach VM does not preclude

             shared read/write file mapping.  Mach does, in fact, support

             the 4.2 mmap call for the purposes of mapping special device

             memory (typically used for frame buffers).   The  mmap  call

             will also work on normal files but will not map files shared

             between processes.    This  restriction  was  not  based  on

             technical issues, but was an intentional modification of the

             mmap semantics.  The Mach designers felt it was important to

             discourage  programmers from writing programs which depended

             on sharing data which might or  might  not  be  consistently

             maintained in a loosely coupled environment.

             9. Acknowledgements

              The  Mach  VM  implementation  was  done  primarily by Avie

             Tevanian, Michael Young and David Golub.  The implementation

             has  been ported five different machine types and has yet to

             need modification to accommodate new architectures.


              The authors would also like to acknowledge others who  have

             contributed  to  the  Mach  kernel  including  Mike Accetta,

             Robert Baron, David Black, Jonathan Chew, Eric  Cooper,  Dan

             Julin, Glenn Marcy and Robert Sansom.  Bob Beck (of Sequent)

             and Charlie Hill (of North American Philips) helped with the

             port  to the Balance 21000.  Fred Olivera and Jim Van Sciver

             (both formerly of  Encore)  helped  with  the  port  to  the

             MultiMax.
                                      REFERENCES

             [1]   Mike Accetta, Robert Baron, William Bolosky, David
                   Golub, Richard Rashid, Avadis Tevanian, Michael Young.
                   Mach: A New Kernel Foundation for UNIX Development.
                   In Proceedings of Summer Usenix.  July, 1986.

             [2]   Sequent Computer Systems, Inc.
                   Dynix Programmer's Manual
                   Sequent Computer Systems, Inc., 1986.

             [3]   Encore Computer Corporation.
                   UMAX 4.2 Programmer's Reference Manual
                   Encore Computer Corporation, 1986.

             [4]   Leach, P.L., P.H. Levine, B.P. Douros, J.A.  Hamilton,
                   D.L. Nelson and B.L. Stumpf.
                   The Architecture of an Integrated Local Network.
                   IEEE Journal on Selected Areas in Communications
                      SAC-1(5):842-857, November, 1983.

             [5]   Rashid, R., Tevanian, A., Young, M., Golub, D., Baron,
                   R., Black, D., Bolosksy, W. and Chew, J.
                   Machine-Independent Virtual Memory Management for
                      Paged Uniprocessor and Multiprocessor
                      Architectures.
                   Technical Report , Carnegie-Mellon University,
                      February, 1987.

             [6]   Satyanarayanan, M., et.al.
                   The ITC Distributed File System: Principles and
                      Design.
                   In Proc. 10th Symposium on Operating Systems
                      Principles, pages 35-50.  ACM, December, 1985.

             [7]   Alfred Z. Spector, Dean S. Daniels, Daniel J. Duchamp,
                   Jeffrey L. Eppinger, Randy Pausch.
                   Distributed Transactions for Reliable Systems.
                   In Proceedings of the Tenth Symposium on Operating
                      System Principles, pages 127-146.  ACM, December,
                      1985.
                   Also available in Concurrency Control and Reliability
                      in Distributed Systems, Van Nostrand Reinhold
                      Company, New York, and as Technical Report
                      CMU-CS-85-117, Carnegie-Mellon University,
                      September 1985.

             [8]   Young, M., Tevanian, A., Rashid, R., Golub, D.,
                   Eppinger, J., Chew, J., Bolosky, W., Black, D. and
                   Baron, R.
                   The Duality of Memory and Communication in the
                      Implementation of a Multiprocessor Operating
                      System.
                   Technical Report , Carnegie-Mellon University,
                      February, 1987.

             [9]   Tevanian, A., Rashid, R., Golub, D., Black, D.,
                   Cooper, E., and Young, M.
                   Mach Threads and the UNIX kernel:  The Battle for
                      Control.
                   Technical Report , Carnegie-Mellon University, April,
                      1987.

                                  Table of Contents
             1. Introduction                                            0
             2. The Problems of a Mapped File Interface                 0
             3. The Uses of Shared Memory                               0
                  3.1. Fine grain multiprocessing                       0
                  3.2. Fast IPC                                         1
                  3.3. Database management                              1
                  3.4. Efficient file access                            1
             4. Mach Memory Primitives                                  1
                  4.1. Mach virtual memory operations                   1
                  4.2. Managing external pagers                         2
             5. A Unix Interface for File Mapping                       3
             6. Uses of Mapped Files in Mach                            4
                  6.1. File Mapping and Shared Libraries                4
                  6.2. File Mapping and Standard I/O                    4
             7. The Effect of Mach Memory Mapping on Performance        5
             8. Conclusion                                              6
             9. Acknowledgements                                        6

                                    List of Tables
             Table 4-1:                                                 2
             Table 4-2:                                                 2
             Table 4-3:                                                 3
             Table 6-1:                                                 5
             Table 6-2:                                                 5
             Table 6-3:                                                 5