MACH I486/I386 INSTALLATION NOTES

                          Carnegie Mellon University
                             Pittsburgh, PA 15213
                                  6 July 1994

1. Introduction
  The  Mach i486/i386 release is a complete system that is compatible with both
the Mach 2.5 monolithic kernel and the Mach 3.0  micro  kernel  and  UX  single
server  combination.  On  IBM PS/2 machines with the microchannel architecture,
only Mach 3.0 is supported. For the duration of this document,  any  references
to  IBM  PS/2  machines  refer  specifically  to  PS/2's  with the microchannel
architecture.  This system has an application environment that is close to  BSD
4.3-Tahoe.  It  has  been  distributed  since  1990.   Most of the applications
provided in this release will run with either the Mach 2.5 or Mach 3.0  kernel.
There  are  a  few  programs where different versions must be used depending on
which kernel you are using.  This system can be used  to  build  the  Mach  3.0
micro-kernel and Unix server.

  The programs and libraries come from the 4.3BSD-TAHOE release.  Additionally,
we provide the Mach specific programs, include files,  and  libraries  (libmach
and  libthreads).    The  CMUCS  library  and  some of the CMUCS programs (most
notably rfs and sup) are also included with this  release.  Lastly,  since  the
Mach  I486/I386  2.5  kernel does not support BSD file system labels, most file
system tools are CMU tools derived from 4.3BSD.

  This release requires the recipient to have a Mach 2.5 or  Mach  3.0  license
from  CMU  and  BSD4.3  license  from  University  of  California which in turn
requires either a UNIX/32V, SYSTEM III or SYSTEM V source  license  from  AT&T.
Further,  we  are  only  allowed  to  distribute  Sun NFS to sites with Sun NFS
educational licenses.

  All the releases that are made by CMU are done only by an  Internet  transfer
protocol called SUP (Software Update Protocol).

  Two  additional  Mach  components can be uploaded with this system:  Mach 3.0
and MDOS.  Mach 3.0 divides the traditional  monolithic  kernel  into  a  micro
kernel  and  a server program.  The latter provides a "personality" to make the
whole behave like a particular operating system.    MDOS  is  a  DOS  emulation
package  for  use  under Mach 3.0.  It uses the i486/i386 hardware Virtual 8086
mode to run an emulated DOS as a Mach 3.0 task. To find out  about  MDOS,  read
the file mdos.ps on mach.cs.cmu.edu in the /usr/mach/public/doc/unpublished.

  The  initial sup will put both a Mach 3.0 kernel/server and a Mach 2.5 kernel
on the root of the hard disk. By default, the system will boot  Mach  3.0.  For
more    information   about   Mach   3.0,   read   the   documents   mach3_sup,
mach3_build.{ps,doc} and mach3_setup.{ps,doc} in  the  Mach  public  FTP  area,
mach.cs.cmu.edu, /usr/mach/public/doc/unpublished.

  This document assumes a working knowledge of the installation and maintenance
of a 4.3BSD system. If you are unfamiliar with the 4.3BSD  system,  you  should
read the system maintainers documentation for 4.3BSD.
2. Hardware Requirements for Mach on i386 Machines
  We only support machines with:
   - either an i386 or i486 processor
   - at least 5 Meg of memory.  We typically use 8Meg - 16Meg.
   - an  AT/ISA  compatible  bus, or IBM PS/2 microchannel bus. EISA buses
     can be used but  currently  none  of  our  drivers  use  the  32  bit
     functionality of the EISA bus.
   - an approved disk controller: (You should get at least 100Meg of disk.
     We typically use 300Meg drives.)
        * WD 1007 compatible disk controllers.
        * IDE disks (these are WD 1007 compatible).
        * Adaptec 1542B compatible SCSI controller.
        * Adaptec 1542C SCSI controller is supported by Mach 3.0 only.
        * SCSI controllers that make disks appear to  the  kernel  as  IDE
          disks, such as on IBM PS/2's.
        * ST506 controller [Note: they are awfully slow.]
   - displays:
        * simple displays in 25 x 80 character mode.
        * Color  SVGA  support from XFree86 Release 2.0 which supports the
          following accelerated chipsets:
             - 8514/A (and true clones)
             - ATI Mach8, Mach32
             - Cirrus CLGD5426, CLGD5428
             - S3 86C911, 86C924, 86C801, 86C805, 86C928
             - Western Digital WD90C31
        * And the following SVGA chipsets:
             - Tseng ET3000, ET4000AX, ET4000/W32
             - Western Digital/Paradise PVGA1
             - Western Digital WD90C00, WD90C10, WD90C11, WD90C30, WD90C31
             - Genoa GVGA
             - Trident  TVGA8800CS,  TVGA8900B,   TVGA8900C,   TVGA8900CL,
               TVGA9000
             - ATI 28800-4, 28800-5, 28800-a
             - NCR 77C22, 77C22E
             - Cirrus   Logic   CLGD5420,  CLGD5422,  CLGD5424,  CLGD5426,
               CLGD5428, CLGD6205,  CLGD6215,  CLGD6225,  CLGD6235  Compaq
               AVGA
             - OAK OTI067, OTI077
   - high  density  3  1/2"  and/or 5 1/4" floppies at 1.44Meg and 1.2Meg,
     respectively.

  We support but do not require:
   - Intel 80387 hardware floating point. (recommended)
   - The built-in serial line: COMi
   - The built-in parallel port: LPTi
   - ethernet controller boards (non-IBM PS/2):
        * 3COM's EtherLink I and EtherLink II (sometimes  known  as  3c501
          and 3c503),
        * Western Digital's WD8003E and WD8013E ethernet boards.
        * SMC's  WD8003E  Elite  and WD8013E Elite ethernet boards(Western
          Digital sold its WD8003 ethernet product to  SMC  shortly  after
          reengineering the board.  This board is called the WD8003 Elite.
          A recently sampled board seems to work fine, but there have been
          problems  with  some early units.  (They would stop transmitting
          after a while.))
        * D-Link's Ethernet Pocket LAN Adapter DE-600
        * Intel's iMX586 or PC586/ENET586 ethernet board (Now obsolete)
   - The IBM token ring adapter (IBM PS/2)
   - Mice
        * Logitech 3-button mouse
        * Logitech Mouseman mouse
        * Microsoft 2-button mouse
        * PS2 mouse
   - Wangtek 1/4" standard 3M streamer.

  WE DO NOT SUPPORT:
   - NFS for commercial licensees of NFS

  NOTE: While Mach does not require a network interface for  normal  operation,
our  method  of installation assumes that you can get the files from CMU to the
target machine over the internet.

  Mach is being used at CMU on numerous i486, i386 and i386sx clones.

3. The Bootstrap Disks
  This distribution is intended to be loaded onto an empty  disk;  it  contains
all  the  binaries  and  sources that are needed.  The Mach boot floppies are a
pair of High Density (HD) floppy disks.  You can write 3 1/2" or 5  1/4"  disks
for  either  a  Mach  2.5  or  Mach 3.0 kernel; the data contained are the same
independent of floppy capacity.

  The first disk contains a bootstrap program and a copy of the "Mach  Kernel".
The  second  disk  contains  a file system with Unix binaries.  These disks are
intended to be used not only during the boot process, but also to recover  from
problems that might prevent you from being able to boot off the hard disk.

  The second disk contains (approximately):
      PORTFILE

      bin:
      [               dd              ls              setup
      cat             echo            mkdir           sh
      chmod           ed              mv              stty
      cp              hostname        pwd             sync
      date            ln              rm              tar

      dev:
      MAKEDEV and devices

      etc:
      badblocks       fdisk           ifconfig        passwd          route
      badsect         fsck            init            rc              services
      clri            group           mkfs            reboot          termcap
      diskutil        halt            mknod           restore         umount
      dump            hosts           mount           rfshost         vtoc

      mnt:
      tmp:

      usr/bin:
              rfs     sup
      usr/games:
              rain
      usr/ucb:
              ftp     telnet

  The  installation  process  presumes  that  you are going to boot your target
i486/i386 machine from the floppy disks that we have provided and then transfer
the  files from CMU onto the target machine.  In this document, we presume that
you are going to access the Mach binaries and sources via the  internet.    tar
and dump/restore are also provided, here, to allow you to copy the sources into
some other local machine and then to transfer them to the PC by tape,  floppies
or  lan  access.  There is some cleverness needed to install the system from an
intermediary machine. If you  plan  to  do  this,  refer  to  Appendix  IV  for
instructions.

  You  will  be  requesting binaries and sources from a database machine at CMU
using the sup database update program/protocol.  (See  the  sup  manual  page).
Your  machine  will  authenticate  to  the database machine; it must explicitly
supply an encryption key (CRYPT) in the protocol negotiations.

  The first steps in preparing for a internet distribution are:
   - Verify that you have a Mach 2.5 license.
   - Verify that your site has internet access.
   - Verify that your machine has an acceptable network interface.
   - Register your machine name, internet address,  and  CRYPT  with  CMU.
     Send  this information to mach@cs.cmu.edu.  You should chose your own
     CRYPT, a character string at least  6  characters  long  or  we  will
     assign a random one.
   - Specify  what  machine  you wish to FTP the floppy images to if it is
     different from the machine you plan to SUP to.

  You will need to have a machine running a Unix system that is able  to  dd  a
disk  image  on to a floppy of the suitable size. You can either sup or ftp the
floppy images from us. The SUP collection is floppy.image. (see the list of SUP
collections  in Appendix III).  For either sup or ftp you will need to register
the name of the machine you will be using with us before you will  have  access
to the images.

4. Before You SUP



4.1. Low Level Disk Formatting
  You  might  need  to  perform  a  "low level format" of your hard disk.  This
procedure partitions the disk into sectors and then looks for bad areas on  the
disk.    It usually takes several hours.  Some manufacturers (HP, Toshiba, ...)
ship the disks preformatted.  Also, some computer stores will format  the  disk
for  you  before they ship the system.  In our experience, ESDI disks generally
need to be formatted, IDE disk should never be formatted, and while SCSI  disks
can be formatted, this seems unnecessary.

  The  documentation  you  got with your disk controller or machine or DOS will
tell you how to format your disk.  The procedures vary widely  and  are  beyond
the scope of this discussion.  PLEASE DO NOT CALL US IF YOU ARE HAVING PROBLEMS
WITH THIS STEP.



4.2. Manual Pages
  You should acquaint yourself with the attached manual pages for the programs:
diskutil, fdisk, vtoc, badblocks and sup.



4.3. Booting to Single User mode
  In  the  guide  below,  we  presume  that  nothing  will  go  wrong.   In our
experience, 80% - 90% of the installations proceed smoothly,  but  there  is  a
common  set  of  pitfalls.   We annotate problem areas with superscripts; these
numbers refer to comments in Appendix I.

  The most common problem seems to be corrupting the  floppy  disks.  To  avoid
doing  this  always  attempt  to sync the disks via sync, reboot or halt before
removing the disk or powering off the machine. You are running  Unix  on  these
floppies  and  it  does not take well to having its file system yanked out from
underneath it. Sometimes the fsck command can  repair  a  damaged  floppy,  but
sometimes you can't get that far.

  We  will  presume for the discussion below that you are performing a "simple"
installation.  In particular, that you do not want to preserve part of the disk
for  other  systems  (like  DOS,  MDOS, or OS/2), you do not have excessive bad
blocks in inopportune places (where the system would put the bad  block  table)
and  that  you  do  not  have to override the disk geometry parameters that are
maintained internal to BIOS.  We will discuss all these matters in the  section
DONT CLOBBER MY DISK.

  You  use  the  floppies  to  bring up Mach in "single user" mode.  Insert the
"Mach Kernel" disk and reset (or power toggle) the machine.  The system  should
soon print out
                     1
                boot: 
At  this  prompt,  you  either type a carriage return (or enter), or wait for a
"timeout".  Then you will see a number printed out, a pause, a "+", etc.    The
bootstrap is reading in the kernel.

  Shortly,  you will be instructed to "insert file system".  At this point, you
remove the "Mach Kernel" disk and insert the "Mach file system" disk.  Once you
have  switched floppies, you proceed with the boot process by typing a carriage
                  2
return (or enter)  .  Next, you will see several lines of  printout;  the  Mach
                                                 3
kernel  describes  the  hardware  that  it finds  .  Then you will see a lot of
activity on the floppy as fsck is run.  And  finally,  you  will  get  the  "#"
prompt,  indicating  that  you are executing at "single user" level and may now
type commands.  You might want to do an
                ls -R
at this point and play with the system a bit.    Note:  operating/loading  from
floppies is rather slow and not indicative of the true system performance.



4.4. Disk Types
  The  kernel  prints  out  many lines of hardware description.  If you have an
IDE/ESDI/ST506 disk subsystem, or a SCSI subsystem emulating  IDE,  you  should
see:
        hdc0: port = 1f0, spl = 5, pic = 14.
        hd0:  stat = 104, spl = 5, pic = 14. (controller 0, slave 0)
and maybe a line for one more slave
        hd1:  stat = 118, spl = 5, pic = 14. (controller 0, slave 1)
And if you have a SCSI disk subsystem, you may see:
        ahac0:port = 300, spl = 5, pic = 11.
        aha0: stat = 104, spl = 5, pic = 11. (controller 0, slave 0)
and maybe lines for several additional slaves
        aha1: stat = 118, spl = 5, pic = 11. (controller 0, slave 1)

  You might even have both types of disk.

  Many SCSI controllers, such as those on PS/2's, make SCSI disks appear to the
kernel as IDE disks. In this case, your SCSI disk will appear to the kernel  as
hd0  rather  than  aha0. If your SCSI disk is called hd0, you must follow these
instructions as if it were an IDE disk.  Mach on the PS/2's supports SCSI, only
through  this  IDE  interface, when the disk controller makes this possible. On
non-PS/2's, the kernel may support SCSI directly.

  Several of the installation procedures in the rest of this document  need  to
have  the  disk  device  indicated.    For  all of these instances, we supply a
"magic" argument {**D*I*S*K**}.  If  you  have  one  IDE/ESDI  disk,  you  type
nothing whenever {**D*I*S*K**} is indicated.  The default is /dev/rhd0c. If you
want to install  on  the  second  IDE/ESDI  drive,  you  must  manually  supply
/dev/rhd1c  for  {**D*I*S*K**}.    Finally,  if  you  have a SCSI disk, you use
/dev/rsd0c in place of {**D*I*S*K**}.  For those with only one  SCSI  disk  and
who  are  generally  lucky,  you  might  just  "rm"  /dev/rhd0c  and link it to
/dev/rsd0c.  I do this.



4.5. Initializing your Disk
  Now you use the Mach procedures on the installation floppy to initialize your
hard disk.
type
                diskutil clobber_my_disk {**D*I*S*K**}
This  initializes  a  disk for use under Mach.  It will destroy all/any data on
the disk.  If you do not wish to trash all the data  on  your  disk,  read  the
section  "DONT  CLOBBER MY DISK".  On most disks, this procedure takes about 15
minutes per 100Meg.  On an ST506 disk, it is much longer.  Note: IDE/SCSI disks
do not typically report bad blocks; these are handled in the controller.  Note:
when this operation completes you do not have file systems; you  must  run  the
setup program (below).

5. Installation and System Setup



5.1. Supping files
  Installing  Mach  is a simple cook book process.  You follow the recipe below
to bootstrap over the internet.

   1. Using ed, edit /PORTFILE and set the crypt= value to  be  the  CRYPT
                   4
      you  told CMU .  /PORTFILE is a sup control file.  You should remove
      the line starting with bin.cmu unless you are a local  CMU  site  as
      you will not have permission to get that collection.

   2. If  you  have a SCSI disk, you must edit the /bin/setup program used
      below.  Using ed, edit /bin/setup and search for
                              disk=hd0
      and change it to
                              disk=sd0
      You are done editing.

   3. type
                      setup
      Called with NO arguments "setup" creates a "root"  file  system  and
      mounts  it  under  /mnt.    It  then creates a "usr" file system and
      mounts   it   under   /mnt/RFS/.LOCALROOT/usr.       The    pathname
      RFS/.LOCALROOT is explained further in the section "Root, Super-root
      and RFS".

   4. type
              setup <machine name> <internet address> [<internet gateway>]
      Now you should be on the network.  You might try  to  telnet  by  IP
      address somewhere, to verify that your network connection is active.
      The <internet gateway> is necessary for your machine/site to find  a
      path to CMU; it is not necessary at CMU.

   5. type
                      setup sup
                                                      4,5,6
      This  invokes sup on the control file /PORTFILE      .  Your machine
      will  be  requesting  from  CMU  all  the  binaries  for  the   i386
      distribution.    On  our  local ethernet, this takes about 1/2 hour;
      over the internet, we have seen times in the 2 to 3 hour range.   If
      there are failures, just restart this step by
      retyping
                               7
                      setup sup 
      Repeat  this  until  everything completes.  The sup protocol records
      what it has successfully  transferred  from  previous  attempts  and
      transfers  any  files  still  required.    When sup has successfully
      completed  the   /mnt/RFS/.LOCALROOT   and   /mnt/RFS/.LOCALROOT/usr
      partitions  on  the  hard disk will be populated with all the system
      binaries and there will be the following  three  directories  first,
      bin.root,  and  bin.usr  in  /mnt/RFS/.LOCALROOT/sup.  Each of these
      directories contains two sup client side control files:  last  which
      contains  a  list  of  all  the files that were transferred and when
      which contains the time at which the sup was completed.

   6. Before booting from your hard disk,
              cd /mnt/RFS/.LOCALROOT/etc
      and edit the file netstart (use ed as the editor).    Fill  in  your
      machine  name,  ip  address,  broadcast  address  and gateway in the
      appropriate places.  You also should verify that your  machine  name
      and ip address are in the file, hosts.

      fstab  is  setup  for  an  EDSI/IDE disk.  Copy fstab.scsi on top of
      fstab, if you are using a SCSI disk.

      The file /mnt/mach is a link to mach.MK.STD+WS which is a  Mach  3.0
      micro-kernel. If you would perfer to boot Mach 2.5, change /mnt/mach
      to link to mach.25 .

   7. Now it is time to reboot off the hard disk.
      type
                      reboot
      After you get the message "syncing disks ... done", and  the  screen
      goes  blank  and  it  goes  back to a bios message remove the floppy
      disk. If you  remove  it  too  soon,  it  is  likely  to  be  in  an
      inconsistant  state  that  will cause it to fail on subsequent uses.
      If you fail to remove it all the system will attempt to boot off the
      floppy again -- rather than the hard disk.

   8. Note that the template /etc/passwd file allows root to login with no
      password.  This is so that you will be able to  add  yourself  as  a
      user  and change the root password after you boot off the hard disk.
      YOU SHOULD NOT LEAVE THE ROOT WITHOUT A PASSWORD AFTER YOU HAVE  SET
      UP YOUR MACHINE.

      The  login prompt prints a banner indicating that the system is Mach
      2.5. This string is defined  in  /etc/gettytab,  and  isn't  changed
      automatically even if you are in fact running Mach 3.0.

   9. When you reboot, you must create the file system space allocated for
      the user data.  If your disk is less than 150Meg,  the  d  partition
      will fill the disk and you are expected to use this space for system
      files and your personal files.  In this case, you  should  skip  the
      next paragraphs.

      Otherwise,  if  you  are happy with using the remainder of your disk
      for a single Mach/Unix file system, type
              eval `vtoc -m e {**D*I*S*K**}` 4096 512
      vtoc -m will type to stdout the beginning of a mkfs line  to  create
      your  "e" partition.  You may now mount the "e" partition.  You will
      probably want /etc/fstab to always mount it.  There is  a  prototype
      line  in  the  distributed  /etc/fstab  that will mount /dev/hd0e on
      /usr1; change the xx to rw.  On Mach 2.5  systems,  this  line  will
      also  arrange for the swap file to be on /dev/rhd0e, which we assume
      is a lot bigger that /dev/rhd0d.  (For SCSI, you will find /dev/sd0e
      instead  of  /dev/hd0e.)   You will also note that in the /etc/fstab
      file there are two lines for  /dev/hd0d.    The  first  line  has  a
      trailer  that  indicates  that  a  swap  file  should  be  set up on
      /dev/hd0d.  You need to cancel this  line  (change  rw  to  xx)  and
      enable the next line (change xx to rw).  This moves the swap file to
      /dev/hd0e. These comments on paging apply only to  Mach  2.5.    For
      information  on  paging  under  Mach  3.0,  see the section entitled
      Paging under Mach 3.0. A 12M  paging  file  was  created  on  the  d
      partition  during  the  SUP.  This  is probably not large enough and
      should be increased and perhaps moved to the e partition.

      If you do not  want  to  organize  the  rest  of  the  disk  as  one
      partition, read the vtoc manual page.  A very prudent thing to do at
      this time, would be to run the programs fdisk, vtoc, and  badblocks.
      These  will  print  out the various disk "labels".  You want to save
      the data ON PAPER.  If something catastrophic ever happens you  will
      be able to reconstruct what your disk looked like.

  10. The  floppy  devices  may  be  wrong  for  the type of drive on your
      machine.  They are setup for 5 1/4" floppies  via  the  installation
      process.  You make the devices for the 3 1/2" floppy by
      typing
                      cd /dev
                      rm -f *floppy *fd0
                      ./MAKEDEV f30
      or for the 5 1/4" floppy by
      typing
                      cd /dev
                      rm -f *floppy *fd0
                      ./MAKEDEV f50
      MAKEDEV  f31 or MAKEDEV f51 can be used to make devices for a second
      disk drive. It will be known by the names fd1 and rfd1.

  11. Edit all the site dependent BSD files below.  You should look at the
      BSD installation manual for exact details.
         - /etc/hosts
         - /etc/rfsd-hosts  -  a  CMU  file  that lists all hosts that are
           allowed rfs access
         - /etc/motd
         - /etc/termcap
         - /etc/namedb
         - /etc/resolv.conf
         - /etc/sendmail.{cf,fc}
         - /etc/passwd
         - /etc/group
         - /etc/printcap - if you have printers
         - /etc/nmbroadcast - contains one line with the  local  broadcast
           ip address

  12. Once  the  installation  is completed to this point, there are still
      some more files that you might like to get.

      In particular initial sup does not bring over  the  whole  Mach  3.0
      binary  release.  If you intend to run a Mach 3.0 system, you should
      sup the bin.mach3 collection.

      In /sup on your machine, there is a control file SUPFILE  that  will
      allow you to upgrade your binaries to latest version from CMU.  Copy
      the file to MYSUPFILE and edit in your CRYPT.  You will notice  that
      there are several commented out lines at the bottom of the file that
      you might want to enable.
         - The optional collection bin.all, gets you 4Meg - 6Meg of  files
           that  are  seldom used, like /usr/lib/learn and /usr/lib/*_p.a.
           If you are concerned about disk space, you probably do not want
           this collection.
         - For Color X11R5, there are two choices:  bin.X11R5 is the whole
           36Meg distribution.  The four sup  collections,  bin.X11R5base,
           bin.X11R5+fonts,  bin.X11R5+inc, bin.X11R5+lib, will also bring
           over the same stuff.    bin.X11R5base  is  the  "necessary  and
           sufficient" 25Meg subset.  bin.X11R5+fonts are the 100dpi fonts
           and the huge misc font files.  The  +inc  and  +lib  should  be
           obvious.
         - bin.mach3  will  bring  over  binaries into /usr/mach3 that you
           need when running Mach 3.0.    This  also  corresponds  to  the
           mach3.release collection with release=i386. There are two lines
           in SUPFILE corresponding to the bin.mach3 collection.  You need
           to  make  sure  the  right  line  for you has no # as the first
           character and the other one begins with a #.  The  #  character
           marks the rest of the line as a comment.  IBM PS/2 users should
           uncomment the line containing  the  string  release=ps2,  while
           other  users  should use the other line. The release=ps2 option
           specifies that you want PS/2 versions of the kernel and server.
         - mdos will bring over the sources for  the  MDOS  dos  emulation
           package.

      After you have edited your sup control file, you run:
              sup -dov MYSUPFILE
      It will only take a few minutes to verify you are up to date; if you
      need to bring over  a  few  changed  programs,  it  will  take  just
      slightly longer.

      One  directory  that sup brings over, /usr/release, is worth noting.
      In it there is a file NOTES, which tells you what has changed in the
      current release; actually is an archive of all the change histories.
      Also in the directory is mach-afs-nfs, which  is  a  binary  of  the
      latest  released  Mach  2.5  kernel.    If you copy it into mach and
      reboot, you will be running the latest distributed 2.5 kernel.

      The Mach 3.0 kernel and UX server are distributed but not  installed
      by  the  bin.mach3  collection. This collection has releases for ISA
      bus kernels  and  a  PS/2  release  for  kernels  that  support  the
      microchannel  bus.  See the comments above regarding the release=ps2
      option.  The  kernel   and   severs   need   to   be   copied   from
      usr/mach3/mach_servers  to  the  appropriate  locations  on the root
      partition before they will be used for booting. See the Mach3  Setup
      document for details.

  13. Instructions for Supping the sources can be found in Appendix III.



5.2. Daemons
  /etc/rc and /etc/rc.local will select the daemons you need for:
   - NO network
   - a network
   - a 2.5 kernel
   - a 3.0 kernel

To  determine  whether  to start the network daemons, we evaluate the predicate
/bin/inet.  (For example, you might have a laptop that is not connected to  the
network.)   If it returns FALSE, we presume there is NO network.  If it returns
TRUE, there is.  A simple stratagem is to copy /bin/false to /bin/inet  if  you
DO NOT want network services; copy /bin/true if you DO want them.

  To  determine  whether  the kernel is 3.0 Mach, we look for and then evaluate
the predicate /usr/mach3/bin/mach3.  If it returns FALSE, we presume the kernel
is  2.5 Mach.  If it returns TRUE, the kernel is 3.0 Mach.  Some of the daemons
are different for each system; if you are curious look at /etc/rc.local.  NOTE:
we assume that you have placed the "3.0 release subtree" in /usr/mach3.



5.3. X11R5 and Mice


5.3.1. X11R5
  Color  X11R5  currently is not supported on IBM PS/2's. If you're not using a
PS/2, you probably want to use X11R5 with new SVGA cards and  one  megabyte  of
video memory.  The X11R5 we release is XFree86 Release 2.0.

  The  X11R5  binaries are the ones we use at CMU. Our support organization has
chosen to put X11R5 in /usr/misc/.X11, rather than the traditional /usr/X11  or
/usr/X386.      This  means  when  you  sup  X11R5  it  will  be  installed  in
/usr/misc/.X11 and you need to put /usr/misc/.X11 on your path.

  Now for the hard part.  Read:
   - /usr/misc/.X11/lib/etc/README,
   - /usr/misc/.X11/lib/etc/README.mach

and whatever else you can find about the X11R5 SVGA server.  One of  the  truly
hard/magical  parts  of the server is coming up with a Xconfig file to describe
your monitor/svga card.  The X11R5 documentation describes the process in  gory
detail,  at least twice.  In /usr/misc/.X11/lib, you will find some Xconfig's I
have played with:
        XconfigGWa{,3} for the Diamond Speed Star and Crystal Scan 1024NI
        XconfigGWb{,3} for the Diamond Speed Star and NEC 4FG
        XconfigINa{,3} for the Cardinal 700 with NEC 4FG
        Xconfig256k{,3}for generic cards with 256k of memory.
The "3" suffix is used if you have a 3 button mouse. Lastly, if you  specify  a
fixed  chipset  and clock like these configurations do, I believe that any mach
kernel will work.  BUT you should really be at X142F or MK76/UX36 if  you  want
to have X11R5 svga card "probing" work.


5.3.2. Mice
  Mach  supports  several  kinds  of  external  mice, the logitech three button
mouse, the microsoft two button mouse, the PS2 mouse and the  logitech  mousman
mouse.    We  do  not  support any kind of bus mouse.  The way you indicate the
mouse type and com port is a bit magical; you set the mouse device minor.   The
value you set the minor to is computed by the formula:
        <type> * 8 + <com port>
<com  port>  is  0, or 1 or ... depending on which com port you plug your mouse
into.  (Some architectures prefer to make com0 the modem line.)
<type>  and <minor> are:

        Mouse Name              <type value>    <com0 minor> <com1 minor>
logitech mouse                          0               0       1
microsoft mouse                         1               8       9
ps2 mouse                               2               16      17
no real mouse at all                    3               24      25
logitech mouse man (M+ or V type)       4               32      33

We have implemented a neat hack for small notebooks so that they don't have  to
be  saddled with a HUGE mouse.  Scroll lock toggles a mode wherein "seldom used
'function keys'" are used to represent mouse actions.  F1, F2, F3 are the left,
middle,  and  right mouse button.  The first key stroke represents a down click
and the second key stroke represents an up click for the mouse  button.    Then
the  up down, right, left, arrow keys actually move the mouse.  And if you have
a standard pad with home, pageup, end,  and  pagedown  filling  in  the  square
around  the  up,  down,  right,  and left arrow keys then the former set do the
obvious and move the mouse along the diagonals.



5.4. The Environment
  Mach 2.5 I386 has the same kernel features as the Mach 2.5 for all the  other
supported  platforms.    The  software  environment  starts  with  4.3BSD-TAHOE
environment, with one major exception.  The Mach 2.5 kernel  does  not  support
BSD  file  system  labels; so most file system tools are CMU tools derived from
4.3BSD.

  You are also provided with all the Mach programs, include files and libraries
and  the  CMUCS library and some programs (most notably rfs and sup).  However,
these files are not in the /usr/mach tree or /usr/cs tree as is the  case  with
Mach on other hardware, but are integrated into the BSD tree.

  The compile environment/tools, i.e., cc, as, ld, size, nm, strip, ar, and gdb
all come from the GNU products of the Free Software Foundation (FSF).  There is
one  exception,  cpp; we use a CMU modified 4.3BSD cpp.  All of the program and
library sources have been compiled without using the "traditional"  switch  and
only  a  few  programs  needed "writable-strings".  You should be aware of what
these two features do; see  the  gcc  manual  page.    You  may  need  them  to
successfully port your applications.

  Finally,  one  feature  about  the  load/execution  function should be noted.
Program text starts at 0x10000 (64K).  This means that you can not  dereference
a  pointer  to  0 or any small integer value.  This will cause programs to core
dump that were "accidentally" working on other architectures.    Only  a  small
number of 4.3BSD-TAHOE programs that had to be fixed to deal with this.  (SunOS
and Mach on the Sun Architecture machines have a similar restriction.)
5.5. BSD4.3-TAHOE Source Compilation
  Since the system sources,  /usr/src,  are  basically  4.3BSD-TAHOE,  the  BSD
standard compilation procedures applies.  The typical way to build a program is
to go to the appropriate directory and type make.  You  install  it  by  typing
make  install.    Note:  If  the  program  <foo>.cmucs  exists,  it was used in
preference to the  original  BSD  program  <foo>.    Also,  the  compile  tools
mentioned  above,  should  be taken from /usr/src/gnu; the BSD version has been
left for reference purposes.



5.6. Building Kernels
  This section tells you how to build Mach 2.5  kernels.  Different  procedures
apply to Mach 3.0. See the document Building Mach 3.0 (mach3_build.ps).

  First,  you  must  decide  what kernel to build.  The mach.sys sup collection
retrieves a rather old Mach 2.5 kernel.  This corresponds to the  functionality
in the official Mach 2.5 release.  The mach.mainline (and mach.nfs) collections
retrieve essentially what is actively used at CMU today.

  To build a new kernel, go to the kernel source tree.  Then type
                make CONFIG=STD+WS-afs-nfs doconf config
This will create a directory, STD+WS-afs-nfs.  You can go into  this  directory
and type ./make.  This will initiate a standard BSD style kernel build.



5.7. Installing/Booting Kernels
  This  section  applies  to  Mach 2.5 only. Different procedures apply to Mach
3.0. See the document Setup for Mach 3.0 (mach3_setup.ps).

  The kernel that you have built should be placed  on  the  root  of  the  file
system.  Give it some name other than /mach [or /vmunix], initially, so you can
fall back to the old kernel if necessary.  To invoke your kernel
type
                /etc/reboot
The old kernel will shutdown, then the hardware performs self test, and lastly,
you are prompted for a kernel to boot.  The system types out:
        boot:
If  you  type nothing, mach is booted. (If you type carriage return (or enter),
mach is also booted.)  You may type a file name of a kernel to boot.    If  you
had put your kernel in the file /mach.new, you would type
                /RFS/.LOCALROOT/mach.new
to  boot  this kernel.  Note: From the section on Root, Super-root and RFS, you
should understand why the /RFS/.LOCALROOT is necessary.  Aside:  you  may  also
supply flags on the boot line, above.
   - -a causes the kernel to ask for the file system root partition.
   - -s causes the system to boot "single user".
   - -d causes symbols for the debugger to be loaded.

Once  you are happy with your kernel, you want to install it as /mach.  The old
/mach has a link count of three; the three files /mach, /vmunix and /../../mach
have  to  be  linked  together.    You  also  want  to save the old kernel.  My
preference for doing this is to:
                cp -p /mach /mach.old
                cp -p /mach.new /mach
This way after you set up the links once and  never  worry  about  them  again.
Alternatively, you might
                rm -f /mach.old  /../../mach.old /../../vmunix.old

                mv /mach /mach.old
                mv /vmunix /vmunix.old
                mv /../../mach /../../mach.old

                mv /mach.new /mach
                ln /mach /vmunix
                ln /mach /../..



5.8. Root, Super-Root and RFS
  Since  1982, CMUCS kernels have had a facility that lets you access files and
devices on other machines.  We call this the remote  file  system,  RFS.    The
client  side  exists  in every Mach kernel; the server is a privileged program,
rfsd, that is run on each machine that will permit access to its  local  files.
We have even ported the server to non-Mach operating systems.

  RFS  refers  to remote files/devices in a location dependent way.  The remote
file name must not look strange to Mach/Unix programs that  parse  file  names.
Thus, the generic name is
                /../<remote machine name>/<path on that machine>
for example
                /../wb1/etc/passwd
                /../wb1/dev/rmt0
What  this  implies is that in Mach, the root file system, "/", is not inode 2.
The kernel automatically "chroots" (changes the root) to /RFS/.LOCALROOT as  it
boots.  Thus "/.." and "/../.." are well defined and not equal to "/".

  The  local  machine must have an "RFS link" to the remote machine.  To make a
link in /.., type:
                cd /..

                rfshost <IP ADDRESS> <host name> <host nic names>
For example:
                rfshost 128.2.250.16 wb1.cs.cmu.edu wb1
or even
                rfshost `grep wb1.cs.cmu.edu /etc/hosts`
You may create as many entries as you like and as many aliases as you like.   A
special  quoting  mechanism  is necessary to remove an RFS link.  If you are in
the directory containing the RFS link, link,
                rm .///<link>
will remove the RFS link, link.

  By default, RFS accesses files on the server using the  user  id,  rfsd,  and
group  id,  system.    However,  the  server must be told that your machine may
access its files.  The file /etc/rfsd-hosts,  on  the  server,  should  contain
single  lines  indicating  the  internet address of machines allowed to contact
this machine.  (If you change the file, you must kill and restart rfsd.)

  You can also authenticate yourself to RFS, using the program, rfs.  rfs  will
prompt  you  for  a  user,  group, account, password, and "Identify?"  Give the
default answer for account and "Identify".  After running rfs, you will have  a
shell  that  will  allow  you to access files on any remote RFS hosts using the
specified uid and group.   Note:  you  must  create  a  local  magic  file  for
authentication to work.  You must type
                cd /..
                rfshost 0.0.0.0 CONTROL



5.9. Paging under Mach 2.5
  The  Mach  2.5  kernel  pages  out  to  the file named pagingfile on the disk
partition specified in the /etc/fstab file.



5.10. Paging under Mach 3.0
  The file /mach_servers/paging_file  is  a  symbolic  link  to  a  file  on  a
filesystem  other  than  the  root, which the kernel uses as paging space.  The
kernel interprets the destination of the link in a special way.    The  default
value is
                paging_file -> /dev/hd0d/paging_file
The  syntax /dev/hd0d/paging_file refers to the file paging_file on the root of
the filesystem on /dev/hd0d.  Since the Mach 3.0 kernel contains no file system
code  it  cannot extend the size of its paging file. The paging file created by
the setup script is 12 megaytes. If you  have  enough  disk  space  you  should
increase this to between 20 and 40 megabytes.

  You  may  want to move the paging file to your partition on /dev/hd0e.  To do
this you must follow four  steps:  create  the  new  file,  make  the  link  in
/mach_servers  point  to  the  new paging file, reboot your system, and finally
remove the original paging file. The following sequence of steps will create  a
20  megabyte  paging  file  on  /dev/hd0e and remove the default paging file on
/dev/hd0d. The example assumes that /dev/hd0e is mounted on /usr1 and /dev/hd0d
is mounted on /usr.
                cd /mach_servers
                dd if=/dev/rhd0c of=/usr1/paging_file bs=256k count=80
                chmod 600 /usr1/paging_file
                rm paging_file
                ln -s /dev/hd0e/paging_file
                reboot
                <when system reboots and you log in again in as root>
                rm /usr/paging_file
Take care never to remove a paging file that the kernel is currently paging on.
In the above example, we removed the link to the paging file; this is safe.  It
would not have been safe to remove /usr/paging_file before rebooting.



5.11. Changing Time Zones
  As  distributed  the time zone is set to eastern standard time, i.e. EST5EDT.
If you need to change time zones you will need to perform two tasks. First, you
will need to re-link /etc/zoneinfo/localtime as follows:
        login as root
        cd  /etc/zoneinfo
        rm  localtime
        ln  xxx  localtime   (substitute appropriate timezone file for xxx)

  Second,  you  will need to patch time zone variable (i.e. _tz) in the kernel.
Prior to doing this you will need to calculate the appropriate patch  value  in
hex  of  the  difference  in  minutes  between  your  local  zone  time and GMT
(universal time). The value of this constant for  eastern  standard  time,  for
example  is  x12c  hex  (i.e.  300  decimal).  This  is the value that you will
initially see for _tz. To change to Pacific Daylight Time, as an  example,  _tz
should be patched to x1e0 hex (i.e. 480 decimal).



5.12. The Kernel Debugger
  Mach 2.5 has a version of "adb" in the kernel.  The key sequence "control-alt
d" will enter the kernel debugger.  As you would expect, ":c"  gets  you  back.
Once  in  the  kernel debugger, you are on your own.  You might look at the BSD
documentation on adb and kdb for a list of the commands.  A laconic description
of  the debugger may be found in Appendix V. Symbols have to be loaded with the
kernel, for kdb to be able to use them.   If  the  kernel  file  is  executable
(determined  by  the file's permission bits), the boot program always loads the
symbols.  The boot line flag, -d, will force symbols to be loaded.

6. Replicating The System
  NOTE:  If you have one or two local machines, we will allow  you  to  upgrade
them  directly  from  CMU.    But  if  you have a larger site, you must take an
approach described in this section.



6.1. Cloning
  The easiest way to mass produce systems  is  to  set  up  one  machine  as  a
"cloning"  machine.  Below, we assume you are cloning onto your second ESDI/IDE
drive, /dev/rhd1c.  If you are using  SCSI,  you  would  substitute  /dev/rsd1c
wherever  /dev/rhd1c  is  specified.    (And you would use /boot.sd rather than
/boot.hd.)

  The recipe follows:
   - bring your disk over to cloning machine
   - low level format the new disk
   - run "clobber_my_disk"  on  the  new  disk  (diskutil  clobber_my_disk
     /dev/rhd1c)
   - fill the disk:
        * eval `vtoc -m a /dev/rhd1c` 4096 512
        * fsck /dev/rhd1a
        * mount /dev/hd1a /mnt
        * mkdir /mnt/RFS
        * mkdir /mnt/RFS/.LOCALROOT
        * mkdir /mnt/RFS/.LOCALROOT/usr
        * eval `vtoc -m d /dev/rhd1c ` 4096 512
        * fsck /dev/rhd1d
        * mount /dev/hd1d /mnt/RFS/.LOCALROOT/usr
   - copy everything you need from the cloning disk to the new disk.
   - plug your disk back into your own machine

Clearly,  you do not have to mount both file systems at the same time.  What is
critical is that you perform the vtoc  commands  and  that  on  the  root  file
system,  you  create RFS/.LOCALROOT and change directory there before you begin
copying data.

  You may use any procedure that works under BSD to copy the cloning disk.  You
could "dump|restore" root and usr from the one disk to the new disk.  You could
"tar crf|tar xf".  You could load via a streamer into the  new  disk.    Follow
whichever procedure you are most comfortable with.

  These procedures do not install a boot block on the disk.  To do this type:
        dd if=/boot.hd of=/dev/rhd1c bs=b
This will copy an image of the boot program, which is stored in /boot.hd to the
boot area on the new disk.  It occupies roughly 9 sectors.



6.2. Using Sup
  You might want to set up a sup repository at your site that is upgraded  from
CMU  on  a  regular  basis.   You would then add site dependent information and
local improvements to this base.  Then local machines would sup from this local
repository/server.    The  information in the /usr/mach/public/sup directory on
mach.cs.cmu.edu provides an example of how to set up your local site; refer  to
the  section  Sup'ing  Sources.    We  advocate  sup  because  it allows you to
propagate to each machine at your site only the changes in the repository  that
have  happened  since  the  machine  last was upgraded by sup.  This allows ALL
machines to keep current with  a  minimum  overhead.    sup  does  all  of  the
bookkeeping.



6.3. Floppies
  The Mach 2.5 kernel sources have the tools to produce customized 3 1/2" and 5
1/4" floppies.  Two scripts are in the standi386at/binaries  directory.    MKfs
will  make  the  file  system floppy, and MKkernel will make the kernel floppy.
Both take a single argument of "3h" or "5h" which specifies the floppy size  as
3  1/2" or 5 1/4", respectively.  You must run these commands as "root" and the
floppies must have been previously formatted.

  You can make Mach 3.0 boot floppies using the scripts MK3fs and MK3kernel.

  More simply, you can just copy the floppy images you  got  for  the  original
installation.

7. DONT CLOBBER MY DISK



7.1. Minor Variations
  Three simple cases of disk setup arise that can still be handled by
                      diskutil clobber_my_disk {**D*I*S*K**}.
In  the first case, you might need/want to override what BIOS believes the disk
geometry to be.  BIOS allows only 10 bits of cylinder numbers.    If  you  have
more,  either you can not use them, or you have to lie to BIOS about the number
of sectors per track and number of  heads  so  that  the  "virtual"  number  of
cylinders  falls  under  1024.    If  you  specify  the "-p" option to diskutil
clobber_my_disk, it  will  interactively  prompt  you  for  the  true  geometry
information.

  In  the second case, you have bad blocks in what would be the bad block area.
diskutil clobber_my_disk will abort very early on.  You fix this by moving  the
start  of  the  "Mach  (BIOS)  partition"  forward (see section The Disk Layout
below).  You type:
        diskutil clobber_my_disk -o <offset in sectors> {**D*I*S*K**}
The Mach (BIOS) partition will start at <offset in sectors> on the disk.   This
quantity  should  be  an  integral  number of cylinders.  NOTE: You specify the
number in SECTORS.

  In the last case, you might have a stupid  low  level  format  program  which
marks  all  the  sectors  of  a  track  bad  if  any  sector  is bad.  diskutil
clobber_my_disk has a heuristic; it looks for several sector errors  before  it
labels  the  track  as  bad.  This will cause a lot of needless rattling of the
disk (error retries and recalibration), before  the  track  is  marked  bad  by
diskutil  clobber_my_disk.    The  "-t" option to diskutil clobber_by_disk (and
badblocks) will cause the program to mark the entire track bad if there is  one
bad sector.

  Lastly, you can combine any or all of the options described above.



7.2. Room Enough for DOS or MDOS
  If  you  are starting out with an empty disk and want to leave room for a DOS
partition at the front of the disk, there is a very easy way to do this.  Use
        diskutil clobber_my_disk -o <offset in sectors> {**D*I*S*K**}
as noted in the previous section and specify the number of sectors you want  to
leave for the DOS partition.  (This should be a integral number of cylinders.)

  Next,  you  boot up DOS from a floppy and run DOS's fdisk to create a primary
DOS partition that uses ONLY the initial cylinders of the disk  that  you  have
set  aside.    Then  you run DOS format to format the DOS c drive.  Lastly, you
populate the c drive.  NOTE: in our experience, using fdisk from DOS 3.3 or DOS
5.0,  it is very easy to allocate the right number of cylinders.  DOS 4.1 fdisk
is harder to use for this purpose.

  MDOS (the Mach  DOS  emulation  server)  does  not  actually  require  a  DOS
partition  to  run.  It  will  read  DOS  application  programs out of the Unix
partitions. But is is easier to load software from DOS floppies to a  real  DOS
partition  than  to  a  Unix partition. If you think that you might want to run
MDOS eventually, you should look at the mdos_info document now  and  decide  if
you want to leave room for a DOS partition.

  If DOS partitions are already on the disk, the next section will explain what
you need to do.



7.3. The Disk Layout
  At the start of the disk (sector 0), there is a BIOS boot block that has code
and  a  partition table.  (NOTE: BIOS calls this table a partition table.  Unix
refers to regions of the disk that are separate file systems as partitions.  To
try to avoid the obvious confusion, we call to the former a "(BIOS) partition",
and the latter a partition.)  The (BIOS) partition table has four entries;  one
is  designated  as  "active".   The boot process finds the active partition and
invokes it.  This table makes it possible to divide the disk  up  into  several
disjoint areas.  Thus Mach and DOS can both coexist on the same disk.

  The  "Mach (BIOS) partition" begins with a boot program that can occupy up to
29 sectors.  This is followed by  one  sector  for  a  vtoc  (volume  table  of
contents).   The vtoc specifies the override disk geometry and then divides the
"Mach (BIOS) partition" into the standard  Mach/Unix  file  system  partitions.
The  vtoc  is  followed  by four sectors that record bad blocks and a number of
sectors that are used  as  bad  block  replacements.    At  the  next  cylinder
boundary, the first Mach partition begins; this is typically the "root".

  All the structures described above need to be initialized for Mach to be able
to use the disk.  The programs, fdisk, vtoc, and badblocks, edit the  necessary
structures.    They  will let you edit every field in every structure.  We will
not describe them in detail; see the manual pages for more information.

  We also provide a simpler interface:
                diskutil clobber_my_disk {**D*I*S*K**}
This initializes the structures to  use  the  whole  disk  for  Mach.    It  is
equivalent to the following three commands:
                diskutil finit {**D*I*S*K**}
                badblocks -w {**D*I*S*K**}
                diskutil fs {**D*I*S*K**}
The  first  step,  diskutil finit, does a quick and basic initialization of the
structures to an empty state.  Then, badblocks scans the disk  for  bad  spots.
Finally,  diskutil  fs  puts  the basic Mach partitions, "a" - "e" on the disk.
(This uses the Mach default layout.)

  You may replace diskutil finit with diskutil init.  This DOES NOT  initialize
the  sector  0  disk  layout information.  You MUST use fdisk to pick a "(BIOS)
partition" for Mach, before you run this alternate sequence.   You  should  put
the  sector  start  address  for  the  "Mach  (BIOS)  partition"  on a cylinder
boundary.  You follow this method, if the disk already  has  (BIOS)  partitions
that you need to preserve.

8. Known Features/Problems/Bugs



8.1. gas
  To  be  compatible  with  the  AT&T  assembler,  the  gas  assembler has been
generated to accept "#" and "/" as comment characters.   This  means  that,  at
present, there is no way to indicate division in assembler expressions.

9. Mach Support
  Since the Mach project is no longer an active reseach project at CMU, most of
the support and futher developement of Mach has to come from the  community  of
users.  This  community  can  be  reached  through  two  mailing lists that are
maintained at CMU and the NetNews BB comp.os.mach.

  The two mailing lists to which you may wish to be added are:

machi386@cs.cmu.edu
                covers questions related to running Mach on i386/i486 hardware.

mach3@cs.cmu.edu
                covers topics of more general interest about Mach 3.0.

  Subscription to both of these lists is handled by the majordomo program.  For
information on how to use this interface send mail to majordomo-mach@cs.cmu.edu
with the word "help" in the body of the message.
I. Trouble Shooting the Installation

   1. One BIOS never gets this far.  We would suggest that you get  either
      an  AMI  or  PHOENIX BIOS as a replacement. (We believe that the new
      boot.fd code of Mar 1, 1991 has solved  this  problem.  If  you  are
      still seeing it, please contact us at mach@cs.cmu.edu)

   2. Occasionally,  people type an extra carriage return which is gobbled
      down and you are not given an opportunity to put in the file  system
      disk.    The  kernel  will  panic  shortly  and  you  will  have  an
      opportunity to try again.  You must use both disks to load Mach.

   3. It is very important that  one  line  in  the  hardware  description
      contains  your  ethernet hardware address.  If you do not see such a
      line, then the  kernel  has  not  recognized  your  ethernet  board.
      Either  the  board is unacceptable or the jumper settings are wrong.
      Refer to Appendix II to get the appropriate jumper settings.

   4. Be careful not to delete the prefix=/usr at the end of  the  bin.usr
      line  in  PORTFILE. If you do, sup will try to load all the files in
      the bin.usr collection on to the root partition and will run out  of
      space.

   5. During the sup of the first collection several commands are executed
      that can cause trouble.  The  16-sector  boot  program  (sd.boot  or
      hd.boot)  is  written  on the the beginning of your hard drive. Only
      one of these attempts will succeed, depending on what sort  of  hard
      disk  you  have.    After that a 12M paging file is created on the d
      partition of the hard drive.

   6. If you get an access error back from sup, we might not have put your
      site/machine into our authentication table yet.  More likely is that
      your installation's name server  does  not  respond  when  our  site
      queries  it, asking it to translate your machine's IP address to its
      name.  Please send a copy of the supfile command  and  command  line
      that  you  are  using  and  the  transcript  of  the  sup session to
      mach@cs.cmu.edu.

   7. sup has a very long timeout.  It takes minutes  for  it  to  realize
      that a connection has closed.  If you are connecting to us from some
      far away place, you might want to run sup  or  "setup  sup"  in  the
      background.    You  NEVER want to power cycle the machine; since you
      are in the process of loading your machine, it is VERY  likely  that
      the  buffer pool has not been flushed to disk and you will see a lot
      of inconsistencies when you next fsck

   8. If the system crashed or you had to reboot before sup completed, you
      must  start  the  setup  phase  from  scratch.  Call  setup  with no
      arguments, which will make new file systems. Otherwise there may  be
      files  on your system which are corrupt, but which sup thinks are ok
      and will not replace.



I.1. A Few More Anomalies

   - If you can not low level format your disk, talk to  the  manufacturer
     or sales office.  This is a routine "BIOS/DOS" procedure.  We can not
     help you.

   - If you personally installed a 80387, make sure  that  there  are  not
     switches  to  change  or  a setup program, to run to tell the machine
     about the fpu.

   - Unless you are running X, Mach will use a "monochrome 80 x  25"  mode
     of  character display.  Some vga cards misbehave; you might be better
     off with a simple monochrome board if you have one.   Also,  be  sure
     you  have  initialized  your  vga  board  for  this mode; some boards
     require special setup.

   - Believe it or not, we have found at least one keyboard that does  not
     work  with  Mach  -- it does work with DOS.  What will happen is that
     after you get the single user prompt on the floppy boot, you will not
     be able to type.
II. ETHERNET
  In the presentation below, you will see that we prefer IRQ 9 for the ethernet
interrupt level.  On some 8 bit cards, there is no option for IRQ 9; you should
use  IRQ  2  instead  --  which just happens to map to IRQ 9 on a 16 bit AT BUS
machine.



II.1. WD8003 & Etherlink II & WD8003 Elite
  The first two of these boards  use  the  NS  8390  ethernet  chip;  they  are
programmed "basically" the same with a few localized differences to account for
the board logic.  The new SMC WD8003 Elite uses custom logic and  is  described
later.


II.1.1. EtherLink II
  This  board  has nicely labeled jumpers.  There are only two jumpers: one for
the memory address and one for the port.  You may use either 0xd8000 or 0xdc000
for  the  memory  address.    But  0xdc000  is  used  by the Adaptec 1542B SCSI
controller to map its ROM BIOS, so for SCSI configurations you should ONLY  use
0xd8000.    The  thick/thin ether setting and IRQ are made by software.  We use
the port address to imply a setting of IRQ and thick vs thin ether.
                PORT                    IRQ     ETHER TRANSCEIVER
                0x280                   9       thin
                0x2A0                   9       thick
                0x2E0                   5       thin
                0x300                   5       thick


II.1.2. WD8003 & WD8013
  We can accept:
                port            irq             memory
                0x280           9               0xd0000
                0x2A0           9               0xd0000
                0x2E0           5               0xd0000
                0x300           5               0xd0000
The WD8013 is the 16 bit card.  It is very nicely laid out and all the  jumpers
are labeled.  Select a set of options consistent with the above table.

  For the WD8003, there are five sets of jumpers that must be set.  A schematic
of the board jumpers  is  shown  later  with  one  acceptable/preferred  jumper
arrangement.  NOTE: with the DELL 320SLT, you must use a setting with IRQ 5.

  W1:  Sets  the  Port  address.    We use 280 which is indicated in the figure
below.  If you interpret (jumper) shorts as 1 then the map of 16 possible  port
ranges is given below:  (The *'d ports are the ones we support.)
port            0x200   0x220   0x240   0x260
pattern         0xF     0x7     0xB     0x3

port            0x280*  0x2A0*  0x2C0   0x2E0*
pattern         0xD     0x5     0x9     0x1

port            0x300*  0x320   0x340   0x360
pattern         0xE     0x6     0xA     0x2

port            0x380   0x3A0   0x3C0   0x3E0
pattern         0xC     0x4     0x8     0x0

  The  jumper  labeled 2 in the W1 set, reduces the number of board wait states
from 4 to 2.

  W2: selects the IRQ level that the board is to use.  We use  IRQ2  that  gets
remapped to IRQ9 on ISA bus machines.  The possibilties are:
        jumper 11 -> IRQ2               jumper 9 -> IRQ3
        jumper  7 -> IRQ5               jumper 5 -> IRQ5
        jumper  3 -> IRQ6               jumper 1 -> IRQ7

  W3:  Is  shorted  for thin ether, otherwise all the jumpers are open.  w4: Is
open for thin ether, otherwise shorted.  w5: Is only meaningful for thin  ether
and we wanted it shorted.

  Below is a picture of the board and jumpers set up for thin ether.

                  W4

                                                                E
                                                                T
        2468a W1                _ W3                            H
         || |                   _                               E
                                _                               R
                                _
                                _                               T
                                _                               A
                                                                P
                                                                S
                                                | W5

                b97531 W2
                |
II.1.3. WD8003 Elite
  This is a reworking of the WD8003.  It is necessary to read its documentation
and use the DOS setup utility that is provided with it.  Choose  a  port/memory
address that is compatible with the table below.
                port            irq             memory
                0x280           9               0xd0000
                0x2A0           9               0xd0000
                0x2E0           5               0xd0000
                0x300           5               0xd0000



II.2. Etherlink I
  We can accept:
                port            irq
                0x300           2
A  schematic  of  the board jumpers is shown below with one acceptible/prefered
jumper arrangement.
                I/O ADDR        MEM
                4 5 6 7 8 9     EN

                . . . . X X      X
                X X X X X X      X
                X X X X . .      .


                MEM     1 1 1 1 1 1 1 1
                ADDR    2 3 4 5 6 7 8 9

                        . . X X . X X X
                        X X X X X X X X
                        X X . . X . . .


                INTERRUPT           DMA
                2 3 4 5 6 7     1 2 3 1 2 3
                |               |     |
II.3. PC586
  We can accept:
                PORT            IRQ             MEMORY
                0x0d0000        9               0x0d0000
                0x0c0000        5               0x0c0000
                0xf00000        12              0xf00000

  A schematic of the board jumpers is shown below with one  acceptible/prefered
jumper arrangement.  NOTE: This is not the specification for an iMX586 which is
the equivalent board but layed out differently.

  Jumper 1: E27-E32 selects > 8 Mhz bus.

  The board static ram must be jumpered to address 0xD0000
        Jumper 2: E28-E33
        Jumper 3: E29-E24
        Jumper 4: E30-E25
        Jumper 5: E31-E26

  Jumper 6 thru jumper 13 choose  one:    The  board  must  be  configured  for
interrupt request line 9.  This is jumper 10 set to E41-E49.

  Jumper 14: E54-E55 selects 0WS mode.

  Jumper 15: is left alone.

  Jumpers  16  thru Jumpers 21:  E1-E18 control whether the board uses cheapnet
or standard ethernet.  The figure below shows it using cheapernet.    Move  the
jumpers down for standard ethernet.

  The  figure  below  visually  shows  the  jumper pins of interest. Those pins
marked with X's are the jumpered pins. E56 --- E58 may be  missing  from  older
cards.

                                                J  J  J  J  J  J
                                                1  1  1  1  2  2
                                                6  7  8  9  0  1

                                             E1 X  X  X  X  X  X E6
                                             E7 X  X  X  X  X  X E12
                                            E13 .  .  .  .  .  . E18
         J15

        X E19
        X E20
        . E21

                                J  J  J  J  J
                                1  2  3  4  5

                      E56 X     .  .  X  X  X E22-E26
                      E57 X     X  X  X  X  X E27-E31
                      E58 .     X  X  .  .  . E32-E36
                       .  .  .  .  X  .  .  . E37-E44
                       .  .  .  .  X  .  .  . E45-E52

                       J  J  J  J  J  J  J  J
                       0  0  0  0  1  1  1  1
                       6  7  8  9  0  1  2  3

                                                J14

                                        E53 .  X  X E55
III. Sup Collections



III.1. Binary Collections
  Edit  the  control  file  below, replacing CRYPT with your crypt.  You choose
among the optional collections as was explained earlier.

bin.root host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT
bin.usr host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT prefix=usr
#bin.cmu host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT
#bin.all host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT
#bin.X11R4 host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT
#bin.X11R4small host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT
#bin.X11R5 host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT
#bin.X11R5base host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT
#bin.X11R5+fonts host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT
#bin.X11R5+inc host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT
#bin.X11R5+lib host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT
#bin.mach3 host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT
#bin.mach3 host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT release=p
#mdos host=x29.mach.cs.cmu.edu hostbase=/i386 base=<BASE> crypt=mdos
#floppy.image host=x29.mach.cs.cmu.edu hostbase=/i386 base=/ crypt=CRYPT

  There are two control lines above applying to the bin.mach3 collection.   You
need  to  make  sure the right line for you has no # as the first character and
the other one begins with a #. The # character marks the rest of the line as  a
comment.    IBM  PS/2  users  should  uncomment  the line containing the string
release=ps2, while other users should  use  the  other  line.  The  release=ps2
option specifies that you want PS/2 versions of the kernel and server.

  NOTE: the bin.cmu collection is only available for machines at CMU.



III.2. Source Collections
  The  source  kit  for  Mach  includes  all of 4.3BSD-TAHOE, plus all the Mach
group's sources, plus some of the CMUCS sources, and several of the  FSF  (gnu)
components.    These sources will take up about 100Meg of disk space.  You will
need about another 40Meg, if you want to compile them.

  Edit the control file below (which can be found in  /sup/SUPFILE),  replacing
CRYPT with your crypt.  For each line in the control file, create the top level
directory  in  which  the  data  will  be  stored  and  set   the   permissions
appropriately.   (Change to the base directory (/usr/src) and mkdir each prefix
directory.)
type
        sup -dov <control file>
Repeat this command until sup completes successfully.  Note: It  will  probably
take  several  attempts  and  you probably want to do this at night.  Each, the
src.<dir> collection below, brings over the BSD/MACH sources necessary to build
the  programs  in the <dir> directory.  For example, src.etc is the sources for
the /etc directory and src.usr.lib is obviously the sources  for  the  /usr/lib
directory.  src.gnu contains the gnu sources used to build the binary tools and
the compiler.  Lastly, we have the mach.<dir> collections for  kernel  sources.
mach.sys   contains   sources  for  the  Mach  2.5  official  release.    While
mach.mainline and mach.nfs contain kernel  sources  for  essentially  the  most
recent monolithic Mach kernel used at CMU.

src.MISC host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src crypt=CRYPT
src.bin host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=bin crypt=
src.cci host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=cci crypt=
src.doc host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=doc crypt=
src.etc host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=etc crypt=
src.games host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=games cr
src.include host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=includ
src.lib host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=lib crypt=
src.man host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=man crypt=
src.new host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=new crypt=
src.old host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=old crypt=
src.tests host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=tests cr
src.ucb host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=ucb crypt=
src.undoc host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=undoc cr
src.usr.bin host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=usr.bi
src.gnu host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=gnu crypt=
src.usr.lib host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=usr.li
src.nfs host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=nfs crypt=
mach.sys host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=sys crypt
mach.mainline host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=sys
mach.nfs host=x29.mach.cs.cmu.edu hostbase=/i386 base=/usr/src prefix=sys crypt

  NOTE:  the  src.nfs and mach.nfs collections are only available to sites with
Sun NFS educational licenses.

  The collections for the Mach 3.0 sources are  described  in  our  public  FTP
directory  public/doc/notes/mach3_supinfo. You need to be enabled separately to
sup those colllections. Just send mail to  mach@cs.cmu.edu  with  your  machine
name and IP address to request to be enabled.

  If  you  do  not  have the space on your machine, but have some other machine
(non I386 even) running Mach, you may put the control file there  and  run  the
above  procedure.    Note: you will have to register this new machine at CMU in
order to run sup.

  You can obtain Mach 2.5 I386 sources without using the Mach operating system.
You  MUST  have  a  Mach  2.5  license  and you MUST use the CMU sup program to
request the sources, though.  Everything you need to know about the sup program
is   available   for  anonymous  FTP  access  on  the  machine  mach.cs.cmu.edu
(128.2.209.192), in the directory /usr/mach/public/sup.    There  is  a  manual
page,  the  program  sources,  library sources, and sample "collection" control
files.  There is also a README file that describes the contents  further.    If
you  do  not  have  sup  and  are running 4.3BSD, you should have all the files
necessary to build sup.  If you have problems building  sup  under  some  other
operating system, let us know; we might be able to help.
IV. Installation from an intermediary machine
  The  setup script that comes on the floppy disks assumes that the target i386
is connected to the net and doing the sups from CMU directly. It  assumes  that
it  is  running  as  root,  so  that  the userids and groupids of the files are
preserved. This is necessary for a dozen or so  set[ug]id  files  in  /bin  and
/etc.  Setup  also  executes  three  commands  during  the  sup  of  the  first
collection.

  If you want to sup to an intermediary  machine  you  need  to  copy  the  sup
commands  from  the  setup  script  and  execute them on the intermediary being
careful to remove the e (execute) flag for the first collection.
        sup -dov PORTFILE first
        sup -dov PORTFILE bin.root
        sup -dov PORTFILE bin.usr
PORTFILE looks as follows: You need to edit it to include  your  crypt  and  to
change  the  base  directory to the directory on the intermediary machine where
you want the i386 binarires to be placed
first     host=x29.mach.cs.cmu.edu hostbase=/i386 base=/mnt/RFS/.LOCALROOT cryp
bin.root  host=x29.mach.cs.cmu.edu hostbase=/i386 base=/mnt/RFS/.LOCALROOT cryp
bin.usr   host=x29.mach.cs.cmu.edu hostbase=/i386 base=/mnt/RFS/.LOCALROOT cryp
You should do the sup as root on the intermediary machine to preserve user  and
group ids.

  Next  you  need  to do the first two steps of the setup command on the target
i386 machine and then copy the binaries from the intermediary  machine  to  the
hard-disk /RFS/.LOCALROOT.

  Finally you need to execute the following three commands on the i386
        execute cd dev; umask 0; tar xvf TARDEV
        execute dd if=boot.hd of=/dev/rhd0c
           or
        execute dd if=boot.sd of=/dev/rsd0c
        execute ln mach ../..; ln mach vmunix
before you can boot off the hard disk.
V. KDB commands
  Kdb is the kernel debugger for the Mach 2.5 kernel.  The following is a brief
list of the kdb commands. kdb uses the same command format as adb and expertise
in  adb is assumed.  The Mach 3.0 kernel has a different debugger called ddb. A
man page for it comes with the Mach 3.0 kernel sources.
To enter the debugger:

                ctrl-alt-d


        The format commands:
                 <addr>/<letters>
and write commands
                <addr>/{w,W} values
function exactly as you would expect from adb.  (And note that / and ?
are treated the same.)  So you can use kdb to disassemble code, look at
memory locations and change memory locations.

        $r      -       will print out the register values
        <rname/var      accesses the value of register_name/variable
        >rname/var      sets the value of register_name/variable

        The neat features are the "step/breakpoint" commands, which are
again analogous to the adb functions:
        :s      -       single step one instruction
        :c,C    -       continue until the next breakpoint
                        (these both takes counts ala adb syntax)
        :p,P    -       print the instructions while single stepping
        :j      -       step until the next call or return and count
                         the instructions
        :J      -       step until we return to this nesting level
                         (show functions entered and instruction
                          counts.)
        :S      -       step over the function call you are stopped at
        :r,R    -       set a temporary break at the return address, so
                         you effectively step out of this function. (Note:
                         make sure you have done the push %ebp, movl %esp,
                         %ebp before you try this.)

  Breakpoints are set with <addr>:B and <addr>:D and listed with $B, just  like
adb.    You  may  not  provide  commands  to  execute when a breakpoint is hit.
<addr>:b #, <addr>:d and $b are very different breakpoints.  They use the  i386
hardware  match  facilities.    You can set up to 4 breakpoints and you have to
specify which one  to  ":b".    Right  now  they  work  analogous  to  the  "B"
breakpoints. But someday, I will implement access to the hardware break on read
and break on write features; all that is supported now is break on execute.
        $l      -       lists the state of all the threads
        $L      -       lists the state and stack of all the threads

        $k      -       does a stack trace
        $c      -       does a stack trace
<thread>$K      -       does a stack trace for the give thread
<addres>$C      -       does a stack trace at the given frame.
   <map>$m      -       prints the map at address <map>
<addres>$Pp     -       prints port
<addres>$PO     -       prints object
<addres>$PM     -       prints map
<addres>$PP     -       prints "page structure"

<function>! arg0 arg1 ...       invokes function with the given arguments

        R!      -       invokes the function to sync the disk and reboot
        Q!      -       invokes the function to reboot

        pb!     -       invokes the playback function.  The screen is small
                         compared to the info you might want to display; pb
                         will play back each line and wait for a space or
                         return before continuing.  Any other character
                         terminates playback.  The buffer is 64k.
VI. Manual Pages
                               Table of Contents
1. Introduction                                                               1
2. Hardware Requirements for Mach on i386 Machines                            1
3. The Bootstrap Disks                                                        1
4. Before You SUP                                                             1
     4.1. Low Level Disk Formatting                                           1
     4.2. Manual Pages                                                        1
     4.3. Booting to Single User mode                                         1
     4.4. Disk Types                                                          2
     4.5. Initializing your Disk                                              2
5. Installation and System Setup                                              2
     5.1. Supping files                                                       2
     5.2. Daemons                                                             3
     5.3. X11R5 and Mice                                                      3
          5.3.1. X11R5                                                        3
          5.3.2. Mice                                                         3
     5.4. The Environment                                                     3
     5.5. BSD4.3-TAHOE Source Compilation                                     4
     5.6. Building Kernels                                                    4
     5.7. Installing/Booting Kernels                                          4
     5.8. Root, Super-Root and RFS                                            4
     5.9. Paging under Mach 2.5                                               4
     5.10. Paging under Mach 3.0                                              4
     5.11. Changing Time Zones                                                4
     5.12. The Kernel Debugger                                                4
6. Replicating The System                                                     4
     6.1. Cloning                                                             4
     6.2. Using Sup                                                           5
     6.3. Floppies                                                            5
7. DONT CLOBBER MY DISK                                                       5
     7.1. Minor Variations                                                    5
     7.2. Room Enough for DOS or MDOS                                         5
     7.3. The Disk Layout                                                     5
8. Known Features/Problems/Bugs                                               5
     8.1. gas                                                                 5
9. Mach Support                                                               5
I. Trouble Shooting the Installation                                          6
     I.1. A Few More Anomalies                                                6
II. ETHERNET                                                                  7
     II.1. WD8003 & Etherlink II & WD8003 Elite                               7
          II.1.1. EtherLink II                                                7
          II.1.2. WD8003 & WD8013                                             7
          II.1.3. WD8003 Elite                                                8
     II.2. Etherlink I                                                        8
     II.3. PC586                                                              9
III. Sup Collections                                                         11
     III.1. Binary Collections                                               11
     III.2. Source Collections                                               11
IV. Installation from an intermediary machine                                12
V. KDB commands                                                              13
VI. Manual Pages                                                             14