MACH KERNEL MONITOR
          (WITH APPLICATIONS USING THE PIE ENVIRONMENT)



                         23 August 1990



                            Ted Lehr
                           David Black

        Department of Electrical and Computer Engineering
                 and School of Computer Science

                   Carnegie Mellon University

                       Pittsburgh PA 15213



                            ABSTRACT

Factors  such  as  the  decomposition of parallel programs affect
their performance.  Measurements of parallel program  performance
are improved if supported by information such as how programs are
scheduled.  This manual  describes  how  to  use  MKM,  the  Mach
(context-switch)  kernel  monitor.    Special  examples  of  data
obtained  by  using  MKM  are  shown  via  the  PIE   performance
monitoring environment.

1 The Mach Kernel Monitor:  The Need to Monitor Context-Switching

The  performance of computations on parallel machines is affected

by user designed attributes such as the parallel decomposition of

the   computations  and  by  operating  system  actions  such  as

scheduling.    One  way  of  determining  how  computations   are

scheduled  is  to  detect  and time-stamp the context-switches of

their threads.



Certain Mach configurations (ie. those with  the  EXP  extension)

include the Mach Kernel Monitor (MKM) for monitoring kernel-level

behavior.  Currently, MKM only monitors context-switches of  user

selectable  threads.    It  permits  simultaneous  monitoring  of

independent computations so that multiple users  may  selectively

observe  as many computations as they desire, collecting only the

data about those they are interested in regardless of  what  else

is running on the system.



After discussing the implementation and system calls of MKM, this

manual gives some examples using the  PIE  (For  introduction  to

PIE,  see  "Visualizing Performance Debugging," in IEEE Computer,

October 1989, by Ted Lehr, et ala.).  performance monitoring  and

visualization  system.    Using  the PIE examples, the scheduling

information  collected  by  MKM  fulfills  the  double  role   of

visualizing   scheduling   performance  in  general  as  well  as

visualizing the influence of the scheduler on user algorithms.

2 Implementation

An MKM monitor consists of:

   - A data structure  consisting  of  buffers  for  storing
     information  about  detected  events  (in  the  current
     implementation, a  monitor  can  detect  only  context-
     switch events) and state information.

   - A list of threads that can be observed by the monitor.

   - Event  detection  sensors within Mach context-switching
     code.

   - Entries within thread  data  structures  for  assigning
     monitors to threads.

These data structures are operated upon by several monitor system

calls. Future versions of the monitor may contain data structures

for  monitoring  message  sends  and recieves or paging behavior.

Currently, the only calls recognized by a Mach kernel monitor are

ones concerned with detection of context-switches.



The  monitor_create  call  creates  a  monitor within the calling

task.  The call returns the monitor id and the size of the  event

buffer  in  the  kernel.   The user uses this size to allocate an

appropriatly sized user buffer  into  which  monitor_read  writes

context-switch data read from the kernel.  monitor_create returns

the monitor in a suspended  state.    monitor_resume  starts  the

monitor.    monitor_suspend  permits  the user to suspend (pause)

monitoring.      monitor_terminate    destroys    the    monitor.

monitor_read  reads the context-switch event data from the kernel

into a user supplied buffer.  monitor_read  calls  are  valid  as

long   as  its  argument  is  a  valid,  non-terminated  monitor.

thread_monitor enables individual threads for monitoring.  When a

thread  calls  thread_monitor  the associated monitor will detect

each time the thread context-switches.  thread_unmonitor disables

a thread from being monitored.

    #include <mach.h>
    #include <mach/kernel_event.h>
    #include <mach/monitor.h>

    main()
    {
        int                 buf_size;
        monitor_t           my_monitor;
        int                 j,num_events=MONITOR_MIG_BUFFER_S
        kern_mon_buffer_t   kernel_events;

        buf_size = REQUESTED_SIZE;
        monitor_create(task_self(), &this_monitor, &buf_size)
        monitor_resume(this_monitor);
        thread_monitor(this_monitor,UNIQUE_ID,thread_self());

        for(i = 0; i < 300; i++) sleep(1);

        thread_unmonitor(this_monitor, thread_self());
        kernel_events = (kern_mon_buffer_t)
          malloc(sizeof(kern_mon_data_t)*MONITOR_MIG_BUFFER_S
        while (num_events == MONITOR_MIG_BUFFER_SIZE) {
          monitor_read(this_monitor,kernel_events,&num_events
          for (j = 0; j < num_events; j++) {
            printf("%8.8x %8.8x %8.8x %8.8x %8.8x\n",
                   kernel_events[j].third_element,
                   kernel_events[j].second_element,
                   kernel_events[j].hi_time,
                   kernel_events[j].lo_time,
                   kernel_events[j].first_element);
            }
        }
        monitor_terminate(this_monitor);
    }

         Figure 1:  Simple Example Program Using Monitor



Figure  1 shows an example program using monitoring.  The program

runs as a single thread.  The constant REQUESTED_SIZE is assigned

to  buf_size.   This is the requested size of the monitor buffers

allocated  inside  the  kernel.    After  creating  and  resuming

(starting)   the   monitor,   the   program  enables  itself  for

monitoring.  UNIQUE_ID is some constant that the  user  knows  is

unique  across  all  the  threads  in his program.  In this case,

since there is  only  one  thread,  the  value  of  UNIQUE_ID  is

arbitrary.



After  executing  a  sleep  statement  300  times,  the thread is

disabled  for  monitoring.    Then  a  user  routine  is  called,

print_events,  that  repeatedly calls monitor_read and prints the

events until the kernel_buffer is empty.    Note  that  the  user

buffer   is   only   MONITOR_MIG_BUFFER_SIZE  big  because  of  a

limitation on MIG buffer sizes.   Thus,  the  program  must  call

monitor_read  until  it returns less than MONITOR_MIG_BUFFER_SIZE

events.  When this occurs, the  program  knows  that  the  kernel

buffer  is  empty.    When  print_events  returns, the monitor is

terminated.  Note that in this program, monitor_suspend is  never

called.

The   context-switch  data  structure  saved  for  each  relevant

context-switch is:


    typedef
    struct  kernel_event {
        unsigned    event_type;      /* type           */
        unsigned    first_element;   /* stopped thread */
        unsigned    second_element;  /* started thread */
        unsigned    third_element;   /* flag and cpu   */
        unsigned    hi_time;         /* hi time stamp  */
        unsigned    lo_time;         /* lo time stamp  */
    } kern_mon_data_t, *kern_mon_buffer_t;



The members of  the  structure  consist  of  the  type  of  event

(currently,   only   one   type  of  kernel  event  is  detected:

context-switches), the  stopped-thread  and  started-thread,  the

processor   on  which  the  threads  switched,  and  a  timestamp

separated into seconds and microseconds fields.  If  one  of  the

threads  is  unknown,  its id is set to -1.  The most significant

bit of the processor  field  is  1  if  that  event  overwrote  a

previous, unread event (ie. overflow).

  NOTE:
     Currently, there is no internal protection guarding  against
     requesting  too  much  memory  for buffers.  It is suggested
     that no more than a half megabyte should be  requested.    A
     rule  of  thumb  is that the greater the thread-to-processor
     ratio, t, of one's computation,  the  more  context-switches
     there  will  be.   Assume that when t>1.0, there will be ten
     context-switches per second.    The  size  of  the  internal
     buffers   then   depends   on   how  often  they  are  read.
     monitor_read retrieves at most n = sizeof(kern_mon_data_t) x
     MONITOR_MIG_BUFFER_IZE bytes each time the buffers are read.
     Assume that once  one  monitor_read  is  made  to  read  the
     buffers,  the  user  repeats  the call until the buffers are
     empty.    In  such  case,  if  the  user  makes  bursts   of
     monitor_read  calls once every d seconds, a good buffer size
     would be 10d*n.

Figure 2 is schematic depicting a case in which  two  independent

non-communicating  Mach tasks have created separate MKM monitors.

Each monitor is represented by a port in its parent task.   Thus,

the  task  that creates a monitor obtains rights to the port that

represents the monitor; only tasks that possesses such rights can

access  the  monitor.  In our example, unless task B gives task A

rights to the monitor created by B, task A cannot access it.



Figure 2 also shows non-intersecting  sets  of  circular  buffers

allocated  to  each monitor for holding context-switch events.  A

buffer is assigned  to  each  processor  in  order  to  eliminate

contention  between  processors  for  buffers.    When  a  thread

context-switches, a software context-switch sensor detects which,

if any, monitor is tracking the thread and writes an event to the

appropriate buffer.  Eventually,  a  task  holding  rights  to  a

monitor  will  release  those  rights  and terminate the monitor.

This can be done either explicitly while the task  is  alive,  or

implicitly  when  the  task  terminates.    In  either  case, the

termination of  a  particular  monitor  is  accomplished  by  the

kernel.























































         Figure 2:  General Kernel Monitor Architecture
monitor_create

#include <mach.h>
#include <mach/kernel_event.h>

kern_return_t monitor_create(owner_task, new_monitor, buffer_size
        task_t          owner_task;
        monitor_t       *new_monitor;   /* out */
        int             *buffer_size;   /* out */


Description

monitor_create creates a new monitor within the task specified by

owner_task argument. buffer_size is the requested size (in number

of   events)   for   the  monitor  kernel  buffer  used  to  hold

context-switch events.  When monitor_create returns,  buffer_size

is maximum number of events that kernel buffer may hold before it

overflows.  When the  monitor  is  created  send  rights  to  its

monitor  kernel  port are given to it and returned in new_monitor

to the caller.  The new monitor is returned in a suspended state.

To  get  a  new monitor to run, first monitor_create is called to

get the new monitor's identifier,(monitor).  Then  monitor_resume

is called to get the monitor to execute.

Arguments

owner_task      The task which is to contain the new monitor.


new_monitor     The new monitor.


buffer_size     The  size  (in  number  of events) of the monitor
                buffer in kernel.

Returns

KERN_SUCCESS    A new monitor has been created.


KERN_INVALID_ARGUMENT
                parent_task is not a valid task.

Notes

Currently,  there  is  no  internal  protection  guarding against

requesting too much memory for buffers.  It is suggested that  no

more  than  a half megabyte should be requested.  A rule of thumb

is that the greater the thread-to-processor ratio,  t,  of  one's

computation,  the  more  context-switches  there will be.  Assume

that when t > 1.0, there will be ten context-switches per second.

The  size  of the internal buffers then depends on how often they

are read.  Each time the buffers are read, (see monitor_read)  at

most n = sizeof(kern_mon_data_t) x MONITOR_MIG_BUF_SIZE bytes are

retrieved.  Assume that once one monitor_read is made to read the

buffers,  the  user repeats the call until the buffers are empty.

In such case, if the user makes bursts of monitor_read calls once

every d seconds, a good buffer size would be 10d*n.

See Also

monitor_resume, monitor_terminate, monitor_suspend, monitor_read,

thread_monitor, thread_unmonitor, monitor
monitor_resume

#include <mach.h>
#include <mach/kernel_event.h>

kern_return_t monitor_resume(target_monitor)
        monitor_t       target_monitor;


Arguments

target_monitor  The monitor to be resumed.

Description

Sets the state  of  target_monitor  to  MONITOR_RUN.    When  the

monitor is in this state, it can detect events.

Returns

KERN_SUCCESS    The monitor has been resumed.


KERN_FAILURE    The monitor state is MONITOR_SHUTDOWN.


KERN_INVALID_ARGUMENT
                target_monitor is not a monitor or its port is no
                longer valid.

See Also

monitor_create, monitor_terminate, monitor_suspend, monitor_read,

thread_monitor, thread_unmonitor, monitor
monitor_suspend

#include <mach.h>
#include <mach/kernel_event.h>

kern_return_t monitor_suspend(target_monitor);
        monitor_t       target_monitor;


Arguments

target_monitor  The monitor to be suspended.

Description

Sets the state of target_monitor to MONITOR_PAUSE.  No events are

detected   when  the  monitor  is  in  this  state  although  any

previously detected events may be read by monitor_read.

Returns

KERN_SUCCESS    The monitor has been suspended.


KERN_FAILURE    The monitor state is MONITOR_SHUTDOWN.


KERN_INVALID_ARGUMENT
                target_monitor is not a monitor or its port is no
                longer valid.

See Also

monitor_create, monitor_terminate, monitor_resume,  monitor_read,

thread_monitor, thread_unmonitor, monitor
monitor_terminate

#include <mach.h>
#include <mach/kernel_event.h>

kern_return_t monitor_terminate(target_monitor)
        monitor_t       target_monitor;



Description

monitor_terminate    destroys    the    monitor    specified   by

target_monitor.

Arguments

target_monitor  The monitor to be destroyed.

Returns

KERN_SUCCESS    The monitor has been destroyed.


KERN_INVALID_ARGUMENT
                target_monitor  is  not  a  valid  monitor or its
                monitor port no longer exists.

See Also

monitor_create,  monitor_resume,  monitor_suspend,  monitor_read,

thread_monitor, thread_unmonitor, monitor
monitor_read

#include <mach.h>
#include <mach/kernel_event.h>

/* only current interpretion of kernel_event */

typedef
struct  kernel_event {  /* unit kernel event */
     unsigned   event_type;      /* the type of kernel event  */
     unsigned   first_element;   /* the stopped thread        */
     unsigned   second_element;  /* the started thread        */
     unsigned   third_element;   /* flag and cpu number       */
     unsigned   hi_time;         /* hi time stamp             */
     unsigned   lo_time;         /* lo time stamp             */
} kern_mon_event, *kern_mon_event_t, kern_mon_data_t,
  *kern_mon_buffer_t;

kern_return_t monitor_read(target_monitor, buffer, events_read)
        monitor_t               target_monitor;
        kern_mon_buffer_t       buffer;
        int                     events_read;


Description

monitor_read  returns  events detected by target_monitor into the

buffer argument.  events_read is the number of  events  returned.

Each  call  to  monitor_read is limited to returning a maximum of

MONITOR_MIG_BUF_SIZE events, a limitation  of  MIG  buffer  size.

Buffer  data  is  aligned  around  event boundaries but it is the

responsibility of user code  to  properly  declare  and  allocate

buffer

Arguments

target_monitor  The monitor for which events are being read.


buffer          The  user's  buffer into which the events will be
                written.


events_read     The number of events read by the call.

Returns

KERN_SUCCESS    The monitor buffer was successfully read.


KERN_INVALID_ARGUMENT
                target_monitor  is  not  a monitor or the monitor
                port is not valid.

Notes

A rule of thumb  is  that  the  greater  the  thread-to-processor

ratio,  t,  of one's computation, the more context-switches there

will  be.    Assume  that  when  t  >  1.0,  there  will  be  ten

context-switches  per  second.   In order to prevent the internal

buffers from overflowing, monitor_read should be called at  least

once  every  MONITOR_MIG_BUF_SIZE/10 seconds which in the current

implementation is about every 30  seconds.    Or,  if  each  time

monitor_read  is  called  it  is immediately followed by repeated

calls until the internal  buffers  are  empty,  these  bursts  of

repeated    calls    should    occur    every   every   B/(10   x

sizeof(kern_mon_data_t)) seconds where  B  is  the  size  of  the

internal buffer in bytes.

See Also

monitor_resume, monitor_terminate, monitor_suspend, monitor_read,

thread_monitor, thread_unmonitor, monitor
thread_monitor

#include <mach.h>
#include <mach/kernel_event.h>

kern_return_t thread_monitor(target_monitor,unique_id,target_thre
        monitor_t               target_monitor;
        int                     unique_id;
        thread_t                target_thread;


Arguments

target_monitor  The monitor which will observe target_thread


unique_id       An id for thread identification outside kernel.


target_thread   The thread which will be monitored.

Description

thread_monitor   enables   target_thread   for   monitoring    by

target_monitor  argument.   The caller is responsible for keeping

unique_id unique among all threads that target_monitor  observes.

target_thread can be observed by only one monitor at a time.

Returns

KERN_SUCCESS    The  thread  has  been  enabled to be observed by
                monitor.


KERN_FAILURE    The monitor state is MONITOR_SHUTDOWN  or  thread
                is not active.


KERN_INVALID_ARGUMENT
                target_monitor is not a monitor, target_thread is
                not a thread, or the monitor port is not valid.

See Also

monitor_create,         monitor_terminate,        monitor_resume,

monitor_suspend, monitor_read, thread_unmonitor, monitor
thread_unmonitor

#include <mach.h>
#include <mach/kernel_event.h>

kern_return_t thread_unmonitor(target_monitor, target_thread)
        monitor_t               target_monitor;
        thread_t                target_thread;


Arguments

target_monitor  The monitor which observes target_thread


target_thread   The thread which will be disabled.

Description

thread_unmonitor disables target_thread from being  monitored  by

target_monitor.

Returns

KERN_SUCCESS    The thread has been disabled from monitoring.


KERN_INVALID_ARGUMENT
                target_monitor is a valid monitor,  target_thread
                is  not  a  thread,  or  the  monitor port is not
                valid.

See Also

monitor_create,        monitor_terminate,         monitor_resume,

monitor_suspend, monitor_read, thread_monitor, monitor

3 Examples of Context-Switch Monitoring

Before  giving  examples  of  some  results achieved using MKM, a

brief description of the  PIE  environment  is  necessary.    The

Parallel  Programming  and Instrumentation Environment (PIE) is a

software development environment for debugging performance  using

special   development   and   data   analysis  tools.  PIE  is  a

"computational   laboratory"   in   which   programmers    design

experiments to evaluate the real behavior of computations.



PIE  is  a  portable system whose basic platform is a workstation

running the X Window System.  It supports several sequential  and

parallel  languages.  Currently, PIE's monitoring instrumentation

runs on Vax and Sun  workstations,  Encore  Multimax,  and  Warp.

Although  PIE can be ported to other Unix-like operating systems,

its current form is implemented on  top  of  the  Mach  operating

system.

























                 Figure 3:  Organization of PIE



Figure  3  depicts  the general organization of PIE.  This manual

only  presents  the  visualization  component  of   PIE,   called

PIEscope,  because  of  its relevance in showing context-switches

detected by MKM.  The context-switches shown in the examples were

detected by MKM and retrieved by PIE using the monitor_read call.

The begin and end of  the  threads  were  recorded  using  simple

methods in PIE.



3.1 Interpreting the PIE Figures



























Figure 4:  Execution and Cpu Views of Incomplete Gang Scheduling

The two views in Figure 4 are examples of PIE's principle formats

for representing performance information.  These particular views

show  the  execution of a matrix multiplication computation.  The

top view is an example of the execution barscope view; the bottom

view  is  an  example of the cpu barscope view.  In the execution

barscope view, time is measured in microseconds on the horizontal

while the threads of the computation are ordered on the vertical.

This particular view shows the part of the execution  from  about

0.0  to  36.7  seconds.  The time of execution for each thread is

depicted by the dark rectangles.



The cpu barscope shows thread-to-processor assignments during the

execution  of  a  computation.  As in the execution barscope, the

cpu barscope displays time in microseconds on the horizontal.  On

the vertical, however, the processors used by the computation are

ordered and arbitrarily numbered on the vertical.  Opposite  each

cpu  are  alternating  sets of patterned rectangles.  A patterned

rectangle represents an identifiable  executing  thread  while  a

white   rectangle  is  a  period  when  none  of  the  respective

computation's threads are running on the  associated  cpu.    PIE

allows  a user to arbitrarily assign unique colors or patterns to

as many threads per cpu-view as he wishes.



3.2 Gang Scheduling

Sometimes, the number of threads is greater than  the  number  of

processors.    The  two  views  of Figure 4 are execution and cpu

barscopes of an entire matrix multiply computation for which five

processors  were allocated.  In each view, a pair of time cursors

delimit approximately the same period in time, one in  which  the

collector,  again represented by dark diagonally slashed bars, is

running on cpu 12.































Figure 5:  The Execution of Two Threads on Three Kernels:  XF29, 

3.3 Comparing Schedulers for a Uniprocessor

PIE and MKM can also monitor sequential computations.  The  three

views  in  Figure  5  are  execution  barscopes that were used to

evaluate the Mach scheduler.    Each  view  shows  the  same  two

threads  time-sharing  one  processor.    As  one  moves down the

Figure, the views represent newer versions of Mach.  Because  the

views  depict  uniprocessor  executions, cutting a vertical swath

through a view at any  point  slices  through  only  one  running

thread ... only a single black rectangle.



The  top  view  of  Figure 5 depicts an execution on the old XF29

kernel.  The next view depicts the same computation on  the  less

primitive  CS5a kernel.  The X96 kernel in the bottom view is the

most advanced.



The views show that the two threads do not behave identically  on

three  kernels.    XF29  uses  a simple scheduling algorithm that

switches  the  threads  roughly  every  100  milliseconds.    The

schedulers  of the latter two kernels use a progressive algorithm

which attempt to increase the length of the time slices allocated

to  each  thread.    Despite  good  intentions,  the  progressive

algorithm of CS5a fails to  dramatically  reduce  the  number  of

context-switches   because   it  permits  threads  to  switch  to

themselves  repeatedly  as  indicated  by  the  preponderance  of

"squiggles."    X96 corrects this drawback by preempting a thread

from switching to itself.

                        Table of Contents
   1 The  Mach  Kernel  Monitor:    The  Need   to   Monitor    1
     Context-Switching
   2 Implementation                                             1
   3 Examples of Context-Switch Monitoring                     11
       3.1 Interpreting the PIE Figures                        11
       3.2 Gang Scheduling                                     11
       3.3 Comparing Schedulers for a Uniprocessor             12

                         List of Figures
   Figure 1:   Simple Example Program Using Monitor             1
   Figure 2:   General Kernel Monitor Architecture              3
   Figure 3:   Organization of PIE                             11
   Figure 4:   Execution  and  Cpu  Views of Incomplete Gang   11
               Scheduling
   Figure 5:   The  Execution  of  Two  Threads   on   Three   11
               Kernels:  XF29, CS5a, X96