## Slide 1: System Challenges of Intermittent Computing
Kiwan Maeng
Notes: talk about our paper,

## Slide 2: Recap: Just-In-Time (JIT) Checkpointing Enables Intermittent Execution
prep
encrypt string
out
Workload
Checkpointing threshold
Time
Voltage
Notes: ~4:00
This can be solved by a technique called the JIT C.
Just to make things clear, the solution of a JIT C that I’ll introduce is an alternative solution from the task-based approach that my colleague, Emily, presented earlier.

## Slide 3: Recap: JIT Checkpointing Enables Intermittent Execution
encrypt
1
2
prep
…
!
Energy is low!!
Time
Voltage
Notes: hits

## Slide 4: Recap: JIT Checkpointing Enables Intermittent Execution
!
Energy is low!!
encrypt
1
2
prep
Checkpoint!!
Time
Voltage

## Slide 5: Recap: JIT Checkpointing Enables Intermittent Execution
encrypt
Restore
…
encrypt
1
2
prep
Time
Voltage

## Slide 6: Recap: JIT Checkpointing Enables Intermittent Execution
encrypt string
!
encrypt
1
2
prep
Time
Voltage

## Slide 7: Recap: JIT Checkpointing Enables Intermittent Execution
encrypt string
out
encrypt string
encrypt
1
2
prep
Time
Voltage

## Slide 8: Real-world Applications Need More Than Computation
Sense the temperature every 10 seconds!
Periodic Execution
I need to stay alive while I’m communicating!
Atomic Execution
Smart agriculture
[Vasisht 2017]
Wildlife tracking
[Zhang 2004]
Notes: Because these systems do not require a battery to operate, they have a lot of potentials in the field where periodic battery replacement is infeasible,
such as ..

## Slide 9: Intermittence Complicates Additional Execution Models
Sense the temperature every 10 seconds!
Periodic Execution
I need to stay alive while I’m communicating!
Atomic Execution
Notes: Because these systems do not require a battery to operate, they have a lot of potentials in the field where periodic battery replacement is infeasible,
such as ..

## Slide 10: Outline
Challenge 1. Periodic Execution
Solution 1. CatNap
Challenge 2. Atomic Execution
Solution 2. Samoyed
Future Work
Notes: This is going to be..

## Slide 11: Power Failures Complicate Periodic Execution
Sense the temperature every 10 seconds!
Notes: So why is it hard to run program periodically on intermittent systems? First, varying incoming power makes periodic execution complicated. Let’s again, say that the programmer wants the system to collect a temperature data every 10 seconds.

## Slide 12: Power Failures Complicate Periodic Execution
Time
Voltage

## Slide 13: Power Failures Complicate Periodic Execution
Time
Voltage

## Slide 14: Power Failures Complicate Periodic Execution
Time
Voltage

## Slide 15: Power Failures Complicate Periodic Execution
Time
Voltage

## Slide 16: Power Failures Complicate Periodic Execution
Time
Voltage
10s

## Slide 17: Power Failures Complicate Periodic Execution
Time
Voltage

## Slide 18: Power Failures Complicate Periodic Execution
Time
Voltage

## Slide 19: Power Failures Complicate Periodic Execution
Time
Voltage
> 10s

## Slide 20: Concurrent Execution Complicate Periodic Execution
Sense the temperature every 10 seconds and do compression!
Notes: Another problem can occur when multiple code are being executed concurrently. For example, one might write a program that collects data every 10 seconds, and concurrently compresses the data.

## Slide 21: Concurrent Execution Complicate Periodic Execution
Time
Voltage

## Slide 22: Concurrent Execution Complicate Periodic Execution
Time
Voltage

## Slide 23: Concurrent Execution Complicate Periodic Execution
Time
Voltage

## Slide 24: Concurrent Execution Complicate Periodic Execution
Time
Voltage
…
Not enough energy!

## Slide 25: Concurrent Execution Complicate Periodic Execution
Time
Voltage
…
Not enough energy!
> 10s

## Slide 26: Concurrent Execution Complicate Periodic Execution
Time
Voltage
…
Not enough energy!
> 10s
Can we run periodic code in intermittent devices?

## Slide 27: Outline
Challenge 1. Periodic Execution
Solution 1. CatNap
Challenge 2. Atomic Execution
Solution 2. Samoyed
Future Work
* Kiwan Maeng and Brandon Lucia, Adaptive Low-Overhead Scheduling for Periodic and Reactive Intermittent Execution. PLDI 2020
Notes: This is going to be..

## Slide 28: Idea 1: Quality degradation
32bit
8bit
Notes: One possible solution to this is reducing the quality of the program. For example, the program might choose to collect a less accurate sample, while using less energy and thus keeping up with the programmer-specified periodic requirement. This is possible because many sensors can be configured to use less energy, while being less accurate.

## Slide 29: Idea 2: Schedule Code Execution and Recharging
Notes: This problem can be solved with smart scheduling. Instead of using too much energy right before the data collection, if the system had spreaded the compression at the “right moments”, the system would have run correctly, as you can see from the right figure.

## Slide 30: CatNap: Computation and Recharge Scheduler
Degradation Logic
Programming Model
Scheduler
32bit
8bit
Feasibility Test
Notes: Don’t go into detail

## Slide 31: Programmer Specifies Time-critical Events and Time-insensitive Tasks
Event
Code with a time requirement (periodic/reactive requirement)
Short, atomic
e.g., sensor read, communication, …
Event
Task
Task
Code without a time requirement
Long, interruptible
e.g., compute
Notes: CatNap requires the programmer to write a program as a collection of events and tasks. Events are code that has a time requirement. Code that must run periodically or reactively should be declared as an event. Events run atomically, and must be kept short. Usually, things like a sensor read or a communication must become an event. Tasks, on the other hand, are code without a time requirement. They can be long, and can be interrupted by an event or a recharge. Tasks usually hold computations.

## Slide 32: CatNap Schedules According to Priorities
Events
High priority
Event
Task
Recharge (event)
Event buffer recharge
Middle priority
Tasks
Low priority
Recharge (task)
Task buffer recharge
Low priority
Notes: Then, CatNap scheduler shedules events, tasks, an recharges with different priorities. CatNap runs events with the highest priority, as soon as they arrive. When the energy reserve for events is not full, CatNap prioritizes recharging the buffer over running the tasks or recharging for the tasks.

## Slide 33: CatNap Schedules According to Priorities
Events
High priority
Event
Task
Recharge (event)
Event buffer recharge
Middle priority
Tasks
Low priority
Recharge (task)
Task buffer recharge
Low priority
If a set of events and recharges are schedulable, CatNap can always schedule them! (proof: paper)
Notes: Then, CatNap scheduler shedules events, tasks, an recharges with different priorities. CatNap runs events with the highest priority, as soon as they arrive. When the energy reserve for events is not full, CatNap prioritizes recharging the buffer over running the tasks or recharging for the tasks.

## Slide 34: CatNap Schedules According to Priorities
Events
High priority
Event
Task
Recharge (event)
Event buffer recharge
Middle priority
Tasks
Low priority
Recharge (task)
Task buffer recharge
Low priority
If a set of events and recharges are schedulable, CatNap can always schedule them! (proof: paper)
How do you know?
Notes: Then, CatNap scheduler shedules events, tasks, an recharges with different priorities. CatNap runs events with the highest priority, as soon as they arrive. When the energy reserve for events is not full, CatNap prioritizes recharging the buffer over running the tasks or recharging for the tasks.

## Slide 35: A Feasibility Test Checks If Events are Schedulable
32bit
8bit
Not schedulable
Schedulable
Main idea: Does a set of events use more energy than what can be recharged?
Event 1
Event 2
Event 3
Theorem
Assume an event uses energy and has a period of . If an incoming power is and , the events and charges can be scheduled if:
Full proof is provided as an Appendix of the paper.
DETAIL
Notes: We developed a mathematical formula to test the schedulability with a given input power. Of course, you do not need to digest the formula right now. If you are interested, a full proof of the feasibility test is provided as an Appendix.

## Slide 36: CatNap Schedules According to Priorities
Events
High priority
Event
Task
Recharge (event)
Event buffer recharge
Middle priority
Tasks
Low priority
Recharge (task)
Task buffer recharge
Low priority
If a set of events and recharges are schedulable, CatNap can always schedule them! (proof: paper)
What if it’s not?
Notes: Then, CatNap scheduler shedules events, tasks, an recharges with different priorities. CatNap runs events with the highest priority, as soon as they arrive. When the energy reserve for events is not full, CatNap prioritizes recharging the buffer over running the tasks or recharging for the tasks.

## Slide 37: Quality Degradation Makes Infeasible Schedule Feasible
32bit
8bit
Programmer provides set of degradation rules
Notes: One possible solution to this is reducing the quality of the program. For example, the program might choose to collect a less accurate sample, while using less energy and thus keeping up with the programmer-specified periodic requirement. This is possible because many sensors can be configured to use less energy, while being less accurate.

## Slide 38: Evaluation: CatNap Enables Periodic Execution
Ran periodic and compute-intensive workloads concurrently
Ran by harvesting RF energy
Compared with InK [Yıldırım 2018]
38
Periodic temperature sensing every 0.57s (event)
Downsampling with a square filter (task)
Notes: Next, we concurrently ran a periodic workload of measuring the temperature every 0.57 second, and a compute-intensive workload of downsampling the data with a square filter. Again, we ran the evaluation on a real energy-harvesting setup and compared with InK. For CatNap, the … was programmed as an event , while … as a task

## Slide 39: Evaluation: CatNap Enables Periodic Execution
Chart: Incoming Power (dBm)
| 29.75 | 28.5 | 27.25 | MEAN
CatNap | 0.5711 | 0.5744 | 0.5785 | 0.5747
InK | 0.8184 | 2.2045 | 4.1741 | 2.399
Target period
(closer is better)
Notes: This graph shows the resulting period of the actually sampled data. On the X-axis, different incoming power configuration is shown. For each configuration, the period of the actually sampled data is plotted for CatNap and InK. The target period specified by the programmer is shown as a red line. It is a good system if the bar is close to the red line. As you can see, CatNap meets the period requirement in all the incoming power, while InK violates the requirement heavily when the incoming power gets smaller. CatNap meets with the period nicely mainly because the downsampling task did not touch the energy reserve for the temperature measuring event, and the temperature sensing event can always run whenever needed.

## Slide 40: Outline
Challenge 1. Periodic Execution
Solution 1. CatNap
Challenge 2. Atomic Execution
Solution 2. Samoyed
Future Work
Notes: This is going to be..

## Slide 41: Power Failure Breaks Atomicity
Workload
AES
prep
encrypt string
out
Time
Voltage
Notes: To demonstrate the problem with peripherals, let’s look at the system with a hardware encryption accelerator.

## Slide 42: Power Failure Breaks Atomicity
Workload
AES
wait
prep
encrypt string
out
Time
Voltage
Notes: offloads
In this work, we only target blocking peripheral, where the cpu starts the execution and waits while it finishes.

## Slide 43: Power Failure Breaks Atomicity
encrypt string
!
Energy is low!!
AES
wait
…
…
prep
Time
Voltage

## Slide 44: Power Failure Breaks Atomicity
!
AES
wait
Checkpoint!!
encrypt string
…
prep
Time
Voltage

## Slide 45: Power Failure Breaks Atomicity
!
AES
wait
encrypt string
…
Cannot checkpoint…
(peripheral state not always visible)
prep
Time
Voltage
Notes: However, the state of the peripheral may not always be able to be checkpointed.

## Slide 46: Power Failure Breaks Atomicity
!
wait
encrypt string
…
Cannot checkpoint…
(peripheral state not always visible)
prep
Time
AES
output buffer
internal circuitry
input buffer
Notes: However, the state of the peripheral may not always be able to be checkpointed.

## Slide 47: Power Failure Breaks Atomicity
encrypt string
AES
wait
prep
Time
Voltage

## Slide 48: Power Failure Breaks Atomicity
encrypt string
AES
wait
…
wait
Undefined state!
prep
Time
Voltage
Notes: maybe it is not even running, or maybe it is running with some garbage data.
This can ultimately cause a critical failure such as program hanging indefinitely, or producing a wrong result.

## Slide 49: Power Failure Breaks Atomicity
Workload
AES
wait
prep
encrypt string
out
Time
Voltage
This region must be atomic! (not interrupted by checkpoints/failures)
Notes: offloads
In this work, we only target blocking peripheral, where the cpu starts the execution and waits while it finishes.

## Slide 50: Initial Attempt: Selectively Disabling Checkpoints
prep
encrypt string
out
Workload
AES
wait
What if we never collect a checkpoint here?
Notes: In the previous example, the problem happened when we tried to checkpoint in the middle of the accelerator operation.
So one might think, it can be easily solved by never collecting a checkpoint while the accelerator is running. Let’s say we never collect a checkpoint in the yellow region, and always go back and
restart the entire region when power fails in the middle.
This approach can avoid the accelerator getting into an undefined state. However, different problems still remain.

## Slide 51: Initial Attempt: Selectively Disabling Checkpoints
AES
…
51
prep
encrypt string
wait
encrypt string
wait
encrypt string
wait
The program never ends!
Notes: If the accelerator operation is too long, the system will keep reexecuting the accelerator from the beginning, without every finishing.

## Slide 52: Outline
Challenge 1. Periodic Execution
Solution 1. CatNap
Challenge 2. Atomic Execution
Solution 2. Samoyed
Future Work
* Kiwan Maeng and Brandon Lucia, Supporting Peripherals in Intermittent Systems with Just-In-Time Checkpoints. PLDI 2019
Notes: This is going to be..

## Slide 53: Idea: Peripheral Operations Usually Can Be Decomposed into Smaller Operations
53
AES
AES
AES
str[0:N]
str[0:N/2]
str[N/2:N]
Notes: For example, an AES encryption of a string of length N can be broken down into two smaller instances of an AES encryption, with each taking half of the original string as its input

## Slide 54: Solution: Peripheral Access Decomposition
AES
prep
encrypt string
out
wait
Specifies the decomposition rule

## Slide 55: Solution: Peripheral Access Decomposition
AES
prep
encrypt string
out
wait
Adds necessary instrumentation
Notes: Now, to sum up,

## Slide 56: Solution: Peripheral Access Decomposition
AES
prep
encrypt string
out
wait
Dynamically runs decomposition
MEM
Hello, world!
Notes: On runtime, the system will dynamically decompose the peripheral operation if necessary.
For example, if the peripheral operation is too large to finish in one energy cycle,

## Slide 57: Solution: Peripheral Access Decomposition
AES
prep
enc
out
Dynamically runs decomposition
wait
enc
wait
MEM
Hello, world!
Notes: The runtime system dynamically decompose it into a smaller operation using the user-provided rule.

## Slide 58: Solution: Peripheral Access Decomposition
AES
prep
out
Dynamically runs decomposition
wait
MEM
Hello, world!
wait
wait
wait
Notes: And this can happen recursively, until each operation becomes small enough.

## Slide 59: Solution: Peripheral Access Decomposition
AES
prep
wait
MEM
Hello, world!
wait
wait
wait
wait
wait
wait
out
Memoizes the appropriate size
Notes: After decomposing sufficiently, the system can run each peripheral operations with checkpointing in between.
After finding the appropriate size, the system memorizes the size and use it in the future instead of doing the dynamic search every time.

## Slide 60: Solution: Peripheral Access Decomposition
Check the energy use of the decomposed code
…
…
Too large
Sufficiently small
60
Notes: You may have noted that this approach does not work if even the maximally decomposed operation is too large to run.
We have a energy profiler that synthesizes the smallest possible peripheral operation and measures the energy use on compile time to make sure the decomposition always work.

## Slide 61: Evaluation: Kitchen Monitoring ML application
61
Send Bluetooth low-energy (BLE) alert if faucet or food dispenser is on.
Using microphone, ML accelerator, and BLE module.
Notes: You may have noted that this approach does not work if even the maximally decomposed operation is too large to run.
We have a energy profiler that synthesizes the smallest possible peripheral operation and measures the energy use on compile time to make sure the decomposition always work.

## Slide 62: Evaluation: Kitchen Monitoring ML application
62
Our work
Prior work
Notes: You may have noted that this approach does not work if even the maximally decomposed operation is too large to run.
We have a energy profiler that synthesizes the smallest possible peripheral operation and measures the energy use on compile time to make sure the decomposition always work.

## Slide 63: Outline
Challenge 1. Periodic Execution
Solution 1. CatNap
Challenge 2. Atomic Execution
Solution 2. Samoyed
Future Work
Notes: This is going to be..

## Slide 64: Summary and Future Work
CatNap enables periodic execution with recharge scheduling, feasibility test, and degradation.
Samoyed enables atomic execution with dynamic region decomposition.
What is next?
  What if there is not enough power at all (e.g., night)?
  How fast/slow is the app going to be?
  Can we do node-to-node communication?
Notes: This is going to be..

## Slide 65: System Challenges of Intermittent Computing
Kiwan Maeng
Notes: talk about our paper,