## Slide 1
Autotuning and ECE Computing Infrastructure
18-613: Foundations of Computer Systems 9th Lecture, April 18, 2019
Instructor:
Franz Franchetti

## Slide 2: Outline
Autotuning
ECE software
Andrew software
PSC software
Computing infrastructure

## Slide 3: Programmer Demographics
Black Belt Programmer
Performance libraries, device drivers
C, Assembly, low-level tricks
Goal: performance above all
Software engineers
Large applications
C++, Java, C#
Goal: Maintenance vs. performance
Average programmers
Small ad-hoc applications
C, C++, Java, Perl, Python
Goal: implement their algorithm quickly
Notes: 3

## Slide 4: Compilers: The Fundamental Problem
+=

Matrix-matrix multiplication
for i=1:N
for j=1:N
for k=1:N
C[i,j] += A[i,k]*B[k,j]
for i=1:NB:N
for j=1:NB:N
for k=1:NB:N
for i0=i:NU:i+NB
for j0=j:NU:j+NB
for k0=k:NU:k+NB
for k00=k0:1:k0+NU
for j00=j0:1:j0+NU
for i00=i0:1:i0+NU
C[i00,j00] +=
A[i00,k00]*B[k00,j00]
Tiled matrix-matrix multiplication
+=

Problem: which transformation order? What parameter values?
Notes: 4

## Slide 5: How to Overcome Compiler Limitations?
Autotuning Write parameterized program and empirically find good parameters
Program generation Automatically generate big basic blocks and special case code
Parameter: tile size, levels
for (i = 0; i < 4; i++)
A[i] = B[i] * C[i];
A[0] = B[0] * C[0];
A[1] = B[1] * C[1];
A[2] = B[2] * C[2];
A[3] = B[3] * C[3];
Parameter: which loop, unroll factor
+=

Notes: 5

## Slide 6: Autotuning: From Simple to “Really Hard”
Level 0: simple C program implements the algorithm cleanly
Level 1: C macros plus search script use C preprocessor for meta-programming
Level 2: scripting for code specialization text-based program generation, e.g., ATLAS
Level 3: add compiler technology internal code representation, e.g., FFTW’s genfft
Level 4: synthesize the program from scratch high level representation, e.g., TCE and Spiral
Notes: Productive code when port to another machine
Search mechanism
Better sol than trying out all
Framwork first
Can do through search
But more smart ones
Arch is not exact
Extract degree of freedom
Interaction of parameters is non-trivial
Can guess, but not scale to new arch..
How to automate search space of auto-tunig
Heavily parameterized framework
Parameter space? stability?
Happy that space is not too different

## Slide 7: Step 1: Basic C Level Optimizations
Level 0: simple C program implements the algorithm cleanly
Level 1: C macros plus search script use C preprocessor for meta-programming
http://www.cs.cmu.edu/afs/cs/academic/class/15213-s12/www/
Notes: 7

## Slide 8: Unrolling & Accumulating: Double *
Case
  Intel Haswell
  Double FP Multiplication
  Latency bound: 5.00. Throughput bound: 0.50
FP * | Unrolling Factor L |  |  |  |  |  |  | 
K | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12
1 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 
2 |  | 2.51 |  | 2.51 |  | 2.51 |  | 
3 |  |  | 1.67 |  |  |  |  | 
4 |  |  |  | 1.25 |  | 1.26 |  | 
6 |  |  |  |  | 0.84 |  |  | 0.88
8 |  |  |  |  |  | 0.63 |  | 
10 |  |  |  |  |  |  | 0.51 | 
12 |  |  |  |  |  |  |  | 0.52
Accumulators
Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 9: Autotuning: From Simple to “Really Hard”
Level 0: simple C program implements the algorithm cleanly
Level 1: C macros plus search script use C preprocessor for meta-programming
Level 2: scripting for code specialization text-based program generation, e.g., ATLAS
Level 3: add compiler technology internal code representation, e.g., FFTW’s genfft
Level 4: synthesize the program from scratch high level representation, e.g., TCE and Spiral
Notes: Productive code when port to another machine
Search mechanism
Better sol than trying out all
Framwork first
Can do through search
But more smart ones
Arch is not exact
Extract degree of freedom
Interaction of parameters is non-trivial
Can guess, but not scale to new arch..
How to automate search space of auto-tunig
Heavily parameterized framework
Parameter space? stability?
Happy that space is not too different

## Slide 10: ATLAS: Code Generation for MMM
Source: Markus Püschel, ETH Zürich: How to Write Fast Numerical Code, 2011 https://www.inf.ethz.ch/personal/markusp/teaching/263-2300-ETH-spring11/course.html
Notes: Productive code when port to another machine
Search mechanism
Better sol than trying out all
Framwork first
Can do through search
But more smart ones
Arch is not exact
Extract degree of freedom
Interaction of parameters is non-trivial
Can guess, but not scale to new arch..
How to automate search space of auto-tunig
Heavily parameterized framework
Parameter space? stability?
Happy that space is not too different

## Slide 11: ATLAS: Architecture
Source: Markus Püschel, ETH Zürich: How to Write Fast Numerical Code, 2011 https://www.inf.ethz.ch/personal/markusp/teaching/263-2300-ETH-spring11/course.html
Notes: Productive code when port to another machine
Search mechanism
Better sol than trying out all
Framwork first
Can do through search
But more smart ones
Arch is not exact
Extract degree of freedom
Interaction of parameters is non-trivial
Can guess, but not scale to new arch..
How to automate search space of auto-tunig
Heavily parameterized framework
Parameter space? stability?
Happy that space is not too different

## Slide 12: Autotuning: From Simple to “Really Hard”
Level 0: simple C program implements the algorithm cleanly
Level 1: C macros plus search script use C preprocessor for meta-programming
Level 2: scripting for code specialization text-based program generation, e.g., ATLAS
Level 3: add compiler technology internal code representation, e.g., FFTW’s genfft
Level 4: synthesize the program from scratch high level representation, e.g., TCE and Spiral
Notes: Productive code when port to another machine
Search mechanism
Better sol than trying out all
Framwork first
Can do through search
But more smart ones
Arch is not exact
Extract degree of freedom
Interaction of parameters is non-trivial
Can guess, but not scale to new arch..
How to automate search space of auto-tunig
Heavily parameterized framework
Parameter space? stability?
Happy that space is not too different

## Slide 13: Example FFT: Recursive FFT Algorithm

## Slide 14: FFTW: Compiler and Autotuner for FFTs
Source: Markus Püschel, ETH Zürich: How to Write Fast Numerical Code, 2011 https://www.inf.ethz.ch/personal/markusp/teaching/263-2300-ETH-spring11/course.html
FFTW
Library infrastructure
2
3
4
5
64
32
6
Codelets
Codelet generator
Recursive functions needed
Vectorization (partially)
Threading
Adaptation mechanism (plan)
(10–20 types)
Notes: Productive code when port to another machine
Search mechanism
Better sol than trying out all
Framwork first
Can do through search
But more smart ones
Arch is not exact
Extract degree of freedom
Interaction of parameters is non-trivial
Can guess, but not scale to new arch..
How to automate search space of auto-tunig
Heavily parameterized framework
Parameter space? stability?
Happy that space is not too different

## Slide 15: FFTW: genfft and the Cooley Tukey FFT
Source: Matteo Frigo: “A Fast Fourier Transform Compiler,” In Proceedings ACM PLDI 1999 http://www.fftw.org/pldi99-slides.ps.gz
Notes: Productive code when port to another machine
Search mechanism
Better sol than trying out all
Framwork first
Can do through search
But more smart ones
Arch is not exact
Extract degree of freedom
Interaction of parameters is non-trivial
Can guess, but not scale to new arch..
How to automate search space of auto-tunig
Heavily parameterized framework
Parameter space? stability?
Happy that space is not too different

## Slide 16: FFTW: genfft at Work
Source: Matteo Frigo: “A Fast Fourier Transform Compiler,” In Proceedings ACM PLDI 1999 http://www.fftw.org/pldi99.pdf
2-point FFT
Algebraic Simplification
Notes: Productive code when port to another machine
Search mechanism
Better sol than trying out all
Framwork first
Can do through search
But more smart ones
Arch is not exact
Extract degree of freedom
Interaction of parameters is non-trivial
Can guess, but not scale to new arch..
How to automate search space of auto-tunig
Heavily parameterized framework
Parameter space? stability?
Happy that space is not too different

## Slide 17: Autotuning: From Simple to “Really Hard”
Level 0: simple C program implements the algorithm cleanly
Level 1: C macros plus search script use C preprocessor for meta-programming
Level 2: scripting for code specialization text-based program generation, e.g., ATLAS
Level 3: add compiler technology internal code representation, e.g., FFTW’s genfft
Level 4: synthesize the program from scratch high level representation, e.g., TCE and Spiral
Notes: Productive code when port to another machine
Search mechanism
Better sol than trying out all
Framwork first
Can do through search
But more smart ones
Arch is not exact
Extract degree of freedom
Interaction of parameters is non-trivial
Can guess, but not scale to new arch..
How to automate search space of auto-tunig
Heavily parameterized framework
Parameter space? stability?
Happy that space is not too different

## Slide 18: Spiral’s Domain-Specific Program Synthesis
νp
μ
Architectural parameter:
Vector length,
#processors, …
rewriting
defines
Kernel:
problem size,
algorithm choice
pick
search
abstraction
abstraction
Model: common abstraction
= spaces of matching formulas
architecture
space
algorithm
space
optimization

## Slide 19: How Spiral Works
Algorithm Generation
Algorithm Optimization
Implementation
Code Optimization
Compilation
Compiler Optimizations
Problem specification (“DFT 1024” or “DFT”)
algorithm
C code
Fast executable
performance
Search
controls
controls
Spiral
Complete automation of the implementation and optimization task
Basic ideas:
Declarative representation of algorithms
Rewriting systems to generate and optimize algorithms at a high level of abstraction

## Slide 20: Autotuning: From Simple to “Really Hard”
Level 0: simple C program implements the algorithm cleanly
Level 1: C macros plus search script use C preprocessor for meta-programming
Level 2: scripting for code specialization text-based program generation, e.g., ATLAS
Level 3: add compiler technology internal code representation, e.g., FFTW’s genfft
Level 4: synthesize the program from scratch high level representation, e.g., TCE and Spiral
Notes: Productive code when port to another machine
Search mechanism
Better sol than trying out all
Framwork first
Can do through search
But more smart ones
Arch is not exact
Extract degree of freedom
Interaction of parameters is non-trivial
Can guess, but not scale to new arch..
How to automate search space of auto-tunig
Heavily parameterized framework
Parameter space? stability?
Happy that space is not too different

## Slide 21: Outline
Autotuning
ECE software
Andrew software
PSC software
Computing infrastructure

## Slide 22
http://www.ansys.com/

## Slide 23: Cadence
https://www.cadence.com/

## Slide 24
https://www.comsol.com/

## Slide 25
http://www.coventor.com/

## Slide 26
https://www.mentor.com/

## Slide 27: Outline
Autotuning
ECE software
Andrew software
PSC software
Computing infrastructure

## Slide 28: Andrew Software
SPSS
IMSL
Maple
Mathematica
Matlab
SAS
S-PLUS
Wolfram Alpha
R/R Studio
Python
MySQL, MS SQL Server, PostgreSQL
https://www.cmu.edu/computing/software/all/

## Slide 29: Outline
Autotuning
ECE software
Andrew software
PSC software
Computing infrastructure

## Slide 30: PSC Software
Abaqus (finite elements)
Abinit (density functional theory)
Anaconda (data science platform)
ANSYS
BLAST (protein sequence alignment)
Caffe (deep learning)
CFOUR (computational chemistry)
Chainer (neural nets)
Desmond (molecular dynamics)
DReAMM (MCell simulation)
https://www.psc.edu/resources/software

## Slide 31: PSC Software (2)
GAMESS (ab initio quantum chemistry)
Gurobi (optimization system)
Julia (programming language)
Keras (neural networks, on top of Theano and TensorFlow)
LevelDB (key-value store)
LS-DYNA (finite element program)
Mathematica, Matlab, R
MCell (Monte Carlo cell simulation)
MCT (library for creating coupled models)
MUMPS (solver for large linear systems)
SuperLU (solves sparse linear systems)

## Slide 32: PSC Software (3)
NAMD, NWCHEM, LAMMPS, CHARMM, CFOUR, Quantum Espresso, SIESTA,
OpenCV (computer vision)
PETSc (PDE solver)
Python, Spark, TensorFlow, Theano, Torch
PyTorch (deep learning)
Scikit-learn (data mining)
SCOTCH (graph partitioning and clustering)

## Slide 33: Outline
Autotuning
ECE software
Andrew software
PSC software
Computing infrastructure

## Slide 34: Outline
Personal Computing
CMU Andrew Computing
ECE Physical Spaces
ECE Compute Clusters
ECE Data Science Cloud
ECE HTCondor
CIT Partnerships
PSC Bridges
XSEDE Project
Cloud Providers

## Slide 35: Introductions
Dan Fassinger
Executive Manager
ECE IT Services
Jim McKinney
Data Center Manager
ECE IT Services
Hours: M-F 8a-5p
Location:
Hamerschlag Hall A200 suites
Docs and resources: https://userguide.its.cit.cmu.edu/
Email: help@ece.cmu.edu

## Slide 36: Computing Options: Personal Computing
Personal computer (2018)
  Laptop or desktop
  Intel Core i5/i7 w/ HT, 2-4 cores
  8GB to 64GB DDR4
  500GB SSD
  Integrated graphics (Intel HD or Iris)
  1GB LAN / 802.11ac WLAN
Typical programs and problem sets
Personal productivity, internet browser
Development workflow tools
Concept testing and simulation
Notes: Benefits:
Control of environment, agility
Sole use of resources, no contention with other users
Limiting factors
Network I/O – 700Mbps at best with reliability issues
Power – limited battery capacity
Mostly single threaded applications, additional cores are idle
Memory bandwidth
Disk capacity
Conflicting software, resource contention (email, cloud sync, Matlab, Excel)
Data safety (malware, hardware failure)
Collaboration with others is manual and error prone
Software licensing – seats are costly

## Slide 37: Computing Options CMU Andrew Computing
Public Clusters
  Workstation or Desktop
  Most University software installed
Virtual Andrew
  VMWare Horizon Client (VDI)
  Cluster software accessible remotely
Linux Timeshares
  SSH and X-session
  Restarted nightly
Campus Cloud
  SaaS, PaaS w/ fee ($$)
  Guest VM instance with managed environment
Ready to use
Prepared and managed for you
Good for productivity or moving small data
Comparable or worse performance compared to personal laptop
Rental capacity
Personal server w/o physical responsibility
Notes: Variations on a theme – prepared computing, much like prepared food
Can be drive-through, fast, sit-down, but all managed and handled by someone else
Spontaneous changes outside sandbox not possible

## Slide 38: Computing Options: ECE Physical Spaces
Ugrad/grad labs
  HH 1303, 1204, A101, A104 – Equipment stations
Linux cluster/lab
  HH 1305
  Workstation class systems
Capstone Lab
  HH 1307
Teaching space (ex. 18-240 18-100)
GPU SDK, LabView
Console access for graphical Linux simulations (EDA and FEA tools)
All require cardkey access
Notes: EDA – Electronic Design Automation
Examples – Cadence, Synopsys
FEA – Finite Element Analysis
Examples – Comsol, Ansys
Be aware of lab times – long term jobs may interfere with teaching labs

## Slide 39: Computing Options: ECE Compute Clusters
Numbers cluster
  Ece[000:031].ece.local.cmu.edu
  RedHat Enteprise Linux
  Condor access
  Engineering software
  Shared storage
GUI cluster
  Ece-gui-[000-007].ece.cmu.edu
  FastX or X-session for remote graphical access
PowerEdge R430
2 x Intel Xeon E5-2640 v4, 2.4GHz, 8GT/s QPI, 10 cores w/ HT
128GB 2400MT/s RDIMM
iSCSI link to SAN
Housed in Cyert Data Center
Notes: Rules for usage
Be reasonable – this is a shared resource
  Jobs needing multiple systems may need more horsepower
Graphical environment
  running full GUI consumes resources
If you need a full desktop, login to HH 1305 or ECE-GUI machines and submit job to larger compute
If you use VNC, reconnect to session instead of spawning new – avoids consuming many console sessions
If machine is under load from job, talk to ITS about getting more resources instead of making the system unusable

## Slide 40: Computing Options: ECE Data Science Cloud
Large memory and GPU
  Moderate sized simulations and parallel compute jobs
  Customized environment
  Fast storage access
  10GB uplinks
PowerEdge R930
  4 x Intel Xeon E7-8870 v3, 9.6GT/s QPI, 18 cores w/ HT
  3TB 2133 MT/s RDIMM
PowerEdge R730
  2 x Intel Xeon E5-2698 v3, 9.6GT/s QPI, 16 cores w/ HT
  768GB 2133MT/s RDIMM
  2 x Nvidia Tesla K80 GPU (x2)
Notes: Access by request
This class has access
Requires conversation/justification, faculty sponsorship
All machines dedicated/bare metal
Hostnames
  Dsc-[01,02,03].ece.local.cmu.edu
  DSC-01 -> 3TB
  DSC-02 -> GPU
  DSC-03 -> 512GB

## Slide 41: Computing Options: ECE HTCondor
Access via ECE Numbers Cluster
Submitting first Condor job
  Prepare
  Compile
  Submit
  Retrieve
Use with Matlab, Comsol, Cadence, std. engineering simulations
Batch submission system
Job queuing, scheduling
Serial or parallel jobs
Harness compute power of entire clusters
Notes: Increases throughput but not latency – unable to improve huge long-running jobs
Better at repeated simulations with varying parameters
Highlights
  Monitors job
  Add fault tolerance – recover from failures
  Flocking sends job to available resources if specified cluster is constrained
Researchers can have priority over other jobs
  Job can be pre-empted by a higher priority job
  Console processes have highest priority
Striking a balance
  30-45 minute jobs are best
  Short jobs in large quantity – too much overhead
  Long jobs in small quantity – risk eviction and inefficient
Types of jobs
  Write own code
  Submit entire VMs
  Matlab
    Portable across architectures and operating systems
    Can be precompiled to Java – improves performance and avoids licensing issues

## Slide 42: Computing Options: CIT Partnerships
Venkat Viswanathan
  Co-location in PSC Monroeville data center
  12 x HPE Blades
    12 x XL1x0r Gen9 Intel Xeon E5-2683v4, 16 core
      128GB DDR4 RAM
    48 x Nvidia Tesla K80
  Managed by Venkat partnership group

## Slide 43: Computing Options: PSC Bridges
Hosted by Pittsburgh Supercomputing Center in Monroeville
Bridges Architecture
Bridges Virtual Tour
Large Memory Systems (3TB)
Many Nvidia GPUs
Extremely Large Memory Systems (12TB)
Slurm job scheduler

## Slide 44: Computing Options: Xsede Project (PSC)
Xsede resources
  SCSC Comet – 144 GPUs
  Open Science Grid – Condor - 1000 cores avg available
  JetStream – IU and TACC – ½ Petaflop
Notes: XSEDE is a single virtual system that scientists can use to interactively share computing resources, data and expertise. People around the world use these resources and services — things like supercomputers, collections of data and new tools — to improve our planet.

## Slide 45: Computing Options: Cloud Providers
Amazon AWS
  https://aws.amazon.com/grants/
  https://aws.amazon.com/education/awseducate/
Google Cloud Compute
  https://cloud.google.com/edu/
  https://lp.google-mkto.com/CloudEduGrants_Faculty.html
Microsoft Azure
  https://www.microsoft.com/en-us/research/academic-programs/
  https://azure.microsoft.com/en-us/free/
Notes: https://aws.amazon.com/research-credits/
https://portal.azure.com/
https://azure.microsoft.com/en-us/pricing/details/app-service/
https://blogs.msdn.microsoft.com/education/2013/05/05/is-there-academic-pricing-for-windows-azure-no-but-theres-something-betterfree-azure/