## Slide 1
14-513
18-613

## Slide 2: Synchronization: Advanced 18-213/18-613: Introduction to Computer Systems 24th Lecture, November 26th, 2024

## Slide 3: Review: Semaphores
Semaphore: non-negative global integer synchronization variable
Manipulated by P and V operations:
  P(s): [ while (s == 0) wait(); s--; ]
    Dutch for “Proberen” (test)
  V(s): [ s++; ]
    Dutch for “Verhogen” (increment)
OS kernel guarantees that operations between brackets [ ] are executed indivisibly/atomically
    Only one P or V operation at a time can modify s.
    When while loop in P terminates, only that P can decrement s
Semaphore invariant: s ≥ 0

## Slide 4: Review: Using Semaphores to Protect Shared Resources via Mutual Exclusion
Basic idea:
  Associate a unique semaphore mutex, initially 1, with each shared variable (or related set of shared variables)
  Surround each access to the shared variable(s) with P(mutex) and
  V(mutex) operations
mutex = 1
P(mutex)
cnt++
V(mutex)

## Slide 5: Review: Using Lock for Mutual Exclusion
Basic idea:
  Mutex is special case of semaphore that only has value 0 (locked) or 1 (unlocked)
  Lock(m): [ while (m == 0); m=0; ]
  Unlock(m): [ m=1]
~2x faster than using semaphore for this purpose
  And, more clearly indicates programmer’s intention
mutex = 1
lock(mutex)
cnt++
unlock(mutex)
mutex = 1
P(mutex)
cnt++
V(mutex)
vs.

## Slide 6: Note about Examples
Lecture examples will use semaphores for both counting and mutual exclusion
  Code is much shorter than using pthread_mutex

## Slide 7: Review: Using Semaphores to Coordinate Access to Shared Resources
Basic idea: Thread uses a semaphore operation to notify another thread that some condition has become true
  Use counting semaphores to keep track of resource state.
  Use binary semaphores to notify other threads.
The Producer-Consumer Problem
  Mediating interactions between processes that generate information and that then make use of that information
  Single entry buffer implemented with two binary semaphores
    One to control access by producer(s)
    One to control access by consumer(s)
  N-entry buffer implemented with semaphores + circular buffer
producer
thread
Shared buffer
consumer
thread

## Slide 8: Today
Using semaphores to schedule shared resources CSAPP 12.5.4
  Readers-writers problem
Other concurrency issues CSAPP 12.7
  Races
  Deadlocks
  Thread safety
  Interactions between threads and signal handling

## Slide 9: Readers-Writers Problem
Problem statement:
  Reader threads only read the object
  Writer threads modify the object (read/write access)
  Writers must have exclusive access to the object
  Unlimited number of readers can access the object concurrently
Occurs frequently in real systems, e.g.,
  Online airline reservation system
  Multithreaded caching Web proxy
W1
W3
W2
R1
R3
R2
Read/
Write
Access
Read-only
Access

## Slide 10: Readers/Writers Examples
W1
W3
W2
R1
R3
R2
W1
W3
W2
R1
R3
R2

## Slide 11: Variants of Readers-Writers
First readers-writers problem (favors readers)
  No reader should be kept waiting unless a writer has already been granted permission to use the object.
  A reader that arrives after a waiting writer gets priority over the writer.
Second readers-writers problem (favors writers)
  Once a writer is ready to write, it performs its write as soon as possible
  A reader that arrives after a writer must wait, even if the writer is also waiting.
Starvation (where a thread waits indefinitely) is possible in both cases.

## Slide 12: Solution to First Readers-Writers Problem
int readcnt; /* Initially 0 */
sem_t mutex, w; /* Both initially 1 */
void reader(void)
{
while (1) {
P(&mutex);
readcnt++;
if (readcnt == 1) /* First in */
P(&w);
V(&mutex);
/* Reading happens here */
P(&mutex);
readcnt--;
if (readcnt == 0) /* Last out */
V(&w);
V(&mutex);
}
}
void writer(void)
{
while (1) {
P(&w);
/* Writing here */
V(&w);
}
}
Readers:
Writers:
rw1.c
A reader that arrives
after a waiting writer
gets priority over the writer
Notes: Readers can keep arriving while writers are blocked on their P(&w) with w=0

## Slide 13: Readers/Writers Examples
W1
W3
W2
R1
R3
R2
W1
W3
W2
R1
R3
R2
w = 0
readcnt = 0
W1
W3
W2
R1
R3
R2
w = 1
readcnt = 0
w = 0
readcnt = 2

## Slide 14: Solution to First Readers-Writers Problem
int readcnt; /* Initially 0 */
sem_t mutex, w; /* Both initially 1 */
void reader(void)
{
while (1) {
P(&mutex);
readcnt++;
if (readcnt == 1) /* First in */
P(&w);
V(&mutex);
/* Reading happens here */
P(&mutex);
readcnt--;
if (readcnt == 0) /* Last out */
V(&w);
V(&mutex);
}
}
void writer(void)
{
while (1) {
P(&w);
/* Writing here */
V(&w);
}
}
Readers:
Writers:
rw1.c
Arrivals: R1 R2 W1 R3

## Slide 15: Solution to First Readers-Writers Problem
int readcnt; /* Initially 0 */
sem_t mutex, w; /* Both initially 1 */
void reader(void)
{
while (1) {
P(&mutex);
readcnt++;
if (readcnt == 1) /* First in */
P(&w);
V(&mutex);
/* Reading happens here */
P(&mutex);
readcnt--;
if (readcnt == 0) /* Last out */
V(&w);
V(&mutex);
}
}
void writer(void)
{
while (1) {
P(&w);
/* Writing here */
V(&w);
}
}
Readers:
Writers:
rw1.c
Arrivals: R1 R2 W1 R3
R1
readcnt == 1
w == 0

## Slide 16: Solution to First Readers-Writers Problem
int readcnt; /* Initially 0 */
sem_t mutex, w; /* Both initially 1 */
void reader(void)
{
while (1) {
P(&mutex);
readcnt++;
if (readcnt == 1) /* First in */
P(&w);
V(&mutex);
/* Reading happens here */
P(&mutex);
readcnt--;
if (readcnt == 0) /* Last out */
V(&w);
V(&mutex);
}
}
void writer(void)
{
while (1) {
P(&w);
/* Writing here */
V(&w);
}
}
Readers:
Writers:
rw1.c
Arrivals: R1 R2 W1 R3
R1
readcnt == 2
w == 0
R2

## Slide 17: Solution to First Readers-Writers Problem
int readcnt; /* Initially 0 */
sem_t mutex, w; /* Both initially 1 */
void reader(void)
{
while (1) {
P(&mutex);
readcnt++;
if (readcnt == 1) /* First in */
P(&w);
V(&mutex);
/* Reading happens here */
P(&mutex);
readcnt--;
if (readcnt == 0) /* Last out */
V(&w);
V(&mutex);
}
}
void writer(void)
{
while (1) {
P(&w);
/* Writing here */
V(&w);
}
}
Readers:
Writers:
rw1.c
Arrivals: R1 R2 W1 R3
R1
readcnt == 2
w == 0
R2
W1

## Slide 18: Solution to First Readers-Writers Problem
int readcnt; /* Initially 0 */
sem_t mutex, w; /* Both initially 1 */
void reader(void)
{
while (1) {
P(&mutex);
readcnt++;
if (readcnt == 1) /* First in */
P(&w);
V(&mutex);
/* Reading happens here */
P(&mutex);
readcnt--;
if (readcnt == 0) /* Last out */
V(&w);
V(&mutex);
}
}
void writer(void)
{
while (1) {
P(&w);
/* Writing here */
V(&w);
}
}
Readers:
Writers:
rw1.c
Arrivals: R1 R2 W1 R3
R1
readcnt == 1
w == 0
R2
W1

## Slide 19: Solution to First Readers-Writers Problem
int readcnt; /* Initially 0 */
sem_t mutex, w; /* Both initially 1 */
void reader(void)
{
while (1) {
P(&mutex);
readcnt++;
if (readcnt == 1) /* First in */
P(&w);
V(&mutex);
/* Reading happens here */
P(&mutex);
readcnt--;
if (readcnt == 0) /* Last out */
V(&w);
V(&mutex);
}
}
void writer(void)
{
while (1) {
P(&w);
/* Writing here */
V(&w);
}
}
Readers:
Writers:
rw1.c
Arrivals: R1 R2 W1 R3
R1
readcnt == 2
w == 0
R2
W1
R3

## Slide 20: Solution to First Readers-Writers Problem
int readcnt; /* Initially 0 */
sem_t mutex, w; /* Both initially 1 */
void reader(void)
{
while (1) {
P(&mutex);
readcnt++;
if (readcnt == 1) /* First in */
P(&w);
V(&mutex);
/* Reading happens here */
P(&mutex);
readcnt--;
if (readcnt == 0) /* Last out */
V(&w);
V(&mutex);
}
}
void writer(void)
{
while (1) {
P(&w);
/* Writing here */
V(&w);
}
}
Readers:
Writers:
rw1.c
Arrivals: R1 R2 W1 R3
readcnt == 1
w == 0
R2
W1
R3

## Slide 21: Solution to First Readers-Writers Problem
int readcnt; /* Initially 0 */
sem_t mutex, w; /* Both initially 1 */
void reader(void)
{
while (1) {
P(&mutex);
readcnt++;
if (readcnt == 1) /* First in */
P(&w);
V(&mutex);
/* Reading happens here */
P(&mutex);
readcnt--;
if (readcnt == 0) /* Last out */
V(&w);
V(&mutex);
}
}
void writer(void)
{
while (1) {
P(&w);
/* Writing here */
V(&w);
}
}
Readers:
Writers:
rw1.c
Arrivals: R1 R2 W1 R3
readcnt == 0
w == 1
W1
R3

## Slide 22: Other Versions of Readers-Writers
Shortcoming of first solution
  Continuous stream of readers will block writers indefinitely
Second version
  Once writer comes along, blocks access to later readers
  Series of writes could block all reads
FIFO implementation
  See rwqueue code in code directory
  Service requests in order received
  Threads kept in FIFO
  Each has semaphore that enables its access to critical section

## Slide 23: Solution to Second Readers-Writers Problem
int readcnt, writecnt; // Initially 0
sem_t rmutex, wmutex, r, w; // Initially 1
void reader(void)
{
while (1) {
P(&r);
P(&rmutex);
readcnt++;
if (readcnt == 1) /* First in */
P(&w);
V(&rmutex);
V(&r)
/* Reading happens here */
P(&rmutex);
readcnt--;
if (readcnt == 0) /* Last out */
V(&w);
V(&rmutex);
}
}
A reader that arrives after a writer must wait, even if the writer is also waiting
void writer(void)
{
while (1) {
P(&wmutex);
writecnt++;
if (writecnt == 1)
P(&r);
V(&wmutex);
P(&w);
/* Writing here */
V(&w);
P(&wmutex);
writecnt--;
if (writecnt == 0);
V(&r);
V(&wmutex);
}
}

## Slide 24: Managing Readers/Writers with FIFO
Idea
  Read & Write requests are inserted into FIFO
  Requests handled as remove from FIFO
    Read allowed to proceed if currently idle or processing read
    Write allowed to proceed only when idle
  Requests inform controller when they have completed
Fairness
  Guarantee every request is eventually handled
R
W
R
W
W
R
R
R
W
R
Time
Requests
Allowed
Concurrency

## Slide 25: Readers Writers FIFO Implementation
Full code in rwqueue.{h,c}
/* Queue data structure */
typedef struct {
sem_t mutex; // Mutual exclusion
int reading_count; // Number of active readers
int writing_count; // Number of active writers
// FIFO queue implemented as linked list with tail
rw_token_t *head;
rw_token_t *tail;
} rw_queue_t;
/* Represents individual thread's position in queue */
typedef struct TOK {
bool is_reader;
sem_t enable; // Enables access
struct TOK *next; // Allows chaining as linked list
} rw_token_t;

## Slide 26: Readers Writers FIFO Use
In rwqueue-test.c
/* Get write access to data and write */
void iwriter(int *buf, int v)
{
rw_token_t tok;
rw_queue_request_write(&q, &tok);
/* Critical section */
*buf = v;
/* End of Critical Section */
rw_queue_release(&q);
}
/* Get read access to data and read */
int ireader(int *buf)
{
rw_token_t tok;
rw_queue_request_read(&q, &tok);
/* Critical section */
int v = *buf;
/* End of Critical section */
rw_queue_release(&q);
return v;
}
Enqueue write request.
Blocked until its your turn.
(One writer per turn)
R
W
W
R
R
R
W
R
Enqueue read request.
Blocked until its your turn.
(Multiple readers OK in same turn)

## Slide 27: Library Reader/Writer Lock
Data type pthread_rwlock_t
Operations
  Acquire read lock
  Pthread_rwlock_rdlock(pthread_rw_lock_t *rwlock)
  Acquire write lock
  Pthread_rwlock_wrlock(pthread_rw_lock_t *rwlock)
  Release (either) lock
  Pthread_rwlock_unlock(pthread_rw_lock_t *rwlock)
Observation
  Library must be used correctly!
    Up to programmer to decide what requires read access and what requires write access

## Slide 28: Today
Using semaphores to schedule shared resources
  Readers-writers problem
Other concurrency issues
  Races
  Deadlocks
  Thread safety
  Interactions between threads and signal handling

## Slide 29: Recall: One Worry: Races
A race occurs when correctness of the program depends on one thread reaching point x before another thread reaches point y
/* a threaded program with a race */
int main(int argc, char** argv) {
pthread_t tid[N];
int i;
for (i = 0; i < N; i++)
Pthread_create(&tid[i], NULL, thread, &i);
for (i = 0; i < N; i++)
Pthread_join(tid[i], NULL);
return 0;
}
/* thread routine */
void *thread(void *vargp) {
int myid = *((int *)vargp);
printf("Hello from thread %d\n", myid);
return NULL;
}
race.c

## Slide 30: Race Elimination
Don’t share state
  E.g., use malloc to generate separate copy of argument for each thread
Use synchronization primitives to control access to shared state
  Different shared state can use different primitives

## Slide 31: Today
Using semaphores to schedule shared resources
  Producer-consumer problem
Other concurrency issues
  Races
  Deadlocks
  Thread safety
  Interactions between threads and signal handling

## Slide 32: Another Worry: Deadlock
Def: A process is deadlocked iff it is waiting for a condition that will never be true.
Typical Scenario
  Processes 1 and 2 needs two resources (A and B) to proceed
  Process 1 acquires A, waits for B
  Process 2 acquires B, waits for A
  Both will wait forever!
More fully (and beyond the scope of this course), a deadlock has four requirements
  Mutual exclusion
  Circular waiting
  Hold and wait
  No pre-emption

## Slide 33: Deadlocking With Semaphores
int main(int argc, char** argv)
{
pthread_t tid[2];
Sem_init(&mutex[0], 0, 1); /* mutex[0] = 1 */
Sem_init(&mutex[1], 0, 1); /* mutex[1] = 1 */
Pthread_create(&tid[0], NULL, count, (void*) 0);
Pthread_create(&tid[1], NULL, count, (void*) 1);
Pthread_join(tid[0], NULL);
Pthread_join(tid[1], NULL);
printf("cnt=%d\n", cnt);
return 0;
}
void *count(void *vargp)
{
int i;
int id = (int) vargp;
for (i = 0; i < NITERS; i++) {
P(&mutex[id]); P(&mutex[1-id]);
cnt++;
V(&mutex[id]); V(&mutex[1-id]);
}
return NULL;
}
Tid[0]:
P(s0);
P(s1);
cnt++;
V(s0);
V(s1);
Tid[1]:
P(s1);
P(s0);
cnt++;
V(s1);
V(s0);

## Slide 34: Deadlock Visualized in Progress Graph
Locking introduces the
potential for deadlock:
waiting for a condition that will never be true
Any trajectory that enters
the deadlock region will
eventually reach the
deadlock state, waiting for either s0 or s1 to become nonzero
Other trajectories luck out and skirt the deadlock region
Unfortunate fact: deadlock is often nondeterministic (race)
Thread 0
Thread 1
P(s0)
V(s0)
P(s1)
V(s1)
V(s1)
P(s1)
P(s0)
V(s0)
Forbidden region
for s0
Forbidden region
for s1
Deadlock
state
Deadlock
region
s0=s1=1

## Slide 35: Avoiding Deadlock
int main(int argc, char** argv)
{
pthread_t tid[2];
Sem_init(&mutex[0], 0, 1); /* mutex[0] = 1 */
Sem_init(&mutex[1], 0, 1); /* mutex[1] = 1 */
Pthread_create(&tid[0], NULL, count, (void*) 0);
Pthread_create(&tid[1], NULL, count, (void*) 1);
Pthread_join(tid[0], NULL);
Pthread_join(tid[1], NULL);
printf("cnt=%d\n", cnt);
return 0;
}
void *count(void *vargp)
{
int i;
int id = (int) vargp;
for (i = 0; i < NITERS; i++) {
P(&mutex[0]); P(&mutex[1]);
cnt++;
V(&mutex[id]); V(&mutex[1-id]);
}
return NULL;
}
Acquire shared resources in same order
Tid[0]:
P(s0);
P(s1);
cnt++;
V(s0);
V(s1);
Tid[1]:
P(s0);
P(s1);
cnt++;
V(s1);
V(s0);
Notes: Note: OK to release resources in opposite order

## Slide 36: Avoided Deadlock in Progress Graph
Thread 0
Thread 1
P(s0)
V(s0)
P(s1)
V(s1)
V(s1)
P(s0)
P(s1)
V(s0)
Forbidden region
for s0
Forbidden region
for s1
s0=s1=1
No way for trajectory to get stuck
Processes acquire locks in same order
Order in which locks released is immaterial

## Slide 37: Demonstration
See program deadlock.c
100 threads, each acquiring same two locks
Risky mode
  Even numbered threads request locks in opposite order of odd-numbered ones
Safe mode
  All threads acquire locks in same order

## Slide 38: Livelock Visualized in Progress Graph
Livelock is similar to a deadlock, except the threads change state, but remain in a deadlock trajectory.
Thread 0
Thread 1
Forbidden region
for s0
Forbidden region
for s1
Livelock
state
Livelock
region

## Slide 39: Deadlock, Livelock, Starvation
Deadlock
  One or more threads is waiting on a condition that will never be true
Livelock
  One or more threads is changing state, but will never leave a deadlock / livelock trajectory
Starvation
  One or more threads is temporarily unable to make progress

## Slide 40: Today
Using semaphores to schedule shared resources
  Readers-writers problem
Other concurrency issues
  Races
  Deadlocks
  Thread safety
  Interactions between threads and signal handling

## Slide 41: Crucial concept: Thread Safety
Functions called from a thread must be thread-safe
Def: A function is thread-safe iff it will always produce correct results when called repeatedly from multiple concurrent threads.
Classes of thread-unsafe functions:
  Class 1: Functions that do not protect shared variables
  Class 2: Functions that keep state across multiple invocations
  Class 3: Functions that return a pointer to a static variable
  Class 4: Functions that call thread-unsafe functions

## Slide 42: Thread-Unsafe Functions (Class 1)
Failing to protect shared variables
  Fix: Use P and V semaphore operations (or mutex)
  Example: goodcnt.c
  Issue: Synchronization operations will slow down code

## Slide 43: Thread-Unsafe Functions (Class 2)
Relying on persistent state across multiple function invocations
  Example: Random number generator that relies on static state
static unsigned int next = 1;
/* rand: return pseudo-random integer on 0..32767 */
int rand(void)
{
next = next*1103515245 + 12345;
return (unsigned int)(next/65536) % 32768;
}
/* srand: set seed for rand() */
void srand(unsigned int seed)
{
next = seed;
}

## Slide 44: Thread-Safe Random Number Generator
Pass state as part of argument
  and, thereby, eliminate static state
Consequence: programmer using rand_r must maintain seed
/* rand_r - return pseudo-random integer on 0..32767 */
int rand_r(int *nextp)
{
*nextp = *nextp*1103515245 + 12345;
return (unsigned int)(*nextp/65536) % 32768;
}

## Slide 45: Thread-Unsafe Functions (Class 3)
Returning a pointer to a static variable
Fix 1. Rewrite function so caller passes address of variable to store result
  Requires changes in caller and callee
Fix 2. Lock-and-copy
  Requires simple changes in caller (and none in callee)
  However, caller must free memory.
char *lc_itoa(int x, char *dest)
{
P(&mutex);
strcpy(dest, itoa(x));
V(&mutex);
return dest;
}
/* Convert integer to string */
char *itoa(int x)
{
static char buf[11];
sprintf(buf, "%d", x);
return buf;
}

## Slide 46: Thread-Unsafe Functions (Class 4)
Calling thread-unsafe functions
  Calling one thread-unsafe function makes the entire function that calls it thread-unsafe
  Fix: Modify the function so it calls only thread-safe functions 

## Slide 47: Reentrant Functions
Def: A function is reentrant iff it accesses no shared variables when called by multiple threads.
  Important subset of thread-safe functions
    Require no synchronization operations
    Only way to make a Class 2 function thread-safe is to make it reentrant (e.g., rand_r )
Reentrant
functions
All functions
Thread-unsafe
functions
Thread-safe
functions
Notes: Class 2: Persistent state across invocations

## Slide 48: Thread-Safe Library Functions
All functions in the Standard C Library (at the back of your K&R text) are thread-safe
  Examples: malloc, free, printf, scanf
Most Unix system calls are thread-safe, with a few exceptions:
Thread-unsafe function Class Reentrant version
asctime 3 asctime_r
ctime 3 ctime_r
gethostbyaddr 3 gethostbyaddr_r
gethostbyname 3 gethostbyname_r
inet_ntoa 3 (none)
localtime 3 localtime_r
rand 2 rand_r

## Slide 49: Today
Using semaphores to schedule shared resources
  Readers-writers problem
Other concurrency issues
  Races
  Deadlocks
  Thread safety
  Interactions between threads and signal handling

## Slide 50: Review: Signal Handling
Action
  Signal can occur at any point in program execution
    Unless signal is blocked
  Signal handler runs within same thread
  Must run to completion and then return to regular program execution
Icurr
Inext
Handler
Receive
signal

## Slide 51: Threads / Signals Interactions
Many library functions use lock-and-copy for thread safety
  Because they have hidden state
  malloc
    Free lists
  fprintf, printf, puts
    So that outputs from multiple threads don’t interleave
  sprintf
    Not officially asynch-signal-safe, but seems to be OK
OK for handler that doesn’t use these library functions
Icurr
Inext
Handler
Receive
signal
fprintf.lock()
fprintf.unlock()

## Slide 52: Bad Thread / Signal Interactions
What if:
  Signal received while library function holds lock
  Handler calls same (or related) library function
Deadlock!
  Signal handler cannot proceed until it gets lock
  Main program cannot proceed until handler completes
Key Point
  Threads employ symmetric concurrency
  Signal handling is asymmetric
Icurr
Inext
Handler
Receive
signal
fprintf.lock()
fprintf.unlock()
fprintf.lock()
fprintf.unlock()

## Slide 53: Threads Summary
Threads provide another mechanism for writing concurrent programs
Threads are growing in popularity
  Somewhat cheaper than processes
  Easy to share data between threads
However, the ease of sharing has a cost:
  Easy to introduce subtle synchronization errors
  Tread carefully with threads!
For more info:
  D. Butenhof, “Programming with Posix Threads”, Addison-Wesley, 1997