## Slide 1
14-513
18-613

## Slide 2: The Memory Hierarchy 18-213/18-613: Introduction to Computer Systems 9th Lecture, February 14, 2022

## Slide 3: Announcements
Lab 3 (attacklab) due Thurs 2/16
Homework 4 due Thurs 2/16
Homework 5 released today

## Slide 4: Today
The memory abstraction CSAPP 6.1.1
RAM : main memory building block CSAPP 6.1.1
Locality of reference CSAPP 6.2
The memory hierarchy CSAPP 6.3
Storage technologies and trends CSAPP 6.1.2-6.1.4

## Slide 5: Writing & Reading Memory
Write
  Transfer data from CPU to memory movq %rax, 8(%rsp)
  “Store” operation
Read
  Transfer data from memory to CPU movq 8(%rsp), %rax
  “Load” operation
From 4th lecture

## Slide 6: Traditional Bus Structure Connecting CPU and Memory
A bus is a collection of parallel wires that carry address, data, and control signals.
Buses are typically shared by multiple devices.
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus

## Slide 7: Memory Read Transaction (1)
CPU places address A on the memory bus.
ALU
Register file
Bus interface
A
0
A
x
Main memory
I/O bridge
%rax
Load operation: movq A, %rax
CPU chip

## Slide 8: Memory Read Transaction (2)
Main memory reads A from the memory bus, retrieves word x, and places it on the bus.
ALU
Register file
Bus interface
x
0
A
x
Main memory
%rax
I/O bridge
Load operation: movq A, %rax

## Slide 9: Memory Read Transaction (3)
CPU read word x from the bus and copies it into register %rax.
ALU
Register file
Bus interface
x
Main memory
0
A
%rax
I/O bridge
Load operation: movq A, %rax
x

## Slide 10: Memory Write Transaction (1)
CPU places address A on bus. Main memory reads it and waits for the corresponding data word to arrive.
y
ALU
Register file
Bus interface
A
Main memory
0
A
%rax
I/O bridge
Store operation: movq %rax, A

## Slide 11: Memory Write Transaction (2)
CPU places data word y on the bus.
y
ALU
Register file
Bus interface
y
Main memory
0
A
%rax
I/O bridge
Store operation: movq %rax, A

## Slide 12: Memory Write Transaction (3)
Main memory reads data word y from the bus and stores it at address A.
y
ALU
Register file
Bus interface
y
Main memory
0
A
%rax
I/O bridge
Store operation: movq %rax, A

## Slide 13: Today
The memory abstraction
RAM : main memory building block
Locality of reference
The memory hierarchy
Storage technologies and trends

## Slide 14: Random-Access Memory (RAM)
Key features
  RAM is traditionally packaged as a chip.
    or embedded as part of processor chip
  Basic storage unit is normally a cell (one bit per cell).
  Multiple RAM chips form a memory.
RAM comes in two varieties:
  SRAM (Static RAM)
  DRAM (Dynamic RAM)

## Slide 15: RAM Technologies
DRAM
1 Transistor + 1 capacitor / bit
  Capacitor oriented vertically
Must refresh state periodically
SRAM
6 transistors / bit
Holds state indefinitely (but will still lose data on power loss)

## Slide 16: SRAM vs DRAM Summary
Trends
  SRAM scales with semiconductor technology
    Reaching its limits
  DRAM scaling limited by need for minimum capacitance
    Aspect ratio limits how deep can make capacitor
    Also reaching its limits
Trans. Access Needs Needs
per bit time refresh? EDC? Cost Applications
SRAM 6 or 8 1x No Maybe 100x Cache memories
DRAM 1 10x Yes Yes 1x Main memories,
frame buffers
EDC: Error detection and correction

## Slide 17: Enhanced DRAMs
Operation of DRAM cell has not changed since its invention
  Commercialized by Intel in 1970.
DRAM cores with better interface logic and faster I/O :
  Synchronous DRAM (SDRAM)
    Uses a conventional clock signal instead of asynchronous control
  Double data-rate synchronous DRAM (DDR SDRAM)
    Double edge clocking sends two bits per cycle per pin
    Different types distinguished by size of small prefetch buffer:
      DDR (2 bits), DDR2 (4 bits), DDR3 (8 bits), DDR4 (16 bits)
    By 2010, standard for most server and desktop systems
    Intel Core i7 supports DDR3 and DDR4 SDRAM

## Slide 18: Conventional DRAM Organization
d x w DRAM:
  d⋅ w total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip (toy example)
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
Memory
controller
(to/from CPU)
Notes: ~8kB rowbuffer

## Slide 19: Reading DRAM Supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2.
Step 1(b): Row 2 copied from DRAM array to row buffer.
Cols
Rows
RAS = 2
0
1
2
3
0
1
2
Internal row buffer
16 x 8 DRAM chip
3
addr
data
2
/
8
/
Memory
controller

## Slide 20: Reading DRAM Supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1.
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU.
Step 3: All data written back to row to provide refresh
Cols
Rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
CAS = 1
addr
data
2
/
8
/
Memory
controller
supercell
(2,1)
supercell
(2,1)
To CPU

## Slide 21: Memory Modules
: supercell (i,j)
64 MB
memory module
consisting of
eight 8Mx8 DRAMs
addr (row = i, col = j)
Memory
controller
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit word main memory address A
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit word
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56

## Slide 22: Today
The memory Abstraction
DRAM : main memory building block
Locality of reference
The memory hierarchy
Storage technologies and trends

## Slide 23: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
DRAM
CPU
SSD
Disk
Effective CPU cycle time: accounts for parallelism within CPU (e.g., multiple cores per CPU)

## Slide 24: Locality to the Rescue!
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality.

## Slide 25: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 26: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial or Temporal
Locality?
temporal
spatial
temporal
spatial
Temporal
Spatial

## Slide 27: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
Answer: yes
Stride-1 reference
pattern
Hint: array layout is row-major order
• • •
a
[0]
[0]
a
[0]
[N-1]
• • •
a
[1]
[0]
a
[1]
[N-1]
• • •
a
[M-1]
[0]
a
[M-1]
[N-1]
• • •

## Slide 28: Locality Example
Question: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Answer: no
Stride N reference
pattern
• • •
a
[0]
[0]
a
[0]
[N-1]
• • •
a
[1]
[0]
a
[1]
[N-1]
• • •
a
[M-1]
[0]
a
[M-1]
[N-1]
• • •
Note: If M is very small
then good locality. Why?

## Slide 29: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < N; i++)
for (j = 0; j < N; j++)
for (k = 0; k < M; k++)
sum += a[k][i][j];
return sum;
}
Answer: make j the inner loop
$ time ./loopijk
real 0m2.765s
user 0m2.328s
sys 0m0.422s
$ time ./loopkij
real 0m1.651s
user 0m1.234s
sys 0m0.422s

## Slide 30: Today
The memory abstraction
DRAM : main memory building block
Locality of reference
The memory hierarchy
Storage technologies and trends

## Slide 31: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
They suggest an approach for organizing memory and storage systems known as a memory hierarchy.

## Slide 32: Example Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers.
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache.
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.
Notes: Note: Text in red describes an inclusive memory hierarchy. Latest Intel CPUs have exclusive L2s, i.e. any data item in L2 is NOT in L3.

## Slide 33: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea (Ideal): The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 34: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 35: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 36: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)
Impact of spatial locality on number of misses?

## Slide 37: General Caching Concepts: 3 Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache starts empty and this is the first reference to the block.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.
Conflict miss
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    E.g. Block i at level k+1 must be placed in block (i mod 4) at level k.
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.

## Slide 38: Examples of Caching in the Mem. Hierarchy
Hardware MMU
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB pages
64-byte blocks
64-byte blocks
4-8 byte words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
4
On-Chip L1
Hardware
10
On-Chip L2
NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 39: Quiz Time!
Canvas Quiz: Day 9 – Memory Hierarchy

## Slide 40: Today
The memory abstraction
RAM : main memory building block
Locality of reference
The memory hierarchy
Storage technologies and trends

## Slide 41: Storage Technologies
Magnetic Disks
Store on magnetic medium
Electromechanical access
Nonvolatile (Flash) Memory
Store as persistent charge
Implemented with 3-D structure
  100+ levels of cells
  3 bits data per cell

## Slide 42: What’s Inside A Disk Drive?
Spindle
Arm
Actuator
Platters
Electronics
(including a
processor
and memory!)
SCSI
connector
Image courtesy of Seagate Technology

## Slide 43: Disk Geometry
Disks consist of platters, each with two surfaces.
Each surface consists of concentric rings called tracks.
Each track consists of sectors separated by gaps.
Spindle
Surface
Tracks
Track k
Sectors
Gaps

## Slide 44: Disk Capacity
Capacity: maximum number of bits that can be stored.
  Vendors express capacity in units of gigabytes (GB) or terabytes (TB), where 1 GB = 109 Bytes and 1 TB = 1012 Bytes
Capacity is determined by these technology factors:
  Recording density (bits/in): number of bits that can be squeezed into a 1 inch segment of a track.
  Track density (tracks/in): number of tracks that can be squeezed into a 1 inch radial segment.
  Areal density (bits/in2): product of recording and track density.
Tracks

## Slide 45: Disk Operation (Single-Platter View)
The disk surface
spins at a fixed
rotational rate
By moving radially, the arm can position the read/write head over any track.
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.
spindle
spindle
spindle
spindle
spindle

## Slide 46: Disk Operation (Multi-Platter View)
Arm
Read/write heads
move in unison
from cylinder to cylinder
Spindle

## Slide 47: Disk Access – Service Time Components
After BLUE read
Seek for RED
Rotational latency
After RED read
Data transfer
Seek
Rotational
latency
Data transfer
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 48: Disk Access Time
Average time to access some target sector approximated by:
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time (Tavg seek)
  Time to position heads over cylinder containing target sector.
  Typical Tavg seek is 3—9 ms
Rotational latency (Tavg rotation)
  Time waiting for first bit of target sector to pass under r/w head.
  Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min
  Typical rotational rate = 7,200 RPMs
Transfer time (Tavg transfer)
  Time to read the bits in the target sector.
  Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min
time for one rotation (in minutes)
fraction of a rotation to be read

## Slide 49: Disk Access Time Example
Given:
  Rotational rate = 7,200 RPM
  Average seek time = 9 ms
  Avg # sectors/track = 400
Derived:
  Tavg rotation = 1/2 x (60 secs/7200 RPM) x 1000 ms/sec = 4 ms
  Tavg transfer = 60/7200 x 1/400 x 1000 ms/sec = 0.02 ms
  Taccess = 9 ms + 4 ms + 0.02 ms
Important points:
  Access time dominated by seek time and rotational latency.
  First bit in a sector is the most expensive, the rest are free.
  SRAM access time is about 4 ns/doubleword, DRAM about 60 ns
    Disk is about 40,000 times slower than SRAM,
    2,500 times slower than DRAM.

## Slide 50: I/O Bus
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Expansion slots for
other devices such
as network adapters.

## Slide 51: Reading a Disk Sector (1)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
mouse
keyboard
Monitor
Disk
I/O bus
Bus interface
CPU initiates a disk read by writing a command, logical block number, and destination memory address to a port (address) associated with disk controller.

## Slide 52: Reading a Disk Sector (2)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
Disk controller reads the sector and performs a direct memory access (DMA) transfer into main memory.

## Slide 53: Reading a Disk Sector (3)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
When the DMA transfer completes, the disk controller notifies the CPU with an interrupt (i.e., asserts a special “interrupt” pin on the CPU).

## Slide 54: Nonvolatile Memories
DRAM and SRAM are volatile memories
  Lose information if powered off.
Nonvolatile memories retain value even if powered off
  Read-only memory (ROM): programmed during production
  Electrically eraseable PROM (EEPROM): electronic erase capability
  Flash memory: EEPROMs, with partial (block-level) erase capability
    Wears out after about 100,000 erasings
Uses for Nonvolatile Memories
  Firmware programs stored in a ROM (BIOS, controllers for disks, network cards, graphics accelerators, security subsystems,…)
  Solid state disks (replacing rotating disks)
  Disk caches

## Slide 55: Solid State Disks (SSDs)
Pages: 512B to 4KB, Blocks: 32 to 128 pages
Data read/written in units of pages.
Page can be written only after its block has been erased.
A block wears out after about 100,000 repeated writes.
Flash
translation layer
I/O bus
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and
write logical disk blocks
DRAM
Buffer

## Slide 56: SSD Performance Characteristics
Benchmark of Samsung 940 EVO Plus
Sequential access faster than random access
  Common theme in the memory hierarchy
Random writes are somewhat slower
  Erasing a block takes a long time (~1 ms).
  Modifying a block page requires all other pages to be copied to new block.
  Flash translation layer allows accumulating series of small writes before doing block write.
Sequential read throughput 2,126 MB/s Sequential write tput 1,880 MB/s
Random read throughput 140 MB/s Random write tput 59 MB/s
https://ssd.userbenchmark.com/SpeedTest/711305/Samsung-SSD-970-EVO-Plus-250GB

## Slide 57: SSD Tradeoffs vs Rotating Disks
Advantages
  No moving parts  faster, less power, more rugged
Disadvantages
  Have the potential to wear out
    Mitigated by “wear leveling logic” in flash translation layer
    E.g. Samsung 940 EVO Plus guarantees 600 writes/byte of writes before they wear out
    Controller migrates data to minimize wear level
  In 2022, about 2 times more expensive per byte
    1TB SSD is 8¢/GB. 1TB HDD is 4¢/GB. 12TB HDD is 3¢/GB
Applications
  Smartphones, laptops
  Increasingly common in desktops and servers

## Slide 58: Summary
The speed gap between CPU, memory and mass storage continues to widen.
Well-written programs exhibit a property called locality.
Memory hierarchies based on caching close the gap by exploiting locality.
Flash memory progress outpacing all other memory and storage technologies (DRAM, SRAM, magnetic disk)
  Able to stack cells in three dimensions

## Slide 59: Supplemental slides

## Slide 60: Storage Trends
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/MB 880 100 30 1 0.1 0.06 0.02 44,000
access (ns) 200 100 70 60 50 40 20 10
typical size (MB) 0.256 4 16 64 2,000 8,000 16.000 62,500
DRAM
SRAM
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/GB 100,000 8,000 300 10 5 0.3 0.03 3,333,333
access (ms) 75 28 10 8 5 3 3 25
typical size (GB) 0.01 0.16 1 20 160 1,500 3,000 300,000
Disk
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/MB 2,900 320 256 100 75 60 320 116
access (ns) 150 35 15 3 2 1.5 200 115

## Slide 61: CPU Clock Rates
1985 1990 1995 2003 2005 2010 2015 2015:1985
CPU 80286 80386 Pentium P-4 Core 2 Core i7(n) Core i7(h)
Clock
rate (MHz) 6 20 150 3,300 2,000 2,500 3,000 500
Cycle
time (ns) 166 50 6 0.30 0.50 0.4 0.33 500
Cores 1 1 1 1 2 4 4 4
Effective
cycle 166 50 6 0.30 0.25 0.10 0.08 2,075
time (ns)
Inflection point in computer history
when designers hit the “Power Wall”
(n) Nehalem processor
(h) Haswell processor