## Slide 1
14-513
18-613

## Slide 2: Network Programming: Part I 18-213/18-613: Introduction to Computer Systems 20th Lecture, March 27th, 2025

## Slide 3: Today
Networking Overview
Global IP Internet CSAPP 11.3
Sockets Interface CSAPP 11.4

## Slide 4
This lecture may be boring,
let me check IG for cool reelz!

## Slide 5
Wait, how does the
“Internet”
actually work to
watch reelz?

## Slide 6
How does my app/browser know?
Who is IG?
Where is IG?
How do I get to IG?
Get bytes from IG?
“Stream” from IG?
Not mix up things?
….

## Slide 7: A First Thought Experiment for Design: “Internet is a Series of (Dedicated) Tubes”
Let me pay attention 
Greg/Swarun are more entertaining

## Slide 8: Series of Tubes Doesn’t Work 
Deployment
  Every “App” needs to install “copper” “fiber” end to end to its users
Heterogeneity of Users
  IG needs to worry about “pipe” inside CMU, my home, airport, SBUX, …
Geography/Society/Politics
  What about users in India, China, UK, how do I get pipes?
Scale/Cost
  More users come in? More devices come in?
Efficiency
  I paused to listen to lecture, but pipe is still costing me!
Fault Tolerance
  What if pipe bursts  insta fails
…..

## Slide 9: Great Ideas in Networking: Statistical Multiplexing not Dedicated Tubes
“The Internet”
Is a Shared Resource

## Slide 10: Great Ideas in Networking: Datagrams/Packet-Switched Networks
1
2
3

## Slide 11: Great Ideas in Networking: Federation
Still paying
attention 

## Slide 12: Well, the Internet does actually have tubes at physical level 

## Slide 13: Great Ideas in Networking: Protocols

## Slide 14: Great Ideas in Networking: Layering
Application
Application
Channel
Host to
Host
Hardware

## Slide 15: Physical Layer: Establishes the Channel
Medium? Light? Radio frequency? Electrical signals?
  What color(s) of light? How bright?
  What RF frequencies? How powerful?
  What signals represent what values?
  What shape are the connectors?
  How far can cables run?
  Etc.
We have a functioning physical layer once we can send and receive signals.

## Slide 16: Physical Layer: Bandwidth vs. Latency
Bandwidth = bits/second
  Improved with parallelism or faster clock rate
Latency = Function of signal propagation speed
  Limited by speed of light
  Major paradigm shift would be needed to make traffic to India or China less latent
Latency tends to be limiting at a global scale
  Speed of light over long distances
Bandwidth may be limited at local scale, e.g. data center
  How to divide up and recombine messages to utilize parallelism?
  How to clock faster without losing signal to noise.
Physical

## Slide 17: Link Layer: Manages the Channel
When do we start transmitting? When do we stop?
When do we start receiving? When do we stop?
Who is sending? Who is receiving?
How do we know if it is correct?
What happens if there is contention for, or collision in, a shared channel?
Key contributions: Framing, among others
We have a functioning link layer once we can build a functioning local area network (LAN) of at least two stations.
Data link
Physical

## Slide 18: Network layer: Scaling up
Passing messages among multiple networks
  For scale
  Of different types (wired, wireless, fiber, infrared, etc)
  Managed by different domains, etc.
Globally meaningful addressing: IPv4, IPv6
Ability to choose paths among multiple options
We have a functioning network layer once we can connect multiple networks, identify hosts among them, and messages can find their way across networks from source to destination.
Network
Data link
Physical

## Slide 19: Transport Layer: Meaningful endpoints
Hosts don’t do communication – various aspects of software systems do
  Consider how many different sessions your Web browser has with servers. Now add for your IM sessions, upgrades-in-progress, music streaming, etc.
Endpoints enable the establishment of sessions
  Classic model is <IPaddress:port>:<IPaddress:port>
  Client: Ephemeral port. Host: Well-known port
Character of communication
  Reliable/session-oriented, e.g. TCP
  Unreliable/datagram, e.g. UDP
  Etc.
The transport layer exists once we have the ability to establish communication from end-point to end-point with well-understood properties.
Transport
Network
Data link
Physical

## Slide 20: Application Layer: Purposeful Communication
Defined by the messaging we, as programs, bake into our applications, shaped by our applications
  e.g., client-server interactions, peer-to-peer interactions, etc.
E.g., HTTP: PUT, GET, POST, etc.
E.g., DNS: queries, responses, updates, etc.
MIME, VOIP protocols, etc.
Application protocols exist when applications can communicate
Application
Transport
Network
Data link
Physical
Application
Transport
Network
Data link
Physical
Network
Data link
Physical
Network
Data link
Physical

## Slide 21
When connecting to Instagram, How does my app/browser know?
What is IG?
Who is IG?
Where is IG?
How do I get to IG?
Get bytes from IG?
“Stream” from IG?
Not mix up things?
….

## Slide 22: A Client-Server Transaction
Most network applications are based on the client-server model:
  A server process and one or more client processes
  Server manages some resource
  Server provides service by manipulating resource for clients
  Server activated by request from client (vending machine analogy)
Client
process
Server
process
1. Client sends request
3. Server sends response
4. Client
handles
response
2. Server
handles
request
Resource
Note: clients and servers are processes running on hosts
(can be the same or different hosts)

## Slide 23: What is IG really?
$ sudo tcpdump -nn > insta_pcap
Anything on
The Global Internet
is just an
“IP” address
e.g., 157.240.229.174

## Slide 24: Who is IG = 157.240.229.174?
“IP” addresses
Assignment
And ownership

## Slide 25: Global IP Internet
Based on the TCP/IP protocol family
  IP (Internet Protocol)
    Provides basic naming scheme and unreliable delivery capability of packets (datagrams) from host-to-host
  UDP (Unreliable Datagram Protocol)
    Uses IP to provide unreliable datagram delivery from process-to-process
  TCP (Transmission Control Protocol)
    Uses IP to provide reliable byte streams from process-to-process over connections
Accessed via a mix of Unix file I/O and functions from the sockets interface
Notes: IP: host2host
UDP/TCP: proc2proc

## Slide 26: Hardware and Software Organization of a Client-Server Internet Application
TCP/IP
Client
Network
adapter
Global IP Internet
TCP/IP
Server
Network
adapter
Internet client host
Internet server host
Sockets interface
(system calls)
Hardware interface
(interrupts)
User code
Kernel code
Hardware
and firmware

## Slide 27: A Programmer’s View of the Internet
1. Hosts are mapped to a set of 32-bit IP addresses
  128.2.203.179
  127.0.0.1 (always localhost)
2. The set of IP addresses is mapped to a set of identifiers called Internet domain names
  128.2.217.3 is mapped to www.cs.cmu.edu
3. A process on one Internet host can communicate with a process on another Internet host over a connection

## Slide 28: Aside: IPv4 and IPv6
The original Internet Protocol, with its 32-bit addresses, is known as Internet Protocol Version 4 (IPv4)
1996: Internet Engineering Task Force (IETF) introduced Internet Protocol Version 6 (IPv6) with 128-bit addresses
  Intended as the successor to IPv4
Majority of Internet traffic still carried by IPv4
We will focus on IPv4, but will show you how to write networking code that is protocol-independent.
IPv6 traffic at Google

## Slide 29: (1) IP Addresses
32-bit IP addresses are stored in an IP address struct
  IP addresses are always stored in memory in network byte order (big-endian byte order)
  True in general for any integer transferred in a packet header from one machine to another.
    E.g., the port number used to identify an Internet connection.
/* Internet address structure */
struct in_addr {
uint32_t s_addr; /* network byte order (big-endian) */
};

## Slide 30: Dotted Decimal Notation
By convention, each byte in a 32-bit IP address is represented by its decimal value and separated by a period
    IP address: 0x8002C2F2 = 128.2.194.242
Use getaddrinfo and getnameinfo functions (described later) to convert between IP addresses and dotted decimal format.

## Slide 31: How do I get to some IP (e.g., IG)?
Routing Protocols

## Slide 32: Why don’t I need to know this IP thing?
Domain Name System (DNS)
Names  “IP” addresses

## Slide 33: (2) Internet Domain Names
.net
.edu
.gov
.com
cmu
berkeley
mit
cs
ece
whaleshark
128.2.210.175
ics
unnamed root
pdl
www
128.2.131.66
amazon
www
54.230.48.28
First-level domain names
Second-level domain names
Third-level domain names

## Slide 34: Domain Naming System (DNS)
The Internet maintains a mapping between IP addresses and domain names in a huge worldwide distributed database called DNS
Conceptually, programmers can view the DNS database as a collection of millions of host entries.
  Each host entry defines the mapping between a set of domain names and IP addresses.
  In a mathematical sense, a host entry is an equivalence class of domain names and IP addresses.

## Slide 35: Properties of DNS Mappings
Can explore properties of DNS mappings using nslookup
  (In our examples, the output is edited for brevity)
Each host has a locally defined domain name localhost which always maps to the loopback address 127.0.0.1
Use hostname to determine real domain name of local host:
linux> nslookup localhost
Address: 127.0.0.1
linux> hostname
whaleshark.ics.cs.cmu.edu

## Slide 36: Properties of DNS Mappings (cont)
Simple case: one-to-one mapping between domain name and IP address:
Multiple domain names mapped to the same IP address:
linux> nslookup whaleshark.ics.cs.cmu.edu
Address: 128.2.210.175
linux> nslookup cs.mit.edu
Address: 18.62.1.6
linux> nslookup eecs.mit.edu
Address: 18.62.1.6

## Slide 37: (3) Internet Connections
Clients and servers communicate by sending streams of bytes over connections. Each connection is:
  Point-to-point: connects a pair of processes.
  Full-duplex: data can flow in both directions at the same time,
  Reliable: stream of bytes sent by the source is eventually received by the destination in the same order it was sent.
A socket is an endpoint of a connection
  Socket address is an IPaddress:port pair
A port is a 16-bit integer that identifies a process:
  Ephemeral port: Assigned automatically by client kernel when client makes a connection request.
  Well-known port: Associated with some service provided by a server (e.g., port 80 is associated with Web servers)

## Slide 38: Well-known Service Names and Ports
Popular services have permanently assigned well-known ports and corresponding well-known service names:
  echo servers: echo 7
  ftp servers: ftp 21
  ssh servers: ssh 22
  email servers: smtp 25
  Web servers: http 80
Mappings between well-known ports and service names is contained in the file /etc/services on each Linux machine.

## Slide 39: Anatomy of a Connection
A connection is uniquely identified by the socket addresses of its endpoints (socket pair)
  (cliaddr:cliport, servaddr:servport)
Connection socket pair
(128.2.194.242:51213, 208.216.181.15:80)
Server
(port 80)
Client
Client socket address
128.2.194.242:51213
Server socket address
208.216.181.15:80
Client host address
128.2.194.242
Server host address
208.216.181.15
51213 is an ephemeral port
allocated by the kernel
80 is a well-known port
associated with Web servers

## Slide 40: Using Ports to Identify Services
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
Web server
(port 80)
Echo server
(port 7)
Service request for
128.2.194.242:7
(i.e., the echo server)
Kernel
Kernel
Client
Client

## Slide 41: Today
Network Layers: Bird’s Eye View
Global IP Internet
Sockets Interface

## Slide 42: Sockets Interface
Set of system-level functions used in conjunction with Unix I/O to build network applications.
Created in the early 80’s as part of the original Berkeley distribution of Unix that contained an early version of the Internet protocols.
Available on all modern systems
  Unix variants, Windows, OS X, IOS, Android, ARM

## Slide 43: Sockets
Client
Server
What is a socket?
  To the kernel, a socket is an endpoint of communication
  To an application, a socket is a file descriptor that lets the application read/write from/to the network
    Remember: All Unix I/O devices, including networks, are modeled as files
Clients and servers communicate with each other by reading from and writing to socket descriptors
The main distinction between regular file I/O and socket I/O is how the application “opens” the socket descriptors
clientfd
serverfd

## Slide 44: Socket Programming Example
Echo server and client
Server
  Accepts connection request
  Repeats back lines as they are typed
Client
  Requests connection to server
  Repeatedly:
    Read line from terminal
    Send to server
    Read reply from server
    Print line to terminal

## Slide 45: Echo Server/Client Session Example
whaleshark: ./echoserveri 6616
Connected to (BAMBOOSHARK.ICS.CS.CMU.EDU, 33707) (A)
server received 26 bytes (B)
server received 17 bytes (C)
Connected to (BAMBOOSHARK.ICS.CS.CMU.EDU, 33708) (D)
server received 29 bytes (E)
bambooshark: ./echoclient whaleshark.ics.cs.cmu.edu 6616 (A)
This line is being echoed (B)
This line is being echoed
This one is, too (C)
This one is, too
^D
bambooshark: ./echoclient whaleshark.ics.cs.cmu.edu 6616 (D)
This one is a new connection (E)
This one is a new connection
^D
Client
Server

## Slide 46: Echo Server + Client Structure
5. Drop client
4. Disconnect client
3. Exchange
data
2. Start client
1. Start server
Client / Server
Session
Client
Server
socket read
socket write
socket read
terminal write
terminal read
socket write
Connection
request
socket read
close
close
EOF
accept
open_listenfd
open_clientfd
Await connection
request from client

## Slide 47: Echo Server + Client Structure
5. Drop client
4. Disconnect client
3. Exchange
data
2. Start client
1. Start server
Client / Server
Session
Client
Server
rio_readlineb
rio_writen
rio_readlineb
fputs
fgets
rio_writen
Connection
request
rio_readlineb
close
close
EOF
Await connection
request from client
accept
open_listenfd
open_clientfd

## Slide 48: Recall: Unbuffered RIO Input/Output
Same interface as Unix read and write
Especially useful for transferring data on network sockets
  rio_readn returns short count only if it encounters EOF
    Only use it when you know how many bytes to read
  rio_writen never returns a short count
  Calls to rio_readn and rio_writen can be interleaved arbitrarily on the same descriptor
#include "csapp.h"
ssize_t rio_readn(int fd, void *usrbuf, size_t n);
ssize_t rio_writen(int fd, void *usrbuf, size_t n);
Return: num. bytes transferred if OK, 0 on EOF (rio_readn only), -1 on error

## Slide 49: Recall: Buffered RIO Input Functions
Efficiently read text lines and binary data from a file partially cached in an internal memory buffer
  rio_readlineb reads a text line of up to maxlen bytes from file fd and stores the line in usrbuf
    Especially useful for reading text lines from network sockets
  Stopping conditions
    maxlen bytes read
    EOF encountered
    Newline (‘\n’) encountered
#include "csapp.h"
void rio_readinitb(rio_t *rp, int fd);
ssize_t rio_readlineb(rio_t *rp, void *usrbuf, size_t maxlen);
ssize_t rio_readnb(rio_t *rp, void *usrbuf, size_t n);
Return: num. bytes read if OK, 0 on EOF, -1 on error

## Slide 50: Echo Server: echo function
void echo(int connfd)
{
size_t n;
char buf[MAXLINE];
rio_t rio;
Rio_readinitb(&rio, connfd);
while((n = Rio_readlineb(&rio, buf, MAXLINE)) != 0) {
printf("server received %d bytes\n", (int)n);
Rio_writen(connfd, buf, n);
}
}
The server uses RIO to read and echo text lines until EOF (end-of-file) condition is encountered.
  EOF condition caused by client calling close(clientfd)
echo.c

## Slide 51: Echo Client: Main Routine
#include "csapp.h"
int main(int argc, char **argv)
{
int clientfd;
char *host, *port, buf[MAXLINE];
rio_t rio;
host = argv[1];
port = argv[2];
clientfd = Open_clientfd(host, port);
Rio_readinitb(&rio, clientfd);
while (Fgets(buf, MAXLINE, stdin) != NULL) {
Rio_writen(clientfd, buf, strlen(buf));
Rio_readlineb(&rio, buf, MAXLINE);
Fputs(buf, stdout);
}
Close(clientfd);
exit(0);
}
echoclient.c

## Slide 52: Echo Server + Client Structure
5. Drop client
4. Disconnect client
3. Exchange
data
2. Start client
1. Start server
Client / Server
Session
Client
Server
rio_readlineb
rio_writen
rio_readlineb
fputs
fgets
rio_writen
Connection
request
rio_readlineb
close
close
EOF
Await connection
request from client
accept
open_listenfd
open_clientfd

## Slide 53: Iterative Echo Server: Main Routine
#include "csapp.h”
void echo(int connfd);
int main(int argc, char **argv)
{
int listenfd, connfd;
socklen_t clientlen;
struct sockaddr_storage clientaddr; /* Enough room for any addr */
char client_hostname[MAXLINE], client_port[MAXLINE];
listenfd = Open_listenfd(argv[1]);
while (1) {
clientlen = sizeof(struct sockaddr_storage); /* Important! */
connfd = Accept(listenfd, (SA *)&clientaddr, &clientlen);
Getnameinfo((SA *) &clientaddr, clientlen,
client_hostname, MAXLINE, client_port, MAXLINE, 0);
printf("Connected to (%s, %s)\n", client_hostname, client_port);
echo(connfd);
Close(connfd);
}
exit(0);
}
echoserveri.c

## Slide 54: Socket Address Structures
Generic socket address:
  For address arguments to connect, bind, and accept (next lecture)
  Necessary only because C did not have generic (void *) pointers when the sockets interface was designed
  For casting convenience, we adopt the Stevens convention:
  typedef struct sockaddr SA;
struct sockaddr {
uint16_t sa_family; /* Protocol family */
char sa_data[14]; /* Address data */
};
sa_family
Family Specific
Notes: Sa_family = AF_INET
Address data is address

## Slide 55: Socket Address Structures
Internet (IPv4) specific socket address:
  Must cast (struct sockaddr_in *) to (struct sockaddr *) for functions that take socket address arguments.
0
0
0
0
0
0
0
0
sa_family
Family Specific
struct sockaddr_in {
uint16_t sin_family; /* Protocol family (always AF_INET) */
uint16_t sin_port; /* Port num in network byte order */
struct in_addr sin_addr; /* IP addr in network byte order */
unsigned char sin_zero[8]; /* Pad to sizeof(struct sockaddr) */
};
sin_port
AF_INET
sin_addr
sin_family

## Slide 56: Host and Service Conversion: getaddrinfo
getaddrinfo is the modern way to convert string representations of hostnames, host addresses, ports, and service names to socket address structures.
  Replaces obsolete gethostbyname and getservbyname funcs.
Advantages:
  Reentrant (can be safely used by threaded programs).
  Allows us to write portable protocol-independent code
    Works with both IPv4 and IPv6
Disadvantages
  Somewhat complex
  Fortunately, a small number of usage patterns suffice in most cases.

## Slide 57: Host and Service Conversion: getaddrinfo
Given host and service, getaddrinfo returns result that points to a linked list of addrinfo structs, each of which points to a corresponding socket address struct, and which contains arguments for the sockets interface functions.
Helper functions:
  freeadderinfo frees the entire linked list.
  gai_strerror converts error code to an error message.
int getaddrinfo(const char *host, /* Hostname or address */
const char *service, /* Port or service name */
const struct addrinfo *hints,/* Input parameters */
struct addrinfo **result); /* Output linked list */
void freeaddrinfo(struct addrinfo *result); /* Free linked list */
const char *gai_strerror(int errcode); /* Return error msg */

## Slide 58: Linked List Returned by getaddrinfo
ai_canonname
result
ai_addr
ai_next
addrinfo structs
Socket address structs
NULL
ai_addr
ai_next
NULL
ai_addr
NULL

## Slide 59: addrinfo Struct
Each addrinfo struct returned by getaddrinfo contains arguments that can be passed directly to socket function.
Also points to a socket address struct that can be passed directly to connect and bind functions.
(socket, connect, bind to be discussed next lecture)
struct addrinfo {
int ai_flags; /* Hints argument flags */
int ai_family; /* First arg to socket function */
int ai_socktype; /* Second arg to socket function */
int ai_protocol; /* Third arg to socket function */
char *ai_canonname; /* Canonical host name */
size_t ai_addrlen; /* Size of ai_addr struct */
struct sockaddr *ai_addr; /* Ptr to socket address structure */
struct addrinfo *ai_next; /* Ptr to next item in linked list */
};

## Slide 60: Host and Service Conversion: getnameinfo
getnameinfo is the inverse of getaddrinfo, converting a socket address to the corresponding host and service.
  Replaces obsolete gethostbyaddr and getservbyport funcs.
  Reentrant and protocol independent.
int getnameinfo(const SA *sa, socklen_t salen, /* In: socket addr */
char *host, size_t hostlen, /* Out: host */
char *serv, size_t servlen, /* Out: service */
int flags); /* optional flags */

## Slide 61: Conversion Example
#include "csapp.h"
int main(int argc, char **argv)
{
struct addrinfo *p, *listp, hints;
char buf[MAXLINE];
int rc, flags;
/* Get a list of addrinfo records */
memset(&hints, 0, sizeof(struct addrinfo));
// hints.ai_family = AF_INET; /* IPv4 only */
hints.ai_socktype = SOCK_STREAM; /* Connections only */
if ((rc = getaddrinfo(argv[1], NULL, &hints, &listp)) != 0) {
fprintf(stderr, "getaddrinfo error: %s\n", gai_strerror(rc));
exit(1);
}
hostinfo.c

## Slide 62: Conversion Example (cont)
/* Walk the list and display each IP address */
flags = NI_NUMERICHOST; /* Display address instead of name */
for (p = listp; p; p = p->ai_next) {
Getnameinfo(p->ai_addr, p->ai_addrlen,
buf, MAXLINE, NULL, 0, flags);
printf("%s\n", buf);
}
/* Clean up */
Freeaddrinfo(listp);
exit(0);
}
hostinfo.c

## Slide 63: Running hostinfo
whaleshark> ./hostinfo localhost
127.0.0.1
whaleshark> ./hostinfo whaleshark.ics.cs.cmu.edu
128.2.210.175
whaleshark> ./hostinfo x.com
199.16.156.230
199.16.156.38
199.16.156.102
199.16.156.198
whaleshark> ./hostinfo google.com
172.217.15.110
2607:f8b0:4004:802::200e

## Slide 64: Today
Network Layers
Global IP Internet
Sockets Interface
Next time
Using getaddrinfo for host and service conversion
Writing clients and servers
Writing Web servers!

## Slide 65: Additional slides

## Slide 66: Basic Internet Components
Internet backbone:
  collection of routers (nationwide or worldwide) connected by high-speed point-to-point networks
Internet Exchange Points (IXP):
  router that connects multiple backbones (often referred to as peers)
  Also called Network Access Points (NAP)
Regional networks:
  smaller backbones that cover smaller geographical areas (e.g., cities or states)
Point of presence (POP):
  machine that is connected to the Internet
Internet Service Providers (ISPs):
  provide dial-up or direct access to POPs

## Slide 67: Internet Connection Hierarchy
IXP
IXP
Backbone
Backbone
Backbone
Backbone
IXP
POP
POP
POP
Regional net
POP
POP
POP
POP
POP
Small Business
Big Business
ISP
POP
POP
POP
POP
Pgh employee
Cable
modem
DC employee
POP
T3
T1
ISP (for individuals)
POP
DSL
T1
Colocation
sites
Private
“peering”
agreements
between
two backbone
companies
often bypass
IXP

## Slide 68: IP Address Structure
IP (V4) Address space divided into classes:
Network ID Written in form w.x.y.z/n
  n = number of bits in host address
  E.g., CMU written as 128.2.0.0/16
    Class B address
Unrouted (private) IP addresses:
  10.0.0.0/8 172.16.0.0/12 192.168.0.0/16
Class A
Class B
Class C
Class D
Class E
0 1 2 3 8 16 24 31
0
Net ID
Host ID
Host ID
Host ID
Net ID
Net ID
Multicast address
Reserved for experiments
1
0
1
0
1
1
1
0
1
1
1
1
1

## Slide 69: Evolution of Internet
Original Idea
  Every node on Internet would have unique IP address
    Everyone would be able to talk directly to everyone
  No secrecy or authentication
    Messages visible to routers and hosts on same LAN
    Possible to forge source field in packet header
Shortcomings
  There aren't enough IP addresses available
  Don't want everyone to have access or knowledge of all other hosts
  Security issues mandate secrecy & authentication

## Slide 70: Evolution of Internet: Naming
Dynamic address assignment
  Most hosts don't need to have known address
    Only those functioning as servers
  DHCP (Dynamic Host Configuration Protocol)
    Local ISP assigns address for temporary use
Example:
  Laptop at CMU (wired connection)
    IP address 128.2.213.29 (bryant-tp4.cs.cmu.edu)
    Assigned statically
  Laptop at home
    IP address 192.168.1.5
    Only valid within home network

## Slide 71: Evolution of Internet: Firewalls
Firewalls
  Hides organizations nodes from rest of Internet
  Use local IP addresses within organization
  For external service, provides proxy service
    Client request: src=10.2.2.2, dest=216.99.99.99
    Firewall forwards: src=176.3.3.3, dest=216.99.99.99
    Server responds: src=216.99.99.99, dest=176.3.3.3
    Firewall forwards response: src=216.99.99.99, dest=10.2.2.2
Corporation X
Firewall
Internet
10.2.2.2
1
4
2
3
176.3.3.3
216.99.99.99

## Slide 72: Hardware Organization of a Network Host
main
memory
I/O
bridge
MI
ALU
register file
CPU chip
system bus
memory bus
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
Expansion slots
network
adapter
network

## Slide 73: Computer Networks
A network is a hierarchical system of boxes and wires organized by geographical proximity
  BAN (Body Area Network) spans devices carried / worn on body
  SAN* (System Area Network) spans cluster or machine room
    Switched Ethernet, Quadrics QSW, …
  LAN (Local Area Network) spans a building or campus
    Ethernet is most prominent example
  WAN (Wide Area Network) spans country or world
    Typically high-speed point-to-point phone lines
An internetwork (internet) is an interconnected set of networks
  The Global IP Internet (uppercase “I”) is the most famous example of an internet (lowercase “i”)
Let’s see how an internet is built from the ground up
* Not to be confused with a Storage Area Network

## Slide 74: Lowest Level: Ethernet Segment
Ethernet segment consists of a collection of hosts connected by wires (twisted pairs) to a hub
Spans room or floor in a building
Operation
  Each Ethernet adapter has a unique 48-bit address (MAC address)
    E.g., 00:16:ea:e3:54:e6
  Hosts send bits to any other host in chunks called frames
  Hub slavishly copies each bit from each port to every other port
    Every host sees every bit
  [Note: Hubs are obsolete. Bridges (switches, routers) became cheap enough to replace them]
host
host
host
hub
100 Mb/s
100 Mb/s
port

## Slide 75: Next Level: Bridged Ethernet Segment
Spans building or campus
Bridges cleverly learn which hosts are reachable from which ports and then selectively copy frames from port to port
host
host
host
host
host
hub
hub
bridge
100 Mb/s
100 Mb/s
host
host
hub
100 Mb/s
100 Mb/s
1 Gb/s
host
host
host
bridge
host
host
hub
A
B
C
X
Y

## Slide 76: Conceptual View of LANs
For simplicity, hubs, bridges, and wires are often shown as a collection of hosts attached to a single wire:
host
host
host
...

## Slide 77: Next Level: internets
Multiple incompatible LANs can be physically connected by specialized computers called routers
The connected networks are called an internet (lower case)
host
host
host
...
host
host
host
...
WAN
WAN
LAN 1 and LAN 2 might be completely different, totally incompatible
(e.g., Ethernet, Fibre Channel, 802.11*, T1-links, DSL, …)
router
router
router
LAN 1
LAN 2

## Slide 78: Logical Structure of an internet
Ad hoc interconnection of networks
  No particular topology
  Vastly different router & link capacities
Send packets from source to destination by hopping through networks
  Router forms bridge from one network to another
  Different packets may take different routes
router
router
router
router
router
router
host
host

## Slide 79: The Notion of an internet Protocol
How is it possible to send bits across incompatible LANs and WANs?
Solution: protocol software running on each host and router
  Protocol is a set of rules that governs how hosts and routers should cooperate when they transfer data from network to network.
  Smooths out the differences between the different networks

## Slide 80: What Does an internet Protocol Do?
Provides a naming scheme
  An internet protocol defines a uniform format for host addresses
  Each host (and router) is assigned at least one of these internet addresses that uniquely identifies it
Provides a delivery mechanism
  An internet protocol defines a standard transfer unit (packet)
  Packet consists of header and payload
    Header: contains info such as packet size, source and destination addresses
    Payload: contains data bits sent from source host

## Slide 81: Transferring internet Data Via Encapsulation
LAN2
protocol
software
client
LAN1
adapter
Host A
LAN1
data
(1)
data
PH
FH1
(4)
data
PH
FH2
(6)
data
(8)
data
PH
FH2
(5)
LAN2 frame
protocol
software
LAN1
adapter
LAN2
adapter
Router
data
PH
(3)
FH1
data
PH
FH1
(2)
internet packet
LAN1 frame
(7)
data
PH
FH2
protocol
software
server
LAN2
adapter
Host B
PH: internet packet header
FH: LAN frame header

## Slide 82: Other Issues
We are glossing over a number of important questions:
  What if different networks have different maximum frame sizes? (segmentation)
  How do routers know where to forward frames?
  How are routers informed when the network topology changes?
  What if packets get lost?
These (and other) questions are addressed by the area of systems known as computer networking