## Slide 1: Model Checking for Embedded Systems
Edmund Clarke, CMU
High-Confidence Embedded Systems Workshop, May 1st

## Slide 2: Embedded Software verification projects
Bridging the gap between legacy code and formal specification
Verification of a real-time operating system
Verifying concurrent embedded C programs
Certifying compilation with proof-carrying code

## Slide 3: More Efficient Model Checking Algorithms
Counterexample-Guided Abstraction Refinement for Hybrid Systems
Making Bounded Model Checking complete

## Slide 4: 1. Bridging the Gap between Legacy Code and Formal Specification
Daniel Kroening

## Slide 5: Legacy Software
Software is the most complex part of today's safety critical embedded systems
Most embedded systems are legacy designs
Written in a low level language such as ANSI-C or even assembly language
Existing tools do not address the verification problem
Goal: Verify legacy code with respect to
  a formal specification
  A high level design
  Safety properties
Notes: Most embedded systems are legacy designs, i.e., written in a low level language such as ANSI-C or even assembly language, or at least contain components that are written in this manner. Very often performance requirements enforce the use of these languages. These systems are a bigger problem than the new, high level designs, but the existing tools do not address the verification problem. We present technology that allows the verification of such legacy code with respect to a formal specification.

## Slide 6: Verification of Legacy Code
CPROVER
CBMC
ANSI-C Source
=?
=?
Formal Specification (PVS)
Other Design (State Charts, …)
Bug Hunting for Security & Safety
Functional Verification
Safety problems because of pointers and arrays
Run time guarantees (WCET)
Program bugs (exceptions)
CBMC

## Slide 7: ANSI-C Bounded Model Checking
Problem: Fixpoint computation is too expensive for software
Idea:
  Unwind program into equation
  Check equation using SAT
Advantages:
  Completely automated
  Allows full set of ANSI-C, including full treatment of pointers and dynamic memory
Properties:
  Simple assertions
  Security (Pointers/Arrays)
  Run time guarantees (WECT)

## Slide 8: Current Project
Verify Safety Properties of a part of a train controller provided by GE
  Termination / WCET
  Correctness of pointer constructs
  The code uses two channels for redundancy: Check that they compute the same result
  Arithmetic consistency checks, involving multiplication and division
The code contains x86 assembly language

## Slide 9: Future Work
Interval abstraction for floating point aritmetic
Concurrent ANSI-C programs (SpecC)
Object oriented languages (C++, Java)
Statechart-like specification language

## Slide 10: 2. Verification of a Real-Time Operating Systems
Flavio Lerda

## Slide 11: Real-Time Operating System
Present in many embedded systems
  Handles main functionalities
Correctness is crucial
  Affects the safety of the whole system
Two type of properties
  Timing properties
  Functional properties
Embedded System
Real-Time OS
Application
Software
Hardware

## Slide 12: Timing Properties
Worst Case Execution Time Analysis
  For ANSI-C
  Based on existing low-level analysis
  Uses bounded model checking
C Source
Annotated
C Source
WCET for
Basic blocks
WCET Estimate
CBMC
WCET estimate
is valid or not
Estimation
Algorithm
Updated estimate
Initial estimate
Termination
threshold
Final WCET
estimate

## Slide 13: Functional Properties
Does the system behave as expected?
Apply to different components of the OS
Check behavioral properties
Embedded System
Real-Time OS
Application
Software
Hardware
Scheduler
Memory
Management
Inter-Process
Communication
Interface to
the hardware

## Slide 14: Results
Case study: MicroC/OS
  Real-Time Operating System
  Freely available
  Written in ANSI-C
Prototype tools
  For both type of properties
Preliminary Results
  On small subsystems

## Slide 15: 3. Verifying Embedded Concurrent C programs
Sagar Chaki
Joel Ouaknine
Karen Yorav

## Slide 16: Overview
Based on the counterexample guided abstraction refinement paradigm
  Completely automated
State explosion avoid by abstraction techniques like predicate abstraction
  Predicate minimization
Can handle concurrency
  Two-level abstraction refinement

## Slide 17: Schematic
Abstraction
Theorem
Prover
Verification
Model
Checker
Reachability
Analyzer
Simulation
Checker
Yes
System OK
Counterexample
Valid?
C Program
Model
Yes
Abstraction
Refinement
Abstraction
Guidance
Improved
Abstraction
Guidance
No
No

## Slide 18: Case Study
Metal casting controller
30,000 lines of C
  No recursion or dynamic memory allocation
Verified sequential properties
  10 minutes CPU time, 300 MB memory
Attempting concurrent properties
  About 25 threads
  No dynamic thread creation

## Slide 19: 4. Certifying Compilation with Proof-Carrying Code
Joint work Clarke/Lee
Student: Stephen Magill

## Slide 20
Certifying Compilation
Certifying
Compiler
CPU
Source
code
Proof
Object
code
Proof
Checker
Reasonable in size (0-10%).
Simple,
small (<52KB),
and fast.
Trusted Computing
Base

## Slide 21
Certifying Compilation
Certifying
Compiler
CPU
Source
code
Proof
Object
code
Proof
Checker
Trusted Computing
Base
Type directed.
- Requires sound, decidable type system for the property of interest
+ Automatic

## Slide 22
Adding Model Checking
Certifying
Compiler
CPU
Source
code
Proof
Object
code
Proof
Checker
Trusted Computing
Base
Do model checking here
Generate an explicit proof
+ Properties handled in a uniform manner
+ Still automatic
+ Great opportunities for integration of the two approaches

## Slide 23
Adding Model Checking
Certifying
Compiler
CPU
Source
code
Proof
Object
code
Proof
Checker
Trusted Computing
Base
Do model checking here
Generate an explicit proof
Proof size?

## Slide 24: 5. Counterexample-Guided Abstraction Refinement for Hybrid Systems
Joint project Clarke/Krogh:
Students:
A. Fehnker, Z. Han, J. Ouaknine,
O. Stursberg, M. Theobald

## Slide 25
Hybrid Systems:
  Include continuous and discrete state variables
  Model embedded systems
  Applications: cars, robots, chemical plants,...
Key Challenge:
  Verification of properties of Hybrid System models
Common Approach:
  Employ abstraction to reduce complexity
  Finding a good abstraction is difficult …
Our Approach:
  Automated search for a good abstraction
  Based on Counterexample-Guided Abstraction Refinement

## Slide 26: CEGAR: Abstraction, Validation and Refinement
Verification Problem: Given: initial location + set and bad location
  Verify: bad location can never be reached
STEP1: Build initial abstraction
STEP2: Model check abstraction
no CE  DONE (safe)
STEP3: For each transition in CE:
validate transition
refine abstraction
Case 1: S2 is not reachable
S2
S1
Case 2: Part of S2 not reachable
Concrete Model:
Abstract Model:
Case 3: All of S2 reachable
Case 2,3  next transition
Case 1  GOTO STEP 2
STEP4: DONE (unsafe)

## Slide 27: Summary and Results
Car Steering Example
Common reachability analysis: 185 sec
CEGAR with multiple over-approximations: 69 sec
As before, with considering fragments: 20 sec
following
leading
Adaptive Cruise Control
Common reachability analysis: 728 sec
CEGAR with multiple over-approximations: 495 sec
As before, with considering fragments: 43 sec
Main Ideas of CEGAR for Hybrid Systems
  explore dynamics only in part of the system relevant to the property
  local refinement within a location
  framework for different over-approximation methods
  consider fragments of counterexamples

## Slide 28: 6. Making Bounded Model Checking Complete
Daniel Kroening
Joel Ouaknine
Ofer Strichman

## Slide 29: Bounded Model Checking
A technique for incremental search for logical design errors
Competes with traditional Model Checkers
Often finds errors orders of magnitude faster than traditional model checkers.
Widely adopted by the chip-design industry in the last 3 years.
Applicable to high confidence embedded systems such as embedded controllers and communication protocols.

## Slide 30: The Bounded Model Checking loop
k = 0
yes
k++
k ¸ CT
no
Counterexample
Bug found
No counter
example
Design correct
The Completeness
Threshold
BMC(M,,k)

## Slide 31: How deep should we look for bugs ?
In order to prove systems correct, a pre-computed “completeness threshold” must be known.
The completeness threshold is a number CT such that, if no bug is found of length CT or less, then there is no bug at all
The value of CT depends on the model M and the property
Computing CT for general Linear Temporal Logic formulas has so far been an open problem

## Slide 32: Computing the completeness threshold
Our solution is based on a graph-theoretic analysis of the automaton where
  M is the automaton representing the verified system
  is the (Buchi) automaton representing the negation of the property
The completeness threshold (CT) is a function of the diameter and the Recurrence-diameter of the product automaton