## Slide 1: Synthesis and Verification Formal and Semi-Formal Verification
Task | Students | Advisor | Mentors
684.004 Abstraction in Model Checking | Yuan Lu, Pankaj Chauhan, Anubhav Gupta | Edmund Clarke | Steven German, IBM Rob Gerth, Intel Carl Pixley, Motorola Somnath Viswanath, AMD Xudong Xhao, Richard Raimi
684.005 Combining Model Checking with Theorem Proving | Sergey Berezin | Edmund Clarke | Rob Gerth, Intel Richard Raimi, Motorola Xudong Zhao, Intel
684.007 Model Checking without BDDs | Anubhav Gupta, Pankaj Chauhan | Edmund Clarke | Cindy Eisner, IBM Haifa Carl Pixley, Motorola
New Task Efficient Image Computation Algorithms | Pankaj Chauhan | Edmund Clarke | Jim Kukula, Synopsys
Contract #: TJ-684

## Slide 2: Accomplishments!
Yuan Lu (now at BroadComm Inc.) and Marius Minea (now PostDoc at Berkeley) graduated in the year 2000!

## Slide 3: Automatic Abstraction by Counterexample-guided Refinement
Edmund M. Clarke
Yuan Lu
Pankaj Chauhan
Anubhav Gupta
Joint work with
Orna Grumberg, Somesh Jha, Helmut Veith

## Slide 4: 684.004: Abstraction in Model Checking
Description:
  Counterexample-guided Abstraction Refinement
Goals:
  To provide a new abstraction technique to verify large designs.
July 29, 2026
<number>

## Slide 5: 684.004: Abstraction in Model Checking
Plans and directions for the current year (2000):
  Experiment with other abstraction refinement techniques
  Experiment on benchmark and industrial designs
  Abstraction in the context of bounded model checking Experiment on industrial designs (PCI bus protocol)
July 29, 2026
<number>

## Slide 6: 684.004: Abstraction in Model Checking
Accomplishments for the current year (2000):
  Yuan Lu graduated!
  Automatic abstraction generation
  Release of aSMV tool
  Extensive experimentation with impressive results

## Slide 7: 684.004: Abstraction in Model Checking
Plans and directions for the next year (2001):
  Extending the methodology to include all ACTL countertexamples
  Using SAT for refinement of large state spaces
July 29, 2026
<number>

## Slide 8: 684.004: Abstraction in Model Checking Milestones
Automatic abstraction function generation (31-Dec-2000)
Development of hierarchical verification algorithms (31-Dec-2000)
Extending the methodology to include all ACTL* counterexamples and implementation (31-Dec-2001)
Using SAT based techniques for refinement of large state spaces (31-March-2001)
July 29, 2026
<number>

## Slide 9: 684.004: Abstraction in Model Checking Deliverables
Report on hierarchical model checking without flattening for hierarchical circuit descriptions (Planned 31-Dec-2000)
Report on model checking of hierarchically structured SMV and StateCharts for embedded systems and mixed hardware designs (Planned 31-Dec-2001)
Report/Paper on Extension of methodology for all counterexamples (Planned 31-Dec-2001)
New version of aSMV with this feature (Planned 30-March-2001)
Report/Paper on refinement using large state spaces (Planned 31-June-2001)
New version of aSMV with SAT based refinement (Planned 31-Dec-2002)
July 29, 2026
<number>

## Slide 10: Existential Abstraction
M
Mh
Given an abstraction function h : S  Sh, the concrete states are grouped and mapped into abstract states
h
h
h
M < Mh and
Mh |=   M |= 

## Slide 11: Our Abstraction Methodology (CAV’2000)
Th is not spurious
check spurious
counterexample
Th
stop
Mh |= 
generate
counterexample Th
Mh |= 
model check
Mh
generate initial
abstraction
M and 
refinement
Th
is spurious

## Slide 12: Highlights of Our Methodology
Impressive results, on average, 3.5x time, 17x space improvements!
A large Fujitsu multimedia processor verified
Handles all ACTL* loop/path counterexample
But….
  What about non-loop/non-path counterexamples?
  What if infeasible to check validity of counterexamples?

## Slide 13: General Counterexamples for ACTL*
Not all the counterexamples in ACTL* are linear (path or loop).
  How to refine the abstraction when a counterexample is not linear?
  What are counterexamples?
  How to generate “readable” counterexamples?

## Slide 14: Tree-like Counterexamples
What does the counterexample for
(AG p)  (AF q) look like?
(AG p)  (AF q)
p
EF p
q
q
q
q
EG q
q
q
q
q
p
(EF p)  (EG q)
 (EF p)  (EG q)

## Slide 15: Counterexamples for ACTL
Theorem All ACTL formulas have tree-like counterexamples.
Why tree-like counterexamples ?
  easy to diagnose
  decomposable to simple paths and loops

## Slide 16: Generate Counterexamples for ACTL
We propose an algorithm to generate tree-like counterexamples for ACTL
  Traverse the parse tree of the formula in DFS order
  Generate path or loop counterexamples for each node in the parse tree.
  Glue all the sub-counterexamples for the total
Symbolic!

## Slide 17: Using SAT for Abstraction Refinement
Problem Domain: Hardware circuits with more than 5000 latches!
Path/loop counterexamples only
I : Primary Inputs
R: Visible Variables
A: Invisible Variables
V = R U A
|R| << |V|
C
L
I
R
R’
A
A’

## Slide 18: Spurious Path Counterexample
Th is spurious
failure state
The concrete states mapped to the failure state are partitioned into 3 sets

## Slide 19: Checking the Validity of Counterexample
Describe the abstract counterexample using propositional formula
Feed the formula to SAT checker
  Size of SAT problem is linear in the circuit size
  For a spurious trace, dead end states Si,0 are obtained
  Set of dad states is
    could be empty

## Slide 20: Example of Approximation

## Slide 21: Modified Refinement Methodology
Model Check
Mh|= ?
M, Mh and 
SAT for BadStates
Th
stop
Mh |= 
Th is real
Check Th with SAT
Mh |= 
generate
counterexample Th
SAT for Bad & DeadEnd
refinement
BadStates is
empty

## Slide 22: Heuristics for Refinement
Use GRASP (Sakellah et. al.)/Chaff(Mallik et.al.) for checking validity of counterexample
Modify these procedures to identify important variables
  Most backtracked to variable
  Largest transitive fanout in implication graph(IG)
  Unique Implication Points
  Variables from conflicting clauses
  …..

## Slide 23: Implementation Details
visible boolean x;
…..
Modified NuSMV
Intermediate Block
Modified
GRASP/Chaff
Mh|= 
New vars
Th, M
Th, M, Bad, DeadEnd
Sat?, Auxiliary Info

## Slide 24: Future Work
Generate non-path/non-loop counterexamples
Refinement using those counterexamples
Formalize and evaluate the heuristics for picking up visible variables using GRASP/Chaff
Experiments!

## Slide 25: Model Checking and Theorem Proving: A Unified Framework
Sergey Berezin
Edmund M. Clarke

## Slide 26: 684.005: Combining Model Checking with Theorem Proving
Description:
  An approach to unifying Model Checking and Theorem Proving in a single framework
Goals:
  Design a framework to combine new state-of-the-art model checking and theorem proving techniques efficiently
  Develop a tool that supports this framework

## Slide 27: 684.005: Combining Model Checking with Theorem Proving
Plans and directions for the current year (2000):
  Verify a large hardware example (like PCI bus)
  Study how the combination of model checking and theorem proving improves both techniques
  Continue the development of the implementation

## Slide 28: 684.005: Combining Model Checking with Theorem Proving
Accomplishments for the current year (2000):
  Formulated a framework that unifies model checking and theorem proving in a very general way
  Came up with a new methodology for efficient specialization of theorem proving to particular problem domains
  Implemented a "prover generator" as a new version of SyMP based on the above methodology
  Implemented the necessary components of the proof system for combining model checking and theorem proving as an instance of a prover generated by SyMP
  Verified an example of an IBM cache coherence protocol

## Slide 29: 684.005: Combining Model Checking with Theorem Proving
Plans and directions for the next year (2001):
  Include several powerful reduction rules into the default proof-system of SyMP (like various forms of abstraction, compositional reasoning techniques, etc.)
  Verify a few more examples using these reduction rules
  Implement one or more other proof systems (either completely different or specialized and more automated versions of the default system) in the tool and demonstrate that it works as a prover generator

## Slide 30: 684.005: Combining Model Checking with Theorem Proving Milestones
  Implementation of the tool's core, detailed tool design, preliminary experiments on known hardware examples like Tomasulo's algorithm (30-Sep-1999)
  Experimental alpha release of the tool (31-Dec-1999)
  Extensions to the verification methodology and experiments on larger examples (30-Jun-2000)
  Extensions to the theorem prover and the model checking back-end (30-Jun-2001)

## Slide 31: 684.005: Combining Model Checking with Theorem Proving Deliverables
  Prototype of the tool for combining model checking and theorem proving (Completed: 16-Feb-2000), Related Publication(s):P000258 , P000259
  Release of tool for combining model checking and theorem proving (Completed: 10-Jan-2001), P001813
  Doctoral dissertation on combining model checking and theorem proving for hardware verification (Planned: 30-Aug-2001)
  Report on verification methodology for complex hardware using model checking and theorem proving (Planned: 31-Dec-2001)

## Slide 32: Model Checking and Theorem Proving: A Unified Framework
Sergey Berezin
Computer Science Department
Carnegie Mellon University

## Slide 33: Example: IBM Cache Coherence Protocol
Cache1
Home Node
Cache2
Cachen
...
Shared:
P1
Pn
P2
ExclGranted:
...
Shared
reqExcl
grantExcl
invalidate
invAck
Excl
reqShared
grantShared
Cachen

## Slide 34: Coherence Property
At any point in time,
if any cache is Exclusive
then all the other caches are Invalid:
AG c1,c2: c1 != c2 & c1.state = Exclusive  c2.state = Invalid
Cache1
Home Node
Cache2
Cachen
...
Shared:
P1
Pn
P2
ExclGranted:
...
Shared
Excl
Cachen

## Slide 35: Coding the Model in SyMP
module M[type Index] =
begin
datatype State = Invalid | Shared | Excl
stateVar (cache: Index -> State), (channel: Index -> Message),
(exclGranted: bool), (Shared: Index -> bool)
init(cache) := fn _ => Invalid;
init(exclGranted) := false
choose i:
channel(i) = Invalidate =>
next(cache) := (fn x => if x=i then Invalid else cache x endif)
| !exclGranted & channel(i) = reqExcl =>
next(channel i) := grantExcl
next(exclGranted) := true
[......]
endchoose
theorem coherence =
self |= AG(forall i,j: i!=j & cache(i) = Excl -> cache(j) = Invalid)
end
Module with parameter
State variables
Transition system
Property

## Slide 36: Formal Verification Options
Model Checking | Theorem Proving
M ¦= F (F is true in M) | ¦= F (F must be valid in general)
Model and property are cleanly separated: M ¦= F | Model has to be encoded as a formula: ¦= Enc(M)  Enc(F)
State reduction techniques Can analyze extremely complex behaviors | Model structure lost, hard to apply similar reductions
Both have strong and weak points.
Can we combine best features of the two?

## Slide 37: Combining MC & TP
Add expressiveness to efficient decision procedures
Cancel out drawbacks of both techniques
Perhaps, find something new in the middle ground...

## Slide 38: Modifying Gentzen’s Sequent
Theorem proving uses Gentzen’s Sequent format:
A1, A2,… => B1, B2, …
The model from model checking has to be translated into HOL to fit into this sequent.
But we can add the model to the sequent:
M; A1, A2,… => B1, B2, …
Also, make the logic temporal, not just HOL.

## Slide 39: Adding Model Checking
Model checking becomes just another rule:
ModelCheck(M, , ) = true | MC
M;  =>  | 
Other transformations from model checking are added as rules, e.g. Cone of Influence reduction:
V = COI(M, , ) M¦V;  =>  | Cone
M;  =>  | 

## Slide 40: Other Types of Rules
M;  => , A M’; A => AX A, where M’=(S, , S) | AG Induct
M;  => , AG A | 
Induction on time:

## Slide 41: Verifying Cache Coherence
Property in First-Order CTL:
AG(c1,c2: c1 != c2 & c1.state = Exclusive
 c2.state = Invalid)
How to prove:
  Find an inductive invariant
  Induction on time (the AG Induct rule)
    Skolemize, split choose statement, abstract-split (eliminate skolem constants), compute cone of influence, model check
Verified in our tool SyMP

## Slide 42: New Methodology: Features
Adequate representation for the problem domain
Right level of abstraction
  Rules perform exactly the transformations we have in mind while doing verification
  Specialized rules for temporal logic
  Efficient use of model structure
Model checking and theorem proving at the same prompt
Interactive proof construction
  Full user control with possibility of automation

## Slide 43: Overall Picture
Cache1
Home Node
Cache2
Cachen
...
Shared:
P1
Pn
P2
ExclGranted:
...
Shared
Excl
Cachen
Specification language
 => , A1  A2
R
 => , A1  => , A2
 => true
Axiom
Specialized proof system
=> x. x=2  x>0  x+x=4
=> a=2  a>0  a+a=4
a=2 => a>0  a+a=4
a=2 => a>0
a=2 => a+a=4
R
R
R
Replace
Axiom
a=2 => 2>0
Replace
a=2 => 2+2=4
Axiom
Proof Management
User Interface

## Slide 44: Generalizing Further
What made it possible to integrate Model Checking and Theorem Proving?
  Customized sequent and proof system
  Adequate representation for the problem domain
How about other problem domains? (Security protocols, Software verification, highly specialized hardware, etc.)
  The same guidelines should work (*)
But do I have to code it all from scratch again?
  There is certainly some common core that can be reused
Notes: (*) Provided that the verification process can be formulated as a sequence of explicitly defined transformations, and the intermediate results can be adequately represented as a sequent of a special form. In our experience, this is the case for many problem domains in formal verification.

## Slide 45: Architecture with Shared Core
Cache1
Home Node
Cache2
Cachen
...
Shared:
P1
Pn
P2
ExclGranted:
...
Shared
Excl
Cachen
Specification language-2
 => , A1  A2
R
 => , A1  => , A2
 => true
Axiom
proof system - 2
User Interface
Cache1
Home Node
Cache2
Cachen
...
Shared:
P1
Pn
P2
ExclGranted:
...
Shared
Excl
Cachen
Specification language-1
 => , A1  A2
R
 => , A1  => , A2
 => true
Axiom
proof system - 1
=> x. x=2  x>0  x+x=4
=> a=2  a>0  a+a=4
a=2 => a>0  a+a=4
a=2 => a>0
a=2 => a+a=4
R
R
R
Replace
Axiom
a=2 => 2>0
Replace
a=2 => 2+2=4
Axiom
Proof Management

## Slide 46: SyMP: Symbolic Model Prover
“Theorem prover generator”
  Common proof management core
  Common interactive user interface
  Plug-in proof systems
    well-defined interface to custom proof system modules
    Each proof system defines custom sequent and custom set of rules
Currently implemented proof systems:
  Default: combines MC & TP
  Athena: security protocol verification (in progress)

## Slide 47: Verified Example: IBM Cache Coherence
Coded in Default proof system in SyMP
Verified coherence of the Home Node
  Other lemmas are still in progress
Proof: 139 elementary steps (proof rules)
  about half of them are model check rules

## Slide 48: Conclusion
New methodology for combining model checking and theorem proving
New framework for specializing theorem proving to various problem domains
  In particular, MC + TP is one such problem domain
A tool SyMP that implements the framework
Implementation of MC + TP system in the tool
Many existing methodologies can be expressed in the framework and implemented in SyMP

## Slide 49: Future Work
Finish the default proof system
  Ideally, it should include all basic theorem proving for FO temporal logic and most of known model checking transformations
Implement more proof systems for other problem domains
  Athena is being implemented for security protocols
  Plans for software verification system
  Plans for toy systems: natural deduction, CFG, etc.
Improve proof search techniques

## Slide 50: Using Fourier Analysis for Abstraction-Refinement in Model Checking
Anubhav Gupta
Edmund M. Clarke

## Slide 51: 684.007: Model Checking Without BDDs
Description:
  Symbolic model checking without BDDs using alternative data structures and algorithms.
Goals:
  To develop an alternative method of doing model checking without BDDs.

## Slide 52: 684.007: Model Checking Without BDDs
Plans and directions for the current year (2000):
  Explore the use of SAT procedures and BEDs for fixpoint computations.

## Slide 53: 684.007: Model Checking Without BDDs
Accomplishments for the current year (2000):
  Implemented a full CTL model checker that combines SAT procedures with BEDs for fixpoint computations.
  Proposed a new methodology that uses “learning algorithms” for identifying important variables in hardware circuits.
  Came up with a new approach for counterexample-guided abstraction-refinement that views refinement as the standard “AI classification problem”.

## Slide 54: 684.007: Model Checking Without BDDs
Plans and directions for the next year (2001):
  Implement a tool that identifies important variables in a circuit and uses this information to generate good BDD and SAT-split orderings.
  Formalize a counterexample-guided abstraction-refinement framework based on the Fourier Transform.
  Implement a counterexample-guided abstraction-refinement framework based on the Fourier Transform and other learning algorithms.

## Slide 55: 684.007: Model Checking Without BDDs Milestones
  Verifier that combines fixed point computation for mode checking with a sat-solver (31-Jan-2001).
  Formalize counterexample-guided abstraction-refinement framework based on the Fourier Transform (15-May-2001).
  Implement counterexample-guided abstraction-refinement framework based on the Fourier Transform and other learning algorithms and perform experiments (31-Nov-2001).
  Generates good BDD and SAT splitting-orders based on important variables in the circuit (31-Mar-2002).

## Slide 56: 684.007: Model Checking Without BDDs Deliverables
  Verifier that combines fixed point computation for mode checking with a sat-solver (Completed : 31-Jan-2001), Related Publication(s): P001653, P000728
  Report that formalizes counterexample-guided abstraction-refinement framework based on the Fourier Transform (31-May-2001).
  Tool that implements counterexample-guided abstraction-refinement framework based on the Fourier Transform and other learning algorithms (31-Dec-2001).
  Tool that generates good BDD and SAT splitting-orders based on important variables in the circuit (31-Apr-2002).

## Slide 57
Technical presentation for this task follows in PDF format

## Slide 58: Efficient Image Computation Algorithms
Pankaj Chauhan
Dong Wang
Edmund M. Clarke
Joint work with Somesh Jha, Jim Kukula, Helmut Veith

## Slide 59: Efficient Image Computation Algorithms
Description:
  Various techniques for faster image computation
Goals:
  A collection of algorithms for efficient image computation
  Integration of algorithms in NuSMV model checker and extensive experimental evaluation

## Slide 60: Efficient Image Computation Algorithms
Plans and directions for the current year (2000):
  Compare existing techniques and understand their limitations
  Explore alternate metrics for predicting image computation costs
  Propose, evaluate and tune algorithms that improve these metrics to aid image computation

## Slide 61: Efficient Image Computation Algorithms
Accomplishments for the current year (2000):
  A collection of algorithms based on combinatorial optimization for various metrics
  All these techniques are made available in NuSMV model checker and built an evaluation framework

## Slide 62: Efficient Image Computation Algorithms
Plans and directions for the next year (2001):
  Continue the implementation to include even more techniques
  Evaluate the algorithms on more strength examples
  Explore the use of efficient partitioning schemes for image computation
  Use the techniques for other applications, including efficient abstraction generation

## Slide 63: Efficient Image Computation Algorithms Milestones
  Experimental evaluation of combinatorial optimization based methods (31-Jan-2001)
  Paper on efficient image computation using combinatorial optimization methods (31-June-2001)
  Paper on VarScore algorithm and improved version of Kernighan-Lin based heuristics (31-Sept-2001)
  Improved partitioning method for image compuation (31-Dec-2001)
  Application of techniques to abstraction and non BDD based image computation

## Slide 64: Introduction
Image Computation is the heart of Symbolic Model Checking
Partitioned Transition relations are required for all “real world designs”
Conjunctive and Disjunctive Partitioning are the fundamental partitioning techniques

## Slide 65: The Problem
The goal is to reduce the size of intermediate BDDs
Image Computation depends on:
  Clustering: How the clusters C1, C2,…,Cm are derived from T1, T2,…,Tk?
  Ordering: How the clusters are ordered in the formula for Im(S)
Variants are NP-Complete

## Slide 66: Current State of the Art
Heuristic score based (Ranjan et. al., IWLS’95, Yang’99)
Dependency matrices (Somenzi, Moon et.al. DAC’00, FMCAD’00)
SAT+BDD (Gupta, FMCAD’00)
Procedure:

## Slide 67: Dependency Matrices
Rows correspond to functions T1, T2,…,Tm , columns correspond to variables v1,v2,…,vn
D[i,j]=1 iff vj is in the support of fi, otherwise 0
Average active life-time
 | v1 | v2 | v3 | v’1 | v’2 | v’3
T1 | 1 | 0 | 0 | 1 | 0 | 0
T2 | 1 | 1 | 0 | 0 | 1 | 0
T3 | 1 | 1 | 1 | 0 | 0 | 1
Dependency matrix for 3-bit counter

## Slide 68: Overview of New Techniques
Ordering Algorithms based on sharing graphs
Ordering algorithms based on minimization of 
VarScore Algorithms
Procedure:
Notes: Forward reference to “sharing graphs”—described in the next slide
  Two ordering algorithms are: one based on kernighan lin heuristics and another a hill-climbing algorithm to minimize the metric sum_{(u,v) \in E}w(u,v).|order(v)-order(v)|
Variations of hill climbing and simulated annealing are use to minimize 

## Slide 69: Sharing Graph based Ordering
Construct a “sharing graph” whose vertices correspond to conjuncts
The weight of the edge E(Ti,Tj) is
  High weight  strong interaction
Propose two algorithms to order the vertices of this graph

## Slide 70: Ordering Algorithm KLin
KLinOrder(G(V,E),W)
Split V into L,Li,Ri and R
  Find a good split L,R with Kernighan-Lin Heuristic
  Li and Ri are vertices adjacent to the other half (interface vertices)
Recursively order L-Li,Li,Ri and R-Ri
Order the vertices as L-Li < Li < Ri < R-Ri
G
L
R
Li
Ri
Notes: This ordering algorithm uses graph separators
W is the weight function of weights
Klin algorithm will find a good separator with small cost

## Slide 71: Ordering Algorithm METIS
While partitioning a smaller graph, consider other preplaced vertices as well
Assign node weight 0 to preplaced nodes, while retain edge weights
Partition and order vertices in depth-first fashion
Notes: This ordering algorithm uses graph separators
W is the weight function of weights
Klin algorithm will find a good separator with small cost

## Slide 72: Overview of New Techniques
Ordering Algorithms based on sharing graphs
Ordering algorithms based on minimization of 
VarScore Algorithms
Procedure:
Notes: Forward reference to “sharing graphs”—described in the next slide
  Two ordering algorithms are: one based on kernighan lin heuristics and another a hill-climbing algorithm to minimize the metric sum_{(u,v) \in E}w(u,v).|order(v)-order(v)|
Variations of hill climbing and simulated annealing are use to minimize 

## Slide 73: Ordering by Minimization of 
Average active lifetime  indicates the interaction among various components
  Lower means relatively disjoint support
  We want to minimize 
Rows and columns of dependency matrix are permuted to improve Moon et.al. (FMCAD’00) use an indirect method (PPP)
  Dependency matrix is restricted to the variables that are to be quantified

## Slide 74: Optimization of s
Use combinatorial optmization to reorder conjuncts to get better s (eg. Hill climbing, Simulated Annealing, GA, etc.)
Require careful tuning of many parameters
Provide good performance as long the metric being optimized relates directly to image computation costs

## Slide 75: Simulated Annealing Algorithm
SimAnnealOrder(D)
Compute  for D
for i=1 to NumStarts do
  let ti=t0ri
  for j=1 to NumStarts2 do
    permute two random rows of D to get Di
    if (i < ) then set  = i, D = Di
    else with probability exp(-(i-)/ti) set
     = i, D = Di
endfor
endfor

## Slide 76: Overview of New Techniques
Ordering Algorithms based on sharing graphs
Ordering algorithms based on minimization of 
VarScore Algorithms
Procedure:
Notes: Forward reference to “sharing graphs”—described in the next slide
  Two ordering algorithms are: one based on kernighan lin heuristics and another a hill-climbing algorithm to minimize the metric sum_{(u,v) \in E}w(u,v).|order(v)-order(v)|
Variations of hill climbing and simulated annealing are use to minimize 

## Slide 77: VarScore Algorithms
Image computation equation:
Can be seen as building a parse tree for Im(S)
Variables not appearing other subtrees can be quantified away immediately
Instead of ordering the conjuncts linearly, build a tree so that intermediate BDDs are small

## Slide 78: VarScore Algorithms
We propose two versions of VarScore algorithms
Dynamic version builds the parse tree for each image computation
Static version builds the parse tree once, albeit with some inaccuracies
Clustering is very similar to ordering

## Slide 79: VarScore (Dynamic Version)
Exists
And
AndExists
Conjunct

## Slide 80: VarScore (Static Version)
Dynamic version repeats lots of same operations across image computation
Build a psuedo-tree without S, assuming S contains all variables in support
Size of BDDs are estimated from some function of number of support variables
All subtrees not in the path from S to root can be evaluated in the beginning
  Present state variables can’t be quantified

## Slide 81: Initial Experimental Results
We get about 30-40% average space improvement
Best 2x speedup, average 30-40%
We complete 4 examples which FMCAD’00 couldn’t do
Smaller BDDs yield better running time for larger circuits

## Slide 82: Conclusions
Simulated Annealing performs well on large circuits
Sharing graph based techniques show promise, though not as good as simulated annealing
Spending more time in initial ordering phase speeds up image computation

## Slide 83: Future Work
More experimentation, evaluation
Complete the implementation
Improved algorithms for partitioning
Complete the evaluation of VarScore algorithms
Application of these techniques to other areas(?)

## Slide 84: Questions?

## Slide 85: Partitioned Transition Relations
The transition relation T(V,W,V’) is typically given as a conjunction
Typically, each Ti is a transition relation for one state variable
The set of variables on which Ti depends denoted by Supp(Ti)
V= v1,…,vn : current state variables
V’= v’1,…,v’n : next state variables
W= w1,…,wk : input variables
Q={V U W}

## Slide 86: Image Computation
Monolithic Representation
Infeasible in practice as the BDD for T is too large

## Slide 87: Early Quantification
Result of early quantification:
Gain: Smaller intermediate results

## Slide 88: A Toy Example
A 3-bit counter
Notes: Make a different column of equations to show the support

## Slide 89: Cutpoints for Finer Partitioning
Clustering helps when the circuit is finely partitioned
What if the partition is too coarse (in other words, to large to be represented by a single BDD?
Idea: Introduce cut-points in the circuit of the next state function of a variable [Burch, Singhal ICCAD‘98]
  No need to introduce a latch
  For a conjunct Ti with cut-point c representing a sub-circuit fc, generate two conjuncts Ti[c] and c fc
  Need to quantify away cut-points while computing the image, no need to introduce a latch

## Slide 90: Benchmark Characteristics
Ckt | #FFs | #inputs | log2(#reach)
IU35 | 35 | 163 | 22.49
IU40 | 40 | 159 | 25.85
IU45 | 45 | 183 | 29.82
IU50 | 50 | 615 | 31.57
IU55 | 55 | 625 | 33.94
IU65 | 65 | 632 | 39.32
IU70 | 70 | 635 | 42.07
IU75 | 75 | 322 | 46.59
IU80 | 80 | 350 | 49.8
IU85 | 85 | 362 | 52.14
Ckt | #FFs | #inputs | log2(#reach)
TCAS | 139 | 0 | 106.87
S1269 | 37 | 18 | 30.07
21512 | 57 | 29 | 40.59
S5378 | 179 | 35 | 57.71 (after 8 steps)
S4863 | 104 | 49 | 72.35
S3271 | 116 | 26 | 79.83
S3330 | 132 | 40 | 86.64
Sfeistel | 293 | 69 | 218.77
s1423 | 74 | 17 | 37.41 (after 16 steps)

## Slide 91: Which to use?
For each version of we can either take total lifetime or active lifetime
We ran iu40 with getting different values of various s and found the following correlation coefficients

## Slide 92: Ordering by Minimization of (contd.)
We have shown that this problem is NP-Complete
Idea 1 : Use standard AI heuristics!
  Might be slower, but definitely better then indirect approach, experiments support this hypothesis
  We propose using variations of hill climbing and simulated annealing

## Slide 93: Ordering by Minimization of (contd.)
Metricas defined does not take into account relative sizes of conjuncts
Define a new metric size that weighs each conjunct by the size of it’s BDD