ZOOM(1)             UNIX Programmer's Manual              ZOOM(1)



NAME
     zoom - filtered image scale and translate

SYNOPSIS
          Usage: zoom [options]
          -src %s         source filename
          -dst %s         dest filename
          -s %d%d%d%d     source box (x0 y0 xsize ysize)
          -d %d%d%d%d     dest box
          -sw %d%d%d%d    window (x0 y0 x1 y1)
          -dw %d%d%d%d    dest window
          -map %f%f%f%f   scale and translate: sx sy tx ty (src to dst by default)
          -square         use square mapping (don't stretch pixels)
          -intscale       use integer scale factors
          -filt %s[%s     filter name in x and y (default=triangle)
          -supp %f[%f     filter support radius
          -blur %f[%f     blur factor: >1 is blurry, <1 is sharp
          -window %s[%s   window an IIR filter (default=blackman)
          -mono           monochrome mode (1 channel)
          -dev            print list of known picture devices/file formats
          Where %d denotes integer, %f denotes float, %s denotes string,
          and '[' marks optional following args

DESCRIPTION
     zoom zooms a raster image from one picture file or frame
     buffer to another.  The "zoom" operation, also known as
     "resize", consists of a scale and translation.  The program
     supports arbitrary floating point scale and translation with
     independent control of x and y scales, upsampling (interpo-
     lation) or downsampling (decimation), 1-channel black and
     white or 3-channel color pictures, overlapping source and
     destination windows within the same frame buffer, and separ-
     able filtering with a large choice of filters.  It can also
     be used for in-place separable filtering of images.  The
     algorithm is not limited to integer or rational scale fac-
     tors; it can scale by any floating point number.  The pro-
     gram uses the pic package for all picture I/O, so the zoom
     source code is device-independent, and the program can read
     and write any of the picture file formats and frame buffers
     known by pic.  The program is optimized to be nearly as fast
     as special-purpose code for important special cases such as
     point sampling.  The memory used by the algorithm is modest:
     it is proportional to the picture width times the filter
     width, not proportional to picture area.

     To run zoom, the user specifies the source and destination
     file or frame buffer names, specifies the mapping (zoom
     transformation) and filter.  Most of these options have rea-
     sonable defaults.  The program will read and write the
     full-screen area of the source and destination pictures by
     default; the user can specify subrectangles to read and
     write if desired.  Rectangles can be defined in either of
     two ways: as a "box", which consists of xmin, ymin, xsize,
     ysize, or as a "window", which consists of xmin, ymin, xmax,
     ymax.  By default, the source window is zoomed into the des-
     tination window.  Alternatively, a mapping can be specified
     directly with the -map option.  A mapping can be constrained
     to have equal scale in x and y, or to have integer scale
     factors, using the -square and -intscale options,
     respectively.

     Filters are selected with the -filt option.  If given one
     filter name, -filt will use that filter in both x and y; if
     given two names, different filters can be used in the two
     dimensions.  The command zoom -filt '?' prints the list of
     filters currently known to zoom.  That list is:

          NAME      SUPPORT
          point       0
          box         0.5
          triangle    1
          quadratic   1.5
          cubic       2
          catrom      2
          mitchell    2
          gaussian    1.25
          sinc        4
          bessel      3.24
     The option -filt point gives fast pixel replication, -filt
     triangle (the default) gives bilinear interpolation, which
     is suitable for most purposes, and -filt mitchell gives
     slower, very high quality results.  The other filters are
     provided for experimentation.  The time required by a filter
     is proportional to its support.

     Most of the filters known to zoom are FIR (finite impulse
     response), with an intrinsic support (width), but some of
     them (gaussian, sinc, bessel) are IIR (infinite impulse
     response), and must be truncated at some arbitrary support.
     This can be done with the -supp option.  Again, the defaults
     are reasonable.  The IIR filters can be windowed (brought
     down to zero) with various window functions listed below:

          hanning
          hamming
          blackman
          kaiser
     The sinc and bessel filters are blackman-windowed by
     default.  Filters can be scaled artificially to blur or
     sharpen them with the -blur option.

EXAMPLES
     zoom -src mandrill.dump
         Zoom the mandrill from picture file mandrill.dump into
         the default destination device (whatever that is), map-
         ping the file's rectangle into the device's rectangle,
         with a triangle filter.

     zoom -src mandrill.dump -filt point -square -intscale
         Zoom the mandrill to the default device's full screen,
         but maintain the picture's aspect ratio, and zoom it up
         by an integer factor with point sampling (pixel replica-
         tion)

     zoom -src mandrill.dump -dst iris -d 50 75 100 100
         Zoom the mandrill into an iris window at position
         (50,70) with xsize=ysize=100.

     zoom -src hp -dst hp -s 100 100 640 512 -d 0 0 1280 1024 -filt mitchell
         Zoom from hp to itself with overlapping source and des-
         tination windows, using a mitchell filter.

     zoom -src hp -dst hp -s 0 0 500 500 -d 0 0 500 500 -filt cubic -blur 2
         Blur (low pass filter) an image in-place.

SEE ALSO
     pic(3), Discrete Time Signal Processing, Alan Oppenheim,
     Ronald Schafer, 1989.

AUTHOR
     Paul Heckbert, August 1989.  ph@cs.cmu.edu