## Slide 1: Virtual Memory: Details 15-213/15-513: Introduction to Computer Systems 18th Lecture, July 13, 2022

## Slide 2: Review: Virtual Addressing
Each process has its own virtual address space
Page tables map virtual to physical addresses
Physical memory can be shared among processes
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP k
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation

## Slide 3: Today
Multi-level page tables
Translation lookaside buffers
Activity 1
Concrete examples of virtual memory systems
  “Simple memory system” from CSAPP 9.6.4
  Intel Core i7
Activity 2
Nifty things virtual memory makes possible
  Paging/swapping (disk as extra RAM)
  Memory-mapped files (RAM as cache for disk)
  Copy-on-write sharing
Activity 3

## Slide 4: The problem (with one-level page tables)
byte address space
One 64-bit array element for each 4096-byte page
= bytes = bytes = 512 gigabytes for one page table

## Slide 5: A Two-Level Page Table Hierarchy
Level 1
page table
Level 2
page tables
VP 1024
...
VP 2047
VP 2048
...
VP 3072
PTE 0
...
PTE 1023
PTE 0
...
PTE 1023
1023 null PTEs
PTE 1023
VP 1048576
Virtual
memory
1020 more
null PTEs
PTE 1
PTE 2
PTE 0 (null)
PTE 1023
2048 allocated pages
for code and data
1021 · 1024 + 1023 unallocated pages
1 allocated page
for the stack
VP 0…1023 (unmapped)
VP 3073… 1048575 (unmapped)
1024 unallocated pages
32-bit address space, 4-byte PTEs, 4096-byte pages

## Slide 6: Translating with a k-level Page Table
Page table base register
(PTBR)
VPN 1
0
p-1
n-1
VPO
VPN 2
...
VPN k
PPN
0
p-1
m-1
PPO
PPN
VIRTUAL ADDRESS
PHYSICAL ADDRESS
...
...
the Level 1
page table
a Level 2
page table
a Level k
page table

## Slide 7: The problem (with k-level page tables)
Page table base register
(PTBR)
VPN 1
0
p-1
n-1
VPO
VPN 2
...
VPN k
PPN
PPO
PPN
VIRTUAL ADDRESS
...
...
the Level 1
page table
a Level 2
page table
a Level k
page table
Cache miss!
Cache miss!
Cache miss!
Cache miss!
Cache miss!

## Slide 8: Speeding up Translation with a TLB
Page table entries (PTEs) are cached like any other memory word
  PTEs may be evicted by other data references
  PTE hit still costs cache delay
Solution: Translation Lookaside Buffer (TLB)
  Dedicated cache for page table entries
  TLB hit = page table not consulted
  Can be fairly small: one TLB entry covers 4k or more

## Slide 9: Accessing the TLB
MMU uses the VPN portion of the virtual address to access the TLB:
TLB tag (TLBT)
TLB index (TLBI)
0
p-1
p
n-1
VPO
VPN
p+t-1
p+t
PTE
tag
v
…
PTE
tag
v
Set 0
PTE
tag
v
PTE
tag
v
Set 1
PTE
tag
v
PTE
tag
v
Set T-1
T = 2t sets
TLBI selects the set
TLBT matches tag of line within set

## Slide 10: TLB Hit
MMU
Cache/
Memory
CPU
CPU Chip
VA
1
PA
4
Data
5
A TLB hit eliminates memory accesses to the page table
TLB
2
VPN
PTE
3

## Slide 11: TLB Miss
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
5
6
TLB
VPN
4
PTEA
3
A TLB miss incurs additional memory accesses (PTE lookup) Fortunately, TLB misses are rare. Why?

## Slide 12: Today
Multi-level page tables
Translation lookaside buffers
Activity 1
Concrete examples of virtual memory systems
  “Simple memory system” from CSAPP 9.6.4
  Intel Core i7
Activity 2
Nifty things virtual memory makes possible
  Paging/swapping (disk as extra RAM)
  Memory-mapped files (RAM as cache for disk)
  Copy-on-write sharing
Activity 3

## Slide 13: Simple Memory System Example
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
11
10
9
8
7
6
5
4
3
2
1
0
VPO
PPO
PPN
VPN
Virtual Page Number
Virtual Page Offset
Physical Page Number
Physical Page Offset

## Slide 14: Simple Memory System TLB
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
16 entries
4-way associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
0
0
0
1
1
0
1
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
Translation Lookaside Buffer (TLB)
VPN = 0b1101 = 0x0D

## Slide 15: Simple Memory System Page Table
Only showing the first 16 entries (out of 256)
1
0D
0F
1
11
0E
1
2D
0D
0
–
0C
0
–
0B
1
09
0A
1
17
09
1
13
08
Valid
PPN
VPN
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN
0x0D → 0x2D

## Slide 16: Simple Memory System Cache
16 lines, 4-byte cache line size
Physically addressed
Direct mapped
V[0b00001101101001] = V[0x369]
P[0b101101101001] = P[0xB69] = 0x15
1
11
0
10
1
9
1
8
0
7
1
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx
1
0
1
0
0
1
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx

## Slide 17: Address Translation Example
TLB
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
0
1
0
1
0
1
1
1
1
0
0
0
0
0x0F
0x3
0x03
Y
N
0x0D
Virtual Address: 0x03D4
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
0
0
0
1
0
1
0
1
1
0
1
0
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set

## Slide 18: Intel Core i7 Memory System
L1 d-cache
32 KB, 8-way
L2 unified cache
256 KB, 8-way
L3 unified cache
8 MB, 16-way
(shared by all cores)
Main memory
Registers
L1 d-TLB
64 entries, 4-way
L1 i-TLB
128 entries, 4-way
L2 unified TLB
512 entries, 4-way
L1 i-cache
32 KB, 8-way
MMU
(addr translation)
Instruction
fetch
Core x4
DDR3 Memory controller
3 x 64 bit @ 10.66 GB/s
32 GB/s total (shared by all cores)
Processor package
QuickPath interconnect
4 links @ 25.6 GB/s each
To other
cores
To I/O
bridge

## Slide 19: End-to-end Core i7 Address Translation
CPU
VPN
VPO
36
12
TLBT
TLBI
4
32
...
L1 TLB (16 sets, 4 entries/set)
VPN1
VPN2
9
9
PTE
CR3
PPN
PPO
40
12
Page tables
TLB
miss
TLB
hit
Physical
address
(PA)
Result
32/64
...
CT
CO
40
6
CI
6
L2, L3, and
main memory
L1 d-cache
(64 sets, 8 lines/set)
L1
hit
L1
miss
Virtual address (VA)
VPN3
VPN4
9
9
PTE
PTE
PTE

## Slide 20: Core i7 Level 1-3 Page Table Entries
Page table physical base address
Unused
G
PS
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page table. Significant fields:
P: Child page table present in physical memory (1) or not (0).
R/W: Read-only or read-write access access permission for all reachable pages.
U/S: user or supervisor (kernel) mode access permission for all reachable pages.
WT: Write-through or write-back cache policy for the child page table.
A: Reference bit (set by MMU on reads and writes, cleared by software).
PS: Page size either 4 KB or 4 MB (defined for Level 1 PTEs only).
Page table physical base address: 40 most significant bits of physical page table address (forces page tables to be 4KB aligned)
XD: Disable or enable instruction fetches from all pages reachable from this PTE.
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page table location on disk)
P=0
52
62
63
Notes: Reference bit – used in LRU

## Slide 21: Core i7 Level 4 Page Table Entries
Page physical base address
Unused
G
D
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page. Significant fields:
P: Child page is present in memory (1) or not (0)
R/W: Read-only or read-write access permission for child page
U/S: User or supervisor mode access
WT: Write-through or write-back cache policy for this page
A: Reference bit (set by MMU on reads and writes, cleared by software)
D: Dirty bit (set by MMU on writes, cleared by software)
G: Global page (don’t evict from TLB on task switch)
Page physical base address: 40 most significant bits of physical page address (forces pages to be 4KB aligned)
XD: Disable or enable instruction fetches from this page.
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page location on disk)
P=0
52
62
63

## Slide 22: Core i7 Page Table Translation
CR3
Physical
address
of page
Physical
address
of L1 PT
9
VPO
9
12
Virtual
address
L4 PT
Page
table
L4 PTE
PPN
PPO
40
12
Physical
address
Offset into
physical and
virtual page
VPN 3
VPN 4
VPN 2
VPN 1
L3 PT
Page middle
directory
L3 PTE
L2 PT
Page upper
directory
L2 PTE
L1 PT
Page global
directory
L1 PTE
9
9
40
/
40
/
40
/
40
/
40
/
12
/
512 GB
region
per entry
1 GB
region
per entry
2 MB
region
per entry
4 KB
region
per entry

## Slide 23: Cute Trick for Speeding Up L1 Access
Observation
  Bits that determine CI identical in virtual and physical address
  Can index into cache while address translation taking place
  Generally we hit in TLB, so PPN bits (CT bits) available quickly
  “Virtually indexed, physically tagged”
  Cache carefully sized to make this possible
Physical
address
(PA)
CT
CO
40
6
CI
6
Virtual
address
(VA)
VPN
VPO
36
12
PPO
PPN
Address
Translation
No
Change
CI
L1 Cache
CT
Tag Check

## Slide 24: Today
Multi-level page tables
Translation lookaside buffers
Activity 1
Concrete examples of virtual memory systems
  “Simple memory system” from CSAPP 9.6.4
  Intel Core i7
Activity 2
Nifty things virtual memory makes possible
  Paging/swapping (disk as extra RAM)
  Memory-mapped files (RAM as cache for disk)
  Copy-on-write sharing
Activity 3

## Slide 25: Paging (aka Swapping)
Use (part of) disk as additional working memory
Adds another layer to the memory hierarchy, but…
  “Main memory” is 10–1000x slower than the caches
  Disk is 10,000x slower than main memory
  Enormous miss penalty drives design
Consequences
  Large page (block) size: 4KB and bigger
  Always write-back and fully associative
  Managed entirely in software
    Plenty of time to execute complex replacement algorithms

## Slide 26: Locality to the Rescue Again!
Paging is terribly inefficient
Only works because of locality
At any point in time, programs tend to access a set of active virtual pages called the working set
  Programs with good temporal locality will have small working sets
If working set size < main memory size
  Good performance after compulsory misses
If working set size > main memory size
  Thrashing: Performance meltdown, computer spends most of its time copying pages in and out of RAM
  In the worst case, no forward progress at all (livelock)

## Slide 27: Memory-Mapped Files
Paging = every page of a program’s physical RAM is backed by some page of disk*
Normally, those pages belong to swap space
But what if some pages were backed by … files?
* This is how it used to work 20 years ago. Nowadays, not always true.

## Slide 28: Memory-Mapped Files
Swap space
Physical
memory
Process
virtual memory
File on disk

## Slide 29: Memory-Mapped Files
Swap space
Physical
memory
Process 1
virtual memory
File on disk
Process 2
virtual memory

## Slide 30: Copy-on-write sharing
fork creates a new process by copying the entire address space of the parent process
  That sounds slow
  It is slow
Swap space
Physical
memory
Parent
virtual memory
File on disk
Clever trick:
  Just duplicate the page tables
  Mark everything read only
  Copy only on write faults

## Slide 31: Copy-on-write sharing
Swap space
Physical
memory
Parent
virtual memory
File on disk
Child
virtual memory
Clever trick:
  Just duplicate the page tables
  Mark everything read only
  Copy only on write faults

## Slide 32: Copy-on-write sharing
Clever trick:
  Just duplicate the page tables
  Mark everything read only
  Copy only on write faults
Swap space
Physical
memory
Parent
virtual memory
File on disk
Child
virtual memory
Child wrote to this page

## Slide 33: Today
Multi-level page tables
Translation lookaside buffers
Activity 1
Concrete examples of virtual memory systems
  “Simple memory system” from CSAPP 9.6.4
  Intel Core i7
Activity 2
Nifty things virtual memory makes possible
  Paging/swapping (disk as extra RAM)
  Memory-mapped files (RAM as cache for disk)
  Copy-on-write sharing
Activity 3