## Slide 1: Exploring Congestion Control
Aditya Akella
With Srini Seshan, Scott Shenker and Ion Stoica

## Slide 2: Early Congestion Control
Influences on early congestion control design
  Chiu-Jain analysis
    AIMD most fair, stable and efficient
  Loss recovery mechanism
    Reno-style
    Large penalty on over-shooting
  Simple FIFO drop-tail routers

## Slide 3: Motivation for Our Study
Improvements
  TCP loss recovery
    SACK
  Drop and scheduling policies at routers
    AQM
    ECN
  Flow-level fairness
    DRR

## Slide 4: Questions..
Is AIMD still the only choice?
What other linear policies are viable?

## Slide 5: Outline of the Talk
Motivation for evaluation methodology
  Extreme cases
The methodology
Results
Hybrid algorithms
Summary

## Slide 6: Can There Ever be a Clear Winner?
Possibly not…
AIMD | AIAD | MIMD | MIAD
0.97 | 0.93 | 0.61 | 0.95
AIMD | AIAD | MIMD | MIAD
0.52 | 0.96 | 0.82 | 0.75

## Slide 7: Evaluation Methodology: Motivation
No single algorithms is superior
  Meaningful comparison is tough
Guiding principles
  Algorithms should not be designed for specific scenario(s)
  Robustness more important than optimality
  Aim is to identify key aspects not to pick winners

## Slide 8: Methodology
Motivation from competitive analysis
A – set of algorithms we wish to compare
A =
E – set of environments the algorithms in A might be faced with

## Slide 9: Methodology Contd..
Rank measures worst-case behavior
Average measures mean behavior

## Slide 10: Choosing A and E
A – limited set of algorithms
  Proven ‘good’ via simulations
E – include wide variety while keeping size small
  Some deliberately extreme
  Some to study key aspects
  Other to be realistic (for now)

## Slide 11: Outline of Results
Impact of Loss Recovery
  Reno-style
  SACK-style
Impact of router queuing behavior
  Effect of RED
  Effect of ECN
  Effect of DRR
Discussion

## Slide 12: Reno-style Loss Recovery
AIMD and AIAD provide identical goodput performance
AIMD is the only fair algorithm
AIMD had the best delay and loss rates too
Reno Drop Tail | Goodput |  | Fairness | Delay | Loss
 | C | D | D | D | D
AIMD | 0.07 | 0.01 | 0.09 | 16.44 | 0.00
AIAD | 0.03 | 0.01 | 0.46 | 31.39 | 0.46
MIMD | 0.34 | 0.22 | 0.14 | 0.13 | 0.86
MIAD | 0.40 | 0.21 | 0.29 | 0.19 | 0.52

## Slide 13: SACK-style Loss Recovery
All schemes except MIAD provide reasonable goodput performance
AIMD is the only fair algorithm. Fairness, loss rates, delays of others worsen
Reno Drop Tail | Goodput |  | Fairness | Delay | Loss
 | C | D | D | D | D
AIMD | 0.19 | 0.03 | 0.06 | 5.73 | 0.00
AIAD | 0.14 | 0.01 | 0.99 | 29.74 | 2.06
MIMD | 0.16 | 0.03 | 1.03 | 4.99 | 1.41
MIAD | 0.46 | 0.16 | 0.84 | 17.44 | 3.99

## Slide 14: Effect of RED + Reno-style Recovery
AIMD and AIAD provide best goodput performance
Fairness of all algorithms improves
Loss rates and delays are low for all schemes
Reno Drop Tail | Goodput |  | Fairness | Delay | Loss
 | C | D | D | D | D
AIMD | 0.06 | 0.01 | 0.10 | 4.34 | 0.00
AIAD | 0.06 | 0.01 | 0.17 | 10.39 | 0.84
MIMD | 0.25 | 0.09 | 0.11 | 1.93 | 0.45
MIAD | 0.37 | 0.13 | 0.11 | 9.81 | 1.36

## Slide 15: Effect of RED + SACK-style Recovery
AIAD provides best goodput performance and is reasonably fair.
Reno Drop Tail | Goodput |  | Fairness | Delay | Loss
 | C | D | D | D | D
AIMD | 0.17 | 0.04 | 0.04 | 1.86 | 0.00
AIAD | 0.00 | 0.00 | 0.33 | 12.39 | 1.70
MIMD | 0.25 | 0.06 | 0.24 | 2.19 | 0.69
MIAD | 0.48 | 0.16 | 0.89 | 12.20 | 2.88

## Slide 16: Effect of ECN
Either form of loss recovery (e.g., SACK, shown below)
MIAD, MIMD and AIAD provide best goodput performance
AIMD provides worst goodput performance
AIMD has the best fairness, delay and loss rate
Reno Drop Tail | Goodput |  | Fairness | Delay | Loss
 | C | D | D | D | D
AIMD | 0.26 | 0.06 | 0.04 | 1.55 | 0.00
AIAD | 0.22 | 0.03 | 0.53 | 14.66 | 1.21
MIMD | 0.15 | 0.05 | 0.38 | 2.49 | 0.56
MIAD | 0.04 | 0.01 | 0.83 | 31.09 | 1.87

## Slide 17: Effect of DRR
Either form of loss recovery (e.g., SACK, shown below)
Same ordering as with drop-tail buffers
All algorithms are now fair
Reno Drop Tail | Goodput |  | Fairness | Delay | Loss
 | C | D | D | D | D
AIMD | 0.03 | 0.01 | 0.11 | 20.31 | 0.00
AIAD | 0.04 | 0.01 | 0.10 | 22.71 | 1.13
MIMD | 0.02 | 0.00 | 0.30 | 17.08 | 1.90
MIAD | 0.36 | 0.13 | 0.22 | 5.82 | 3.61

## Slide 18: Putting It All Together

## Slide 19: Reading into the Results
AIMD is the best if we want
  Great fairness
  Low loss and delay
  Reasonable goodput
AIMD is not always supreme if we want
  Reasonable fairness, loss and delay
  Maximum goodput
But…
  AIAD is a always a leading goodput performer

## Slide 20: A Closer Look at AIAD
AIAD’s weakness
  Unfair at times (FIFO drop-tail setting)
Otherwise shows good performance
How can we cure the AIAD’s unfairness?
  Hybrid algorithms

## Slide 21: Hybrid Algorithms
AIMD etc. are pure linear algorithms
Hybrid algorithms allow both additive and multiplicative components
How can the unfairness of AIAD be fixed?
  Hybrid schemes are the answer to AIAD’s unfairness

## Slide 22: Fairness and Hybrid Schemes
Theorem: An algorithm converges to fairness as long as it is not purely additive (both increase and decrease are additive) or purely multiplicative (both increase and decrease are multiplicative)
Caveat: This does not consider unstable schemes (like MIAD)

## Slide 23: Getting Back to AIAD
How can we cure AIAD?
  Add a small multiplicative component to the decrease
  A-I-M-A-D (additive increase, multiplicative additive decrease)
AIMAD provides
  Good convergence to fairness
  Better loss and delay
  Identical goodput performance

## Slide 24: Hybrid Schemes – Results
AIMAD (AIAD with multiplicative component (0.9) in decrease)
MAIMD (AIMD with multiplicative component (1.1) in increase)

## Slide 25: What did Chiu-Jain Say?
Chiu-Jain do not allow additive component a < 0 in decrease
But our theorem allows AIMAD which has a < 0
The catch
  Chiu-Jain’s conditions are sufficient but not necesary

## Slide 26: Summary
Tested the four basic linear alternatives under a variety of situations
Our work in a line
“If an alternate world were to choose a congestion control algorithm, is AIMD the only possible choice? Our answer is no”.