## Slide 1
The Impact of False Sharing on Shared Congestion Management
Aditya Akella and Srinivasan Seshan (Computer Science Department, Carnegie Mellon University)
Shared Congestion Management
Successful in preventing congestion collapse
But, sub-optimal when there are multiple concurrent flows between source and destination
  Competition for bandwidth
  Ensemble shows aggressive behavior
Advantages
  Enforces co-operation amongst multiple concurrent flows from a source to a destination
  Ensures that the ensembles exhibits reasonable AIMD behavior
Disadvantage
  False sharing – two or more flows sharing congestion state may not share the same bottleneck
Congestion Control Today
Shared Congestion Management
What is False Sharing?
When would congestion sharing with Flow 1 and 2 result in false sharing?
  Flows 1 and 2 treated differently by the network e.g. DiffServ
  Flows 1 and 2 take different paths e.g., dispersity routing, NATs
Flow 1
Flow 2
Evaluate the impact, detection and response
  Is congestion control compromised? & Does performance of individual flows suffer?
  When and how can false sharing be detected?
  How should end systems be modified to deal with false sharing?
Dst
Src
Service Differentiation
  Network may give different flows different QoS
    False sharing occurs when endpoint is unaware of QoS
    E.g. IETF’s Diffserv architecture
  Simulation set-up
    Two Diffserv classes – Assured Forwarding (AF) and Best Effort (BE)
    10 flows belong to AF and 40 belong to BE
Impact of False Sharing
False sharing reduces observed flow throughput
False sharing increases observed flow loss rate
Here 1 and 2 are the respective loss event rates of the two flows, 1 and 2 are the throughputs of the individual flows without sharing, R1 and R2 are their RTTs, and Rmin is min (R1, R2)
Bandwidth in Mbps
Path Diversity
  When flows taking different paths are aggregated into a single macroflow,
  Flows might share some/all/none of the bottlenecks
  Results parallel analytic expectations
Fully Shared Bottleneck
Ratio of RTTs
Bandwidth in Mbps
Unshared Bottleneck
Ratio of bottleneck bandwidths
Bandwidth in Mbps
Semi-Shared Bottleneck
Ratio of potential bandwidths
Bandwidth in Mbps
On-going Work
Currently implementing false sharing detection in linux kernel
Responding to real world issues
  Greater degree of noise in measurements
  Short-lived flows
  Realistic traffic patterns
End-System Response
Flows Share a Bottleneck
Flows Share no Bottlenecks
When the 90% confidence intervals for the auto and cross correlation metrics no longer overlap, the detection test outputs a decision of share or no share
It is harder to detect shared bottlenecks (90 secs) than to detect no shared bottlenecks (35 secs), as can be deduced from the detection times
Design Issues
  Start with a default of sharing congestion
    Scheduling – detection tests work best when packets are nicely interleaved
      Possible only when flows belong to the same macroflow
    Delay and loss correlation tests detect false sharing more easily than they detect shared bottlenecks
    One possible concern – host might transmit data too quickly during detection
      Unlikely, as bandwidth achieved during false sharing is limited by the slower flow
  Upon detection – segregate flows
    Congestion Manager – associate flows with different macroflows
    Addition to API to support control of sharing
Time in Seconds
Correlation Measure
Time in Seconds
Correlation Measure
Detection of False Sharing
Unshared: Loss Correlation Plot
Rule: Uncorrelated delays and losses across flows is a strong indicator of false sharing
Exception
All losses on flow 2
Losses on both flows – back2back losses show as a “pile”
All losses on flow 1
Time in Seconds
Fully Shared: Delay Correlation Plot
Note: Strong correlation between flows
Time in Seconds
Delay in Seconds
Unshared: Delay Correlation Plot
Detecting False Sharing: Tests
Loss Correlation Test: Not as good as delay correlation test
Delay Correlation Test: Does not necessarily segregate flows with inherently different RTTs
Out-of-Order Test: Most robust of the three tests and requires single destination host
Tests do not detect false sharing when none exists
  Loss and delay tests either output a decision that shared bottlenecks exists or remain inconclusive
Time in Seconds
Delay in Seconds
Unshared
Semi-Shared
Fully Shared
Three types of bottleneck sharing (unshared, semi-shared, fully-shared)
Diffserv
AF’s share of bottleneck bandwidth in %-age