## Slide 1
Dynamic Balance Force Control for Compliant Humanoid Robots Benjamin J. Stephens, Christopher G. Atkeson Carnegie Mellon University
4º
10º
a)
b)
c)
4.5kg
Overview
Systems that interact with unknown environments or closely with people must be compliant. This work emphasizes the control of balance in such systems and is demonstrated on a humanoid robot.
COM Dynamics
Humanoid robots are a special type of robot that is not rigidly attached to the ground. The ground contacts represent constraints on the dynamics.
Compliant balance is achieved by first computing contact forces that sum to give a desired force on the center of mass (COM) and balance external task forces and torques. Full body torques are computed from the desired contact forces and the Virtual Model Controls[1] associated with the task.
Dynamic Balance Force Control
Posture Control
Heavy Object Lifting
Posture is controlled by applying a virtual torque to the torso. Not only does this maintain posture but allows the robot to handle larger pushes.
Heavy objects can be lifted by applying a virtual force at the hands. This force can help regulate the height of the object. If the mass of the object is large, an integral control can be added to move the robot’s COM backward so that the center of pressure is in the middle of the feet.
Compliant control of balance and lifting allows the robot to help lift a table, even if it is being pushed around.
[1] Pratt, J, P Dilworth, and G Pratt. “Virtual model control of a bipedal walking robot.” Proceedings of the IEEE International Conference on Robotics and Automation, 1997.
Robot Dynamics
COM Controller
COM Dynamics
COM State Mapping
Feed-Forward Control
COM Motion Planner
Task Controller
Virtual Model Control[1]
Contact Force Calculation
Notes: <number>