## Slide 1
Push Recovery by Stepping for Humanoid Robots with Force
Controlled Joints
Benjamin J. Stephens, Christopher G. Atkeson http://www.cs.cmu.edu/~bstephe1
Overview
This paper presents a step recovery controller using online optimal control to simultaneously determine desired center of mass (COM) acceleration and desired footstep locations that is applied to a force-controlled humanoid robot. This force-based controller allows the robot to be compliant and at the same time recover from disturbances such as large pushes.
Floating Body Force Control
Push Recovery Model Predictive Control
PR-MPC simultaneously solves for a trajectory of the COM and footstep locations using optimal control[1]. The goal state places the COM between the two feet after the step with zero velocity.
The dynamics of the system are represented by a Linear Inverted Pendulum model,
Robot control is achieved by Dynamic Balance Force Control[2] using COM accelerations provided by PR-MPC combined with inverse kinematics using low-gain PD servos.
[1] H. Diedam, D. Dimitrov, P. Wieber, K. Mombaur, and M. Diehl, "Online Walking Gait Generation with Adaptive Foot Positioning Through Linear Model Predictive Control,“ International Conference on Intelligent Robots and Systems, IEEE, 2008, pp. 1121-1126.
[2] Stephens, Benjamin J, and Christopher G Atkeson. “Dynamic Balance Force Control for Compliant Humanoid Robots.” In International Conference on Intelligent Robots and Systems, 2010.
[3] Mistry, M, J Nakanishi, G Cheng, and S Schaal. “Inverse kinematics with floating base and constraints for full body humanoid robot control.” International Conference on Humanoid Robots, 2008.
Full Body Control
giving the trajectory over the next N timesteps:
When combined with a quadratic cost function, the solution simplifies to a quadratic programming problem:
PR-MPC is solved online at a rate of 50Hz using the current state of the humanoid robot. Between evaluations, the desired COM acceleration is used to generate desired full body torques.
Real-time PR-MPC
Floating Body Inverse Kinematics
Feed-forward joint torques are computed by considering both the full floating body dynamics and the desired COM accelerations given by PR-MPC. The system of equations is solved with constraints to keep the center of pressure (COP) under each foot.
Full-body reference poses are generated using floating body inverse kinematics[3]. Low-gain PD controls are added to the feed-forward joint torques.
Footstep locations are included in the optimization
The goal location places COM in the center of the two feet after the step(s)
Linear inequality constraints keep the COP in the base of support
Example trajectory output by PR-MPC
Notes: <number>