## Slide 1: System Identification
Wenzhen Yuan
4/12/2022
16-299 Intro to Feedback Control Systems Spring 2022

## Slide 2: What is System Identification?
System
Output
Input
Goal: calculating the function f with the parameter theta
Typically, this is achieved based on the input and output data

## Slide 3: Model of the system?
White box: A physical/analytical description of the dynamics of a system for which a lot of information is known a priori
Black box: A completely empirical description of the dynamics of a system for which essentially no information is known a priori
Gray box: A combination of the two
  If the “known” white-box part can be subtracted out
System
Output
Input

## Slide 4: System identification: model from data
In general, system ID is experimental and heuristic
Experiment design
Selection of model structure – based on prior knowledge and trial and error
Choice of the criterion to fit
Parameter estimation
Model validation
System
Output
Input

## Slide 5: System identification process: Iterative on many levels
Figure credit: Gregory Plett

## Slide 6: Revisit the topic of transfer function
0
Impulse response:
So, when the input signal is an impulse signal, the output response equals to the system’s transfer function
A way to identify the system!
It’s generalized, works for all LTI systems
Unfortunately, it’s difficult to experimentally generate an impulse signal

## Slide 7: Revisit the topic of transfer function
Step response
0
1
Input signal much easier to generate
Non-parametric methods for system ID
Getting a generic model of the system

## Slide 8: Revisit the topic of transfer function
gain
Phase shift

## Slide 9: The Bode Plot
A method that visualizes the frequency response
(Typically use a log/log scale for the gain curve and a log/linear scale for the phase curve)
Notes: Ideal PID controller

## Slide 10: The Bode Plot
What’s the bold plot for s-1, 1, and s?
What’s the gain and phase shift?

## Slide 11: The Bold Plot
Considering a transfer function:
How to calculate the gain and phase shift?

## Slide 12: The Bode Plot

## Slide 13: Revisit the topic of transfer function
gain
Phase shift
To get the transfer function, we can sweep through all the possible frequencies, and measure the corresponding gain and phase shift
ISSUE: impossible to cover all frequencies from 0 to infinite
-- In practice, we can select only a few frequencies and interpolate between the measured data
ISSUE: For very low frequency inputs, this can take hours or days

## Slide 14: Parametric models
Based on an exiting model. Fitting parameters based on experimental data.
Each of these methods has their own advantages and disadvantages and is commonly used in real-world applications. choice of the model structure to use depends on the dynamics and the noise characteristics of the system

## Slide 15: Parametric model: ARX model
Transfer function
Filters are defined as polynomials
The ARX model is parametrized by
Need to assume the order (na and nb)

## Slide 16: State Space model
X – state vector
Y – system output
U – system input
E – stochastic error
A, B, C, D, K: system matrics
Commonly used in modern control methods; a more complete representations of the system
Parameter settings are simpler – only need to select the order/ states, of the model
May require large number of data points so that could be slow

## Slide 17: Summary
System identification: build the model of the system based on input and output sampling
Experiment-based: design the process of data collection
Non-parametric methods and parametric methods
Various model structures available
  Choice of the model is based on an understanding of the system and the system ID algorithm
Disturbance!
Identification tools (Matlab, Matrix or LabVIEW) are available for developing, prototyping and deploying control algorithms