## Slide 1: DARPA Robotics Challenge Lessons Learned Unanswered Questions

## Slide 2: Team Self Reports
www.cs.cmu.edu/~cga/drc
  These slides
  JFR submission
Wanted to counteract failure videos (robot snuff videos)
CMU vs WPI-CMU: CMU “would have avoided falling down if we went as slow as you…”
Autonomy good?

## Slide 3: Operator Errors Dominated
Top six teams
HRI Matters
Software must detect and handle operator errors.
Safety false alarms kill (Typical suicide bug = deliberately fall down safely)
Finals

## Slide 4: Operators vs. Autonomy
Operators want control at all levels: “Nudging”.
Operators not particularly interested in autonomy.
Design system from ground up to be easy for humans to drive, rather than design a system to be autonomous.
Protect the robot from the operator.

## Slide 5: Most Teams Had A Major Bug Slip Through Testing.
Our bug was an incorrect Finite State Machine for the Drill Task, which led to the drill being dropped.
The 2nd day attempt at the drill task failed because the right forearm overheated and shut off. We had a two handed strategy (bad). We had evidence that this could happen, but failed to act on it.
Finals

## Slide 6: Behavior is too fragile
KAIST drill length
CHIMP friction
WPI-CMU parameter tweaking: MA vs. CA (actually battery vs. offboard power?)
TRACLabs – Atlas behavior variations
AIST Nedo – 4cm ground level error - fall

## Slide 7: Geometry is not enough …
Stairs, ladder, doors, terrain, debris: No use of railings, walls, door frame?
Egress: all about bump and go.
Doors: Walk and push: practice in a wind tunnel.

## Slide 8: Sensing and State Estimation more important than AI, control
Accurate state estimation, not fancy control, is key.
Add more sensors (wrist and knee cameras)
Add task specific sensors.

## Slide 9: Need to design for failure
Hardware failure (Atlas arms)
Many components -> something always broken.
Software failure

## Slide 10: Thermal Management
Robotics is the science of wiring and connectors.
Now it is also the science of waste heat disposal:
  Schaft – water cooled
  Hubo – air cooled
  Atlas – Electric wrist motor always overheating

## Slide 11: Slow and Steady vs. Fast and Flaky
We knew we were going to be slow
  Reliable walk
  How we used human operators
  Lack of total autonomy plus communications delay.
Strategy: Assume other teams will rush and screw up (which happened).
Assume Atlas repairs will not be possible.
Finals

## Slide 12: Project Management Rules Team Steel (VRC) Violated
Freeze early and test, test, test.
  Detect crack of doom bug,
  Don’t introduce suicide bug
  Resist temptation to tweak
Put in safety features to be robust to tired distracted human users.
Make sure your safety features don’t kill you. Suicide bug was not robust to false alarms.
Don’t have project leader also run a division: lose an overall firefighter and skeptic.
VRC

## Slide 13: What we should have done
Start with fully teleoperated systems, and then gradually automate and worry about bandwidth limitations.
Formal code releases
Better interfaces
Periodic group activities that simulated tests or did other things that got people to integrate and test entire systems.
VRC

## Slide 14: Kinematic Targets
Both rough terrain and the ladder, locomotion were dominated by tight kinematic targets.
Basically these are all stepping stone problems.
This is different from most research on legged locomotion.
Trials

## Slide 15: Wheels win?
Cars are useful.
All wheeled/tracked vehicles plowed through debris. All other vehicles walked over rough terrain.
KAIST – walked on stairs; Nimbro, RoboSimian – no stairs
Leg/wheel hybrids good if there is a flat floor somewhere under the pile of debris.
Wheeled/tracked vehicles fell: need to consider dynamics, need to be able to get up (CHIMP, NimbRo), and get un-stuck.
Finals

## Slide 16: Trials Finals
8 KAIST
8 IHMC
8 CHIMP
7 NimbRo
7 RoboSimian
7 MIT
7 WPI-CMU
6 DRC-HUBO UNLV
5 TRACLabs
…
27 Schaft
20 IHMC
18 CHIMP
16 MIT
14 RoboSimain
11 TRACLabs
11 WPI-CMU
9 Trooper
8 Thor
8 Vigir
8 KAIST
3 HKU
3 DRC-HUBO-UNLV
Red = Out of the box thinking

## Slide 17: My Awards
Most Improved Robot: DRC-Hubo
Luckiest Team: IHMC
Unluckiest Teams: CHIMP, MIT
Most Cost Effective Robot: Momaru (NimbRo)
Most Aesthetically Pleasing Egress: RoboSimian
Slow But Steady Award: WPI-CMU

## Slide 18: New funding initiatives
Better hands
Skin: mechanical and sensing
Robust robotics (software and hardware)
  “Drunk Robots”
Robust HRI

## Slide 19: Are Challenges a good idea?
Does doing the challenge crowd out other research? It certainly caused us to put some research on hold, but also led to new issues and redirected our research.
Does the challenge make us more productive? In the short term, yes. In the long term?
Conflict between developing conservative and reliable deployable systems, and understanding hard issues like agility.