## Slide 1: Executable Protocol Specification in ESL Edmund Clarke, Steven German Yun Lu, Helmut Veith, Dong Wang
Notes: Say what ESL is
Say authors
Speak with enthusiasm, loudly, firmly, look at audience

## Slide 2: Problems to Solve
Bus protocol standards
  English specifications are often ambiguous, contradictory, and certainly non-executable
  Standards often include behavioral details of the bus
Goal of this research
  Formal specification of bus protocol standards
  Methods for checking contradictions
  Scalable Methodology
Notes: We want to formalize existing specifications from the standards.

## Slide 3: Why Temporal Logic?
Temporal Logic
  Based on formal logic
  Well developed verification algorithms
Transition-based languages (SMV, HDL)
  Standards are typically given in terms of rules
  Describe implementations, not specifications
  Single-cycle transition constraints only
  Not tailored for protocol formalization
Notes: May say “Standards usually not based on state machines”

## Slide 4: Temporal Logic Specification
Gabbay’s executable temporal logic (Gabbay89)
  Declarative past and imperative future
  Not oriented to protocols, no hardware synthesis intended
Motorola’s Logic
Verisity’s e-logic
Executable Specification Language (ESL)
Notes: May say “Gabbay’s logic has fairness constraints, which describes Buchi automata”

## Slide 5: ESL Methodology
Protocol
Specification
Module
Master
Module
Target
Module
Module
Script
Script
Script
Combiner Machine
Mealy Machine
Mealy Machine
Mealy Machine
Tableau
Construction
Verilog
Program
Protocol Module
Module Master
Module
Module Master
Verilog
Simulation
Synthesis
Verilog Module
Submodule
Submodule
Submodule
Generation of SMV
SMV Model Checking
Checking contradictions etc
Additional Functionality
Notes: Modules correspond to devices on the bus
Scripts describes aspects of the device behaviors

## Slide 6: Translate Standards into ESL
Each device becomes a module
Each English specification becomes a script
  A script can contain several formulas
  Scripts are independent of each other semantically
  Scripts may share variables local to the module

## Slide 7: ESL Language
An ESL script is a finite collection of ESL formulas
  Conjunction of ESL formulas
An ESL module includes
  Input, output and local signals
    Input and output signals are global
  Scripts
    can have common signals
    Modeling independent behaviors of the protocol
An ESL protocol consists of ESL modules

## Slide 8: ESL Logic
ESL logic has an LTL-like syntax
  G P F
    P uses only P (immediate past operator)
    F uses only X
    P and F can refer to present time (combinational logic)
    Standards are naturally specified as “past things determine future behaviors”
ESL logic specifies safety properties
  Trace: infinite sequence of valuations At each time frame, trace determines values of each variable
  Semanticsf: ESL  T  T is a trace satisfying f 
Notes: May say “Traces give sets of values for each variables at each time”

## Slide 9: ESL Module: Semantics
Module ex1 script G(a->X b) script G(a->X ~b)
Trace intersection gives {~a}
  Traces(G(aX b))  Traces(G(aX ~b)) = {~a}
  Same effect as conjunction of scripts
  Conflicts are not visible
We need trace combination
  Traces(G(aX b))  Traces(G(aX ~b)) = ({a}{false}  {~a})
If signal “a” becomes true, the scripts will have a conflict/deadlock

## Slide 10: ESL Module: Semantics
Trace Combination = “pointwise intersection”
  Traces(G(aX b))  Traces(G(aX ~b)) = ({a}{false}  {~a})
Trace projection
  Remove local signals
Module Semantics
  projection( (Traces(scripts)))

## Slide 11: Input Language
Types
  Boolean, bit-vector, enumeration
Parameters
  Modeling arbitrary number of devices
Temporal operators
  All safety operators
  (can be rewritten using X, P and local variables)

## Slide 12: Input Language
An example ESL formula
  “Once a master has asserted IRDY, it cannot change IRDY or FRAME until the current data phase completes regardless of the state of TRDY.”
  G IRDY  XkeepIRDY  keepFRAME W com

## Slide 13: Input Language
Notes: Briefly describe

## Slide 14: Synthesis of Executable Models
Preprocessing
Parsing
Type checking
Parameter instantiation
Module Synthesis
Module Connection
Module port connection

## Slide 15: Script Synthesis-Tableau
Marked Tableau construction
  Based on GPVW95
  But we mark atoms in F by a dot
    GPF.
GabX a
tableau
Notes: Square vs round
When we synthesize a Mealy machine to satisfy this specification, un-dotted variables become Mealy machine input conditions; dotted variables become Mealy machine outputs

## Slide 16: Script Synthesis-Automaton
Tableau to nondeterministic automaton
GabX a
nondeterministic automaton
tableau

## Slide 17: Script Synthesis-Determinize
Determinization by powerset construction
GabX a
nondeterministic automaton
deterministic automaton

## Slide 18: Effect of Determinization
Determinization reduces machine size
All 62 PCI formulas ordered by degree of compression
Compression factor
1.0 = no compression
Notes: There are improved algorithms.
We combine states which will be separated because tableau labellings can only represent a conjunction.

## Slide 19: Script Synthesis-Mealy Machine
Mealy machine generation
GabX a
Mealy machine
deterministic automaton

## Slide 20: Combine Scripts
Combiners for a module
Combiners implement trace combination 
  Each non-input signal has its own combiner
Mealy machine
(script)
v1 v2
Mealy machine
(script)
v1 v2
Mealy machine
(script)
v1 v2
Combiner
v1
Combiner
v2
Combiners are implemented by simple combinational logics

## Slide 21: ESL Synthesis
Main correctness theorem
  ModuleSynthesis preserves ESL semantics
    Semantics: projection( (Traces(scripts)))
Main advantages
  One script at a time, avoid state explosion
  Conflicts between scripts are identified

## Slide 22: Debugging Protocols Using SMV/Verilog
Invalid inputs to a Mealy machine
  Mealy machine asserts badinput for invalid inputs
Synchronization Contradiction between scripts
  Combiner asserts contradict for incompatible traces
Property checking
  Temporal model checking
  Verilog monitors in simulation

## Slide 23: PCI Protocol Specification
A subset is specified and verified
  Verilog:
  SMV: passed 70 independently developed temporal formulas

## Slide 24: Related Work
Program synthesis from temporal logic
  For both CTL(Clarke & Emerson 81) and LTL(Manna & Wolper 82)
  Interleaved asynchronous models of computation
  Tableau construction for global state transition system
Monitors (Shimizu, Dill & Hu in FMCAD00)
  Formal bus protocol specification
  Monitor state machines are constructed manually
  Monitor only observes interface signals
    Building monitors may be tricky, e.g. master abort
  Monitor itself is not executable
    Hard to use as a valid input generator

## Slide 25: Related Work
SpecCheck (Bryant et al, FMCAD00)
  Focuses on Micro-steps and consistency
  ESL concentrates on synthesis of executable models In ESL, various properties of the protocol (e.g. deadlock) can be verified by model-checking/simulating the generated SMV/Verilog code.

## Slide 26: Conclusions
Formal protocol specification in ESL
  An Executable subset of LTL
Efficient algorithm to generate Verilog/SMV model
Support protocol debugging
Future work
  Experiment with other industry bus protocols
  Improve language features, esp. embedding into Verilog
  Interface synthesis from standards

## Slide 27: Disjunctive constraints in ESL
Write one script
  For specifications including a signal as part of a disjunction
    If “a” happens, either “b” or “c” is asserted
    If “e” happens, either “b” is deasserted or “d” is asserted
Use ESL constraint atoms between scripts
  Script1: G(a  assign_range(address, 0, 2^32))
  Script2: G(d  address = 0)