## Slide 1: Using Cutwidth to Improve Symbolic Simulation & SAT
Dong Wang Edmund Clarke
Carnegie Mellon Univ.
Yunshan Zhu James Kukula
Synopsys Inc.

## Slide 2: Outline
Terminology
Algorithms based on cutwidth
  Symbolic simulation
  SAT
Ordering algorithms
Experimental results
Related work
Conclusion

## Slide 3: Hypergraph Cutwidth
Given a hypergraph G(V, E) and a linear ordering L for the vertices
  Order vertices according to L
  Each edge covers a range
The cutwidth under L is the maximal number of overlapping edges
Min-cut ordering has the minimal cutwidth
3
2
1
4
5
A hypergraph with two linear order
4
2
1
3
5

## Slide 4: CNF Formula Cutwidth
Hypergraph for a CNF formula
  Vertices are the variables
  Each hyperedge corresponds to a clause
The cutwidth of a CNF under ordering L
  The cutwidth of the hypergraph under L
(V1+V2+V3+V4)(V3+V4)(V2+V3+V5)
4
2
1
3
5

## Slide 5: Combinational Circuit Cutwidth
Directed hypergraph
  Each edge has a source vertex
Combinational circuit cutwidth
  Vertices are the gates
  Each hyperedge corresponds to a gate and its direct fanout gates, that gate is the source
  Cutwidth is defined on a topological order only
1
2
3
4
5
4
2
1
3
5

## Slide 6: Sequential Circuit Cutwidth
Convert to a combinational circuit
gates
primary
inputs
primary
outputs
latches
primary
inputs
primary
outputs
gates
pseudo-primary
outputs
pseudo-primary
inputs
Restrict the ordering
  Pseudo primary inputs are at the beginning
  Pseudo-primary outputs are at the end
  This corresponds to the lifetime of BDDs for registers in symbolic simulation,

## Slide 7: Symbolic Simulation
The order to build BDDs for gates is a topological order
  A gate is ready when all its input gates have BDDs
  A gate is dead when all its output gates have BDDs
  Either BFS or DFS order is used in practice
Simulation proceeds according to timeframe
  BDDs for registers are copied to next timeframe
The size of the intermediate BDDs is usually much bigger than the final size of the BDDs for the registers

## Slide 8: Symbolic Simulation based on Cutwidth
An Observation
  The number of peak live BDDs equals to the cutwidth of the circuit under that order
1
2
3
4
5
4
2
1
3
5
Live BDDs
Algorithm
  Generate a topological order with small cutwidth
  Use this order to schedule gates during simulation

## Slide 9
Use weighted cutwidth
  Weight a hyperedge according to the BDD size
  Generate an ordering minimizing the weighted cutwidth
  The peak live number of BDD nodes is the weighted cutwidth
Heuristics to estimate the weight of a hyperedge
  The sum of the BDD sizes for the source vertex
  Recalculate an ordering when the estimates become inaccurate
Reduce BDD Nodes

## Slide 10: SAT based on Cutwidth
Many practical problems have logarithmic cutwidth
  Why is ATPG easy (Prasad, Chong and Keutzer, DAC99)
DPLL (Davis-Putnam-Logemann-Loveland) SAT algorithm
  can be bounded exponentially by the cutwidth
Modified SAT Algorithm
  Generate a static ordering with small cutwidth
  Use this ordering to pick decision variables
  When conflict happens
    Cache the assignments to variables above the current decision variable in the ordering

## Slide 11: SAT Complexity
Given a set of clauses S and a variable ordering L, the time complexity of the cutwidth based DPLL is O(n 2w), where n is the length of S and w is the cutwidth of S under L
Conflict clause
4
2
1
3
5
assigned
Assignments to cache

## Slide 12: Ordering Algorithm
Minimum cut linear arrangement is NP-complete
Approximation using divide and conquer
  Minimal edge separator using hMetis
  Use terminal propagation to reduce wire length
Works well for undirected hypergraph
  Used to generate ordering for CNF formula
G
G1
G2

## Slide 13: Ordering for Directed Hypergraph
Use the same divide and conquer algorithm
Methods to get directed partitions
  In symbolic simulation, the partitions for pseudo-primary input/outputs are fixed
  An easy fix, not optimal
    After each bipartition, move vertices in partition 1 to partition 0, if at least one of its input is in partition 0
G
G
1
2
3
4
5
1
2
3
4
5

## Slide 14: SAT Experiments
The ordering program is based on hMetis
The cutwidth based SAT algorithm is implemented on top of fgrasp (cutsat)
DIMACS benchmark set is used
10,000 seconds time limit on 360MHz Sun
Second experiments
  9 SAT problems from Superscalar Suite 1.0a
  Adopt heuristics to choose the decision value
    The value a variable used for the last time

## Slide 15: DIMACS Benchmark

## Slide 16: Superscalar Benchmark

## Slide 17: Symbolic Simulation Experiments
Use CUDD 2.3.0
ISCAS93 circuits are used (31 nontrivial ones)
20,000 seconds time limit and 900M memory limit
Compare cutwidth based simulation (cutsim) with BFS and DFS simulation
The improvements on cutwidth
  DFS is 1.6 times smaller than BFS
  cutsim is 3.2 times smaller than DFS

## Slide 18: Symbolic Simulation Results
Compare cutsim with DFS for runtime
  2 circuits: slightly worse
  10 circuits: slightly better
  14 circuits: 2-10 times improvements
  5 circuits: over an order of magnitude faster
Average improvements for cutsim
  over BFS: 4.5 in time, 2.6 in space
  over DFS: 3.9 in time, 2.4 in space
A sample of the results

## Slide 19: Related Work
Bound BDD size by cutwidth
  C. Berman, 1991
  Ken McMillan, 1992
Quantification scheduling
  Moon & Somenzi, 2000
  Chauhan & Clarke et al., 2001
SAT and cutwidth
  David FERNANDEZ-BACA, 1988
  Prasad, Chong & Keutzer, 1999
  Plaisted, Biere & Zhu, 2001
  Aloul, Markov & Sakallah, 2001

## Slide 20: Conclusion
Extend cutwidth to CNF formulae and circuits
  Use cutwidth to measure the complexity
  Design efficient ordering algorithm
Design a SAT algorithm based on cutwidth
  Demonstrate efficiency on two set of benchmarks
  Use cutwidth to predict the performance
Improved symbolic simulation algorithm
  Reduces the memory complexity
  Has big improvements for ISCAS circuits

## Slide 21: Future Work
Improve the ordering algorithm
  Algorithm for directed hypergraph
  Faster approximation algorithms
Experiments on other SAT solvers
Combine static ordering with dynamic information
Apply cutwidth heuristics in quantification scheduling for image computation