## Slide 1: InvisiSpec: Making Speculative Execution Invisible in the Cache Hierarchy
Mengjia Yan† , Jiho Choi† , Dimitrios Skarlatos,
Adam Morrison∗, Christopher W. Fletcher, and Josep Torrellas
University of Illinois at Urbana-Champaign ∗Tel Aviv University
†Authors contributed equally to this work.

## Slide 2: Motivation: Speculative Execution Attacks
Hardware speculative execution offers a big attack surface for covert and side channels
Speculative execution attacks exploit the side effects of instructions on incorrect speculative paths (squashed)
It is crucial to fix this vulnerability efficiently
Compilers and programmers can not reason about it.

## Slide 3: Outline
Background
A comprehensive threat model
Invisible Speculation (InvisiSpec): the first holistic defense mechanism
Evaluation results and current work

## Slide 4: Speculative Execution Attacks
An example of Spectre Variant 1 (array bound checking attack).
1: if (x < array1_size) {
2: val = array1[x]
3: ld array2[val]
4: }
Victim code
Attack to read arbitrary memory:
Train branch predictor
Trigger branch misprediction
Side channel
Speculative execution attacks exploit side effects of instructions on paths that will be squashed
Leaves side effects in cache

## Slide 5: Generalization of Speculative Execution Attacks
1: if (x < array1_size) {
2: val = array1[x]
3: ld array2[val]
4: }
Transient instructions: speculatively-executed instructions that are destined to be squashed.
Speculative execution attack exploits side effects of transient instructions.
Attack | Sources of Transient Instructions
Spectre | Control-flow misprediction
Meltdown | Virtual memory exception
L1 Terminal Fault | 
Speculative Store Bypass | Address alias between a load and an earlier store
Transient Instruction

## Slide 6: Futuristic Speculative Attack Model
Futuristic speculative attack model
  An attacker can exploit any speculative load (load not at the head of ROB).
  It includes all existing attacks and future speculative execution attacks
Attack Model | Sources of Transient Instructions
Futuristic | Various events, such as: • Exceptions • Control-flow mispredictions • Address alias between a load and an earlier store • Address alias between two loads • Memory consistency model violations • Interrupts
Spectre | Control-flow misprediction

## Slide 7: Lifetime of a load instruction
Load reaches head of ROB
Naïve solution
  Delay issuing the load until its visibility point
Load is issued to memory
Load is speculative
Spectre attack model
Futuristic attack model
All prior branches are resolved
unsafe
safe
unsafe
safe
The load becomes unsquashable
Visibility Point

## Slide 8: InvisiSpec
The first holistic defense mechanism against speculative execution attacks
Key idea:
  Make unsafe loads invisible in the cache hierarchy
Visibility Point
Issue an invisible load request
Obtain the value and proceed to use it
Make the load visible in cache
Load is issued to memory
Load reaches head of ROB
Speculative loads are issued as early as in a conventional machine

## Slide 9: Making Unsafe Loads Invisible
LLC
Invisible load request
  No modification to cache states, including
    Cache occupancy
    Replacement information
    Coherence information
    TLB state
  Bring the data, store in Speculative Buffer (SB) and in register
core
L1 cache
SB
Invisible
load request
Returned data
core
L1 cache
SB

## Slide 10: Making Safe Loads Visible
Make the load visible: HW issues a normal request (which changes the caches)
While in the window of invisibility, processor does not receive invalidations
Window of invisibility
Visibility Point
Issue an invisible load request
Obtain the value and proceed to use it
Make the load visible in cache
Load is issued to memory
Load reaches head of ROB
Risk of memory consistency violations

## Slide 11: An Example of Memory Consistency Violation
An example under TSO
P1
Ld lock
Ld counter
Wr
counter
release
lock
P1
caches
Ld
lock
Ld
counter
time
P1 will not receive an invalidation!
P1 will see the lock is free, but has read old counter.

## Slide 12: Maintaining Memory Consistency
Need to issue another access at Visibility Point: Validation
  HW issues a request (which changes caches)
  Data goes into cache. Compare the incoming data and the one in the SB
  If mismatch, squash the load as it violates memory consistency model
Problem: validations may cause a processor stall
P1
caches
Ld
lock
Ld
counter
Wr
counter
release
lock
time
Visibility point
Ld lock
Visibility point
Ld counter
squash and retry

## Slide 13: Maintaining Memory Consistency (II)
For loads with no risk of memory consistency violation: Exposure
  HW issues a request at the Visibility Point
  Load does not need to wait for response to retire
  Data goes into cache. No need to compare data
High performance: does not cause a stall
P1
caches
Ld X
Wr X
time
Visibility point
Ld X
See the paper for the many cases where a load can use exposures

## Slide 14: Pros & Cons of InvisiSpec
Security
  Successfully prevent attacks in both Spectre and Futuristic attack models
High performance
  Speculative loads are issued as early as in a conventional machine
Applicability
  Handle multi-threaded issues
No software changes
Performance overhead
  Double accesses
  May stall due to validations
BUT: - Many can be converted to exposures
- Most hit in L1, and return very quickly

## Slide 15: Average Execution Time for SPEC and PARSEC (Normalized)
Chart: 
| average
Base | 1
Fe-Sp | 1.74
IS-Sp | 1.21
Fe-Fu | 3.08
IS-Fu | 1.72
Conventional
insecure
baseline
Spectre attack model
Delay load until visibility point
Futuristic attack model
InvisiSpec
Delay load until visibility point
InvisiSpec

## Slide 16: Current Work
Reduce performance overhead: selectively enable InvisiSpec

## Slide 17: More in the paper
Security analysis
Details of when to use validations and exposures, and overlapping of them
Details of implementation
Detailed performance and area overhead evaluation results

## Slide 18: Conclusion
InvisiSpec is the first comprehensive defense mechanism against speculative execution attacks in the cache hierarchy
We published the code of our architecture simulator:
https://github.com/mjyan0720/InvisiSpec-1.0