## Slide 1: Recitation #2 15-213 Section F Spring 2006 Jernej Barbic

## Slide 2: Little Endian to Big Endian
32-bit unsigned integer: n = 37 * 224 + 121 * 216 + 80 * 28 + 178
Little Endian:
Big Endian:

## Slide 3: Little Endian to Big Endian
Little Endian:
Big Endian:
unsigned int LE2BE(unsigned int x)
{
unsigned int result =
(x << 24) | ((x << 8) & (0xFF << 16)) |
((x >> 8) & (0xFF << 8)) | ((x >> 24) & 0xFF);
return result;
}

## Slide 4: If-then-else
if (condition)
expression1;
else
expression2;

## Slide 5: If-then-else
( condition & expression1) | (~condition & expression2)
Rewrite as:
if (condition)
expression1;
else
expression2;

## Slide 6: If-then-else
if (condition)
expression1;
else
expression2;
( condition & expression1) | (~condition & expression2)
Rewrite as:
int abs(int x)
{
int sign = x >> 31; // makes either all one or all zero
int neg_x = ~x + 1; // computes –x (2’s complement) *
return (sign & neg_x) | (~sign & x); // if-then-else
}

## Slide 7: 2’s complement: general rule
= -231 + b
= b
b
b

## Slide 8: 2’s complement: some examples
0x0 = 0
0x1 = 1
0x7FFFFFFF = 231-1 // largest 32-bit int
0xFFFFFFFF = -1
0xFFFFFFFE = -2
0x800000000 = -231 // smallest 32-bit int
0x800000001 = -231 + 1

## Slide 9: Floating point
Single precision:
Double precision:
k = 11, n= 52
Note: exponent boundary is NOT aligned with byte boundary e.g. 0xFF7FFFFF has lowest exponent bit zero (is normalized v.)

## Slide 10: Floating point decision diagram
Is e == 0 ?
x = (-1)s * 21-Bias * 0.M
Is e all 1’s ?
Is M == 0 ?
YES
NO
YES
Is s==0 ?
+
-
NaN
x = (-1)s * 2e-Bias * 1.M
NO
+
YES
YES
NO
NO
denormalized
normalized
Bias = 2k-1 - 1
E
E

## Slide 11: Example
1/4 = 1.0 * 2-2 s=0, e = -2 + Bias = 125, M = 0 representation = 3E800000

## Slide 12: Example #2
-7/8 = -1.11 x 2-1 s = 1 e = -1 + Bias = 126 M = 1100…0 representation = 0xBF600000

## Slide 13: Example #3
-17 = -1.0001 x 24 s = 1 e = 4 + Bias = 131 M = 000100…0 representation = 0xC1880000

## Slide 14: Integer as signed int vs float
3490593 =(int) 0x00354321
3490593.0 =(float) 0x4A550C84
Any correlation in bit patterns?

## Slide 15: Integer as signed int vs float
3490593 =(int) 0x354321:
3490593 = 221 * 1.c
So, we also have 3490593.0 = 221 * 1.c Hence: s=0, e=21+Bias=148, M=c00
c
length(c)=21

## Slide 16: Integer as signed int vs float
3490593 =(int) 0x354321:
3490593.0 =(float) 0x4A550C84:
equal bitstrings

## Slide 17: Good coding style
Consistent indentation
Avoid long sequences of commands without a comment
Each source file should have an appropriate header
Have a brief comment at the beginning of each function

## Slide 18: Quiz #1
Location: blackboard
Open book, open notes, closed computer
Available: today at 4:30pm
Duration: 30 minutes
You must start it by tomorrow 11:30pm
Covers: all material so far
Don’t close your browser while taking the quiz
If there are problems, please email professor