## Slide 1: Trikebot Assembly
Version 1.0

## Slide 2: Servo Horn Enlargement
On steering servo, middle of 3-holes
On the head servoes, 2nd from inside (x 4 per servo)

## Slide 3: Motor Mount
2 x 10-24 x ¾” hold aluminum mounts on motor. Note gap should exist

## Slide 4: Motor Mount – plastic angle
Clean and file plastic pieces
Connect both plastic angles- use 2 holes on each side: 10-24 x 5/8” and ¾”

## Slide 5: Motor Mount - Complete

## Slide 6: King Pin Attach
Attach king pin with 3 bolts on each side
6-32 x 5/8”

## Slide 7: Hub to motor shaft attachment
2 set screws hold the hub on
1 set screw hits the shaft flat

## Slide 8: Tire on wheel stretch-fit
Pull on tire to expand for a few seconds
Attach with Cyanoacrylate (super glue)

## Slide 9: Complete Tire to Kingpin
Attach wheel onto the motor hub using two washers and one nut. Use threadlock on nut holding wheel on motor hub.

## Slide 10: Head Preparation
Clean and punch head pieces
Test fit by hand before screwing

## Slide 11: Head servo tapping
Tap four 4-40 holes on the Tilt Plate that attaches to the tilt servo horn.

## Slide 12: Complete Head
Screw together head pieces using plastic screws
Attach two standoffs for the CMUcam using two 4-40 x 3/8 screws.

## Slide 13: Upper Neck
Tap four 4-40 holes for the pan servo horn, then assemble upper neck assembly

## Slide 14: Lower Neck
Clean, file and assemble lower neck components

## Slide 15: Neck to Top Frame attachment
Use fender washers and screws to hold down lower neck on upper frame (the one with the steering servo mount)

## Slide 16: Test fit lower frame
Test fit lower frame– file as needed

## Slide 17: Top KingPin bushing
Fit top bushing piece into slots in lower neck, below top frame assembly

## Slide 18: Attach upper bushing and lower frame to lower neck

## Slide 19: Test fit main body
Clean, file and test fit main body pieces

## Slide 20: Main body final fit
Don’t forget center battery gate holder

## Slide 21: Screw together main body

## Slide 22: Battery holder gate insertion
This may require filing!

## Slide 23: Upper shelf placement
Test fit upper shelf with aluminum side mounts

## Slide 24: Attach upper shelf
4 screws each side: 8-32 x ½”

## Slide 25: Neck assembly and frame attachment
Slide on upper and lower frame and neck assembly and tighten: 6-32 x 5/8”

## Slide 26: Kingpin and wheel assembly
Slide kingpin up through frame
Above upper bushing is 1 wave washer then 1 metal collar

## Slide 27: Steering servo attachment
Tap two 4-40 holes on plastic collar, then attach to round servo horn using two 4-40 x 3/8 screws.
Attach servo horn to servo using the servo horn screw.
Install steering servo with metal collar loose, then tighten while pushing down on collar.

## Slide 28: Screw down steering servo

## Slide 29: Rear axles and wheels
Attach rear axles and wheels, then collars

## Slide 30: Upper neck attachment
Attach neck pan servo
Adjust and attach upper neck assembly

## Slide 31: Attach head to upper neck
Attach tilt servo
Adjust and attach head to tilt servo