## Slide 1: CMRoboBits: Actuators, Motion
Manuela Veloso
Nick Aiwazian
Sonia Chernova
Thanks to Jim Bruce,
Scott Lenser, and Doug Vail
15-491, Fall 2003
Carnegie Mellon

## Slide 2: Intelligent Complete Robot
Action
Actuators
Perception
External World
Sensors
Cognition

## Slide 3: Sony AIBO Robot

## Slide 4: AIBO Actuators
18 degrees of freedom with a continuously controllable range of motion
  3 DOF in each leg (12 total)
  3 DOF in the head
  2 DOF in the tail
  1 DOF in the jaw
Each joint is controlled by specifying to a desired joint angle to OVirtualRobotComm.
2 binary motors for the ears
A speaker for general sound production

## Slide 5: CMPack Walk Engine
Lowest level: desired angles for joints
Interface: CMPack WalkEngine
  One level of abstraction
  More natural settings to specify desired positions
  Includes all the kinematics computation
Supports both walking and kicking

## Slide 6: Forward Kinematics, Inverse Kinematics, & PID Control in a Nutshell
Nick Aiwazian
September 15, 2003

## Slide 7: Forward Kinematics
Determines position in space based on joint configuration
Denavit-Hartenberg Convention
Conceptually simple (follow convention)

## Slide 8: A simple example
What is the position & orientation of the tool (end effector) relative to the origin?

## Slide 9: Solution
Can be solved trigonometrically!

## Slide 10: Inverse Kinematics
Going backwards
Find joint configuration given position & orientation of tool (end effector)
More complex (path planning & dynamics)
Usually solved either algebraically or geometrically
Possibility of no solution, one solution, or multiple solutions

## Slide 11: Another example
What is the configuration of each joint if the end effector is located at (l1, l2, -)? (Solve for (θ1, θ2) when the tool is at {l1, l2, -})
Let’s assume l1 = l2

## Slide 12: Solution
Or
(Two Solutions)

## Slide 13: PID Control
The Basic Problem:
  We have n joints, each with a desired position which we have specified
  Each joint has an actuator which is given a command in units of torque
  Most common method for determining required torques is by feedback from joint sensors

## Slide 14: The Control Loop

## Slide 15: What is PID Control?
Proportional, Integral, & Derivative Control
  Proportional: Multiply current error by constant to try to resolve error
  Integral: Multiply sum of errors by constant to resolve steady state error (error after system has come to rest)
  Derivative: Multiply time derivative of error change by constant to resolve error as quickly as possible

## Slide 16: Summary
These concepts make up the low level functionality of the AIBO
Implemented once and used repeatedly
For more information about PID Control and Forward & Inverse Kinematics take Matt Mason’s Robotic Manipulation course

## Slide 17: Robot Motion
A 51-parameter structure is used to specify the gait of the robot.
Global Parameters:
Height of Body (1)
Angle of Body (1)
Hop Amplitude (1)
Sway Amplitude (1)
Walk Period (1)
Height of Legs (2)
Leg Parameters:
Neutral Kinematic Position (3x4)
Lifting Velocity (3x4)
Lift Time (1x4)
Set Down Velocity (3x4)
Set Down Time (1x4)

## Slide 18: Kicking
A series of set positions for the robot
Linear interpolation between the frames
  Kinematics and interpolation provided by CMWalkEngine
Set robot in desired positions and query the values of the joints

## Slide 20: Very Effective Kicks

## Slide 21: High Sensitivity to Parameters Good Settings for Effective Kick

## Slide 22: High Sensitivity to Parameters Exact Same Settings - Lab

## Slide 23: High Sensitivity to Parameters Good Settings for the Lab

## Slide 24: Approaches for Parameter Setting
Trial and error
  Tedious, but controlled, and provides knowledge of parameters
Search
  Large parameter space, local vs. global optima
Adaptation
  Controlled change by feedback

## Slide 25: Motor Control
Each message to OVirtualRobotComm contains a set of target angles for the joints
  Each target is used for a PID controller (part of the AIBO robot) that controls each motor
  Each target angle is used for one 8ms motor frame
Each message contains at least 4 motor frames (32ms)

## Slide 26: Use of Kicks in Behaviors
Modeling effects of kicking motions
  Ball vision analysis
  Ball trajectory angle analysis
  Kick strength analysis
Kick selection for behaviors
  Selection algorithm
  Performance comparison
(Sonia Chernova’s senior thesis)

## Slide 27: Accuracy of Object Detection Varies -- Robot Standing --
Distance (mm)

## Slide 28: Accuracy of Object Detection Varies -- Robot Pacing --
Distance (mm)

## Slide 29
Distance (mm)
Accuracy of Object Detection Varies – Robot Spinning --

## Slide 30: Ball Trajectory Angle
Estimate the angle of the ball’s trajectory relative to the robot
Track ball’s trajectory after the kick
Retain information about ball position in each vision frame
Calculate angle of trajectory using linear regression

## Slide 31: Angle Analysis
Forward Kick
Right Head Kick
Left Head Kick

## Slide 32: Kick Strength
Estimate the distance the ball will travel after a kick.
Impossible to track entire path of the ball
Calculate only the final location of the ball relative to the kick position
Estimate failure rate of the kick using distance threshold

## Slide 33: Forward Kick Distance Analysis

## Slide 34: Head Kick Distance Analysis

## Slide 35: Kick Selection
Incorporate the kick models into the selection algorithm
  The robot knows its position on the field relative to the goal and the desired ball trajectory
  The robot selects appropriate kick by referencing the kick model
  If no kick fits desired criteria, robot selects closest matching kick and turns/dribbles ball to appropriate position

## Slide 36: Kick Selection Performance
Experiment Results |  | 
Point | CMPack’02 (sec) | Modeling & Prediction (sec)
P1 | 56.7 | 39.8
P2 | 42.5 | 27.2
P3 | 76.5 | 60.0
P4 | 55.0 | 52.0
Total | 57.8 | 44.8

## Slide 37: Kick Selection in Action

## Slide 38: Summary
Effectively moving a four-legged robot is challenging
Effectiveness of motion is highly sensitive to motion parameters
CMWalk provides the kinematics computations, so parameter setting can be at a high level of abstraction.
Ideally, we would like to set parameters automatically.

## Slide 39: The Motion Interface
Sonia Chernova

## Slide 40: The Motion Interface
Walk Engine
Walk Parameters
Frame Interpolator
Motion Frames
Dynamic Walking Motion
Static Frame-Based Motion

## Slide 41: Coordinate Frames
0
2
3
1
y
x
y
x
Motion Coordinate Frame
Vision Coordinate Frame
a
a

## Slide 42: The Walk Engine
All of the inverse kinematics have been done for you!
All you have to deal with are the “motion parameters”
Your Goal: Create fluid, stable motion

## Slide 43: Motion Parameters
Neutral Kinematic Position (3x4)
Lift Velocity (3x4)
Lift Time (1x4)
Down Velocity (3x4)
Down Time (1x4)
Front Leg Height Limit (1)
Back Leg Height Limit (1)
Height of Body (1)
Angle of Body (1)
Hop Amplitude (1)
Sway Amplitude (1)
Walk Period (1)
Leg Parameters (46)
Body Parameters (5)

## Slide 44: Motion Parameters
Neutral Kinematic Position (3D vector relative to the motion coordinate frame) - Position of the leg on the ground at some point during the walk cycle
Think of it as the position the legs would be in if the dog was pacing in place using your walk parameters
Path of the leg during 1 cycle

## Slide 45: Motion Parameters
Lift Velocity (3D vector) – Velocity (mm/sec) with which the leg is lifted off the ground
Down Velocity (3D vector) – Velocity (mm/sec) with which the leg is placed on the ground
Lift Time and Down Time – This controls the order of the legs by specifying a percentage of the time through the time cycle that each leg is moved

## Slide 46: Motion Parameters
Front and Back Leg Height Limit (mm) – Upper bound on the height of the airpath of the front and back legs.
Air path of leg with height limit

## Slide 47: Motion Parameters
Body Angle (radians) – Angle of the body relative to the ground measured at the origin of the motion coordinate frame
Body Height (mm) – Height of the body relative to the ground measured at the origin of the motion coordinate frame
Walk Period (ms) – Time of one walk cycle
Hop and Sway Amplitudes (mm) – Amplitude of vertical and horizontal oscillations (Value usually set to 0)

## Slide 48: Creating a Parameter Set (1)
Motion::WalkParam wp;
wp.leg[0].neutral.set( 125, 82,0);
wp.leg[1].neutral.set( 125,-82,0);
wp.leg[2].neutral.set( -100, 75,0);
wp.leg[3].neutral.set( -100,-75,0);
wp.period = 640;
wp.leg[0].lift_vel.set(0,0, 100);
wp.leg[1].lift_vel.set(0,0, 100);
wp.leg[2].lift_vel.set(0,0, 150);
wp.leg[3].lift_vel.set(0,0, 150);
wp.leg[0].down_vel.set(0,0,-100);
wp.leg[1].down_vel.set(0,0,-100);
wp.leg[2].down_vel.set(0,0,-100);
wp.leg[3].down_vel.set(0,0,-100);
Neutral Leg Position
Lift Velocity
Down Velocity
Motion Cycle
Period (ms)
Parameter Struct
Values are in millimeters, milliseconds or radians!

## Slide 49: Creating a Parameter Set (2)
wp.leg[0].lift_time=0.0000; wp.leg[0].down_time=0.5000;
wp.leg[1].lift_time=0.5000; wp.leg[1].down_time=1.0000;
wp.leg[2].lift_time=0.5000; wp.leg[2].down_time=1.0000;
wp.leg[3].lift_time=0.0000; wp.leg[3].down_time=0.5000;
wp.body_angle = RAD(16.0);
wp.body_height = 98;
wp.hop = 0;
wp.sway = 0;
wp.front_height = 9.0;
wp.back_height = 9.0;
out = fopen("walk_xy.prm","wb");
if(out){
fwrite(&wp,sizeof(wp),1,out);
fclose(out);
}
Leg Order
Save to .prm File
Limit how high the legs are lifted

## Slide 50: Primary Motion Parameters
Neutral Kinematic Position (3x4)
Lift Velocity (3x4)
Lift Time (1x4)
Down Velocity (3x4)
Down Time (1x4)
Front Leg Height Limit (1)
Back Leg Height Limit (1)
Height of Body (1)
Angle of Body (1)
Hop Amplitude (1)
Sway Amplitude (1)
Walk Period (1)
Leg Parameters (46)
Body Parameters (5)

## Slide 51: Running Your Code
Edit: ~/dogs/agent/Motion/genmot/genwalk.cc
Compiling code:
~/dogs/agent/Motion/genmot> make
~/dogs/agent/Motion/genmot> ./genmot
>Kinemaric Errors=[0] [0]
[0] [0]
Saving to the stick:
~/dogs/agent/Motion/genmot> mount /memstick
~/dogs/agent/Motion/genmot> cp walk_xy.prm /memstick/motion/
~/dogs/agent/Motion/genmot> umount /memstick

## Slide 52: Running Your Code
Compiling code:
~/dogs/agent/Motion/genmot> make
~/dogs/agent/Motion/genmot> ./genmot
>Kinemaric Errors=[0] [0]
[0] [0]
Saving to the stick:
~/dogs/agent/Motion/genmot> mount /memstick
~/dogs/agent/Motion/genmot> cp walk_xy.prm /memstick/motion/
~/dogs/agent/Motion/genmot> umount /memstick
What are these errors?

## Slide 53: Questions?

## Slide 54: Frame-Based Motion

## Slide 55: Frame-Based Motion
Each motion is described by a series of “frames” which specify the position of the robot, and a time to interpolate between frames
Movement between frames is calculated through linear interpolation of each joint

## Slide 56
The position of the robot in each frame can be described using any of the following:
  Position of the legs - in terms of angles of each joint or position of the foot in motion coordinates
  Angle of the head (tilt, pan, roll)
  Body height and angle
  Angle of the mouth
struct BodyState{
BodyPosition pos;
LegState leg[4];
HeadState head;
MouthState mouth;
};

## Slide 57: Examples: Valid Motion Frames
LegAng(b,0, 0.0, 1.5, 0.0);
LegAng(b,1, 0.0, 1.5, 0.0);
LegAng(b,2, 0.1, 0.0, 0.2);
LegAng(b,3, 0.1, 0.0, 0.2);
m[n].body = b;
m[n].time = 100;
n++;
BodyPos(b,98,RAD(16));
HeadAng(b, 0.5, 1.5, 0.0);
MouthAng(b,-.7);
LegPos(b,0, 123, 85,0);
LegPos(b,1, 123,-85,0);
LegPos(b,2, -80 , 75,0);
LegPos(b,3, -80 ,-75,0);
m[n].body = b;
m[n].time = 100;
n++;
BodyPos(b,98,RAD(16));
HeadAng(b, 0.5, 1.5, 0.0);
LegPos(b,0, 123, 85, 0);
LegPos(b,1, 123,-85, 0);
LegAng(b,2, 0.1, 0.0, 0.2);
LegAng(b,3, 0.1, 0.0, 0.2); m[n].body = b;
m[n].time = 100;
n++;
m[n].body = b;
m[n].time = 100;
n++;

## Slide 58: Running Your Code
Edit: ~/dogs/agent/Motion/genmot/genmisc.cc
Compiling code:
~/dogs/agent/Motion/genmot> make
~/dogs/agent/Motion/genmot> ./genmot
>Kinemaric Errors=[0] [0]
[0] [0]
Saving to the stick:
~/dogs/agent/Motion/genmot> mount /memstick
~/dogs/agent/Motion/genmot> cp k_bump.mot /memstick/motion/
~/dogs/agent/Motion/genmot> umount /memstick
In your code:
command->motion_cmd = MOTION_KICK_BUMP;

## Slide 59: Joint Angle Limits

## Slide 60: Information
Two readings will be made available off the Webpage.
Wednesday’s lab will be about debugging tools using wavelan communication to and from the robots.
Homework 2 is due in class on Wednesday and Homework 3 will be handed out then.
John deCuir, SONY, USA, will present the new ERS-7 robots at the beginning of the class on Monday, September 22nd.