## Slide 1: Visual Sonar: Obstacle Detection for the AIBO
Paul E. Rybski
15-491 CMRoboBits:
Creating an Intelligent AIBO Robot
Prof. Manuela Veloso

## Slide 2: 2D Spatial Reasoning for Mobile Robots
Extract meaningful spatial data from sensors
Metric
  Accurate sensing/odometry
  Relative positions of landmarks
  Sensors identify distinguishable features
Topological
  Odometry less important
  Qualitative relationships between landmarks
  Sensors identify locations
Edmonton Convention Center
AAAI 2002
http://radish.sourceforge.net

## Slide 3: Using Vision to Avoid Obstacles
Analogous to ultrasonic range sensors
  Given some assumptions, vision can return range and bearing readings to obstacles
  Requires a local model of the world
Visual Sonar on the AIBOs
  Problems:
    Running into other robots during games (?)
    Handling non-standard obstacles outside of games
  Technical challenges:
    AIBO only has a monocular camera
    All spatial reasoning must happen at frame rate
    Not all obstacles are as well-defined as the ball

## Slide 4: Visual Sonar
0.5 m
increments
White wall
Unknown
obstacles
Robot Heading

## Slide 5: Visual Sonar Algorithm
Segment image by colors
Vertically scan image at fixed increments
Identify regions of freespace and obstacles in each scan line
Determine relative egocentric (x,y) point for the start of each region
Update points
  Compensate for egomotion
  Compensate for uncertainty
  Remove unseen points that are too old

## Slide 6: Image Segmentation
Sort pixels into classes
Obstacle:
  Red robot
  Blue robot
  White wall
  Yellow goal
  Cyan goal
  Unknown color
Freespace:
  Green field
Undefined occupancy:
  Orange ball
  White line

## Slide 7: Scanning Image for Objects
Scanlines projected from origin for egocentric coordinates in 5 degree increments
Top view
of robot
Scanlines projected onto RLE image

## Slide 8: Measuring Distances with the AIBO’s Camera
Assume a common ground plane
Assume objects are on the ground plane
  Elevated objects will appear further away
  Increased distance causes loss of resolution

## Slide 9: Identifying Objects in Image
Along each scanline:
  Identify continuous line of object colors
  Filter out noise pixels
  Identify colors out to 2 meters

## Slide 10: Differentiate walls and lines
Filter #1
  Object is a wall if it is a least 50mm wide
Filter #2
  Object is a wall if the number of white pixels in the image is greater than the number of green pixels after it in scanline

## Slide 11: Keeping Maps Current
Spatial:
  All points are updated according to the robot’s estimated egomotion
  Position uncertainty will increase due to odometric drift and cumulative errors due to collisions
  Positions of moving objects will change
Temporal:
  Point certainty decreases as age increases
  Unseen points are “forgotten” after 4 seconds

## Slide 12: Navigating from the AIBO Point of View

## Slide 13: Egocentric Point-Based View

## Slide 14: Interpreting the Data
Point representations
  Single points are very noisy
  Overlaps are hard to interpret
  Point clusters show trends
Occupancy grids
  Probabilistic tessellation of space
  Each grid cell maintains a probability (likelihood) of occupancy

## Slide 15: Calculating Occupancy of Grid Cells
Consider all of the points found in a grid cell
If there are any points at all, the grid is marked as being observed
Obstacles increase likelihood of occupancy
Freespace decreases likelihood of occupancy
Contributions are summed and normalized
If the sum is greater than a threshold (0.3), the cell is considered occupied with an associated confidence

## Slide 16: Probabilistic Representation of Space

## Slide 17: Comparing Points and Grid

## Slide 18: Simple Behavior for Navigating with Visual Sonar
If path ahead is clear, go straight
Else accumulate positions of obstacles to left and right of robot
  Turn towards the most open direction
  Set turn speed proportional to object distance
  Set linear speed inversely proportional to turn speed

## Slide 19: Navigating with Visual Sonar

## Slide 20: Examing Visual Sonar Data from Log Files
Enable dump_vision_rle and dump_move_update in config/spout.cfg
Open captured log file with local model test
  % lmt <logfile>
  Requires vision.cfg file (points at config files)
    colors_file=“colors.txt”;
    thresh_base=“thresh”;
    marker_color_offset=-0.5;
  Commands:
    ‘space’ to step through logfile
    ‘p’ to enable point view
    ‘o’ to enable occupancy-grid view
Notes: The color classification we use tends to not pick up colors blended with pink but does pick up colors blended with white.
This causes a 0.5 pixel bias in the centroid of the color region which then makes distance readings be too small.
The marker_color_offset parameter corrects for this bias by moving the centroid of the colored region.
This parameter should be –0.5 in order to make the colored region move the 0.5 pixels towards the pink region.

## Slide 21: Accessing the Visual Sonar Points
In the file: dogs/agent/WorldModel/LocalModel.h
Simple point interface
  Search region defined by arbitrary bounding box
  Apply a function to each point in a region
  // general query interface
  // basis – unit vector in x direction relative to robot
  // center – center of query relative to robot
  // range – major, minor size of query in basis reference frame
  void query_full(vector2f ego_basis, vector2f ego_center, vector2f range, Processor & proc);
  // easy robot centric interface for rectangles (corresponds to a basis
  // of (1.0,0.0))
  // minv – minimum values for robot relative bounding box
  // maxv – maximum values for robot relative bounding box
  void query_simple(vector2f ego_minv, vector2f ego_maxv,Processor & proc);

## Slide 22: Accessing the Visual Sonar Occupancy Grid
In the file: dogs/agent/WorldModel/LocalModel.h
Occupancy grid interface
  Calculate occupancy of a full grid
  void calc_occ_grid_cells(int x1, int y2, int x2, int y);
  Calculate the occupancy of a single cell
  void calc_occupancy(OccGridEntry *cell, vector2f ego_basis, vector2f ego_center, vector2f range);
  Get a pointer to a grid cell
  const OccGridEntry *get_occ_grid_cell(int x_cell, int y_cell);
Each cell contains information on:
  Observation [0.0,1.0] (0.0=clear, 1.0=obstacle)
  Evidence [0.0,…] (number of readings)
  Confidence of each object class data

## Slide 23: Efficiency Considerations
Points are stored in a binary tree format
  Allows for quicker lookup in arbitrary regions
Too many lookups will cause skipped frames
  Points should be accessed only if absolutely needed
  Redundant lookups should be avoided if at all possible

## Slide 24: Open Questions
How easy is it to follow boundaries?
  Odometric drift will causes misalignments
  Noise merges obstacle & non-obstacle points
    Where do you define the boundary?
How can we do path planning?
  Local view provides poor global spatial awareness
  Shape of AIBO body must be taken into account in order to avoid collisions and leg tangles

## Slide 25: Feature Extraction Ideas
Occupancy Grid
Obstacles
Closest Obstacles
Right Wall
Hough Transform
Door
Reference: P. E. Rybski, S. A. Stoeter, M. D. Erickson, M. Gini, D. F. Hougen, N. Papanikolopoulos, "A Team of Robotic Agents for Surveillance,"
Proceedings of the Fourth International Conference on Autonomous Agents, pp. 9-16, Barcelona, Spain, June 2000.

## Slide 26: Hough Transform* for Lines
Search in the space of parameters for most likely line : y=mx+c
  Set up an accumulator A(m,c)
Each (x,y) point increments the accumulator for each valid line parameter set
The highest-valued entries in A(m,c) correspond to the most likely lines
Downsides
  Accuracy is dependent on discretization of parameters
*Reference : Ballard and Brown, Computer Vision.

## Slide 27: Hough Transform Visualized

## Slide 28: Path Planning from Sensor Information
Global sensor info
  Builds a global world model based on sensing the environment.
  Pros
    Guaranteed to find an existing solution
  Cons
    Computationally heavy
    Requires frequent localization
Local sensor info
  Navigate using sensors around local objects
  Pros
    Much simpler to implement
  Cons
    Not guaranteed to converge – will get stuck in a local minima with no hope of escape
We’d like something in the middle…

## Slide 29: Bug Path Planning References
V. Lumelsky and A. Stepanov, “Path-Planning Strategies for a Point Mobile Automaton Moving Amidst Unknown Obstacles of Arbitrary Shape”, Algorithmica (1987) 2: 403-430.
I. Kamon, E. Rivlin, and E. Rimon, “A New Range-Sensor Based Globally Convergent Navigation Algorithm for Mobile Robots”, in Proc. IEEE Conf. Robotics Automation , 1996.
S. L. Laubach and J. W. Burdick, “An Autonomous Sensor-Based Path-Planner for Planetary Microrovers”, in Proc. IEEE Conf. Robotics Automation, 1999.
…

## Slide 30: Bug Path Planning Methodology
Combine local with global information
Guaranteed to converge if a solution exists
Drive to goal
Follow an obstacle
Encounter
obstacle
“Leaving condition”

## Slide 31: Choosing a locally optimal direction
Case 1: Non-concave obstacle
  Find the endpoints o1 and o2 of the representation of the intersecting obstacle
  Let A1 = angle between target, robot, and o1
  Let A2 = angle between target, robot, and o2
  Direction = min(A1, A2)

## Slide 32: Choosing a locally optimal direction
Case 2: Concave obstacle
  Let M = the point where the direction between the robot and the target would intersect the obstacle
  Let d(M, T) = distance between M and the target
  If d(M, T) < d(o1,T) and d(M,T) < d(o2,T)
    Switch from drive to goal to boundary follow
    Direction = min(A1, A2)
Notes:   Same as last slide…
  Find the endpoints o1 and o2 of the representation of the intersecting obstacle
  Let A1 = angle between target, robot, and o1
  Let A2 = angle between target, robot, and o2
  The point at which this occurs is called the switch point or S

## Slide 33: Tangent Bug Leaving Condition
Let d_followed(T) = the minimal distance from T observed along the obstacle so far
Let P be a reachable point in the visible (within sensor range) environment of the robot
Leaving condition is true when d(P,T) < d_followed(T)