image sensors: device implementations
image sensors:
real device implementations

---
my favorite (but now old) CCD …
my favorite (but now old) CCD …

---
Kodak KAF-400 CCD specs
Kodak KAF-400 CCD specs
must mean for
1/20 second
exposure time

---
pixel size, signal, & signal-to-noise
pixel size, signal, & signal-to-noise
- charge accumulates at a rate proportion to light intensity per unit area of pixel
- capacitance is proportional to pixel area
- so for a given light intensity, exposure time, and cell depth, the signal voltage (accumulated charge / cell capacitance)
  is independent of cell area
- but signal-to-noise improves with larger accumulated charge, hence with cell area

---
additional reading
additional reading
in our AFS readings directory:
  - SENSORS02_05-image_sensors.pdf
    - apparently from somebody’s course
    - encompasses biological and electronic systems
    - I found it on the web
    - I don’t remember where & can’t find it again …
  - sensorsCaptureAttention.pdf
    - comprehensive article on CMOS image sensors

---
other (not CCD) kinds of  modern image sensors
other (not CCD) kinds of
modern image sensors

---
CID: charge injection device
CID: charge injection device
CCDs are inherently serial readout: no way to address an individual pixel
could realize better dynamic range, electronic zooming, etc., if could address individual pixels
CID has been promising “around the corner” possibility for ~20 years

---
CMOS image sensors
CMOS image sensors
uses same
technology as
standard memory
chips
economical:
uses highly-tuned
high-volume
production
allows high
degree of
integration
between imaging
and image
processing

---
Foveon: color-film in silicon
Foveon: color-film in silicon
(with lots of material processing compromises to achieve correct filtering and decent transmission)

---
special purpose hybrid devices e.g., “night vision”, “image intensifiers” etc
special purpose
hybrid devices
e.g., “night vision”,
“image intensifiers”
etc

---
X-ray image intensifier
X-ray image intensifier
similar hybrid methods used in “night vision scopes” (Russian  cheap)