echo-based range sensing

---
example: low-cost radar
automotive DC in / digital radar signal out
applications include
pedestrians / bicycles in urban environment
obstacles / vehicles in highway environment
smart cruise control

---
general principles
  - lidar / ladar
  - radar
  - ultrasound
  - etc
contrasting implementations

---
rangefinder goal
measure the distance to a “target”
  - something like an obstacle in the roadway
   by observing how changes in distance
   cause changes in a measurable property
   of {light, sound, radio waves} that travel
   to and from the target
properties commonly measured:
  - phase of the optical radiation (near)
  - phase of an imposed modulation (middle)
  - time-of-flight (far)

---
optical phase
- principle is interference of a wave that is split in two, travels two different paths, and are then recombined with a time-of-flight difference between them
- used mostly in extremely high precision measurements of very small distances
  - as in machining of very precise parts
not typically used in robotics applications

---
source
detector

---
exercise – not assigned now
suppose the detector in the Michelson interferometer (previous slide) is a CCD
  - what would the image look like when the path difference is between the split beams is an integral number of wavelengths?
  - ½ + integral number of wavelengths?
  - somewhere in between?
  - is there any limit to how big the integer can get before the simple explanation fails and you need to understand more to explain it?

---
time-of-flight (ToF)
- measure the time to “see” or “hear” echo
- range (distance): z = c t / 2
  - t = ToF from source to target back to sensor
  - ½ assumes source & sensor are in same place
light: c ≈ 3 x 108 m s-1
  - in vacuum
  - slower by factor ≈ 1.33 in water, ≈ 1.5 in glass
- radio waves (radar) same as light
- sound (sonar): c ≈ 343 m s-1
  - in air at normal temperature
  - ≈ 1500 m s-1 in water at normal temperature

---
exercise – not assigned now
On an early moon landing an astronaut set up a panel with about ½ m2 of corner cube reflectors. A pulsed laser was aimed at it from earth, and the earth-moon distance thereby measured to high precision. Estimate the ToF between transmitted and received laser pulses. If the laser beam spreads to 1 mile diameter at the moon and the return beam – also spread to about 1 mile diameter on earth – is captured by a 100-inch-diameter telescope, how much energy do you need in each laser pulse to average one detected photon from each pulse? Don’t forget to state your assumptions! [FYI, I think all these numbers are the right order-of-magnitude except for the return beam diameter on earth, which I don’t actually remember; extra credit if you can find and use it!]

---
is ToF easy or hard to measure?
velocity of sound is small enough that it is
easy to measure ToF directly (sonar)
velocity of light (and radio) is big enough
that it is hard to measure ToF directly
unless the range is large, i.e., more that 1 km
so for short-range ranging with light (lidar) or radio (radar) we measure ToF indirectly
i.e., we use the phase of the modulation
mws@cmu.edu 16722 20080304 L07Ta

---
modulation phase
Φc = 2π x / λc
x = path difference, λc = wavelength of light or radar
difficult to measure Φc unless x < λc
use the light or radar as a carrier for a lower frequency ( longer wavelength) modulation that changes slowly compared to the fast rate-of-change of sin(2π fc t)
it is relatively easy to measure how the phase
of the modulation changes with path difference

---
modulation option 1
AM (amplitude modulation, but really intensity modulation): M(t) = A0 sin(2π fm t)
measure phase shift of echo relative to transmission:
A0 sin(2π fm t)  A1 sin(2π fm t + Φm)
Φm = 2π x / λm
(λm = c / fm) >> (λc = c / fc )
so Φm << Φc is relatively easy to measure
time 
amplitude 

---
modulation option 2
FM (frequency modulation):
M(t) = A0 sin(2π fc (1 + Amsin2π fm t) t))
FM radio signal: tone at frequency fm
     M(t) = A0 sin(2π fc (1 + Am sawtooth(t) t))
typical modulation for FMCW laser rangefinder

---
electronics for AM detection
phase sensitive amplifier
generally two channels:
modulation ~ sin(ωt)
one channel reference (“I”) ~ sin(ωt)
second channel reference (“Q”) ~ cos(ωt)
Φ = arctan(SignalQ/SignalI)
maybe do the arithmetic digitally …
but possibly better to do it by analog computing
something like arctan[exp[ln[SignalQ]-ln[SignalI]]]
implemented in components with nonlinear I vs. V

---
exercise – not assigned now
A green laser, wavelength 488 nm, is (amplitude) modulated at 10 MHz. For a target at 100 m range, what is the phase shift of the return signal relative to the transmitted signal and the ratio SignalQ/SignalI. What is n, the phase ambiguity in modulation wavelengths?
Show that if you change the wavelength a small known amount and measure again you can resolve the ambiguity.

---
electronics for FM detection
option 1: simple “mixer”:
combine a sample of the currently
transmitted signal and the (delayed)
received signal using a non-linear amplifier
low frequency signal appears at the
difference frequency ( range)
(A sin(2π ftransmitted t) + B sin(2π freceived t))2
upon expansion, trigonometric identities
reveal a term proportional to
sin(2π (ftransmitted – freceived) t)

---
electronics for FM detection
option 2: FFT module
record the echo vs. time
digitize it
perform an FFT
intensity at each frequency corresponds
to echo strength at corresponding distance

---
exercise – not assigned now
Using the green laser from your AM laser rangefinder to build an FM laser rangefinder, what frequency slew rate (Hz/second) would you need to observe a difference frequency of 10 kHz when the target range is 100 m?
Is there an ambiguity problem with FM modulation? (explain!)