## Slide 1: 15-744: Computer Networking
L-1 Intro to Computer Networks

## Slide 2: Outline
<number>
Administrivia
Layering

## Slide 3: Who’s Who?
<number>
Professor: Srinivasan Seshan
  http://www.cs.cmu.edu/~srini
  srini@cs.cmu.edu
  Office hours: by appt.
TA: Zhuo Chen
  http://www.cs.cmu.edu/~zhuoc/
  Zhuoc [at] cs [at] cmu [dot] edu
Course info
  http://www.cs.cmu.edu/~15744/

## Slide 4: Objectives
<number>
Understand the state-of-the-art in network protocols, architectures and applications
Understand how networking research is done
  Teach the typical constraints and thought processes used in networking research
How is class different from undergraduate networking (15-441)
  Training network programmers vs. training network researchers

## Slide 5: Web Page
<number>
Check regularly!!
Course schedule
Reading list
Lecture notes
Announcements
Assignments
Project ideas
Exams

## Slide 6: Discussion Site
On Piazza
  Please signup at http://piazza.com/cmu/spring2017/15744
<number>

## Slide 7: Discussion Site
For each lecture, post a brief comment about each paper:
  Since I would like to read the reviews before the lecture, you should have this done by 5pm the day before the lecture.
  Learn to critique and appreciate systems papers
Each student will present on the lecture topic once this semester
  10 min presentation
  Choose a relevant but uncovered paper
  Email signup
<number>

## Slide 8: How to read a paper (3-pass approach)
Skim abstract/intro + section headings + references (5-10min)
  Make rough assessment of paper
  Many people will read your paper at this level
Read but ignore details (e.g. proofs) (1hr)
  Good general understanding of techniques
  Identify related work you need to look at
”Virtual re-implementation” (1-3hrs)
  Identify hidden assumptions
  Identify issues with techniques used
<number>

## Slide 9: How to read a paper
Learn to be critical
  Many papers are part “marketing” – trying to show their design in the best possible light
  Some papers may be “old”
Learn to be positive
  Very easy to become overly critical especially once you know topic area
  Focus on what you learned from the paper
Why or why not keep this paper in syllabus?
What issues are left open for future research?
What are the important implications of the work?
What would you have done differently or differently now?
<number>

## Slide 10: Course Materials
<number>
Research papers
  Links to ps or pdf on Web page
  Combination of classic and recent work
  ~40 papers
  Optional readings
Recommended textbooks
  For students not familiar with networking
  Peterson & Davie, Kurose & Ross, Tanenbaum & Wetherall

## Slide 11: Grading
<number>
Homework assignments (15%)
  4 Problem sets & hands-on assignments
Class + discussion site participation (10%)
Midterm exam + final exam (40%)
  Closed book, in-class
2 or 3 person project (35%)
  Main focus of class work
  Make project productive for you!
Notes: <number>

## Slide 12: Class Coverage
<number>
Little coverage of physical and data link layer
Little coverage of undergraduate material
  Students expected to know this or learn this along the way
Focus on network to application layer
We will deal with:
  Protocol rules and algorithms
  Investigate protocol trade-offs
  Why this way and not another?

## Slide 13: Lecture Topics
<number>
Traditional
Layering
Internet architecture
Routing (IP)
Transport (TCP)
Queue management (FQ, RED)
Naming (DNS)
Recent Topics
Data centers
Mobility/wireless
Security
Content delivery
SDN
P2P systems
Privacy
+ some TBD slots

## Slide 14: Homework 0 (due tomorrow)
Email zhuoc@cs.cmu.edu & srini@cs.cmu.edu
  4 lecture choices for presentation
  1 sentence version of project interest areas & list of project partner
    E.g., I want to apply game theory to network routing
  1 request for TBD lecture slot
<number>

## Slide 15: Outline
<number>
Administrivia
Layering

## Slide 16: This/Friday Lecture: Design Considerations
<number>
How to determine split of functionality
  Across protocol layers
  Across network nodes
Assigned Reading
  [SRC84] End-to-end Arguments in System Design
  [Cla88] Design Philosophy of the DARPA Internet Protocols
Optional Reading
  [CT90] Architectural Considerations for a New Generation of Protocols

## Slide 17: What is the Objective of Networking?
<number>
Communication between applications on different computers
Must understand application needs/demands
  Traffic data rate
  Traffic pattern (bursty or constant bit rate)
  Traffic target (multipoint or single destination, mobile or fixed)
  Delay sensitivity
  Loss sensitivity
Notes: <number>
Some example applications: video, audio, telnet, ftp, http, rpc – what are their needs

## Slide 18: Back in the Old Days…
<number>

## Slide 19: Packet Switching (Internet)
<number>
Packets

## Slide 20: Packet Switching
Positives
Interleave packets from different sources
Efficient: resources used on demand
  Statistical multiplexing
General
  Multiple types of applications
Allows for bursty traffic
  Addition of queues
Challenges
Store and forward
  Packets are self contained units
  Can use alternate paths – reordering
Contention
  Congestion
  Delay
<number>

## Slide 21: Internet[work]
<number>
Internet[work]
A collection of interconnected networks
Host: network endpoints (computer, PDA, light switch, …)
Notes: <number>
What if want to communicate between hosts on different Ethernets? Internet as interoperability layer

## Slide 22: Internet[work]
<number>
Internet[work]
A collection of interconnected networks
Host: network endpoints (computer, PDA, light switch, …)
Router: node that connects networks
Notes: <number>
What if want to communicate between hosts on different Ethernets? Internet as interoperability layer

## Slide 23: Challenge
<number>
Many differences between networks
  Address formats
  Performance – bandwidth/latency
  Packet size
  Loss rate/pattern/handling
  Routing
How to translate between various network technologies?

## Slide 24: Challenge 1: Address Formats
<number>
Map one address format to another?
  Bad idea  many translations needed
Provide one common format
  Map lower level addresses to common format

## Slide 25: Challenge 2: Different Packet Sizes
<number>
Define a maximum packet size over all networks?
  Either inefficient or high threshold to support
Implement fragmentation/re-assembly
  Who is doing fragmentation?
  Who is doing re-assembly?

## Slide 26: Gateway Alternatives
<number>
Translation
  Difficulty in dealing with different features supported by networks
  Scales poorly with number of network types (N^2 conversions)
Standardization
  “IP over everything” (Design Principle 1)
  Minimal assumptions about network

## Slide 27: IP Standardization
Minimum set of assumptions for underlying net
  Minimum packet size
  Reasonable delivery odds, but not 100%
  Some form of addressing unless point to point
Important non-assumptions:
  Perfect reliability
  Broadcast, multicast
  Priority handling of traffic
  Internal knowledge of delays, speeds, failures, etc
<number>
Notes: <number>

## Slide 28: How To Find Nodes?
<number>
Internet
Computer 1
Computer 2
Need naming and routing

## Slide 29: Naming
<number>
What’s the IP address for www.cmu.edu?
It is 128.2.11.43
Translates human readable names to logical endpoints
Local DNS Server
Computer 1

## Slide 30: Routing
<number>
R
R
R
R
R
H
H
H
H
R
R
H
R
Routers send packet towards destination
H: Hosts
R: Routers

## Slide 31: Meeting Application Demands
<number>
Reliability
  Corruption
  Lost packets
Flow and congestion control
Fragmentation
In-order delivery
Etc…

## Slide 32: What if the Data gets Corrupted?
<number>
Internet
GET windex.html
GET index.html
Solution: Add a checksum
Problem: Data Corruption
0,9
9
6,7,8
21
4,5
7
1,2,3
6
X

## Slide 33: What if Network is Overloaded?
<number>
Problem: Network Overload
Short bursts: buffer
What if buffer overflows?
  Packets dropped
  Sender adjusts rate until load = resources  “congestion control”
Solution: Buffering and Congestion Control

## Slide 34: What if the Data gets Lost?
<number>
Internet
GET index.html
Problem: Lost Data
Internet
GET index.html
Solution: Timeout and Retransmit
GET index.html
GET index.html

## Slide 35: What if the Data Doesn’t Fit?
<number>
Problem: Packet size
Solution: Fragment data across packets
On Ethernet, max IP packet is 1.5kbytes
Typical web page is 10kbytes
GET
inde
x.ht
ml
GET index.html

## Slide 36: What if the Data is Out of Order?
<number>
Solution: Add Sequence Numbers
Problem: Out of Order
GET
x.ht
inde
ml
GET x.htindeml
GET index.html
ml
4
inde
2
x.ht
3
GET
1

## Slide 37: Lots of Functions Needed
<number>
Link
Multiplexing
Routing
Addressing/naming (locating peers)
Reliability
Flow control
Fragmentation
Etc….

## Slide 38: What is Layering?
<number>
Modular approach to network functionality
Example:
Link hardware
Host-to-host connectivity
Application-to-application channels
Application
Notes: <number>

## Slide 39: Protocols
<number>
Module in layered structure
Set of rules governing communication between network elements (applications, hosts, routers)
Protocols define:
  Interface to higher layers (API)
  Interface to peer
    Format and order of messages
    Actions taken on receipt of a message
Notes: <number>
Human analogy – social customs

## Slide 40: Layering Characteristics
<number>
Each layer relies on services from layer below and exports services to layer above
Interface defines interaction
Hides implementation - layers can change without disturbing other layers (black box)

## Slide 41: Layering
<number>
Host
Host
Application
Transport
Network
Link
User A
User B
Layering: technique to simplify complex systems

## Slide 42: E.g.: OSI Model: 7 Protocol Layers
<number>
Physical: how to transmit bits
Data link: how to transmit frames
Network: how to route packets
Transport: how to send packets end2end
Session: how to tie flows together
Presentation: byte ordering, security
Application: everything else

## Slide 43: OSI Layers and Locations
<number>
Switch
Router
Host
Host
Application
Transport
Network
Data Link
Presentation
Session
Physical

## Slide 44: IP Layering (Principle 2)
<number>
Relatively simple
Sometimes taken too far
Router
Router
Host
Host
Application
Transport
Network
Link

## Slide 45: IP Hourglass
Need to interconnect many existing networks
Hide underlying technology from applications
Decisions:
  Network provides minimal functionality
  “Narrow waist”
Tradeoff: No assumptions, no guarantees.
Technology
Applications
email WWW phone...
SMTP HTTP RTP...
TCP UDP…
IP
ethernet PPP…
CSMA async sonet...
copper fiber radio...
<number>
Notes: <number>

## Slide 46: Is Layering Harmful?
<number>
Sometimes..
  Layer N may duplicate lower level functionality (e.g., error recovery)
  Layers may need same info (timestamp, MTU)
  Strict adherence to layering may hurt performance

## Slide 47: Friday Lecture: Design Considerations
<number>
How to determine split of functionality
  Across protocol layers
  Across network nodes
Assigned Reading
  [SRC84] End-to-end Arguments in System Design
  [Cla88] Design Philosophy of the DARPA Internet Protocols

## Slide 48: Homework 0
(by Friday) Email zhuoc@cs.cmu.edu & srini@cs.cmu.edu
  4 lecture choices for critique/public review
    Note that lecture dates may shift
  1 topic choice for first TBD lecture
  1 sentence version of project interest & list of project partner
    E.g., I want to apply game theory to network routing.
We will be posting some questions on Piazza to answer about the two papers for Friday’s lecture (post response by 5pm on Thursday)
<number>

## Slide 49: Layer Encapsulation
<number>
Get index.html
Connection ID
Source/Destination
Link Address
User A
User B

## Slide 50: Protocol Demultiplexing
<number>
Multiple choices at each layer
FTP
HTTP
TFTP
NV
TCP
UDP
IP
NET1
NET2
NETn
…
TCP/UDP
IP
IPX
Port Number
Network
Protocol Field
Type Field
Notes: <number>